## Slide 1: Chapter 2: Memory
CEG2400 – Embedded System Design

## Slide 2: Overview
1) Memory in a computer system
2) Different memory types
3) Concepts of address, data and program running

## Slide 3: 1) Memory in a computer system
A computer has
  CPU (Central Processing Unit)
  Memory
  Input/output and peripheral devices
  Glue logic circuits

## Slide 4: Inside an ARM microcontroller
Inside ARM
CPU: Central Processing unit
memory
Peripheral devices: serial, parallel interfaces; real-time-clock etc.
Clock
Oscillator
Peripheral devices: USB, serial, parallel bus etc.

## Slide 5: A computer with a micro-controller unit
CPU: Central Process-ing unit
memory
Peripheral devices: USB ports, Graphic card, real-time-clock etc.
Keyboard
mouse
Sensors:
Light,
Temperature
Etc.
actuators :
such as
Motors,
Heaters,
speakers
External interfacing
Peripheral IO interface devices: such as USB bus, parallel bus, RS232 etc.
MCU:

## Slide 6: CPU, MCU are microprocessors
CPU: Central Processing unit
  Requires memory and input output system to become a computer (e.g. Pentium is a CPU).
MCU: micro-controller unit (or single chip computer)
  Contains memory, input output systems, can work independently (e.g. Arm7, 8051 are MCUs).
  Used in embedded systems such as washing machines, mobile phones/pads.

## Slide 7: 2) Different memory types
Random access memory (RAM)
Read only memory (ROM)

## Slide 8: Different kinds of Random access Memory (RAM)
Random access memory (RAM): data will disappear after power down.
  Static RAM (SRAM): each bit is a flip-flop, fast but expensive.
  Dynamic RAM (DRAM): each bit is a small capacitor, and is needed to be recharged regularly; slower but cheap. To be used as primary memory in a computer.
http://thalia.spec.gmu.edu/~pparis/classes/notes_101/img111.gif
http://www.prontotech.com/product/kingston-8gb-dram-memory-module-p_1732875237

## Slide 9: Different kinds of Read Only Memory (ROM)
Read only memory (ROM)
  UV-EPROM
  EEPROM
  FLASH ROM

## Slide 10: UV-EPROM
Data can be erased by putting it under strong Ultra-Violet (UV) light for 1/2 hours.

## Slide 11: Flash memory
Block based read/write, e.g. one block can be 512 or 1024 bytes, etc.
Read/write is slower than DRAM, so it cannot be used as the primary memory of a computer.
www.sandisk.com

## Slide 12: Exercise 0
What are these memory types: (DRAM, SRAM, ROM) in a computer? Explain why.
Central Processing Unit
CPU
Registers: memory type = _______?
Primary memory for storing program and data: memory type=______?
Firmware (basic input/output system or BIOS )
memory type=___________?
Registers 暫存器

## Slide 13: 3) Concepts of address, data and program running
Address-- tells you where to find the storage.
Data-- is the content stored in the address.

## Slide 14: Exercise 1: Binary number and hex number
A binary number can be 1 or 0
4 binary numbers make up a hexadecimal (hex) number (0->F)
Exercise1
  Convert 3AH into binary .
  Convert a binary number 100001011100B into hex and decimal.
Binary | Decimal | Hex
0000 | 0 | 0
0001 | 1 | 1
0010 | 2 | 2
0011 | 3 | 3
0100 | 4 | 4
0101 | 5 | 5
0110 | 6 | 6
0111 | 7 | 7
1000 | 8 | 8
1001 | 9 | 9
1010 | 10 | A
1011 | 11 | B
1100 | 12 | C
1101 | 13 | D
1110 | 14 | E
1111 | 15 | F

## Slide 15: Memory is like a tall building Address cannot change; content (data) can change
Address content, e.g. A 64K-byte RAM
16-bit Address (H=Hex) | 8-bit content (data)
FFFF H | 35H
FFFE H | 23H
… | …
0ACD H | 24H
… | …
0001 H | 32H
0000 H | 2BH

## Slide 16: Memory for storing program and data (An 8-bit machine)
Basic concept Memory is like a tall building Address cannot change; content (data) can change
16-bit Address (H=Hex) | 8-bit content (program /data)
FFFF H | 35H
FFFE H | 23H
… | …
0ACD H | 24H (do something)
… | …
0001 H | 32H
0000 H | 2BH (goto 0ACDH)
After power up , goto 0000H , run
instructions in data

## Slide 17: Two important modules in a 8-bit CPU (because data is 8-bit, e.g. Intel 8051): Program counter and registers
A Central Processing Unit (CPU) has
  PC : program counter to keep track the program
  R0, R1, etc, for general purpose usage
Memory
(data is 8-bit)
An 8-bit CPU (Intel 8051)
Registers (8 bits):
PC: program counter
R0 (general purpose)
R1 (general purpose)

## Slide 18: Program counter (PC)
After CPU reset (power up) , PC=0000H, so the first instruction is always at 0000H.
After each instruction is run,
  PC increments once, or
  PC is set by the instruction it just executed. E.g. goto to a new address.

## Slide 19: How does a computer work? What is the content of Program counter (PC) after each step?
Program is in memory
16-bit Address (H=Hex) | 8-bit content (data)
FFFF H | 35
FFFE H | 23
… | …
0ACD H | 24 (goto FFFF)
… | …
0001 H | 32
0000 H | 2B (goto0ACD)
After power up
PC=0000H
step1
step2
step3
Inside an 8-bit Central Process.Unit
General purpose registers ( 8bits): | R0=xxH R1=yyH …etc.
Program counter (16 bits):
PC xxxxH

## Slide 20: Exercise2 : A simple program , fill in ‘?’
After power up, the first instruction is in 0000H, PC=0000H
Address (H=Hex) | 8-bit content (data)=instructions (Hex) | PC before Running the instruction (hex) | PC after Running the instruction (hex)
0BC8 | Instruction k = 25: (meaning R0<=R0+1) | ? | ?
… | … |  | 
0AC1 | … |  | 
0AC0 | Instruction j = 24 (meaning :goto 0BC8) | ? | ?
… | … |  | 
0001 | Instruction 2=xx |  | 
0000 | Instruction1=2B (meaning : goto 0AC0H) | ? | ?

## Slide 21: Exercise 3: Program to find 2+3=?, Fill in ‘?’
PC=program counter; R0=general purpose register 0
Address (H=Hex) | 8-bit content (data) The machine code is make up for this example | Before the instruction is run |  | After the instruction is run | 
 |  | PC | R0 | PC | R0
0F00 |  | What is the Content after the program is run? |  |  | 
0AD3 | 3F=stop | 0AD3 | ? | ? | ?
0AD2 | C0=Save R0 into address location 0F00 and clear R0 | 0AD2 | ? | ? | ?
0AD1 | 2E=Add 2 to Reg .R0 | 0AD1 | ? | ? | ?
0AD0 | 15=Move 3 into Reg. R0 | 0AD0 | ? | ? | ?
… | … |  |  |  | 
0001 | … |  |  |  | 
0000 | 2B=Goto address 0AD0 | 0000 | 0 (after reset) | ? | ?

## Slide 22: Memory in a 32-bit machine
Moving from 8-bit to 32-bit:
The ARM processor example

## Slide 23: ARM chip

## Slide 24: Memory
We will learn how to use memory in the ARM microcontroller.
We know that the data size is 8-bit for all memory systems (in PC or mainframe alike).
So each location has 8 bits.
  We can deal with them in n-bit groups called words (typically 8, 16, 32 or 64 bits)

## Slide 25: Address in a 32-bit machine (e.g. ARM7)
The address is 32-bit.
  So the address range is from 0000 0000(hex) to FFFF FFFF(hex) totally 2^32=4G locations.
The data is also 32-bit.
  So each data is xxxx xxxx (hex)
But the memory is arranged as 8-bit for one location. So how to do it?
Solution: Arm7 uses 4 address locations to access a 32-bit (4 bytes) data.

## Slide 26: Rules/Examples
Each location must be 8-bit.
For a 32-bit word, you are referring to 4 locations.
0000 0003H | 
0000 0002H | 
0000 0001H | 
0000 0000H | 
A 16-bit word
(0000 0002->
0000 0003H)
One byte
at
0000 0000H
One byte
At
0000 0001H
32-bit
Word
(0000 000 ->
0000 0003H)
Address
data

## Slide 27: Organization of memory in ARM
second 32-bit word
First 32-bit word
n
=32bits (4 bytes)
last 32-bit word
i
th word
•
•
•
•
•
•
0x0000 0010
0x0000 000C
0x0000 0008
0x0000 0004
0x0000 0000
Address
0xFFFF FFFC
0xFFFF FFF8
1Byte 1 Byte 1 Byte 1 Byte
n
=32bits (4 bytes)
Address is
incremented by 4

## Slide 28: Compare 8-bit (e.g.8051) and 32-bit (Arm7) machines
examples
An 8-bit machine program (e.g. 8051) | 
Address (H=Hex) | Each data is 8-bit (1 byte)
0F00 | 13
: | :
0AD2 | 21
0AD1 | 22
0AD0 | 89
… | …
0001 | 4A
0000 | 2D
A 32-bit machine program (e.g. ARM) | 
Address (H=Hex) | Each data is 32-bit (4 bytes)
1E00 0ADC | 1123 556D
1E00 0AD8 | 0012 2A3F
1E00 0AD4 | 2134 5678
1E00 0AD0 | 3A11 89A1
: | 
0000 0008 | 1122 3344
0000 0004 | 9870 A178
0000 0000 | 0000 002A
Address is incremented by 4
Address is incremented by 1

## Slide 29: Integers and Characters
(b) Four characters
character
character
character
character
(a) A signed integer
Sign bit:
for positive numbers
for negative numbers
ASCII
ASCII
ASCII
ASCII
32 bits
8 bits
8 bits
8 bits
8 bits
b
31
b
30
b
1
b
0
b
31
0
=
b
31
1
=
•
•
•

## Slide 30: Exercise 4: More/less significant bytes
Consider the hexadecimal (base 16) 32-bit number 12342A3F(H)=1x167+2x166+3x165+4x164+2x163+10x162+3x161+15x160
This number has four bytes 12, 34, 2A, 3F (4x8=32-bits)
Bytes/bits with higher weighting are “more significant” e.g. the byte 34 is more significant than 2A
Bytes/bits with lower weighting are “less significant”
We also use terms “most significant byte/bit” and “least significant byte/bit”
Excise4: For 12342A3F(H)
  Write the binary number.
  What is the most significant byte/bit?
  What is the least significant byte/bit?

## Slide 31: Big/little endian
Two different ways: byte addresses are assigned across words
  more significant bytes first (big endian)
  less significant bytes first (little endian)
ARM allows both big and little endian addresses
  LPC2100 allows big and small endians

## Slide 32: Examples From http://en.wikipedia.org/wiki/Endianness
  more significant bytes first (big endian)
  less significant bytes first (little endian)
Most significant
least significant

## Slide 33: Exercise 5, fill in ‘?’
Save 0x2EAB057E in memory starting from 0x4000
Address (data in each address location must be 8-bit) | Little endian data | Big endian data
0x4000 | 7E | ?
0x4001 | ? | ?
0x4002 | ? | ?
0x4003 | ? | 7E

## Slide 34: Word alignment
32-bit words align naturally at addresses 0, 4, 8 …
  These are aligned addresses
Unaligned accesses are either not allowed or slower e.g. read a 32-bit word from address 1 (why?)
  E.g 0x2EAB057E from 0x4000 is aligned
  E.g 0x2EAB057E from 0x4001 is misaligned
In ARM
  A word = 32-bits, half-word = 16 bits
  Words aligned on 4-byte boundaries i.e. word addresses must be multiples of 4
  Half words aligned on even byte boundaries

## Slide 35: Example of word alignment
32-bit words align naturally at addresses 0, 4, 8..etc
That means a (address)= 0,4,8,… or
a(address)=4N where N=integer
a is a multiple of N

## Slide 36: End

## Slide 37: References/ reading exercise
http://www.howstuffworks.com/computer-memory.htm
ARM versus Intel: a successful stratagem for RISC or grist for CISC's tricks?
  http://www.edn.com/design/integrated-circuit-design/4369610/ARM-versus-Intel-a-successful-stratagem-for-RISC-or-grist-for-CISC-s-tricks-