## Slide 1: Chapter 4 Addressing modes
CEG2400 Microcomputer Systems

## Slide 2: Objective
In this lecture, you will learn some assembly operations for data transfer from CPU to memory / from memory to CPU

## Slide 3: Overview
Memory concept revision
Data Transfer Instructions - LDR instruction (Load Address into Register)
  Ref: http://infocenter.arm.com/help/index.jsp?topic=/com.arm.doc.dui0041c/Babbfdih.html
Register-indirect addressing using load (LDR) / store (STR)
Block copying

## Slide 4: 1)Memory concept
Program code and data are saved in memory.
They occupy different locations
labels | 32-bit Address (HEX) | 8-bit data Program/Data
Org | 0000 0000 | 03
 | 0000 0001 | 24
 | : | 
TABLE1 | 0001 0000 | 12
 | 0001 0001 | 3B
 | 0001 0002 | A4
 | 0001 0003 | 34
 | 0001 0004 | B2
 | 0001 0005 | D2
: |  | 
TABLE2 | 0002 0000 | 24
 | 0002 0001 | 6C
: |  | 
Four
8-bit
data
form
a
32-bit word
Program
See
appendix
For
big/little
endian
formats

## Slide 5: 2) Data Transfer Instructions - LDR instruction (Load Address into Register)
LDR r1, =adress_label
  It is a pseudo instruction (Combining several instructions)
  Details, see appendix for how it is actually implemented
E.g. LDR r1, =TABLE1
If TABLE1 is at 0001 0000H, then r1 = 0001 0000H after the instruction is run. Similarity for r2 and TABLE 2.
copy1 LDR r1, =TABLE1 ; r1 points to TABLE1
copy2 LDR r2, =TABLE2 ; r2 points to TABLE2
…….
TABLE1 …… ; <source of data>
……
TABLE2 …… ; <destination of data>
  Ref: http://infocenter.arm.com/help/index.jsp?topic=/com.arm.doc.dui0041c/Babbfdih.html

## Slide 6: 3) Register-indirect addressing using load (LDR) / store (STR)
  http://infocenter.arm.com/help/index.jsp?topic=/com.arm.doc.dui0041c/Babbfdih.html

## Slide 7: How we can operate the data inside memory?
In ARM architecture, data must place in register before performing basic operations
You can’t perform operation directly to memory
Data
Data
Memory
Data
Data
Memory
Register
Register

## Slide 8: Reason to use Load (LDR) / store (STR)
Therefore, we need the operation to help us load the data from memory to register, and store the data from register to memory.

## Slide 9: Data Transfer Instructions - single register load/store instructions
Use a value in one register (called the base register) as a memory address [ ] and either loads the data value from that address into a destination register or stores the register value to memory (mem32[r1] means: r1 holds the address, mem32[r1] =data content):
LDR r0, [r1] ; r0 := mem32[r1]
;(content in r1 is an address)
STR r0, [r1] ; mem32[r1] := r0 This is called register-indirect addressing
LDR r0, [r1]
Address
Because we are not accessing the data directly

## Slide 10: Example : Data Transfer Instructions
Use LDR
copy LDR r1, =TABLE1 ; r1 points to TABLE1
LDR r2, =TABLE2 ; r2 points to TABLE2
LDR r0, [r1] ; load first value ….
STR r0, [r2] ; and store it in TABLE2
…….
TABLE1 …… ; <source of data>
……
TABLE2 …… ; <destination of data>

## Slide 11: Exercise 4.1 Fill in the shaded areas.
Address (H) |  |  | Comments | After instruction is run (hex) |  |  | 
 | start | All registers are rest to 0 here |  | 0004 0000 (TABLE2) | R0 | R1 | R2
0001 0000 | copy | LDR r1,=TABLE1 | ;r1 points to TABLE1 |  |  |  | 
 |  | LDR r2,=TABLE2 | ;r2 points to TABLE2 |  |  |  | 
 |  | LDR r0, [r1] | ;load first value |  |  |  | 
 |  | STR r0, [r2] | ;and store it in TABLE2 |  |  |  | 
 |  | : | : |  |  |  | 
0002 0000 | TABLE1 | 12345678 | ;<source of data> |  |  |  | 
 |  | : |  |  |  |  | 
0004 0000 | TABLE2 | 00000063 | ;<destination of data> |  |  |  | 

## Slide 12: Block copy for two data: Data Transfer Instructions
The following example copies data from TABLE1 to TABLE2 (show how to copy two values)
copy LDR r1, =TABLE1 ; r1 points to TABLE1
LDR r2, =TABLE2 ; r2 points to TABLE2
LDR r0, [r1] ; load first value ….
STR r0, [r2] ; and store it in TABLE2
ADD r1, r1, #4 ; add 4 to r1
ADD r2, r2, #4 ; add 4 to r2
LDR r0, [r1] ; load second value ….
STR r0, [r2] ; and store it in TABLE2
…..
TABLE1 …… ; <source of data>
……
TABLE2 …… ; <destination of data>

## Slide 13: Exercise 2 --page1 Block copy for N=5 data : Data Transfer Instructions
Copy N=5 data from TABLE 1 to TABLE2
copy LDR r1, =TABLE1 ; TABLE1=0002 0000H
LDR r2, =TABLE2 ; TABLE2=0004 0000H
MOV r3,#0 ;setup counter at R3
loop1 LDR r0, [r1] ; load first value ….
STR r0, [r2] ; and store it in TABLE2
ADD r1, r1, #4 ; add 4 to r1
ADD r2, r2, #4 ; add 4 to r2
ADD r3, r3, #1 ; increment counter
CMP r3,#5 ; repeat N=5
BNE loop1 ; loop back when N<5
…..
TABLE1 …… ; <source of data>
……
TABLE2 …… ; <destination of data>

## Slide 14: Exercise 2 --page2, Fill in blacks (hex) for the loop after each time line 9 is executed
After line 9 is run | Time=1 | Time=2 | Time=3 | Time=4 | Time=5
R3 (Hex)= | 1 | 2 | 3 | 4 | 5
R0 (Hex) | 0000 00A1 |  |  |  | 
R1 (Hex) | 0002 0004 |  |  |  | 
R2 (Hex) | 0004 0004 |  |  |  | 
Z (zero) of CPSR,Z=1 if result 0 else Z=0 | 0 |  |  |  | 
Table 1, from 0002 0000- 0002 0013H | 0000 00A1 0000 00B2 0000 00C3 0000 00D4 0000 0055 |  |  |  | 
Table 2, from 0004 0000- 0004 0013H | 0000 00A1 0000 0000 0000 0000 0000 0000 0000 0000 |  |  |  | 

## Slide 15: 4) Block copying: We will study these for block data copy
LDR r0, [r1] ; register-indirect addressing
LDR r0, [r1 , # offset] ; pre-indexed addressing
LDR r0, [r1 , # offset]! ; pre-indexed, auto-indexing
LDR r0, [r1], # offset ; post-indexed, auto-indexing

## Slide 16: Use of pre-indexed addressing mode LDR r0, [r1, #offset] Base plus offset addressing
pre-indexed addressing mode
  LDR r0, [r1, #4] ; r0 := mem32 [r1 + 4]
r1 Unchanged
base address
offset
effective address
r1 will not be changed by pre-indexed addressing instructions
LDR r0, [r1, #4] ; r0 : = mem32 [r1 + 4]

## Slide 17: Pre-indexed addressing, LDR r0, [r1, #offset]
Copy and copy2 (shown below) have the same effect
Simple method
Better method using pre-indexing
copy LDR r1, =TABLE1 ; r1 points to TABLE1
LDR r2, =TABLE2 ; r2 points to TABLE2
LDR r0, [r1] ; load first value ….
STR r0, [r2] ; and store it in TABLE2
ADD r1, r1, #4 ; step r1 onto next word
ADD r2, r2, #4 ; step r2 onto next word
LDR r0, [r1] ; load second value …
STR r0, [r2] ; and store it
copy2 LDR r1, =TABLE1 ; r1 points to TABLE1
LDR r2, =TABLE2 ; r2 points to TABLE2
LDR r0, [r1] ; load first value ….
STR r0, [r2] ; and store it in TABLE2
LDR r0, [r1, #4] ; load second value …
STR r0, [r2, #4] ; and store it

## Slide 18: Pre-indexed with auto addressing mode LDR r0, [r1, #offset]!
pre-indexed auto addressing mode, using (!), changes the pointer reg. (e.g. r1 here ) after used.
LDR r0, [r1, #4]! ; r0 := mem32 [r1 + 4]
r1 = r1+offset=r1+#4
base address
offset
effective address
r1 will be changed by pre-indexed addressing instructions
LDR r0, [r1, #4]! ; r0 : = mem32 [r1 + 4]
; r1 := r1 + 4

## Slide 19: Exercise 4.3
AfterLine | r0 | r1 | r2 | 0002 0000-0002 0003 | 0002 0004-0002 0007 | 0004 0000- 0000 4003 | 0004 0004- 0004 0007
1 | 0000 0000 | 0002 0000 | 0000 0000 | 1357 2468 | A123 B246 | 0 | 0
2 |  |  |  |  |  |  | 
3 |  |  |  |  |  |  | 
4 |  |  |  |  |  |  | 
5 |  |  |  |  |  |  | 
6 |  |  |  |  |  |  | 
Copy LDR r1, =TABLE1 ; TABLE1=0002 0000
LDR r2, =TABLE2 ; TABLE2=0004 0000
LDR r0, [r1] ; load first value ….
STR r0, [r2] ; and store it inTABLE2
LDR r0, [r1, #4] ; load second value
STR r0, [r2, #4] ; and store it
LDR r0, [r1, #4]! ; r0 : = mem32 [r1 + 4]
; r1 := r1 + 4
LDR r0, [r1, #4] ; r0 : = mem32 [r1 + 4]
(all in hex)
r1,r2 will NOT be changed by pre-indexed addressing instructions

## Slide 20: Exercise 4.4
Copy LDR r1, =TABLE1 ; TABLE1=0002 0000
LDR r2, =TABLE2 ; TABLE2=0004 0000
LDR r0, [r1] ; load first value ….
STR r0, [r2] ; and store it inTABLE2
LDR r0, [r1, #4]! ; load second value,r1 will change
STR r0, [r2, #4]! ; and store it, r2 will change too
After line | r0 | r1 | r2 | 0002 0000-0002 0003 | 0002 0004-0002 0007 | 0004 0000- 0004 0003 | 0004 0004- 0004 0007
1 | 0000 0000 | 0002 0000 | 0000 0000 | 1357 2468 | A123 B246 | 0 | 0
2 |  |  |  |  |  |  | 
3 |  |  |  |  |  |  | 
4 |  |  |  |  |  |  | 
5 |  |  |  |  |  |  | 
6 |  |  |  |  |  |  | 
(all in hex)
r1,r2 will be changed by pre-indexed addressing instructions
LDR r0, [r1, #4] ; r0 : = mem32 [r1 + 4]
LDR r0, [r1, #4]! ; r0 : = mem32 [r1 + 4]
; r1 := r1 + 4

## Slide 21: Data Transfer Instructions - post-indexed addressing
Another useful form of the instruction is:
This is called: post-indexed addressing - the base address is used without an offset as the transfer address, after which it is auto-indexed:(r1=r1+4)
Using this, we can improve the copy program:
LDR r0, [r1], #4 ; r0 : = mem32 [r1]
; then r1 := r1 + 4
copy LDR r1, =TABLE1 ; r1 points to TABLE1
LDR r2, =TABLE2 ; r2 points to TABLE2
loop LDR r0, [r1], #4 ; get TABLE1 1st word ….
STR r0, [r2], #4 ; copy it to TABLE2
??? ; if more, go back to loop
……
TABLE1 …… ; < source of data >

## Slide 22: Summary :Data Transfer Instructions (LDR-->LDRB)
Size of data can be reduced to an 8-bit byte with:
Summary of addressing modes:
LDR r0, [r1] ; register-indirect addressing
LDR r0, [r1 , # offset] ; pre-indexed addressing
LDR r0, [r1 , # offset]! ; pre-indexed, auto-indexing
LDR r0, [r1], # offset ; post-indexed, auto-indexing
LDR r0, =address_label ; PC relative addressing
LDRB r0, [r1] ; r0 : = mem8 [r1]

## Slide 23: Self study programming exercise:;ex4_2400 ch4 of CENG2400. It is for your own revision purpose, no need to submit answers to tutors.
;http://www.cse.cuhk.edu.hk/%7Ekhwong/www2/ceng2400/ex4_2400_qst.txt;
1) create a project based on this .s code
;2) In keil-ide, use project/rebuild all target files to build the project
;3) use Debug/run_to_cursor_line to run the top line of the program,
;4) use the single step mode to view the memory locations (in DEbug mode/view/memory_wndows)from 0x4000000 to 0x40000013, registers and cpsr after the execution of each statement.
;5) Explain the observations and results.
; declare variables New test12D
AREA |.data|, DATA, READWRITE
Table1 DCD 0x1, 0x1, 0x1, 0x1, 0x1, 0x1, 0x1, 0x1 ,0x1, 0x1
Table2 DCD 0x1, 0x1, 0x1, 0x1, 0x1, 0x1, 0x1, 0x1 ,0x1, 0x1
align
;-------------------------------------------------------------
; User Initial Stack & Heap
AREA |.text|, CODE, READONLY
EXPORT __main
__main
;clear flags
memory_init ; set the memory content in table1
LDR r1, =Table1
LDR r2, =Table2
MOV r3,#0
MOV r0,#0x00
loop ADD r0,r0,#0x11
STR r0,[r1]
ADD r1,r1,#4
ADD r3,r3,#1
CMP r3,#10
BNE loop
NOP
NOP
ex4_1 ;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;
BL memory_reset
LDR r1,=Table1
LDR r2,=Table2
LDR r0, [r1]
STR r0, [r2]
NOP

## Slide 24: Self study exercises (continue)
ex4_2;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;
BL memory_reset
LDR r1,=Table1
LDR r2,=Table2
MOV r3, #0
loop1 LDR r0,[r1]
STR r0,[r2]
ADD r1,r1,#4
ADD r2,r2,#4
ADD r3,r3,#1
CMP r3,#5
BNE loop1
NOP
NOP
ex4_3;;;;;;;;
BL memory_reset
LDR r1,=Table1
LDR r2,=Table2
LDR r0,[r1]
STR r0,[r2]
LDR r0,[r1,#4]
STR r0,[r2,#4]
NOP
NOP
ex4_4;;;;;;;;
BL memory_reset
LDR r1,=Table1
LDR r2,=Table2
LDR r0,[r1]
STR r0,[r2]
LDR r0,[r1,#4]!
STR r0,[r2,#4]!
NOP
NOP
memory_reset ; reset the content in
; table2 to be all 0
LDR r5,=Table2
MOV r6,#0
MOV r7,#0
loop2 STR r6,[r5]
ADD r5,r5,#4
ADD r7,r7,#1
CMP r7,#10
BNE loop2
BX LR
END

## Slide 25: Summary
Learned the addressing modes of the Arm processor

## Slide 26: Appendices

## Slide 27: Appendix 1: MOV
MOV : Move
MOV<suffix> <dest>, <op 1>
dest = op_1
MOV loads a value into the destination register, from another register, a shifted register, or an immediate value.
You can specify the same register for the effect of a NOP instruction, or you can shift the same register if you choose:
MOV R0, R0 ; R0 = R0... NOP instruction
MOV R0, R0, LSL#3 ; R0 = R0 * 8
If R15 is the destination, the program counter or flags can be modified. This is used to return to calling code, by moving the contents of the link register into R15:
MOV PC, R14 ; Exit to caller
MOVS PC, R14 ; Exit to caller preserving flags
(not 32-bit compliant)

## Slide 28: Appendix2: Data Transfer Instructions - ADR instruction
How does the ADR instruction work? Address is 32-bit, difficult to put a 32-bit address value + opcode in a register in the first place
Solution: Program Counter PC (r15) is often close to the desired data address value
ADR r1, TABLE1 is translated into an instruction that adds or subtracts a constant to PC (r15), and puts the results in r1
This constant is known as PC-relative offset, and it is calculated as: addr_of_table1 - (PC_value + 8)
Address opcode
00008FE4 E28F0004 ADR R0, table1 ; pseudo instruction
; now pc=r15= 00008FE4
Real instruction
00008FE4 E28F0004 ADD R0, R15, #4 ;real code
00008FF0 .table1
00008FF0 EQUS “Hello world !"
By programmer

## Slide 29: The use of the pseudo instruction ADR
Address opcode
00008FE4 E28F0004 ADR R0, table1 ; pseudo instruction
; now pc=r15= 00008FE4
Real instruction (generated by the assembler)
00008FE4 E28F0004 ADD R0, R15, #4 ;real code
00008FF0 .table
00008FF0 EQUS “Hello world !"
---Explanation---
The location you want to enter into R0 is “.text”= 00008FF0 , which is the beginning of a string table.
But you cannot place a 32-adress and some opcode into 32-bit
Because ARM designers want to maintain each instruction is 32-bit long
Put location – (PC+8)= 00008FF0-(00008FE4+8)=# 4 instead
Note: # n =the actual number n (not an address)
You write

## Slide 30: End

## Slide 31: Appendix
Big and little endian