## Slide 1: Chapter 6: Serial Interface -- UART (universal asynchronous receiver transmitter )
CEG2400 - Microcomputer Systems
1

## Slide 2: Overview
Introduction to the universal asynchronous receiver transmitter : UART.
UART Hardware Interface
UART Software Interface
Initialize the UART Hardware
Sending data using handshaking
2

## Slide 3: 1) Introduction: Serial interface (universal asynchronous receiver transmitter : UART)
RS232 standard and application, e.g.
3
RS232 port
(UART)
RS232 port
(UART)
RS232 standard
3 wires
+10 V=‘0’=SPACE
-10V=‘1’=MARK
http://docs.sgi.com/library/dynaweb_docs/hdwr/SGI_EndUser/books/IXbricAdd/sgi_html/figures/IXbrick.serialport.pinouts.gif
Pin2
Pin3
pin5
Pin3
Pin2
pin5

## Slide 4: U Universal A Asynchronous R Receiver T Transmitter UART for data communication
Serial data transmission means sending data bits one by one using one wire.
Asynchronous transmission means a data (including one start bit , 8-bit data, and stop bits) can be sent at any time.
4

## Slide 5: Universal asynchronous receiver transmitter : UART
RS232 is a serial communication standard
Since it is asynchronous, no external clock is needed, only 3 wires are required for the simplest RS232 connection {GND, tx(transmit), rx(receive)}
5
+10V=Logic 0=space
-10V= Logic 1=mark
Exercise: Sketch Bit Patterns for character A and B
Start 0 1 2 3 4 5 6 7 stop
http://www.maxim-ic.com/app-notes/index.mvp/id/83/
Bit 0 to 7 (least sig. bit first )
time

## Slide 6: ASCII table http://www.cs.utk.edu/~pham/ascii_table.jpg
6

## Slide 7: EXAMPLES
Sending ASCII
‘5’=0x35=0011 0101b
7
Start bit=0
10101100(stop bit=1)
Least Sign. Bit first
What is this code ?
The whole ASCII serial character has 10 bits
(1 start+8 data + 1 stop bit)
Stop bit=1
Oscilloscope
Probe
T=bit period
=1/baud rate

## Slide 8: If the baud rate is 57600 bits per second Define ‘bit period’ :the amount of time to transmit a logic 1 or 0. (bit period= 1/57600 seconds)
Each bit lasts for (1/Baud rate) seconds
8
bit period =
1/baud rate =(1 / 57600) seconds=17.4 us
Exercise: What is the “bit period” in seconds if the baud rate is 2400?

## Slide 9: Hello world example/references
Manual: UM_LPC21XX_LPC22XX_2.pdf
  https://github.com/sgh/aos/blob/master/doc/processors/UM_LPC21XX_LPC22XX_2.pdf
Application Note: AN10369_1.pdf
  http://uglyduck.ath.cx/PDF/Philips/LPC2000/AN10369_1.pdf
from course/tutorial web page
  astartup.s
  ahello.s (appendix1)
9

## Slide 10: 2) UART
Hardware Interface
10

## Slide 11: UART Hardware Interface
ARM7 output signals are 0->3.3V.
A MAX232 chip is needed to translate the 0->3.3V levels to the +/-10V RS232 levels (with power VCC=5V, the electronic circuit can do that!!)
11

## Slide 12: ARM system support for UART: Memory Map
Software interface involves appropriately programming registers in the memory map to manipulate the hardware
i.e. from 0xE000 C000 to 0xE000 C030 for UART ports
12
Ref: page 9 of ARM7-LPC213x-user manual (Hardware Guide, UM10120)
http://www.nxp.com/documents/user_manual/UM10120.pdf

## Slide 13: Like office addresses for mail delivery
UART Office addresses from floor
  0xE000 C000 to
  0xE000 C030
13
Memory address space

## Slide 14: Reminded that ARM7 has these registers and memory addresses
32-bit memory addresses (0x0000 0000 to 0xFFFF FFFF)
  Registers (R0-R15) ..etc
UART Office
addresses from floor
0xE000 C000 to
0xE000 C030
0xE000 C000 to
0xE000 C030

## Slide 15: Revision
Name the usages of these memory locations in an ARM (LPC21xx) processor
0000 00000000 7FFFh ?_______
ROM, code
4000 00004000 FFFFh ?_______
RAM, data,Stack
E000 C000 E000 C030 ?_______
(UART)

## Slide 16
16
UART Register address map : 0xE000 C000 to 0xE000 C030 U0RBR (read only ) and U0THR (write only) share the same address but have no conflict (because one is for “write” another is for “read”).
Ref: table 96 of ARM7-LPC213x-user manual (Hardware Guide, UM10120)
http://www.nxp.com/documents/user_manual/UM10120.pdf
DLAB=0
DLAB=1

## Slide 17: 3) UART
A general description of
the software Interface
ahello.s
http://www.cse.cuhk.edu.hk/%7Ekhwong/www2/ceng2400/ahello.s
17

## Slide 18
File name : ahello.s
; UART0 registers
U0RBR EQU 0xE000C000
U0THR EQU 0xE000C000
U0IER EQU 0xE000C004
U0IIR EQU 0xE000C008
U0FCR EQU 0xE000C008
U0LCR EQU 0xE000C00C
U0LSR EQU 0xE000C014
U0SCR EQU 0xE000C01C
U0DLL EQU 0xE000C000
U0DLM EQU 0xE000C004
PINSEL0 EQU 0xE002C000
; User Initial Stack & Heap
AREA |.text|, CODE, READONLY
EXPORT __main
__main BL iuart0
loop MOV R0, #'H'
BL writec
MOV R0, #'e'
BL writec
MOV R0, #'l'
BL writec
MOV R0, #'l'
BL writec
MOV R0, #'o'
BL writec
MOV R0, #' '
BL writec
MOV R0, #'w'
BL writec
MOV R0, #'o'
BL writec
MOV R0, #'r'
BL writec
MOV R0, #'l'
BL writec
MOV R0, #'d'
BL writec
MOV R0, #'\n'
BL writec
B loop
iuart0
MOV R1, #0x5 ; PINSEL0 = 0x5
LDR R0, =PINSEL0
STR R1, [R0]
MOV R1, #0x7 ; U0FCR = 0x7
LDR R0, =U0FCR
STRB R1,[R0]
MOV R1, #0x83 ; U0LCR = 0x83
LDR R0, =U0LCR
STRB R1,[R0]
MOV R1, #0x0f ; U0DLL = 0x0f
LDR R0, =U0DLL
STRB R1,[R0]
MOV R1, #0x00 ; U0DLM = 0x0
LDR R0, =U0DLM
STRB R1,[R0]
MOV R1, #0x03 ; U0LCR = 0x03
LDR R0, =U0LCR
STRB R1,[R0]
BX R14 ; return from subroutine
writec LDR R1, =U0LSR
LDRB R1, [R1]
TST R1, #0x40
BEQ writec
LDR R1, =U0THR
STRB R0, [R1]
BX R14 ; return from subroutine
END
18
Part1: define registers
Part2: main
program
Part3: subroutine to initialize uart0
Part4: subroutine to write data
to serial port

## Slide 19: Part 1 of ahello.s ;send hello to the serial line
Define the address locations of the UART0(Universal asynchronous receiver transmitter) registers
; UART0 registers
U0RBR EQU 0xE000C000
U0THR EQU 0xE000C000
U0IER EQU 0xE000C004
U0IIR EQU 0xE000C008
U0FCR EQU 0xE000C008
U0LCR EQU 0xE000C00C
U0LSR EQU 0xE000C014
U0SCR EQU 0xE000C01C
U0DLL EQU 0xE000C000
U0DLM EQU 0xE000C004
PINSEL0 EQU 0xE002C000
19
RS232 port
(UART)
RS232 port
(UART)
RS232 standard
3 wires
+10 V=‘0’=SPACE
-10V=‘1’=MARK
Pin2
Pin3
pin5
Pin3
Pin2
pin5

## Slide 20: Define Uart Registers in assembly (in lpc21xx.h (ARM7) generated by uvision3 of the Keil assembler tool)
; UART0 registers
U0RBR EQU 0xE000C000
U0THR EQU 0xE000C000
U0IER EQU 0xE000C004
U0IIR EQU 0xE000C008
U0FCR EQU 0xE000C008
U0LCR EQU 0xE000C00C
U0LSR EQU 0xE000C014
U0SCR EQU 0xE000C01C
U0DLL EQU 0xE000C000
U0DLM EQU 0xE000C004
PINSEL0 EQU 0xE002C000
20
EQU Pseudo instruction
Define a constant
X EQU 2
This is an assembler directive that is used to give a value to a label name. In this example it assigns X the value 2. Thus when X is used elsewhere in the code, the value 2 will be substituted (similar to using a #define to set up a constant in the C language).

## Slide 21: Part 2 of ahello.s ;send hello to the serial line
In this program, it writes “hello world” to the serial line.
; User Initial Stack & Heap
AREA |.text|, CODE, READONLY
EXPORT __main
__main BL iuart0
loop MOV R0, #'H'
BL writec
MOV R0, #'e'
BL writec
MOV R0, #'l'
BL writec
MOV R0, #'l'
BL writec
MOV R0, #'o'
BL writec
MOV R0, #' '
BL writec
MOV R0, #'w'
BL writec
MOV R0, #'o'
BL writec
MOV R0, #'r'
BL writec
MOV R0, #'l'
BL writec
MOV R0, #'d'
BL writec
MOV R0, #'\n'
BL writec
B loop
Print
hello
world

## Slide 22: Part 3 of ahello.s, (subroutine iuart0: initialize uart0 registers)
iuart0
MOV R1, #0x5 ; PINSEL0 = 0x5
LDR R0, =PINSEL0
STR R1, [R0]
MOV R1, #0x7 ; U0FCR = 0x7
LDR R0, =U0FCR
STRB R1,[R0]
MOV R1, #0x83 ; U0LCR = 0x83
LDR R0, =U0LCR
STRB R1,[R0]
MOV R1, #0x0f ; U0DLL = 0x0f
LDR R0, =U0DLL
STRB R1,[R0]
MOV R1, #0x00 ; U0DLM = 0x0
LDR R0, =U0DLM
STRB R1,[R0]
MOV R1, #0x03 ; U0LCR = 0x03
LDR R0, =U0LCR
STRB R1,[R0]
BX R14
; return from subroutine
22

## Slide 23: Part 4 of ahello.s (subroutine writec: write one character to the serial line)
writec LDR R1, =U0LSR
LDRB R1, [R1]
TST R1, #0x40
BEQ writec
LDR R1, =U0THR
STRB R0, [R1]
BX R14 ; return from subroutine
END
23

## Slide 24: 4) Detailed description of subroutines “iuart0” in ahello.s
Initialize the UART Hardware
Setup data into UART registers
24
UART registers
0xE000 C000 to
0xE000 C030

## Slide 25: Part 3 of ahello.s Initialize uart0 (iuart0) in ahello.s (Appendix1)
iuart0
MOV R1, #0x5
LDR R0, =PINSEL0
STR R1, [R0]
MOV R1, #0x7
LDR R0, =U0FCR
STRB R1,[R0]
MOV R1, #0x83
LDR R0, =U0LCR
STRB R1,[R0]
MOV R1, #0x0f
LDR R0, =U0DLL
STRB R1,[R0]
MOV R1, #0x00;
U0DLM = 0x0
LDR R0, =U0DLM
STRB R1,[R0]
25
Step1:
setup pins
step2
step3
step4

## Slide 26: Subroutine iuart0: Software to initialize the UART in the LPC21xx (ARM7) chipset
inside iuart0
  Step 1: setup pins
    configure pin function select reg. i.e. pin 19=TXD
  Step 2
    configure FIFO control reg.
  Step 3
    configure line control reg. (start, stop bits)
  Step 4
    Configure baud rate
26

## Slide 27: Step1 of iuart0: pin configuration=0x05
Configure the pin for serial interfaces
Arm7 pins are multi functions, depending on initialization.
E.g. configure pin-symbol “p0.0” (pin19 or p0.0) to be the serial transmission pin “TXD”
You must set Bit 1:0 of address 0xE002 C000=“01”.
27

## Slide 28: Exercise 6.1 : which pin (what Px,y) is RXD? PINSEL0--pin function select reg. [0XE002 C000]=0x05 bit0, bit 2are 1
28
Setup
Pin19 or
P0.0 to have
the function
of TXD
Somewhere inside there

## Slide 29: Exercise 6.1 : which pin (what Px,y) is RXD? Answer: P0.1or pin21 PINSEL0--pin function select reg. [0XE002 C000]=0x05 bit0, bit 2are 1
29
Setup
Pin19 or
P0.0 to have
the function
of TXD
Answer: Setup
Pin21 or
P0.1 to have
the function
of RXD

## Slide 30: Step2 of iuart0:—setup FIFO control
iuart0
MOV R1, #0x5
LDR R0, =PINSEL0
STR R1, [R0]
MOV R1, #0x7
LDR R0, =U0FCR
STRB R1,[R0]
MOV R1, #0x83
LDR R0, =U0LCR
STRB R1,[R0]
MOV R1, #0x0f
LDR R0, =U0DLL
STRB R1,[R0]
MOV R1, #0x00;
U0DLM = 0x0
LDR R0, =U0DLM
STRB R1,[R0]
30
What do all of these values do?
Step1:
setup pins
Step2:
setup First IN
First Out
( FIFO) control
step3
Step4
Set
Baud=
57600

## Slide 31: Step2:U0FCR--FIFO control set reg=0x07 [U0FCR]=0x07
31
Set all
bit0,1,2=“111”
for FIFO control

## Slide 32: Step3 of iuart0: Exercise 6.2, Circle which bits are set,discuss their functions. U0LCR—line control set reg=0x83 [U0LCR]=0x83
32

## Slide 33: Exercise 6.2a, which bits are set, and their functions. Answer:8-bit character length, 1 stop bit, no parity, enable division latch Step3:U0LCR—line control set reg=0x83, set reg [U0LCR]= =0x83=1000 0011B
33
Exercise2b: Repeat exercise2a but 7bit data, 1 stop bit , no parity Answer: U0LCR=10000010b=0x82
[U0LCR]=
0x83=
1000 0011B

## Slide 34: Step2 of iuart0:U0DLL—set baud rate=0x0F [U0DLL]=0x0F, set Baudrate=576000
U0DLL = Fpclk / (16 * Baudrate)
If we want 57600 baud (Fpclk=13.824MHz) then U0DLL=15=0x0f (U0DLM(for msc)=00;U0DLL(for lsb)=15)
Check datasheet of how it should be set.
Exercise4a: How to set the baud rate to be 9600?
  Answer4: U0DLL9600 = Fpclk / (16 * Baudrate)
  =13.824MHz / (16 * 9600)=90
  Also U0DLM9600 =00
Exercise4b: How to set Baud rate = 2400?
Useful tool: http://www.binaryhexconverter.com/decimal-to-hex-converter
13824000/(16(16M+L))=2400
13824000/(16*2400)=360=16M+L
M=?_____, L=?_____
34

## Slide 35: 5) Detailed description of subroutines “writec” : Sending data using handshaking
35

## Slide 36: Subroutine Writec: Basic concept of sending a character using the serial port
The sending procedure is slower (e.g. only 57600 bits per second) than your program, so it needs to ask permission to send
Writec()
Sending rate (Baud rate)
is slower than your program can gen. data
True even for usb2
Send-buffer
receiver
no
Is transmitter
Buffer empty ?
Send data
yes

## Slide 37: Read buffer status U0LSR(0xE000 C014)

## Slide 38: U0LSR—line status at U0LSR(0xE000 C014) (if bit6=TEMT (transmitter empty)=1 you can send next data
Bit7 Bit0

## Slide 39: Recall: TST and BEQ
TST
  Same as AND (logical AND) except result of operation is not stored.
  Only the condition code bits (cc) {N,Z,C,V} in CPSR are changed.
    updates the N and Z flags according to the result
    Does not affect the C or V flags.
BEQ
  Branch if result equal to zero (branch if Z=1)
39

## Slide 40: Write character in R0 subroutine when TEMT=1 TEMT=0 meaning transmitter is not empty, not ready to send TEMT=1 meaning transmitter is empty, ready to send
1)Writec ; subroutine to send data in R0 to serial out
2) LDR R1, =U0LSR; (line status reg)
3) LDRB R1, [R1]; get line status
TST R1, #0x40 ;TEMT(bit 6 of ;U0LSR=1=buffer_empty)=0Z=1
5) BEQ writec ;if Z=1(buffer_not_empty),
;loop back writec to wait
6) LDR R1, =U0THR;U0THR=transmit reg
7) STRB R0, [R1]; send data out
8) BX R14 ; return from subroutine
TST : same as “AND”, but result is not saved , affect Z bit in cpsr

## Slide 41: Flow diagram of Writec of ahello.s TEMT=0 meaning transmitter is not empty, not ready to send TEMT=1 meaning transmitter is empty, ready to send
Reason: The sending speed (Bit per second) is slower than your program, need to ask permission to send
If Z=1
Brach if Z=1
5) BEQ writec
6) LDR R1, =U0THR
7) STRB R0, [R1]; send data out
If Z=0
Writec( ); write data in R0
4)TST R1, #0x40 ;TEMT=0 (buffer_not _empty: transmitter not ready) Z=1
;TEMT=1 (buffer_empty: transmitter is ready) Z=0
Is the transmitter buffer is not empty, loop back.
Because TEMT=0 Z=1,
BEQ writec ;if Z=1,loop back to wait
Otherwise send data

## Slide 42: Summary
Studied serial interface in ARM
Studied handshaking in interfacing

## Slide 43: End