## Slide 1: Chapter 8 Peripherals-1-- ARMdemo06.c
CEG2400 - Microcomputer Systems
References
http://www.nxp.com/acrobat_download/usermanuals/UM10120_1.pdf
Trevor Martins , The insider's guide to the Philips ARM7 based microcontrollers, www.hitex.co.uk

## Slide 2: Introduction
Parallel Port (GPIO)
Analog-to-Digital converter ADC
Digital-to-Analog converter DAC
Universal Asynchronous Receiver/Transmitter UART (serial port)

## Slide 3
Pin assignments
LPC213x

## Slide 4: LPC2131 peripherals

## Slide 5: 1) General purpose Input Output (GPIO) http://www.nxp.com/acrobat_download/usermanuals/UM10120_1.pdf
LPC2131/x has two 32-bit General Purpose I/O ports.
  P0[31:0] except P0[31] is output only pin. Pin P0[24]is not available.
  P1[31:16] are IOs, P1[1:15] are not available.
Features
  Direction control of individual bits
  Separate control of output set and clear
  All I/O default to inputs after reset
Applications
  General purpose I/O
  Driving LEDs, or other indicators
  Controlling off-chip devices
  Sensing digital inputs

## Slide 6: Exercise 1
What peripheral modules are available in LPC2131.
Ans: ?__________________
How many parallel input pins and output pins are available in LPC2131?
(i) : Inputs?________________
(ii) : outputs:?__________________
What are the states of the parallel input/output pins after reset: ? ________

## Slide 7: The experiment hardware
switch
green led
red led
Arm board
--We will show how to blink the red-led
video

## Slide 8: Our testing board connector p03(pin26) is input, p0.8(pin33),p0.9(pin34) are outputs

## Slide 9: For 3.3V driving LEDs from a 3.3V system

## Slide 10: Remind you that ARM has
32-bit memory addresses total 4-Gbytes
(0x0000 0000 to 0xFFFF FFFF)
:
; GPIO Port 0 Register address
IO0DIR EQU 0xE0028008; IO direction
IO0SET EQU 0xE0028004; turn on the bits
IO0CLR EQU 0xE002800C;turn off the bits
IO0PIN EQU 0xE0028000; pin assignment
  Registers (R0-R15) ..etc

## Slide 11: Send data to GPIO registers
; GPIO Port 0 Register address
;
IO0DIR EQU 0xE0028008; IO direction
IO0SET EQU 0xE0028004; turn on the bits
IO0CLR EQU 0xE002800C;turn off the bits
IO0PIN EQU 0xE0028000; pin assignment

## Slide 12: Explanation2 of GPIO.c (pure polling program) line 1-6
1) #include <lpc21xx.h> //define IO0PIN ,IO0DIR.. etc
2) #define RED_LED 0x00000100 //set p0.8 as RED LED
3) #define SW1 0x00000008 //set p0.3 as SW1
4) int main(void)
5) { long tmp; // variable for temp storage of port 0 status
//after power up by default all pins are GPIOs, same as PINSEL=0;
6)IO0DIR = RED_LED; // set p0.8 as output
//so IO0DOR=0000 0000 0000 0000 0000 0001 0000 0000
p0.8=output p0.3=input
// p0.8 is output (output), all pins are inputs (include p0.3),

## Slide 13: Explanation3 of GPIO.c (pure polling program) line 7-13
2) #define RED_LED 0x00000100 //set p0.8 as RED LED
3) #define SW1 0x00000008 //set p0.3 as SW1
:
7) while(1)
8) { tmp =IO0PIN & SW1;//read SW1(p0.3)depressed=0
9) if(tmp==0) ; What happens “if (tmp!=0)” is used?
10) IO0SET = RED_LED; //if SW1 pressed LED is on
11) else IO0CLR = RED_LED; // otherwise off the LED
12) }
13) }
Tmp=0x0000 0000 if SW1 is depressed because p0.3 is 0
Tmp=0x0000 0008 if SW1 is not depressed
P0.3
of LPC213x

## Slide 14: Exercise 2: A simple C program GPIO.c When SW1 is depressed, RED-LED is on
1) #include <lpc21xx.h> //define IO0PIN ,IO0DIR.. etc
2) #define RED_LED 0x00000100 //set p0.8 as RED LED
3) #define SW1 0x00000008 //set p0.3 as SW1
4) int main(void)
5) { long tmp; // variable for temp storage of port 0 status
6) IO0DIR = RED_LED; // set p0.8 as output
7) while(1)
8) { tmp =IO0PIN & SW1;//read SW1(p0.3)depressed=0
9) if(tmp==0) ; What happens “if (tmp!=0)” is used?
10) IO0SET = RED_LED; //if SW1 pressed LED is on
11) else IO0CLR = RED_LED; // otherwise off the LED
12) }
13) }
Question (a): What happens “if (tmp!=0)” is used in line 9?
Ans: ?____________________________________________
Question (b): If RED-LED is connected to p0.10, how to change the code?
Ans: ?______________________________________________
Question (c): If SW1 is connected to p0.4, how to change the code?
Ans: ?_______________________________________________________

## Slide 15: Applications
Outputs
  Drive LED
  Drive motor
Inputs
  Read on/off switches
  Scan keyboard

## Slide 16: 2) Analog-to-Digital converter ADC
Program:
Use
read_sensor (int channel)
To read the data
Analog voltages
Applications:
Light sensor (in robot car) ,
temperature sensor,
force sensor.
Ad0.0
Ad0.1
Ad0.2
Ad0.3
Ad0.4
Light sensor0(IRS0)
Light sensor1(IRS1)
Light sensor2(IRS2)
Light sensor3(IRS3)
Light sensor4(IRS4)
ADC
Video demo:
http://www.youtube.com/watch?v=Ol4xGSI51Ck&feature=youtu.be
Code: demo_adc.txt
http://www.cse.cuhk.edu.hk/%7Ekhwong/www2/ceng2400/demo_adc.txt

## Slide 17: Exercise 3 Code for Analog-to-Digital ADC converter pin assignment for sensor pins
#include <lpc21xx.h>
#define ADCR (*((volatile unsigned long *) 0xE0034000))
#define ADDR (*((volatile unsigned long *) 0xE0034004))
int main(void) {
....
//From line 92 of ARMdemo06.c
// We must initialize the IO pin //before using ADC channel
94) PINSEL1 = 0x00400000; // set p0.27 to ad0.0
95) PINSEL1 |= 0x01000000; // set p0.28 to ad0.1
96) PINSEL1 |= 0x04000000; // set p0.29 to ad0.2
97) PINSEL1 |= 0x10000000; // set p0.30 to ad0.3
98) PINSEL1 |= 0x00040000; // set p0.25 to ad0.4
Question (a) : Write one instruction to replace of all instructions from line 94 to 98 . Answer: ? ______________________________________________
Question (b) :How to set the system to use ad0.5
Answer:? ________________________________________________

## Slide 18: PINSEL1 Pin assignment for AD0.1 94) PINSEL1 = 0x00400000; // set p0.27 to ad0.0 PINSEL1 = xxxx 0000 0100 0xxx xxxx xxxx xxxx xxxx bit 31 27 23 19 15 11 7 3 0
Bit23:22=01
Bit23:22
Ref: http://www.nxp.com/acrobat_download/usermanuals/UM10120_1.pdf
Volume 1: LPC213x User Manual UM10120
Bit 19-27 for
ADC
Other bits are
For other
purposes

## Slide 19: Exercise 4
What is the purpose of PINSEL1 register?
  ANS: ?____________________________
Where is the location of PINSEL1 register?
  ANS: ?____________________________
What is the pin number of P0.28
  ANS: ?____________________________
How to set P0.28 pin to be the function of ADC0.1?
  ANS: ?____________________________

## Slide 20: PINSEL1 Pin assignment for AD0.1 94) PINSEL1 |= 0x010000000; // set p0.28 to ad0.1 PINSEL1 = 0000 0001 0000 0000 0000 0000 xxxx xxxx bit 31 27 23 19 15 11 7 3
Bit25:24=01
Bit25:24
Ref: http://www.nxp.com/acrobat_download/usermanuals/UM10120_1.pdf
Volume 1: LPC213x User Manual UM10120

## Slide 21: Exercise 5: Fill in the blanks in the flow diagram of this program Code for Analog-to-Digital ADC converter In C:\Keil\ARM\INC\Philips\lpc21xx.h, ADCR=0xE0003 4000 ADCR=0xE0003 4000, ADDR=0xE0003 4004
From line 71 of ARMdemo06.c
//(1) ADC interface
71) int read_sensor(int channel)
72) {
73) int temp;
74)
75) ADCR=0x1 << ________;//__select channel___ (see Appendix3)
76) ADCR|=_____________; // set up the control bits_
77)
78) while(((temp=ADDR)& ___________)==0); //MSB =1 meaning ADC is done
79) temp>>=6; //?________________________________(bit6->15: 10-bit conversion result)
80) temp&=0x3ff;//TEMP=output IS 0-3V PRESICION IS (10 bits: 2^10=1024 levels)
81)
82) return (temp*33); //?? Why temp*33__________________________
83) }
.....
Loop until
ADC is
done
Conversion Done
Return temp*scale
Conversion not done
Explanation ?_______________
Study ADCR (Analog to digital control reg)
and ADDR (Analog to digital Data reg)
here

## Slide 22: ADCR -- one (AD0) for lpc2131 line 75) ADCR=0x1<<_______(fill in the blank);//see Appendix 3 line 76) ADCR|=_______(fill in the blank);//operational,start convert ADCR= 0000 0001 0010 0000 0000 0010 xxxx xxxx bit 31 27 23 19 15 11 7 3
Point to which
channel
Bit 15:8=10b=2
CLKDIV=2+1=3
Freq=13.824MHz/3=4.608MHz
Ref: http://www.nxp.com/acrobat_download/usermanuals/UM10120_1.pdf

## Slide 23: ADCR -- one (AD0) for lpc2131 line 75) ADCR=0x1<<________(fill in the blank); line 76) ADCR|=_________(fill in the blank);// operational, start convert ADCR= 0000 0001 0010 0000 0000 0010 xxxx xxxx bit 31 27 23 19 15 11 7 3
Bit21=1 operational
Bit24=1
Ref: http://www.nxp.com/acrobat_download/usermanuals/UM10120_1.pdf

## Slide 24: Polling for the completion of Analog-to-digital conversion 78) while(((temp=ADDR)&_________(fill in the blank))==0); ADDR= 1000 0000 0000 0000 xxxx xxxx xx00 0000 //MSB =1 meaning ADC is done //if bit 31 of ADDR is 1, it is done //bit 15:6 contain the result
ADC result

## Slide 25: Find the Analog-to-digital converted result ADC result xx xxxx xxxx ADDR= 1000 0000 0000 0000 xxxx xxxx xx00 0000
78)while(((temp=ADDR)&0x80000000)==0);
79) temp>>=6; temp>>6; = 0000 0010 0000 0000 00xx xxxx xxxx
80) temp&=0x3ff;//TEMP=output IS 0-3V PRESICION is 1024 (10bit ADC precision)
temp&=0x3ff;= 0000 0000 0000 0000 00xx xxxx xxxx
82) return (temp*33);// make it a full integer.
result
polling
result

## Slide 26: 3)Digital-to-Analog converter DAC
Applications
  Sound generation, e.g. MP3 player
  Motor speed control use analog methods
Usage: Similar to Analog-to-Digital converter ADC
Digital-to-Analog converter DAC --
Convert digital codes into
an analog signal
Analog value

## Slide 27: DAC reg. 10-bit

## Slide 28: 4) Universal Asynchronous Receiver / Transmitter UART (serial port)
//init UART0 setting
......
26) #define NEWLINE sendchar(0x0a); sendchar(0x0d)
33) void Init_Serial_A(void) {
34) U0LCR = 0x83; //8 bit length ,DLAB must be 1 to access
35) U0DLL = 0x0F; //Baud rate setting , part1 36) U0DLM = 0x00; //Baud rate setting , part 2
37) U0LCR = 0x03; //DLAB=0 to complete the setting
}
0x0a=New line , 0x0d=carriage return
in ARM06Demo.c, and www.nxp.com/acrobat_download/applicationnotes/AN10369_1.pdf

## Slide 29: line34) U0LCR = 0x83; //8 bit length ,DLAB=1 //U0LCR = 1000 0011b

## Slide 30: Exercise 6: Baud rate setting 35) U0DLL = 0x0F;//=15 36) U0DLM = 0x00;//=0
Because , PCLK=13.824MHz
UART0(baudrate)=PCLK/(16*(16*0+15))
=13.824MHz/3840=57600 is the baud rate
Exercise: Find U0DLL and U0DLM if the required baud rate is 19200.
Answer:?________

## Slide 31: Getchar() in “C” polling method (not interrupt)
40) char getchar(void) {
41) volatile char ch = '0';
42)
43) while ((U0LSR & 0x1)==0)//wait until a byte is received
44) ;
45) ch = U0RBR;// receive character
//(U0RBR - 0xE000 C000,
46)
47) return ch;
48) }
polling
Polling
method
Is bit1 of U0LSR==0?
(receive buffer empty?)
Yes
No,
receive character

## Slide 32: Sendchar() in “C” polling method (not interrupt)
49)///////////////////////////////
50)void sendchar(char ch) {
51) while( (U0LSR & 0x40)==0 );
52)
53) U0THR = ch;// Transmit next character
54) } // at 0xE000 C000 bit7:0
Polling
method
Bit of U0LSR at 0xE000 C014
Is bit6 of U0TH==0?
(Transmitter contains
valid data, previous data
not sent yet?)
Yes
No,
Transmit
Next character
polling

## Slide 33: Print(), Print a string of characters on screen
56) int print(char *p) {
57) while(*p!='\0') { //’\0’ is end of text, = 0x03
58) sendchar(*p++); // if not end of text send characters of the string
59) }
60) return(0);
61)}
......
Example
print(“---Hello world---");NEWLINE;

## Slide 34: Ascii table from http://enteos2.area.trieste.it/russo/IntroInfo2001-2002/CorsoRetiGomezel/ASCII-EBCIDC_table.htm

## Slide 35: Exercise 7: putint( int count) print an integer on screen
63) void putint(int count) {
64) sendchar('0' + count/10000);
65) sendchar('0' + (count/1000) % 10); //%=modulus
66) sendchar('0' + (count/100) % 10);
67) sendchar('0' + (count/10) % 10);
68) sendchar('0' + count % 10);
69)}
‘0’ is 0x30 (ASCII for number zero)
Print an ASCII character representing that digit at one time,
Question:
If “count” is “2597”, what hex numbers have been sent to the serial port?
Answer: ?_________________________

## Slide 36: UART main print example
int main(void) {
......
// Initialize IO pin before using TXD0 and RXD0
PINSEL0 = 0x00000005; // set p0.0 to TXD0, p0.1 to RXD0 and the rest to
GPIO
.....
Init_Serial_A(); // Init COM port
......
NEWLINE;
print("================================================"); NEWLINE;
print("**"); NEWLINE;
print("* CUHK Computer Science and Engineering Department*"); NEWLINE;
print("* LPC2131 ARM Board (ver1.3) *"); NEWLINE;
print("**"); NEWLINE;
print("* I2C (Master Receiver) Test Program (ver1.3)*"); NEWLINE;
print("================================================"); NEWLINE;
NEWLINE;

## Slide 37: Summary
Studied peripherals of the LPC213x ARM processor.

## Slide 38: Appendix ESTR2100 students should study this

## Slide 39
Appendix (1) Our robot
Circuits of this chapter are from this design

## Slide 40: Appendix (1) Watchdog timer register setting
If the system doesn’t give
me any signals for a period
of time (say 2 seconds), that
means it hangs, so I will
Press the reset bottom

## Slide 41: Example http://www.keil.com/download/docs/317.asp
void feed_watchdog (void) { /* Reload the watchdog timer */
WDFEED = 0xAA;
WDFEED = 0x55;
}
void sendhex (int hex) { /* Write Hex Digit to Serial Port */
if (hex > 9) sendchar('A' + (hex - 10));
else sendchar('0' + hex);
}
void sendstr (char *p) { /* Write string */
while (*p) {
sendchar (*p++);
}
}
/* just waste time here for demonstration */
void do_job (void) {
int i;
for (i = 0; i < 10000; i++);
}

## Slide 42: Main and use of feed
int main (void) {
unsigned int i;
init_serial(); /* Initialize Serial Interface */
if( WDMOD & 0x04 ) { /* Check for watchdog time out */
sendstr("Watchdog Reset Occurred\n");
WDMOD &= ~0x04; /* Clear time out flag */
}
WDTC = 0x2000; /* Set watchdog time out value */
WDMOD = 0x03; /* Enable watchdog timer and reset */
for(i = 0; i < 50; i++) {
do_job (); /* the actual job of the CPU */
feed_watchdog(); /*restart watchdog timer, for_loop will run until complete */
}
while (1) { /* Loop forever */
do_job (); /* the actual job of the CPU */
/* no watchdog restart, watchdog reset will occur! */
}
}

## Slide 43: Watchdog Registers

## Slide 44: Watch dog mode reg. WMOD

## Slide 45
Watchdog
Block diagram
void feed_watchdog (void) { /* Reload the watchdog timer */
WDFEED = 0xAA; WDFEED = 0x55;
}

## Slide 46: Appendix(3)
Alternative set bit method in “C”. The command “<<“ is a left shift instruction in the “C” language
Y=0x1<<21;//left shift 21 bits, this sets bit21=1 and other bits= 0
Example: Before shift
  Y=0x1=0000 0000 0000 0000 0000 0000 0000 0001 (Binary)
After shift
  Y= 0000 0000 0010 0000 0000 0000 0000 0000 (Binary)
    bit 31 bit 21 bit0
  Exercise: set bit 9 of register R to be 1, other bits to be 0.
  Answer=0x1<<9;
  So R=0000 0000 0000 0000 0000 0010 0000 0000 (Binary)
  =0x200
Bit9 =1

## Slide 47: Answer 5 : Exercise 5: Fill in the blanks in the flow diagram of this program Code for Analog-to-Digital ADC converter In C:\Keil\ARM\INC\Philips\lpc21xx.h, ADCR=0xE0003 4000 ADCR=0xE0003 4000, ADDR=0xE0003 4004
From line 71 of ARMdemo06.c
//(1) ADC interface
71) int read_sensor(int channel)
72) {
73) int temp;
74)
75) ADCR=0x1<<channel; //select channel
76) ADCR|=0x01200200; //operational, start convert
77)
78) while(((temp=ADDR)&0x80000000)==0); //MSB =1 meaning ADC is done
79) temp>>=6; //shift right 6 bits, remove unused bits
80) temp&=0x3ff;//TEMP=output IS 0-3V PRESICION IS 1024
81)
82) return (temp*33);
83) }
.....
Loop until
ADC is
done
78) while(((temp=ADDR)&0x80000000)==0);
//MSB =1 meaning ADC is done
Conversion Done
Return temp*scale
Conversion not done