## Slide 1: Chapter 12: Software interrupts (SWI) and exceptions
CEG2400 - Microcomputer Systems
[1] ARM7TDMI, Revision: r4p1, Technical Reference Manual
http://infocenter.arm.com/help/topic/com.arm.doc.ddi0210c/DDI0210B.pdf

## Slide 2: A brief introduction (revision) of
interrupt/exception

## Slide 3: What is interrupt/exception?
Main ()
{
:
Doing something
(e.g.
browsing)
:
} ring
_isr() //Interrupt service routine
{
some tasks (e.g. answer
telephone)
}//when finished,
//goes back to main
Can happen anytime
Depends on types of interrupts
Phone rings
Phone rings

## Slide 4: Examples
When your computer is running, a key press will trigger an interrupt to input a character to your system
The dispatcher in the operating system is implemented by timer interrupt.
  Timer interrupts the CPU at a rate of 1KHz
  At each interrupt the system determines which task to run next.

## Slide 5: Important interrupts
Interrupts
Reset
(or power up)
Software
Interrupt
SWI-XX
Hardware
Interrupt
FIQ,IRQ
Timer
ADC
External
Interrupt
EINT
Triggered by power_up/
reset_key
Triggered by hardware sources
Triggered by the software instruction SWI x
SWI

## Slide 6: Interrupt and exception
The terms are used differently by various manufacturers
Traditionally exception means
  The normal operation of a program is interrupted and the processor will execute another piece of software (exception handling) somewhere.
    Interrupt (hardware interrupt) is an exception caused by some hardware condition happening outside the processor (e.g. external hard interrupt, IRQ FIQ).
    Software interrupt (SWI) is an exception caused by an assembly software instruction (SWI 0x?? exception call instruction) written in the software code.
    Trap is an exception caused by a failure condition of the processor (e.g. abort “pre-fetch , data” , undefined instruction, divided_by_zero, or stack overflow etc)

## Slide 7: Important interrupts in words
Reset, a special interrupt to start the system– happens at power up , or reset button depressed)
Software interrupt SWI: similar to subroutine – happens when “SWI 0x??” is written in the program
Hardware interrupt
  FIQ (fast interrupt) or IRQ (external interrupt), when
    the external interrupt request pin is pulled low, or
    an analogue to digital conversion is completed, or
    A timer/counter has made a regular request
Interrupt handling hardware
IRQ
FIQ
Timer/Counter
ADC
UART
End of conversion
Counter overflow
End of transmission
Interrupt request generated
Inside LPC2131

## Slide 8: Introduction to
Software Interrupt (SWI)

## Slide 9: Compare hardware and software interrupt
  Hardware interrupt, e.g.
  Software interrupt
Computer
EINT3
IRQ_Eint1()
{
::
}
A falling edge at EINT3 will trigger the
execution of the interrupt service routine
__irq IRQ_Eint1()
Computer
Main{
:
SWI N
:
}
N-th-sys-routine()
{
::
}
An instruction “SWI N” in
the program will trigger the
execution of
the N-th-sys-routine
(system routine)

## Slide 10: Exception (interrupt) Modes
ARM supports 7 types of exceptions and has a privileged processor mode for each type of exception.
ARM Exception (interrupt) vectors
SWI
IRQ

## Slide 11: Different types of exceptions
Reset (supervisor model, at power up , or reset button depressed)
Undefined Instruction (for co-processors *)
*Prefetch Abort for instruction fetch memory fault
*Data Abort : for data access memory fault
Software Interrupt (SWI) : supervisor mode, operating sys. calls
FIQ (Fast interrupt request)
IRQ (interrupt request)
* not discussed here , refer to http://infocenter.arm.com/help/topic/com.arm.doc.ddi0210c/DDI0210B.pdf

## Slide 12: Student ID: ___________,Date:_____________ Name: __________________________________
What should a CPU do when it enters interrupt?
  Answer: __________________________________
What is the difference between software and hardware interrupt?
  Answer: __________________________________
What is the meaning of Trap?
  Answer: __________________________________
Name all interrupts of LPC2131 and their entry addresses.
  Answer: __________________________________
Exercise 12.1

## Slide 13: common usage of exceptions
For building operating systems
  Reset (supervisor model, at power up , or reset button depressed)
  Undefined Instruction (for co-processors *)
  *Prefetch Abort for instruction fetch memory fault
  *Data Abort: for data access memory fault
  Software Interrupt (SWI) : supervisor mode, operating sys. calls
For embedded systems, hardware systems
  FIQ (Fast interrupt request)
  IRQ (interrupt request)
* not discussed here , refer to http://infocenter.arm.com/help/topic/com.arm.doc.ddi0210c/DDI0210B.pdf

## Slide 14: ARM Registers
32-bit

## Slide 15: Recall program status regs
Copies of the ALU status flags (latched if the
instruction has the "S" bit set).
N = Negative result from ALU flag.
Z = Zero result from ALU flag.
C = ALU operation Carried out
V = ALU operation oVerflowed
* Interrupt Disable bits.
I = 1, disables the IRQ.
F = 1, disables the FIQ.
* T Bit (Architecture v4T only)
T = 0, Processor in ARM state
T = 1, Processor in Thumb state
* Condition Code Flags
Mode
N
Z
C
V
28
31
8
4
0
I F T
Mode of interrupt

## Slide 16: Recall: registers
General registers and Program Counter
Program Status Registers
r15 (pc)
r14 (lr)
r13 (sp)
r14_svc
r13_svc
r14_irq
r13_irq
r14_abt
r13_abt
r14_undef
r13_undef
User32 / System
FIQ32
Supervisor32
Abort32
IRQ32
Undefined32
cpsr
sprsr_fiq
sprsr_fiq
sprsr_fiq
spsr_abt
spsr_svc
sprsr_fiq
sprsr_fiq
spsr_fiq
sprsr_fiq
sprsr_fiq
sprsr_fiq
sprsr_fiq
sprsr_fiq
spsr_irq
r12
r10
r11
r9
r8
r7
r4
r5
r2
r1
r0
r3
r6
r7
r4
r5
r2
r1
r0
r3
r6
r12
r10
r11
r9
r8
r7
r4
r5
r2
r1
r0
r3
r6
r12
r10
r11
r9
r8
r7
r4
r5
r2
r1
r0
r3
r6
r12
r10
r11
r9
r8
r7
r4
r5
r2
r1
r0
r3
r6
r12
r10
r11
r9
r8
r7
r4
r5
r2
r1
r0
r3
r6
r15 (pc)
r15 (pc)
r15 (pc)
r15 (pc)
r15 (pc)
cpsr
cpsr
cpsr
cpsr
cpsr
r14_fiq
r13_fiq
r12_fiq
r10_fiq
r11_fiq
r9_fiq
r8_fiq
sprsr_fiq
sprsr_fiq
sprsr_fiq
sprsr_fiq
sprsr_fiq
spsr_undef
SPSR= Saved Process
Status Reg
Shaded
registers
are extra
Registers
for different
modes

## Slide 17: Mode bits M[0:4] : bit0->bit4 of CPSR
http://infocenter.arm.com/help/topic/com.arm.doc.ddi0210c/DDI0210B.pdf
Mode
N
Z
C
V
28
31
8
4
0
I F T

## Slide 18: We will study Software Interrupt
(SWI)

## Slide 19: Why Software interrupt SWI? “Similar to a subroutine call but more efficient and organized”
Make a list of often used routines
To build system calls in Linux or Windows.
E.g. print character , read keyboard etc..

## Slide 20: SWI software interrupt
For operating sys. (OS) developers to write often used routines
E.g. SWI 0x12 is for “write a character to screen”
So you may have a table of all routines and called by users or OS programs.
SWI table
0x01= reset system
0x02= init timer
:
0x12 = write a charter to screen
0x13= make a beep sound for 0.5 seconds…

## Slide 21: Example E.g.1 For Building OS Operating system calls
SWI software interrupt for writing OS calls
An efficient way for user to make OS calls
Examples, SWI table
  SWI 20 = Print text on screen
  SWI 23 =Read real time clock
  SWI 35 =Keyboard read
  -……
Main()
{
:
:
:
}
Program for SWI x
Print a character
to screen
SWI x ;software interrupt
Supervisor mode

## Slide 22: Code Example
When SWI is in your code:
E.g. SWI vector=SWI 0x11, vector =0x11

## Slide 23: SWI interrupt procedures (enter the supervisor mode)
SWI (software interrupt )
  Caused by “SWI 0x??” in your program
  Arm completes the current instruction.
  Goto SWI exception address 0x08 (short form for 0x000 0008)
  Exception entry, execution procedure (see next slide)
  {Change to supervisor op. mode :CPSR (bit0-4)
  :
  :
  Return from interrupt
    MOVS pc, lr
  return to main}

## Slide 24: Details of entering an interrupt (exception)
Preserves the address of the next instruction in the appropriate Link Register (e.g. r14_svc  r14 of supervisor mode)
Copies the CPSR (Current Program Status Register ) into the appropriate SPSR (Saved Process Status Reg. e.g. SPSR_svc)
Forces the CPSR mode bits to a value which depends on the exception (supervisor, interrupt etc)
Forces the PC (program counter r15) to fetch the next instruction from the relevant exception vector
It may also set the interrupt disable flags to prevent otherwise unmanageable nesting of exceptions.
http://infocenter.arm.com/help/topic/com.arm.doc.ddi0210c/DDI0210B.pdf

## Slide 25: SWI Software interrupt
On SWI, the processor
    (1) copies CPSR to SPSR_SVC
    (2) sets the CPSR mode bits to supervisor mode
    (3) sets the CPSR IRQ to disable
    (4) stores the value (PC + 4) into LR_SVC
    (5) forces PC to 0x08
ADD r0,r0,r1
SWI 0x02
SUB r2,r2,r0
USER Program:0x40002000
to R_Handler
to U_Handler
to S_Handler
to P_Handler
to D_Handler
...
to I_Handler
to F_Handler
Vector Table (spring board)
starting at 0x00 in memory
0x00
0x04
0x08
0x0c
0x10
0x14
0x18
0x1c
(Reset
(Undef instr.)
(SWI)
(Prefetch abort)
(Data abort)
(Reserved)
(IRQ)
(FIQ)
LDR r0,[lr,#­-4]
BIC r0,r0,#0xff000000
// now the vector is in r0
switch (r0){
case 0x00: service_SWI1();
case 0x01: service_SWI2();
case 0x02: service_SWI3();
…
}
MOVS pc, lr
SWI Handler:0x40001000
(S_Handler)
Warning:
What was in R0? User program may have been using this register. Therefore, cannot just use it ­ must first save it first (push stack)
From
www.cs.ucr.edu/~amitra/context_switch/extra/04_swi.ppt
Usage of BIC (Bit Clear)
E.g. BIC R0, R0, #%1011 ;
Clear bit-0, bit-1, bit-3 in R0.
For your reference: SWI Software interrupt execution flow

## Slide 26: Exercise 12.2: SWI handler : Assume the SWI handler is at 0x40001000
i) What is the content of address 0x08? Why?
Answer:?__________________________________________
ii) What will the Processor do when it runs SWI 0x02
Fill in steps that the precessor will do when entering SWI
Step1:_________________
Step2 :_________________
Step3 :_________________
Step4 :_________________
Step5:__________________
SWI handler (from 0x40001000)
:push registers onto stack
LDR r0,[lr,#­-4]
BIC r0,r0,#0xff000000 :swtch(r0) .. etc :
:pop registers from stack
MOVS pc, lr; return from interrupt
User main program (from 0x40002000) | 
Address | instruction
0x40002000 | ADD r0,r0,r1
0x40002004 | SWI 0x02
0x40002008 | SUB r2,r2,r0

## Slide 27: Exercise 12.3 SWI handler
Inside the SWI handler
  i) What are the mode bits M[0:4] : bit0->bit4 of CPSR? Answer: ?______________
  Ii) What is the running mode inside the SWI handler: supervisor or user32?
    ANSWER: ?___________________________________
  III) When the link register lr is used, which lr the processor is using :r14(lr) or r14_svc or r14_irq?
    Answer?__________________________________
The Machine code of SWI 0x02 is 0xea000002 . List the values of r0 after the first and second instruction of the SWI handler.
  LDR r0,[lr,#-­4] ; fill in the blank, r0 = ?_______
  BIC r0,r0,#0xff000000; clear most significant 2 bytes of r0; r0=?_____
  // now the vector is in r0
  switch (r0){
  case 0x00: service_SWI1();
  case 0x01: service_SWI2();
  case 0x02: service_SWI3();
  …
  }

## Slide 28: Details of leaving an interrupt ARM7TDMI tech. ref. (section 2.8 exception)[1]
At the end of the SWI handler: Movs pc,lr
Move the r14, minus an offset to the PC. The offset varies according to the type
(auto) SPSR_svc CPSR.
(auto) Clear the interrupt disable flags that were set on entry
Bye Bye!

## Slide 29: Summary
Learned the basic concept of exceptions and interrupts
  SWI (Software interrupt)

## Slide 30: Appendix
Alternative set bit method in “C”
Y=0x1<<21;//left shift 21 bits, this sets bit21=1 and other bits= 0
Before shift
  Y=0x1=0000 0000 0000 0000 0000 0000 0000 0001 (Binary)
After shift
  Y= 0000 0000 0010 0000 0000 0000 0000 0000 (Binary)
    bit 31 bit 21 bit0
  Exercise: set bit 9 of register R to be 1, other bits to be 0.
  Answer=0x1<<9;
  So R=0000 0000 0000 0000 0000 0010 0000 0000 (Binary)
  =0x200
Bit9 =1