## Slide 1: Chapter 13 Peripherals-2 -- ARMdemo06.c
CEG2400 - Microcomputer Systems
References
http://www.nxp.com/acrobat_download/usermanuals/UM10120_1.pdf
Trevor Martins , The insider's guide to the Philips ARM7 based microcontrollers, www.hitex.co.uk

## Slide 2: Introduction
Timer
Watchdog
Pulse Width Modulation PWM unit
Real time clock

## Slide 3
Pin assignments
LPC213x

## Slide 4: LPC2131 peripherals

## Slide 5: 1) Timer http://www.keilsoftware.com/dd/vtr/3735/8064.htm
Including these Features
  A 32-bit Timer/Counter with a programmable 32-bit Prescaler.
  Counter or Timer operation
  Four 32-bit match registers that allow:
    Set low on match, Set high on match, Toggle on match, Do nothing on match.
Applications
  Interval Timer for counting internal events.
  Pulse Width Demodulator via Capture inputs.
  Free running timer.

## Slide 6: Part 1 of void init_timer_Eint() of EINT.c (interrupt rate =1KHz) ( for init timer , use VICVectAddr0
/* Setup the Timer Counter 0 Interrupt */
void init_timer_Eint (void) {
T0PR = 0;
// set prescaler to 0
T0MR0 =13824; // set interrupt interval to 1mS
// since pclk/1KHz = (11059200 x 5)/(4 x 1000)=13824
T0MCR = 3; // Interrupt and Reset on MR0
T0TCR = 1; // Timer0 Enable
VICVectAddr0 = (unsigned long)IRQ_Exception;
// set interrupt vector in 0 (This becomes the highest priory interrupt)
VICVectCntl0 = 0x20 | 4; // use it for Timer 0 Interrupt
VICIntEnable = 0x00000010; // Enable Timer0 Interrupt
cclk=M*Fosc, M=5
pclk=cclk/4
Pclk=11059200*5/4
------------------------------RECALL-------------------------------------

## Slide 7: Summary of Clocks One oscillator generates two outputs CCLK, PCLK
ARM-LPC213x
FOSC
11.0592MHz
FOSCx5=CCLK for MCU
55.296MHz
CCLK/4=
PCLK =
for peripherals
13.824MHz
PCLK=13.824MHz

## Slide 8: Concept of the timer Operation
PCLK /freq_out=(11059200 x 5/4)/freq_out
=13.824MHz /freq_out
When timer counter (TC)=match reg0 (T0MR0), an pulse is generated, the the timer counter is reset
PCLK=
13.824MHz
Match reg0
T0MR0 =13824
=
When TC==T0MR0
a pulse is sent
The frequency generated =PCLK/T0MR0
Timer
Counter
TC
reset

## Slide 9: Example of a 1KHz=freq_out interrupt generator
PCLK /freq_out= PCLK/1K=(11059200 x 5)/(4 )=13.824 MHz/1K=13824
When timer counter (TC)=match reg0 (T0MR0), an interrupt is generated
Divided by
(pre-scale+1)
Since pre-scale
=T0PR = 0
So divided by 1
PCLK
Or
an input pin
CAPx.y
(See pin
assignment
of lpc2131)
Timer
Counter
TC
Match reg0
T0MR0 =13824
=
Freq_out=
=PCLK/T0MR0
Interrupt request
or output pin (MATx.y)
(1KHz, every 1ms)

## Slide 10: 2) Watchdog timer
For implementing fail safe systems
If the system doesn’t give
me any signals for a period
of time (say 2 seconds), that
means it hangs, so I will
Press the reset bottom

## Slide 11: Example, solar power wireless telephone (register setting , see appendix)
At remote area, maintenance is difficult
If the software does not operate properly (hangs)
  That means it sends no regular signals to the watch dog sensor
Then
  the watch-dog resets the system
If the system doesn’t give
me any signal for a period
of time (say 2 seconds), that
means it hangs, so I will
Press the reset bottom

## Slide 12: Software
Main
{
  While(1)
  { Do_the _neccessary();
  Send_a_pulse_to_watch_dog();
  }
}
If the software hangs, it will not Send_a_pulse_to_watch_dog();
so the system is reset by the watch_dog_hardware
If the system doesn’t give
me any signal for a period
of time (say 2 seconds), that
means it hangs, so I will
Press the reset bottom

## Slide 13: Example http://www.keil.com/download/docs/317.asp
void feed_watchdog (void) { /* Reload the watchdog timer */
WDFEED = 0xAA;
WDFEED = 0x55;
}
void sendhex (int hex) { /* Write Hex Digit to Serial Port */
if (hex > 9) sendchar('A' + (hex - 10));
else sendchar('0' + hex);
}
void sendstr (char *p) { /* Write string */
while (*p) {
sendchar (*p++);
}
}
/* just waste time here for demonstration */
void do_job (void) {
int i;
for (i = 0; i < 10000; i++);
}

## Slide 14: Demo to see how watchdog action
int main (void) {
unsigned int i;
init_serial(); /* Initialize Serial Interface */
if( WDMOD & 0x04 ) { /* Check for watchdog time out */
sendstr("Watchdog Reset Occurred\n");
WDMOD &= ~0x04; /* Clear time out flag */
}
WDTC = 0x2000; /* Set watchdog time out value */
WDMOD = 0x03; /* Enable watchdog timer and reset */
for(i = 0; i < 50; i++) { /* for this 50 times do_job will run successfuly
do_job (); /* the actual job of the CPU */
feed_watchdog(); /*restart watchdog timer, for_loop will run until complete */
}
while (1) { /* Loop forever, but watch dog will rest the MCU */
do_job (); /*so do_job( ) will not run for_ever, MCU will soon be reset*/
/* no watchdog restart, watchdog reset will occur! */
}
}
void feed_watchdog (void) { /* Reload the watchdog timer */
WDFEED = 0xAA;
WDFEED = 0x55;
}

## Slide 15: Watchdog Registers

## Slide 16: Watch dog mode reg. WMOD

## Slide 17
Watchdog
Block diagram
void feed_watchdog (void) { /* Reload the watchdog timer */
WDFEED = 0xAA; WDFEED = 0x55;
}

## Slide 18: Applications of watchdog timers
Space robot
www.links9 99.net
Pay Telephone box
www.viewimages.com
Industrial machine
http://www.maxengineering.us/img/machine1.jpg
Solar power wireless
emergency telephone
http://www.homepower.ca/

## Slide 19: Exercise 13.1 Describe how watch dog timers are used in the following examples.
?______________________
?______________________
?______________________
?______________________
Space robot
www.links9 99.net
Pay Telephone box
www.viewimages.com
Industrial machine
http://www.maxengineering.us/img/machine1.jpg
Solar power wireless
emergency telephone
http://www.homepower.ca/
Student ID:_________,Date:_________ Name: ____________________________

## Slide 20: 3) Pulse Width Modulation PWM unit Use on-off time to control energy delivery
The DC motor speed is determined by the on/off time of the motor enable signal MLE
On/off (MEL)
Battery +
DC Motor

## Slide 21: Timing diagrams of pulse width modulation
Comparing two pulse modulated signals S1,S2
Toff2
T =Period 1ms
Ton2
S1
S2
Ton1
Toff1
time

## Slide 22: P W M
Pin1=PWM5
Pin31=PWM2
PWM5=
Right-motor
PWM2=
Left-motor
PWM-YOU-TUBE

## Slide 23: In ARMdemo06.c Setting up the PWM system
Define PWM frequency constant
  17) #define PWM_FREQ 276480 //set PWM frequency to 50 Hz, since timer is 13824KHz
Set up PWM pins
  97) PINSEL1 |= 0x00000400; // set p0.21 to PWM5-right motor
  98) PINSEL0 |= 0x00008000; // set p0.7 to PWM2-left motor
Enable PWM
  Setup 122) PWMPCR=0x0000 2000; // enable pwm5;(bit 13 is set to 1)
  123) PWMPCR|=0x0000 0400;// enable pwm2 ;(bit 10 is set to 1)
Setting match registers for PWM timer
  124) PWMMCR=0x0000 0002; (BIT 1 IS SET TO 1) //PWM match contr.reg.
Setup PWM frequency using PWM_FREQ defined earlier
  125) PWMMR0 = PWM_FREQ; //set PWM frequency to 50 Hz

## Slide 24: In ARMdemo06.c Use of PWM modules after setting up
Define motors full speeds for left/right motors
  127) //set robot to full speed
  128) leftPWM=PWM_FREQ;//set a value you prefer
  129) rightPWM=PWM_FREQ; //a value you prefer
Ask the left /right motors to run at full speed
  130) PWMMR2 = leftPWM;// left motor PWM to full speed
    // PWMMR2 = leftPWM/2 ; //will run at half speed, etc
  131) PWMMR5 = rightPWM;//right motor PWM to full speed
    // PWMMR5 = leftPWM/2 ; //will run at half speed, etc
Enable PWM
  132) PWMLER = 0x25; //enable match 0,2,5 latch to effective
  133) PWMTCR=0x09;

## Slide 25: Code for Pulse Width Modulation PWM ARM06demo.c (with line numbers)
17) #define PWM_FREQ 276480 //set PWM frequency to 50 Hz, since timer is 13824KHz
//FREQ_of_PWM=13824000/276480=50
85) int main(void) {
…..
89)long leftPWM,rightPWM;
.....
// Initialize IO pin for PWM
97) PINSEL1 |= 0x00000400; // set p0.21 to PWM5-right motor
98) PINSEL0 |= 0x00008000; // set p0.7 to PWM2-left motor
.....
122) PWMPCR=0x2000; // enable pwm5
123) PWMPCR|=0x0400;// enable pwm2
124) PWMMCR=0x0002;
125) PWMMR0 = PWM_FREQ; //set PWM frequency to 50 Hz
PINSEL0 =0xE002 C000
PINSEL1=0xE002 C004
See http://www.nxp.com/acrobat_download/usermanuals/UM10120_1.pdf
PCLK =13.824MHz (see previous slide)
The formula: will set PWM frequency =
PCLK/PWM_FREQ=
13.824MHz/ 276480=50Hz

## Slide 26: Code for Pulse Width Modulation PWM ARM06demo.c (refer to line numbers)
17) #define PWM_FREQ 276480 //set PWM frequency to 50 Hz,
……
122) PWMPCR=0x0000 2000; // enable pwm5;(bit 13 is set to 1)
123) PWMPCR|=0x0000 0400;// enable pwm2 ;(bit 10 is set to 1)
124) PWMMCR=0x0000 0002;
125) PWMMR0 = PWM_FREQ; //set PWM frequency to 50 Hz
Chapter 15 of http://www.nxp.com/documents/user_manual/UM10120.pdf

## Slide 27: Code for Pulse Width Modulation PWM ARM06demo.c (refer to line numbers)
17) #define PWM_FREQ 276480 //set PWM frequency to 50 Hz,
……
122) PWMPCR=0x0000 2000; // enable pwm5
123) PWMPCR|=0x0000 0400;// enable pwm2
124) PWMMCR=0x0000 0002; (BIT 1 IS SET TO 1) //PWM match contr.reg.
125) PWMMR0 = PWM_FREQ; //set PWM frequency to 50 Hz

## Slide 28: Code for Pulse Width Modulation PWM ARM06demo.c (refer to line numbers)
17) #define PWM_FREQ 276480 //set PWM frequency to 50 Hz,
……
122) PWMPCR=0x0000 2000; // enable pwm5
123) PWMPCR|=0x0000 0400;// enable pwm2
124) PWMMCR=0x0000 0002;
125) PWMMR0 = PWM_FREQ; //set PWM frequency to 50 Hz
PCLK =13.824MHz (see previous slide)
The formula: will set PWM frequency =
PCLK/PWM_FREQ=
13.824MHz/ 276480=50Hz

## Slide 29: Code for Pulse Width Modulation PWM
17) #define PWM_FREQ 276480
:
127) //set robot to full speed
128) leftPWM=PWM_FREQ;//set a value you prefer
129) rightPWM=PWM_FREQ; //a value you prefer
130) PWMMR2 = leftPWM;// left motor PWM width to full speed
131) PWMMR5 = rightPWM;//right motor PWM width to full
132) PWMLER = 0x25; //enable match 0,2,5 latch to effective
133) PWMTCR=0x09;
leftPWM
rightPWM

## Slide 30: 133) PWMTCR=0x09;//=0000 1001B, enable counter,PWM

## Slide 31: Use of the L293 H bright circuit
A chip for generating enough current to drive 2 motors controlled by 4 signals
2 (1A) 1Y(3)
1(EN1/2)
7(2A) (2Y)6
10(3A) (3Y)11
9(EN3/4)
15(4A) (4Y)14
PWMMR2
L_DIR
PWMMR5
R_DIR
Left-motor
Right-motor

## Slide 32: Exercise 13.2 Application– driving a robot Fill in “?__”
Left-motor forward
P0.16 =L_DIR =?___
P0.17=L_DIRinv=?__
Left motor backward
P0.16 =L_DIR=?__
P0.17= L_DIRinv=?__
Left-motor speed
=PWMMR2
Right-motor forward
P0.18 = R_DIR =?__
P0.19= R_DIRinv=?__
Left motor backward
P0.18 = R_DIR=?__
P0.19= R_DIRinv=?__
Right-motor speed
=PWMMR5
L293 see next slide
When IN1=1, IN2=0, L-motor forward
When IN1=0, IN2=1, L-motor backward
When IN3=1, IN4=0, R-motor forward
When IN3=0, IN4=1, R-motor backward

## Slide 33: Setting drive direction pins
18) #define L_DIR 0x00010000 //set p0.16 left motor dir.
19) #define L_DIRinv 0x00020000 //set p0.17 inverted left motor dir.
20) #define R_DIR 0x00040000 //set p0.18 right motor dir.
21) #define R_DIRinv 0x00080000 //p0.19 inverted right motor dir.
22) #define TEST_PIN 0x00010000 //set p1.16 as Test pin
:
135) //set p0.16-p0.19 as output
136) IO0DIR|=L_DIR; //p0.16
137) IO0DIR|=L_DIRinv; //p0.17
138) IO0DIR|=R_DIR; //p0.18
139) IO0DIR|=R_DIRinv; //p0.19
140) IO1DIR|=TEST_PIN;// p1.16 as Outputs
Set p0.16-19 as output
pins

## Slide 34: Four line (170-173) to start the robot move forward
170) IO0SET|=L_DIR;
171) IO0CLR|=L_DIRinv;
172) IO0SET|=R_DIRinv;
173) IO0CLR|=R_DIR;

## Slide 35: sensors
wheel rotation sensors

## Slide 36: Left Wheel sensor – LWheelsen (same for Right wheel sensor RWheelsen)
Our motor and
speed encoder
Each wheel rotation=
88 on/off changes
IR receiver
IR light source
Darkened
part
blocks light
LWSensor
RWSensor
encoder-YOUTUBE

## Slide 37: Setup for LWheelsen = p0.6 (LPC213-pin30), Rwheelsen = p0.3(LPC213x-pin26)
// set p0.0 to TXD0, p0.1 to RXD0 and the rest to GPIO
//After power up (reset value) , all GPIOs are inputs
//So by default p0.6 (LWheelsen), p0.3(Rwheelsen) are inputs
91)PINSEL0 = 0x00000005;
:
23) #define LWheelSen 0x00000040 //p0.6 as left wheel sensor input
24) #define RWheelSen 0x00000008 //p0.3 as right wheel sensor input

## Slide 38: Sensor connection
LWsensor
RWSensor

## Slide 39: It uses a timer interrupt service routine programs
void init_timer (void)
  Setup 1000 timer interrupt for _IRQ exception()
_IRQ exception()
  Capture the rotation count, (each rotation 88 counts.)
  Result saved at lcount, rcount

## Slide 40: Read wheel count (lcount, rcount) using interrupts
IR receiver
Speed Encoder
sensor
interrupts
time
Main( )
{
Setup( );
:
:
}
_IRQ exception() //1000Hz
{
:
read wheel speed
Update rcount
Update lcount
:
}
1000 interrupts per second

## Slide 41: Read wheel count, result at lcount, rcount
265) void __irq IRQ_Exception() //timer interrupt running at 1000Hz
266) {
267) timeval++;
268) //generate square wave at test pin
269) if((timeval%2)==0) IO1SET|=TEST_PIN;
270) else IO1CLR|=TEST_PIN;
271) //=================
272)
273) //get the current wheel sensor values
274) lcur=IO0PIN & LWheelSen;
275) rcur=IO0PIN & RWheelSen;
276)
277) //count the number of switchings
278) if(lcur!=lold) {
279) lcount++;
280) lold=lcur;
281) }
282) if(rcur!=rold) {
283) rcount++;
284) rold=rcur;
285) }
286)
287) T0IR = 1; // Clear interrupt flag
288) VICVectAddr = 0; // Acknowledge Interrupt
289) }
CEG2400 Ch9 Peripherals V93b
time
1000 interrupts per second
Left wheel: each interrupt checks if the wheel sensor
output has changed state . If yes, lcount++
IR receiver
P0.6 (left wheel) , or P0.3 (right wheel)
23) #define LWheelSen 0x00000040
24) #define RWheelSen 0x00000008
lcount records the number of counts (number of times the IR light is chopped v=by the rotating disk) of the left wheel since the program starts
Same for rcount of the right wheel

## Slide 42: Explanation1 , line265-271
265) void __irq IRQ_Exception()
266) {
267) timeval++;// increases at 1000 per second
268) //generate square wave at test pin
269) if((timeval%2)==0) IO1SET|=TEST_PIN;
270) else IO1CLR|=TEST_PIN;
271) //=================
:
:
:
For testing purpose
You can observe a waveform at this pin

## Slide 43: Explanation2, line 273-275
23) #define LWheelSen 0x00000040 //bit 6 is1, others 0, p0.6 as left wheel sensor input
:
273) //get the current wheel sensor values
274) lcur=IO0PIN & LWheelSen; // read left sensor
275) rcur=IO0PIN & RWheelSen; // read right sensor
Meaning: if LWSesnor is 1 //current status of LW sensor=1
  lcur=IO0PIN & LWheelSen =IO0PIN & 0x0000 0040 = 0x0000 0040
Meaning: if LWSesnor is 0 //current status of LW sensor=0
  lcur=IO0PIN & LWheelSen =IO0PIN & 0x0000 0040 = 0x0000 0000
LWSensor
Bit6 of IO0PIN
P0.6 of LPC213x

## Slide 44: Exercise 13.3 IF Lwsensor is 25Hz, what is the value of lcount incremented in ¼ seconds? ANS:?_______________________________
273) //Explanation3, line273-289// get the current wheel sensor values
274) lcur=IO0PIN & LWheelSen; // read left sensor
275) rcur=IO0PIN & RWheelSen; // read right sensor
276)
277) //count the number of switching
278) if(lcur!=lold) {
279) lcount++;
280) lold=lcur;
281) }
282) if(rcur!=rold) {
283) rcount++;
284) rold=rcur;
285) }
286)
287) T0IR = 1; // Clear interrupt flag
288) VICVectAddr = 0; // Acknowledge Interrupt
289) }
CEG2400 Ch9 Peripherals V93b
44
If there is change increment lcount
time
1000 interrupts per second
Left wheel: each interrupt checks if the wheel sensor
output has changed state . If yes, lcount++
LWsenor

## Slide 45: Explanation4, line174-183 In main() “ f ” command: Forward 100 steps and stop when lcount>100, stop left motor when rcount>100, stop right motor
Main()
:
174) if(cin=='f') {
175) lcount=0; //reset left step count
176) rcount=0; //reset right step count
177) //stop when stepcount reach 100 steps
178) while((lcount<=100)||(rcount<=100)) {
179) if(lcount>=100) {
180) IO0CLR|=L_DIRinv;//stop left motor
181) IO0CLR|=L_DIR;
182) lcount=0xff;
183) }
184) if(rcount>=100) {
stop right motor
similar to the left motor procedures above}
:}
Interrupt service routine
Running at 1000Hz
Update lcount and rocunt
As the wheels rotate
265) void __irq IRQ_Exception()
266) {
:
274)lcur=IO0PIN & LWheelSen;
275)rcur=IO0PIN & RWheelSen;
:
278)if(lcur!=lold) {
279) lcount++;
280) lold=lcur;
281)}
282)if(rcur!=rold) {
283) rcount++;
284) rold=rcur;
285)}
:
289) }
1000Hz
Interrupt
rate

## Slide 46: Timer interrupt at 1KHz,interrupt service routine is at IRQ_Exception; Refer to the notes on how to set timer interrupt
291) /* Setup the Timer Counter 0 Interrupt */ //1KHz
292) void init_timer (void) {
293) T0PR = 0; // set prescaler to 0
294) T0MR0 =13800; // set interrupt interval to 1mS
295) T0MCR = 3; // Interrupt and Reset on MR0
296) T0TCR = 1; // Timer0 Enable
297) VICVectAddr0 = (unsigned long)IRQ_Exception;//interrupt vector in 0
298) VICVectCntl0 = 0x20 | 4; // use it for Timer 0 Interrupt
299) VICIntEnable = 0x00000010; // Enable Timer0 Interrupt
300) }

## Slide 47: Exercise 13.4
If the wheel is running very fast, say LWsensor is 400Hz , can you use the method to sample the wheel? Why?
ANS:?_____________________________
Discuss a method to measure the motor speed?
ANS:?______________________

## Slide 48: 4) Real time clock
Read time
and
set alarm

## Slide 49: Summary
Studied peripherals of the LPC213x ARM processor.

## Slide 50: Appendix

## Slide 51
Our robot (ver12 – Old version)
Circuits of this chapter are from this design

## Slide 52
New robot drive circuit ver13.3