## Slide 1: Chapter 15: Higher Level Constructs (C and assembly relation)
CEG2400 - Microcomputer Systems
Reference
Steven Furber, ARM system-on-chip architecture Pearson
http://www.davespace.co.uk/arm/introduction-to-arm/branch.html

## Slide 2: Introduction
Part 1: ARM instructions
Part 2 : using assembly to implement C statements.
  Reference
  http://www.heyrick.co.uk/assembler/qfinder.html

## Slide 3: Part 1
Instructions

## Slide 4: Instructions CEG2400 ARM Instruction quick reference.doc http://www.cse.cuhk.edu.hk/~khwong/www2/ceng2400/ARM_Instruction_quick_reference.doc
Instructions
Arithmetic ADD{condition}{S} Rd, Rn, <Operand>
ADC{condition}{S} Rd, Rn, <Operand>
SUB{condition}{S} Rd, Rn, <Operand>
SBC{condition}{S} Rd, Rn, <Operand>
RSB{condition}{S} Rd, Rn, <Operand>
RSC{condition}{S} Rd, Rn, <Operand>
MUL{condition}{S} Rd, Rm, Rs
MLA{condition}{S} Rd, Rm, Rs, Rn
UMULL{condition}{S} RdLo, RdHi, Rm, Rs
UMLAL{condition}{S} RdLo, RdHi, Rm, Rs
SMULL{condition}{S} RdLo, RdHi, Rm, Rs
SMLAL{condition}{S} RdLo, RdHi, Rm, Rs
Move MOV{condition}{S} Rd, <Operand>
MVN{condition}{S} Rd, <Operand>
Logical TST{condition} Rn, <Operand>
TEQ{condition} Rn, <Operand>
AND{condition}{S} Rd, Rn, <Operand>
EOR{condition}{S} Rd, Rn, <Operand>
ORR{condition}{S} Rd, Rn, <Operand>
BIC{condition}{S} Rd, Rn, <Operand>
Compare CMP{condition} Rn, <Operand>
CMN{condition} Rn, <Operand>
Branch B{condition} label
BL{condition} label
Load / Store LDR{condition} Rd, <Addressing_mode1>
STR{condition} Rd, <Addressing_mode1>
Stack LDM{condition}<Addressing_mode2> Rn{!}, <register_list>
STM{condition}<Addressing_mode2> Rn{!}, <register_list>

## Slide 5: Required fields
Required fields
<Operand>
Immediate value #<immediate_value>
Register Rm
Logical shift left Rm, LSL #<shift>
Logical shift right Rm, LSR #<shift>
Arithmetic shift right Rm, ASR #<shift>
Rotate right Rm, ROR #<shift>
E.g.
ADD R0, R2, R3,LSL#1 ; R0 = R2 + (R3 << 1)

## Slide 6: Addressing_modes
<Addressing_mode1>
Zero offset [Rn]
Immediate offset [Rn, #+/-< immediate_value>]
Register offset [Rn, +/-Rm]
Post-indexed Immediate offset [Rn], #+/-< immediate_value>
Post-indexed Register offset [Rn], +/-Rm
Pre-indexed Immediate offset [Rn, #+/-< immediate_value>]!
Pre-indexed Register offset [Rn, +/-Rm]!
<Addressing_mode2>
Full Descending FD
Empty Descending ED
Full Ascending FA
Empty Ascending EA

## Slide 7: Optional fields CEG2400 ARM Instruction quick reference.doc
Optional fields
{condition}
EQ Equal
NE Not equal
MI Negative
PL Positive or zero
VS Overflow
VC No overflow
HI Unsigned higher
LS Unsigned lower or same
GE Signed greater than or equal
LT Signed less than
GT Signed greater than
LE Signed less than or equal

## Slide 8: Part 2
Using assembly to implement C statements

## Slide 9: Why?
All higher languages (C, C++, Java) must be translated into assembly language/machine code for execution
Higher level
Language
C, C++, java
Compilation
By a
compiler
Object code
In assembly
Machine
Code in
memory
Assemble
by
an
assembler

## Slide 10: C statements
Pointers
Arrays
Conditional statements : If-then-else; Switch
For loop
Do while loop
While loop

## Slide 11: 1) Pointers in C
int *p; //integer is 32-bit
p = p + 1;
  Since p points to a 4-byte value, p must be incremented by 4
  Increment the pointer once , increment address 4 times
  If p is in register r0 “add r0,r0,#4”
p = p + t;
  ;P in r0, t in r1
  p must be incremented by 4 * t, so if t is in r1
  add r0,r0,r1,lsl #2; t=r1, old p=r0. New_p=old_p+t*4
  Note: r1 lsl #2 = r1 times 4= t times 4
Each memory address is
8-bit
So each 32-bit has 4 locations
8-bit

## Slide 12: Recall : ADD http://www.heyrick.co.uk/assembler/mov.html#add
ADD : Addition
ADD<suffix> <dest>, <op 1>, <op 2>
dest = op_1 + op_2
ADD will add the two operands, placing the result in the destination register. Operand 1 is a register, operand 2 can be a register, shifted register, or an immediate value:
ADD R0, R1, R2 ; R0 = R1 + R2
ADD R0, R1, #256 ; R0 = R1 + 256
ADD R0, R2, R3,LSL#1 ; R0 = R2 + (R3 << 1)
The addition may be performed on signed or unsigned numbers.

## Slide 13: 2) Arrays
Same as pointers since a[i] is the same as *(a + i)

## Slide 14
;//3) Conditionals in C
; User Initial Stack & Heap
AREA |.text|, CODE, READONLY
EXPORT __main
__main ;
;// if (a > b)
;// c = a;
;//else c = b;
;//The assembly code is as follows;
//a, b and c are in r0, r1, r2 resp.
mov r0,#1 ; =a,try #1 or #3 to see result
mov r1,#2 ; =b
cmp r0,r1 ; testing a-b or r0-r1 ; test a<=b
ble L1 ; branch to L1"if b is less or equal than a "
mov r2,r0 ; c=a, since (a<=b fails), hence a>b
b exit ; done
L1 mov r2,r1 ; c=b, because a<=b
exit
end
a>b?
(r0>r1)?
c=a
(r2=r0)
c=b
(r2=r1)
yes
no

## Slide 15: Exercise1 Conditionals in C
if (a <= b)
c = a;
else c = b;
a, b and c are in r0, r1, r2 resp.
Write the assembly code

## Slide 16: Recall: CMP http://www.heyrick.co.uk/assembler/cmp.html#cmp
CMP : Compare
CMP<suffix> <op 1>, <op 2>
status = op_1 - op_2
CMP allows you to compare the contents of a register with another register or an immediate value, updating the status flags to allow conditional execution to take place.
It performs a subtraction, but does not store the result anywhere. Instead, the flags are updated as appropriate.

## Slide 17: Recall: MOV http://www.heyrick.co.uk/assembler/cmp.html#cmp
MOV : Move
MOV<suffix> <dest>, <op 1>
dest = op_1
MOV loads a value into the destination register, from another register, a shifted register, or an immediate value.
You can specify the same register for the effect of a NOP instruction, or you can shift the same register if you choose:
MOV R0, R0 ; R0 = R0... NOP instruction
MOV R0, R0, LSL#3 ; R0 = R0 * 8
If R15 is the destination, the program counter or flags can be modified. This is used to return to calling code, by moving the contents of the link register into R15:
MOV PC, R14 ; Exit to caller
MOVS PC, R14 ; Exit to caller preserving flags
(not 32-bit compliant)

## Slide 18: Conditionals
The method in the previous slide is the most general case, can have many statements in the “if” and “else” parts of the condition
For simple cases such as the example, it may be more efficient to use conditional execution, e.g. “conditional execution gt”
For example the following 3 statements can implement if-then-else:
CMP r0, #0 ; if (x <= 0)
MOVLE r0, #0 ; x = 0; combine MOV+LE in
; one statament is possible in AMR
MOVGT r0, #1 ; else x = 1;
See http://www.davespace.co.uk/arm/introduction-to-arm/conditional.html

## Slide 19: Switches in C (application of if-then-else)
switch (e) {
case 0: point0;
case 1: point1;
…
default: pointx;
}
Can be handled using “if” statements; use previous methods
tmp = e;
if (tmp == 0) {
point0;
}
else
if (tmp == 1) {
point1;
}
…
else {
pointx;
}…

## Slide 20: 4) For loop in C
for (i = 0; i < 10; i++)
  { a[i]=3; }//This code could be optimized
  //in a number of ways, please think about it
  AREA |.data|, DATA, READWRITE
top_of_array DCD 0, 0, 0, 0, 0, 0, 0, 0, 0, 0 ,0
align
; User Initial Stack & Heap
AREA |.text|, CODE, READONLY
EXPORT __main
__main ;
mov r1,#3 ;value 3 to save in a[i]
ldr r2,=top_of_array; r2=pointer to a[0]
mov r0,#0 ;i is r0, initial i=0
Loop1 cmp r0,#10 ; if i >= 10 done
bge exit ; branch exit if greater
str r1,[r2] ; store r1(=3) in a[i] pointed by r
add r2,#4 ; a[0]+i*4 point to next location
add r0,#1 ;i++
b Loop1
exit
end;
r2=a[0]
NEXT
a[i]
Top_of_array
[ ] is Indirect addressing, store the value in r1 into the address pointed by r2

## Slide 21: Exercise 2
for (i = 0; i < 10; i++){
a[i]=i-1;
}
Write the assembly code.

## Slide 22: C-disassembly : for loop
for (i=1;i<10;i++)
{
if (i <= 5)
c = 0;
else
c = 1;
}
;when run “debug” you will get the disassembler window
4: for (i=1;i<10;i++)
5: {
0x000002AC E3A01001 MOV R1,#0x00000001
0x000002B0 EA000005 B 0x000002CC
6: if (i <= 5)
0x000002B4 E3510005 CMP R1,#0x00000005
0x000002B8 CA000001 BGT 0x000002C4
7: c = 0;
8: else
0x000002BC E3A02000 MOV R2,#0x00000000
0x000002C0 EA000000 B 0x000002C8
9: c = 1;
10: }
0x000002C4 E3A02001 MOV R2,#0x00000001
4: for (i=1;i<10;i++)
5: {
6: if (i <= 5)
7: c = 0;
8: else
9: c = 1;
10: }
0x000002C8 E2811001 ADD R1,R1,#0x00000001
0x000002CC E351000A CMP R1,#0x0000000A
0x000002D0 BAFFFFF7 BLT 0x000002B4
11: }

## Slide 23: Recall: LDR or STR http://www.heyrick.co.uk/assembler/str.html#ldr
Single Data Transfer
  The single data transfer instructions (STR and LDR) are used to load and store single bytes or words of data from/to main memory. The addressing is very flexible.
  First, we'll look at the instruction:
  LDR R0, address;(load 4 bytes)
  STR R0, address;(load 4 bytes)
  LDRB R0, address ;(load single byte)
  STRB R0, address; (store single byte)
For “LDRLS” : LS =the optional field, will execute LDR if the condition LS is satisfied .
  LS =Unsigned lower or same

## Slide 24: 5) Do_while one branch is enough
Do_while
{..do_something..
body;
} while (conditional expression);
LOOP {…do_something.. ;
…body… };
bne LOOP ;conditional expression
EXIT

## Slide 25: 6) While_do loop requires 2 branch instructions
While_do (conditional_expr)
{do_something …body;}
LOOP … ; not conditional_expr
beq exit ;branch exit if condition met
…do_something…; main body
b LOOP
EXIT
The main loop has
2 branch instructions: slower

## Slide 26: Alterative method ‘while_do()’, the following is more efficient, because The main loop has only 1 branch instruction only (FAST). Note: Branch is time-consuming to run in hardware, so avoid using too many of them.
C language:
While_do (conditional expr){…do_something...}
Assembly:; do some test first before get into LOOP
b TEST ; goto TEST inside the loop first
; hence one branch is need inside the loop
LOOP … do_something ..; loop main body
TEST…; exit test conditional expression
bne LOOP ;loop back if exit condition not met
EXIT
“Goto exit if test exit condition is met”

## Slide 27: Exercise 3: Write an assembly program segment for the following C-language module. Assume ‘a’ is in register r0, ‘b’ is in register r1 and ‘c’ is in register r2. The variables a, b, and c are unsigned integers.
if (a < b)
c = a;
else c = b;

## Slide 28
; Exercise 4
;Assume a, b and c are in registers r0, r1 and r2 respectively.
;Write the C-language segment of the following ARM assembly program.
__main
;a, b and c are in r0, r1, r2 resp.
mov r0,#2
mov r1,#1
mov r2,#0
cmp r0,r1
ble l1
mov r2,r0
add r2,#2
b end
l1 mov r2,r0
exit nop;
end

## Slide 29: Summary
Studied the relation between assembly and higher level languages

## Slide 30: Appendix1 Recall: AND
AND : Logical AND
AND<suffix> <dest>, <op 1>, <op 2>
dest = op_1 AND op_2
AND will perform a logical AND between the two operands, placing the result in the destination register; this is useful for masking the bits you wish to work on. Operand 1 is a register, operand 2 can be a register, shifted register, or an immediate value:
AND R0, R0, #3 ; R0 = Keep bits zero and one of R0,
discard the rest.
An AND table (result = both):
Op_1 Op_2 Result
0 0 0
0 1 0
1 0 0
1 1 1

## Slide 31
//self studying exercises, no need to submit to the teacher.
//http://www.cse.cuhk.edu.hk/~khwong/www2/ceng2400/testing_C_and_assembly.c
//Appendix: testing C and assembly conversion
// run this program and read contents in the disassembly window in uvision
//Exercises: Use single step to run it, and answer the questions below.
#include <lpc21xx.h>
int a[4],b[4],c,i;
main()
{
for(;;) //testing forever
{
//test 1, looping
for (i=1;i<10;i++)
{ if (i <= 5)
c = 0;
else
c = 1;
}
//Question1a: Where does the program store i and c?
//Question1b: Draw the flow diagram of the program.
//test 2, looping and array
for (i = 0; i < 4; i++)
{a[i]=0; b[i]=0;//clear the arrays
}
for (i = 0; i < 10; i++)
{a[i]=3+i; //set values into the array
}//question2a: Find a bug in the above program.
//question2b: What is the actual result of running the code?
//test 3, looping
i=0,c=0; //clear i,c
while (i<5)
{c++;
i++;
}
//Question3a: Where does the program store i and c?
//Question3b: Draw the flow diagram of the program.
//test 4, test switching
i=0,c=1; //clear variables
for(i=0;i<5;i++)
{
switch (i) {
case 0: c=0;
case 1: c=1;
case 2: c=2;
case 3: c=3;
case 4: c=4;
default: c=0;
} } }
//question4a: Explain how switch-case is implemented here.
//question4b: Suggest an alternative method for the implementation.
}

## Slide 32: Recall: ADR (Pseudo instructions)
ADR : load ADRess
ADR<suffix> <register>, <label>
This loads the address referred into the given register:
00008FE4 OPT l%
00008FE4 E28F0004 ADR R0, text
00008FE8 EF000002 SWI "OS_Write0"
00008FEC E1A0F00E MOV PC, R14
00008FF0 .text
00008FF0 EQUS "Hello!" + CHR$13 + CHR$10 + CHR$0
00008FFC ALIGN
The disassembler shows that
ADR becomes two 32-bit instructions,
So ADR is called a pseudo instruction