## Slide 1: Chapter 16 Feedback control of motors, based on Demo2017.c and PIDRobotDemo.c
CEG2400 - Microcomputer Systems
Reference : www.tic.ac.uk/micromouse/PRESENTATIONS/Heretic.ppt
http://www.cse.cuhk.edu.hk/khwong/ceg2400/PIDRobotDemo093.c

## Slide 2: Objectives
(a)Study DC motors, (b) Servo motors
Study Stepping Motors
Study open-loop and closed-loop control
Control methods
  I) Proportional feedback control
  II) PID (proportional-integral-derivative) control

## Slide 3: 1a) Direct Current (DC) motors
For robots

## Slide 4: Motors
Our robot
DC motor with speed encoder

## Slide 5: Small Direct Current D.C. motors
Speed (~ 1200-2000 rpm).
Operates on a 3~5Volt, Can use gear box (e.g. ratio 58:1) to increase torque
Use H-bridge circuit to boost up current from the TTL level to motor driving level.
田宫四驱车配件15351 PRO版专用双头马达 ,
picture from http://item.taobao.com/item.htm?id=1606576457&tracelog=newcardfavirate

## Slide 6: Motor control chip
H-bridge Chips
L293D: H-bridge circuit, up 2A
LDIR: left motor direction; RDIR: right motor direction
LEN : left motor enable; REN : right motor enable
LEN
LDIR
REN
RDIR
2 (1A) 1Y(3)
1(EN1/2)
7(2A) (2Y)6
10(3A) (3Y)11
9(EN3/4)
15(4A) (4Y)14
Left-motor
Right-motor

## Slide 7: Servo motors (based on DC motor)
Can achieve rotational angle control
Application: robotics, target pointing
The motor shaft is attached to a rotational variable resistor (potentiometer)
When the motor rotation has adjusted the variable resistor to the correct rotational angle, the electronic circuits circuit stops the motor.
https://www.jameco.com/jameco/workshop/howitworks/how-servo-motors-work.html
https://electronicspost.com/describe-the-different-types-of-resistors/
** How do servo motors work: https://www.youtube.com/watch?v=J8atdmEqZsc
https://www.youtube.com/watch?v=hYu9fGE4pCk
Common control method
by adjusting pulse width
1-2ms 0-180o

## Slide 8: Use of servo motors
Making humanoid robots , or
Robot Arms
https://www.youtube.com/watch?v=n_1aVNnz9rA
https://www.youtube.com/watch?v=NZ6V63u_-D8

## Slide 9: 2) Stepping motor (stepper)
Stepping motors are good positional control motors used widely in digital controlled machineries such as digital arm-clocks, printers, disk drives etc.
How does a stepping motor work?
https://www.youtube.com/watch?v=TWMai3oirnM
https://www.youtube.com/watch?v=eyqwLiowZiU
The stepping motor in our robot

## Slide 10: Stepping motor (4-phase) and Circuit
Large current stepping motors need current drivers
Smaller current Stepping motors can be driven by modern microcontrollers directly by GPIO outputs
Digital outputs

## Slide 11: Stepping (stepper)motor control table

## Slide 12: Control method comparisons

## Slide 13: Use of stepping motor
Positional control of robot range scanner.
Ultrasonic
Radar system
on a rotational
platform
obstacle
Transmitter
Receiver
IR Distance sensor

## Slide 14: Stepping motor (stepper) in our robot
For setting the angular positioning of an inferred (IR) distance sensor
Operation:
  First, at initialization, the stepper will be adjusted to the reference position (0 degree, the plate is blocking the Photo interrupter gap).
  Then, it can be rotated to t degrees (with respect to the reference 0 degree)
Infrared (IR) distnace Sensor,
stepper
stepper
Photo interrupter
LED emitter & sensor
t
The photo interrupter

## Slide 15: Other usage
Robot building, micro mouse

## Slide 16: Stepping motor smooth control method
Control method
Rotating Speed
1
Rotating speed
1
Sudden change of speed may result in step-slipping
Gradual change of speed will solve the step-slipping problem
Time

## Slide 17: 3) open-loop and closed-loop control
Feedback control
PID theory and implementation

## Slide 18: Open-loop motor control and its problems
Change motor supply power change speed
Problem: How much power is right?
  Ans: don’t know , depends on internal/external frictions of individual motors.
Problem: How to make the robot move straight?
How to control power (Ton) by ISR & an MCU?
  Solution: Use feedback control to read actual wheel:
  Slower, increase power (+ Ton)
  Faster, reduce power (- Ton)

## Slide 19: Exercise
When using the open-loop control method with a constant PWM signal for both wheels, explain why the robot would slow down when climbing up hill.
  Ans: When climbing up hill, energy is used to act against gravity, hence the robot is running slower.

## Slide 20: Feedback control
The real solution to read the real speed of the wheel and control the speed using feedback control
Require speed encoder to read back the real speed of the wheel at real time.

## Slide 21: First you need to have speed encoders
Read wheel speed.
Use photo interrupter
Use reflective disk to save space
Based on interrupts

## Slide 22: Wheel encoder
Our motor and
speed encoder
Each wheel rotation=
88 on/off changes
IR receiver
IR light source
Darkened
part
blocks light

## Slide 24: Exercise 1: (Fill in ?__)
The Gear ratio =(DC motor speed/wheel speed)=48, and the DC motor speed is 200 Rotations/Second
So the wheel is rotating at 200/48  4 rotations/second.
If the disk has 1 hole, the pulse frequency is observed to have _200_?Hz.
Using the same setup , if the disk has 4 holes, the pulse frequency is _800____?Hz.
Wheel radius is r=0.033m, perimeter is 2*pi*0.033 m
The car is moving at 4 rotations per second=?___ 2*3.14*0.033 *4= 0.83 meters per second (at full speed, quite fast)
The speed encoder gives ?_800_Hz pulses.
Data comes from
http://item.taobao.com/item.htm?spm=2013.1.0.116.KbMxbr&id=15172908917
66mm
This is when the disk has 1 hole.The waveform is 200 Hz
Student ID: ___________,Date:_____________ Name: _______________CENG2400 , Ch 16 PID

## Slide 25: Speed encoder
Demo
movie
田宫四驱车配件15351 PRO版专用双头马达 ,
picture from http://item.taobao.com/item.htm?id=1606576457&tracelog=newcardfavirate

## Slide 26: New speed encoder 2017
Only need two GPIO inputs (PD5,PC6)
Software requireddriver.lib http://www.ti.com/tool/SW-TM4C
And the functions are
  QEIPositionSet()
  QEIPositionGet(QEI0_BASE)
I.e.//Set GPIO pins for QEI. PhA1 -> PC5, PhB1 ->PC6.
GPIOPinTypeQEI(GPIO_PORTC_BASE, GPIO_PIN_5 | GPIO_PIN_6);
Gear box, DC mtoro
Speed encoders

## Slide 27: Speed encoder https://www.pololu.com/product/1443
When the encored rotates, pulses will be sent out
Your system program should read and encode the signals
Using the Encoder from https://www.pololu.com/product/1443
“A two-channel Hall effect encoder is used to sense the rotation of a magnetic disk on a rear protrusion of the motor shaft. The quadrature encoder provides a resolution of 64 counts per revolution of the motor shaft when counting both edges of both channels. To compute the counts per revolution of the gearbox output, multiply the gear ratio by 64. ”
For simplicity, our robot only uses one of the two signals

## Slide 28: 4) Control methods
I) Proportional feedback control
II) PID (proportional-integral-derivative) control

## Slide 29: I) Proportional closed-loop feed back control system
Show the left motor control only
Required speed
=leftRPMset
speed encored
leftRPM
+
-
leftErr
Motor
Alter PWM for driver L293
leftPWM
if (leftErr >deadband)
leftPWM increase by (Pgain * leftErr)

## Slide 30: II) PID (proportional-integral-derivative) control
A more formal and precise method
Used in most modern machines

## Slide 31: control method: PID (proportional-integral-derivative) control
Required speed=
leftRPMset
wheel
Speed
encoder
LeftRPM
+
-
leftRPM
Motor
&
generates PWM
for driver L293
leftPWM
integral control
Igain* leftErr dt
Proportional control
Pgain*leftErr
Derivative control
Dgain*[d(leftErr)/dt]
sum
leftErr
leftPWM

## Slide 32: Introduction
Control for better performance
Use PID, choose whatever response you want
Good performance
Criteria depends
on users and
applications
Too much overshoot/undershoot, not stable
Response too slow
time
Motor speed (w)
required

## Slide 33: Exercise 2: Values to evaluate a control system
Describe the terms in the following diagram
Do you want them to be large or small?
Typically
value=10%
Depends
on application
Rise time
Settling time
0
time
Target
value
overshoot
Steady
state
error
undershoot

## Slide 34: Use of PID control terms are intertwined http://en.wikipedia.org/wiki/PID_controller
Kp (Pgain): Proportional Gain - Larger Kp typically means faster response since the larger the error, the larger the Proportional term compensation. An excessively large proportional gain will lead to process instability and oscillation.
Ki (Igain): Integral Gain - Larger Ki implies steady state errors are eliminated quicker. The trade-off is larger overshoot: any negative error integrated during transient response must be integrated away by positive error before we reach steady state.
Kd (Dgain): Derivative Gain - Larger Kd decreases overshoot, but slows down transient response and may lead to instability due to signal noise amplification in the differentiation of the error.

## Slide 35: Effects of adjusting parameters http://en.wikipedia.org/wiki/PID_controller
Parameter | Rise Time | Overshoot | Settling Time | Steady state error
Kp (Pgain) | Decrease step1 | Increase | Small Change | Decrease
Ki (Igain) | Decrease | Increase | Increase | Eliminate step3
Kd (Dgain) | Small Change | Decrease step2 | Decrease | Small Change

## Slide 36: Software
Demo2017.c
(at course webpage)
Old version: http://www.cse.cuhk.edu.hk/~khwong/www2/ceng2400/PIDRobotDemo093.c

## Slide 37: PID control algorithm
PID control algorithm using interrupt
The main program and the Interrupt service routine (ISR) __Timer0IntHandler
Main( )
{
Setup( );
:
:
}
_Timer0IntHandler//1000Hz
{
intCnt++;
if intCnt==50;
{//PID core // will be run every 50ms
read wheel speed
PID control to adjust PWM
intCnt=0; //reset counter
}
…..
}

## Slide 38: Overview
//////////////main //////////////////////////////////////
Main()
{ setup()
forward (Lstep, Rstep, Lspeed, Rspeed)…..
}
////////////subroutine //////////////////////////////////////////
forward (Lstep, Rstep, Lspeed, Rspeed)
{ lcount=0
if (lcount>=Lstep)
Stop left motor
…same for right motor…
.}
//////////timer triggered , interrupt service routine, 1000Hz///////
_Timer0IntHandler// Interrupt() running at 1000HZ
{ intCnt++;
if intCnt==50;
{//PID core // will be run every 50ms
read wheel speed
PID control to adjust PWM
intCnt=0; //reset counter
}
}
_Timer0IntHandler
see next slide
Interrupt
rate 1000Hz

## Slide 39: Speed encoder interfacing (show left motor only)
Block diagram
encoder sensor)
GPIO
Parallel interface
/int0
CPU
1000Hz timer interrupt
ARM7-microcontroller
Motor & speed encoder

## Slide 40: Exercise 3 (refer to Demo2017.c) _irq interrupt programming method for the main PID loop, using a counter (intcount)
_Timer0IntHandler(void)//timer 1KHz,
{ intCnt++
if(intCnt ==50)
{ //So this PID core is updated at 20Hz (period =50ms)
read wheel speed
Control the PWM using PID (See next slide)
intCnt =0;// reset counter intCnt
}
}
Question: If he line “if(intCnt==50) “ is changed to “if(intCnt==100)”
What will happen to the PID core update period?
Answer: PID core is updated at 10Hz (period =100ms)

## Slide 41: The interrupt service routine enables the loop to run 4 times in a second
Loop once in 50ms

## Slide 42: Part 2 :Algorithm for PID core
For every 50ms
  Find error=(desired value - measured value)
  {If (error>dead band )
    { find
      Error,
      Accumulated error (add up all previous errors)
      Derivative error (current error – previous error)
      PWM+=Kp* Error+
      Ka*(Accumulated error)+
      Kd* Derivative error ;
    }
    Else
      Error <= dead_band, error too small do nothing
Set_point

## Slide 43: part 2: PID core
if(intCnt==50) {//for every 20ms
//caculate the speed of left motor in RPM
leftRPM=lefttimeval;
leftErr = leftRPMset - leftRPM; //caculate left error
if((leftErr<DeadBand*(-1))||(leftErr>DeadBand)) //see next slide
{ //if |left error| > deadband
leftP = Pgain * leftErr; //calculate P Proportional term
leftI = Igain * leftaccErr; //calculate I Integral term
leftD = Dgain * (leftErr - leftlastErr); //calculate D Derivative term
leftPWM += (leftP + leftI + leftD);//update left motor PWM using PID
if(leftPWM>PWM_FREQ)
leftPWM=PWM_FREQ;//prevent over range (max.=PWM_FREQ)
if(leftPWM<0) leftPWM = 0; // (min. = 0)
leftaccErr += leftErr; // accumulate error
leftlastErr = leftErr; //update left last error
:
: // handle right motor similarly…….
}
PID core
P=Proportional
I Integral
D Derivative

## Slide 44: control method: PID (proportional-integral-derivative) control
Required speed=
leftRPMset
IR wheel
Speed
encoder
LeftRPM
+
-
leftRPM
Motor
generates PWM
for driver L293
leftPWM
integral control
Igain* leftErr dt
Proportional control
Pgain*leftErr
Derivative control
Dgain*[d(leftErr)/dt]
sum
leftErr
leftPWM

## Slide 45: Inside the PID core, we will study these lines
5) if((leftErr<DeadBand*(-1))||(leftErr>DeadBand))
:
:
7) leftP = Pgain * leftErr; //calculate P Proportional term
8) leftI = Igain * leftaccErr; //calculate I Integral term
9) leftD = Dgain * (leftErr - leftlastErr);//calculate D Derivative term
10) leftPWM += (leftP + leftI + leftD);//update motorPWM by PID
:
:
14) leftaccErr += leftErr; // accumulate error

## Slide 46: Dead band line5) if((leftErr<DeadBand*(-1))||(leftErr>DeadBand))
Dead-band : A Dead-band (sometimes called a neutral zone) is an area of a signal range or band where no action occurs :
only enable motor when leftErr> a small value (deadband, ie =1 in our robot )
Otherwise may oscillate when leftErr is small
Dead-band
leftErr = leftRPM - leftRPMset; //calculate left error
if(leftErr>DeadBand )
{ activate motor}

## Slide 47: Exercise 4: Discuss what will happen if dead-band is changed from 1 to (a) 0.5, or (b) 2. Example of a dead band ;do nothing “if 10-1<leftPRM <10+1
Typically
value=10%
Depends
on application
Rise time
Settling time
0
time
overshoot
Steady
state
error
undershoot
Dead band
+/- 1
Target speed=
leftRPMset =10
In our example here
leftPWM=276000 at the beginning and
192800 at steady state

## Slide 48: Recall:Parameters for evaluating a control system
Typically
value=10%
Depends
on application
Rise time
Settling time
0
time
Target
value
overshoot
Steady
state
error
undershoot
near steady state
See next slide

## Slide 49: (line 7) Effects of increasing Kp(P) http://en.wikipedia.org/wiki/PID_controller
Parameter | Rise Time | Overshoot | Settling Time | Steady state error
(1) Kp (Pgain) | Decrease step1 | Increase | Small Change | Decrease
Ki (Igain) | Decrease | Increase | Increase | Eliminate step3
Kd (Dgain) | Small Change | Decrease step2 | Decrease | Small Change

## Slide 50: Example: t0t1, The proportional term when the measurement is below the set point (leftRPMset), proportional P term is +ve
leftP = Pgain * leftErr;
leftP= 8000* (10-6)= 8000*4 is positive
This term pushing up “leftPWM”
(more energy delivered to the wheel).
leftErr=
leftRPMset –
leftPRM
=10-6=4
Rise time
0
time
overshoot
undershoot
t1
t3
t2
t4
6
P is
+ve
Target speed=
leftRPMset =10
Usage of the P proportional term
For each 50ms, a new
left RPM (speed of wheel) is measured
leftErr=
leftRPMset –
leftPRM
=30-28=2
leftP = Pgain * leftErr;
leftP= 8000* (0-8)= 8000*2 is positive
This term pushing up “leftPWM”
(more energy delivered to the wheel).
P is
+ve
e.g.
Pgain = 8000;
Igain = 6000;
Dgain = 5000;
In our experiment
leftPWM=276000 at the
beginning and
192800 at steady state
8
(leftErr = leftRPMset-leftRPM )

## Slide 51: Exercise 5: Fill in ?__: t0t1, The proportional term when the measurement is below the set point (leftRPMset), proportional P term is +ve
leftP = Pgain * leftErr;
leftP= 8000* (10-6)= 8000*4 is positive
This term pushing up “leftPWM”
(more energy delivered to the wheel).
leftErr=
leftRPMset –
leftPRM
=10-6=4
Rise time
0
time
overshoot
undershoot
t1
t3
t2
t4
6
P is
+ve
Target speed=
leftRPMset =10
Usage of the P proportional term
For each 50ms, a new
left RPM (speed of wheel) is measured
leftErr=
leftRPMset –
leftPRM
=10-8=2
leftP = Pgain * leftErr;
leftP=?_8000*2____ ,is +ve ?
“leftPWM” is increased or decreased? increase
more/less energy delivered to wheel? more
P is
+ve
e.g.
Pgain = 8000;
Igain = 6000;
Dgain = 5000;
In our experiment
leftPWM=276000 at the
beginning and
192800 at steady state
8

## Slide 52: Example: t1t3,The proportional term when the measurement is below the set point (leftRPMset), the proportional P term is +ve
leftP = Pgain * leftErr;
leftP= 8000* (10-13)= 8000*(-3) is negative
This term lowering down “leftPWM” (less energy delivered to the wheel).
leftErr=
leftRPMset –
leftPRM
=10-13= -3
Rise time
0
time
overshoot
undershoot
t1
t3
t2
t4
13
P is
+ve
Target speed=
leftRPMset =10
Usage of the P proportional term
For each 50ms, a new
left RPM (speed of wheel) is measured
P is
-ve
e.g.
Pgain = 8000;
Igain = 6000;
Dgain = 5000;
In our experiment
leftPWM=276000 at the
beginning and
192800 at steady state

## Slide 53: Understanding PID –a little summary for the P proportional term
When the measurement is below the set point (leftRPMset)
  The motor is currently too slow
  The P term calculated is +ve, need to push the speed higher
When the measurement is above the set point (leftRPMset)
  The motor is running too fast
  The P proportional term is -ve, lowering down the speed.
Increase in Pgain (Kp) will decrease rise time (meaning faster to reach set point) , decrease steady state error (study it later)
  It also increases overshoot

## Slide 54: (line 9 ) Effects of increasing Kd (D) http://en.wikipedia.org/wiki/PID_controller
Parameter | Rise Time | Overshoot | Settling Time | Steady state error
Kp (Pgain) Igain | Decrease step1 | Increase | Small Change | Decrease
Ki (Igain) gainI | Decrease | Increase | Increase | Eliminate step3
Kd (Dgain) | Small Change | Decrease step2 | Decrease | Small Change
dx/dt
dx/dt

## Slide 55: Derivative term
Derivative control
  Dgain*[d(leftErr)/dt]
d(leftErr)/dt =
  =Derivative term
  =current_Err - last_Err
  =leftErr – leftlastErr ; in our program

## Slide 56: Example: time 0 t1, the Derivative term (=current-previous) When the measurement is rising, the Derivative term is -ve
leftD = Dgain * (leftErr – leftlastErr);
leftD= 5000* (3-7)= 5000*( -4) is negative
To do:This term lowering down “leftPWM” (less energy delivered to the wheel).
leftlastErr=
leftRPMset –
eftlastPRM
=10-3=7
leftErr=
leftRPMset –
leftPRM
=10-7=3
Rise time
0
time
Target
Value=
leftRPMset
=10
overshoot
undershoot
¼ seconds
t1
t3
t2
t4
3
7
D is
-ve
leftRPMset =10
Usage of the D Derivative term
For each 50 ms, a new
left RPM (speed of wheel) is
measured
e.g.
Pgain = 8000;
Igain = 6000;
Dgain = 5000;
In our experiment
leftPWM=276000 at the
beginning and
192800 at steady state

## Slide 57: Example: time t1t2, the Derivative term When the measurement is rising, the Derivative term is -ve
Rise time
0
time
overshoot
undershoot
leftD = Dgain * (leftErr – leftlastErr);
leftD= 5000* (-5- (-2))= 5000*(-3) is negative
This term lowering down
“leftPWM” (less energy delivered to the wheel).
leftlastErr=
leftRPMset -leftlastPRM
=10-12= -2
¼ seconds
leftErr=
leftRPMset -leftPRM
=10-15= -5
t1
t3
t2
t4
leftRPMset =10
D is
-ve
15
12
leftPRM
D is
-ve
Usage of the D Derivative term
For each 50 ms, a new
left RPM (speed of wheel) is
measured
e.g.
Pgain = 8000;
Igain = 6000;
Dgain = 5000;
In our experiment
leftPWM=276000 at the
beginning and
192800 at steady state

## Slide 58: Little Summary: Negative D Derivative term
When the measurement (leftRPM) is rising, the change (change= current-previous) of error (error = setpoint-leftRPM ) is -ve = d(Err/dt)=-ve
D Derivative term= Kd*d(Err/dt) is –VE
Decrease energy to motor  decrease overshoot
Rise time
0
time
undershoot
t1
t3
t2
t4
D is
-ve
D is
-ve
Setpoint
目標
overshoot

## Slide 59: Example: time t2t3, the Derivative term When the measurement is falling, the Derivative term is +ve
Rise time
0
time
overshoot
undershoot
leftD = Dgain * (leftErr – leftlastErr);
leftD= 5000* (-1- (-4))= 5000*3 is positive
This term pushing up
“leftPWM” (more energy delivered to the wheel).
Usage of the D Derivative term
For each 50ms, a new
left RPM (speed of wheel) is
measured
leftlastErr=
leftRPMset -leftlastPRM
=10-14= -4
¼ seconds
leftErr=
leftRPMset -leftPRM
=10-11= -1
t1
t3
t2
t4
leftRPMset =10
D is
-ve
14
11
leftPRM
D is
+ve
D is
-ve
e.g.
Pgain = 8000;
Igain = 6000;
Dgain = 5000;
In our experiment
leftPWM=276000 at the
beginning and
192800 at steady state

## Slide 60: Exercise 6:Fill in ?_ time t2t3, the Derivative term When the measurement is falling, the Derivative term is +ve
Rise time
0
time
overshoot
undershoot
leftD = Dgain * (leftErr – leftlastErr);
leftD= ?5000*(3-1), which is +ve or –ve? +ve
“leftPWM” increased or decreased?_increase_
More/less energy delivered to the wheel?_more__
Usage of the D Derivative term
For each 50ms, a new
left RPM (speed of wheel) is
measured
leftlastErr=
leftRPMset -leftlastPRM
=10-9= 1
¼ seconds
leftErr=
leftRPMset -leftPRM
=10-7= 3
t1
t3
t2
t4
leftRPMset =10
D is
-ve
9
7
leftPRM
D is
+ve
D is
-ve
D is
+ve
e.g.
Pgain = 8000;
Igain = 6000;
Dgain = 5000;
In our example
leftPWM=276000 at the
beginning and
192800 at steady state

## Slide 61: Little Summary: Positive D Derivative term
When the measurement (leftRPM) is falling, the change (change= current-previous) of error (error = setpoint-leftRPM ) is +ve
D Derivative term= Kd*d(Err/dt) is +VE
Increase energy to motor  decrease undershoot
Rise time
0
time
t1
t3
t2
t4
D is
+ve
D is
+ve
Setpoint
目標
overshoot
undershoot

## Slide 62: Understanding PID –a little summary for the D derivative term
When the measurement (leftRPM) is rising,
  The motor is gaining speed
  The D derivative term is –ve, so lowering the motor speed  decrease overshoot
When the measurement (leftRPM) is falling,
  The motor is reducing speed
  The Derivative term is +ve, so pushing the motor speed higher  decrease undershoot
  In conclusion, the gradient of the error (Err) determines the adjustment. Depends on whether d(Err)/dt is +ve or –ve.
Increase in Dgain (Kd) will decrease overshoot/undershoot and settling time (system more stable)

## Slide 63: (line 8)Effects of increasing Ki (I) http://en.wikipedia.org/wiki/PID_controller
Parameter | Rise Time | Overshoot | Settling Time | Steady state error
Kp (Pgain) | Decrease step1 | Increase | Small Change | Decrease
Ki (Igain) | Decrease | Increase | Increase | Eliminate step3
Kd (Dgain) | Small Change | Decrease step2 | Decrease | Small Change

## Slide 64: control method: PID (proportional-integral-derivative) control
Required speed=
leftRPMset
IR wheel
Speed
encoder
LeftRPM
+
-
leftRPM
Motor
generates PWM
for driver L293
leftPWM
integral control
Igain* leftErr dt
Proportional control
Pgain*leftErr
Derivative control
Dgain*[d(leftErr)/dt]
sum
leftErr
leftPWM
At steady state, leftErr0, so
So, Pgain*leftErr=0
also Dgain*[d(leftErr)/dt] =0
And if no Integral { Igain* leftErr dt} term, left PWM 0
It is a problem.

## Slide 65: Time  near steady state leftRPMset=leftRPM hence leftErr =0, leftlastErr=0 leftP=0, leftD=0
leftErr = leftRPMset – leftRPM=0
So as leftlastErr = 0
Therefore
Steps
7) leftP = Pgain * leftErr//=0 //calculate P Proportional term
8) leftI = Igain * leftaccErr; //calculate I Integral term
9) leftD = Dgain * (leftErr - leftlastErr)//=0 //calculate D Derivative term
10) leftPWM += (leftP + leftI + leftD);//update left motor PWM using PID
The only valid term is the integral term “leftI”
leftPWM += leftI
The main idea is to create a small term (leftI) to maintain the leftPWM value
e.g.
Pgain = 8000;
Igain = 6000;
Dgain = 5000;
In our experiment
leftPWM=276000 at the
beginning and
192800 at steady state
near steady state : leftP=0 leftD=0

## Slide 66: The integral term is found by adding all previous errors same as leftaccErr=sum{leftErr(t=0)+leftErr(t=1)+.. +leftErr(t=now)}
14) leftaccErr += leftErr;//LeftaccErr is the summation of all previous errors
8) leftI=Igain*leftaccErr// integral term,
:
10) leftPWM += leftI // near steady state, only leftI is valid
:
Don’t worry it will not become infinitive, one measure to safeguard this is:
  11) if(leftPWM>PWM_FREQ);// PWM_FREQ=maximum PWM allowed
  12) leftPWM=PWM_FREQ;//prevent over range
  (max.=PWM_FREQ)
Also, because near steady state , leftaccErr will adjust itself automatically, see next slide
e.g.
Pgain = 8000;
Igain = 6000;
Dgain = 5000;
In our experiment
leftPWM=276000 at the
beginning and
192800 at steady state

## Slide 67: How the integral term adjusts itself automatically near steady state
Near steady state
  8) leftI=Igain*leftacceErr
  10) leftPWM += leftI
If measured speed (leftRPM) > set point
  leftErr is -ve
  leftaccErr (Acculumation) decreases, hence reducing leftaccErr at a suitable value to maintain leftPWM
If measured speed (leftRPM) < set point
  leftErr is +ve
  leftaccErr (Acculumation) increases, hence increasing leftaccErr at a suitable value to maintain leftPWM
Pgain = 8000;
Igain = 6000;
Dgain = 5000;
In our experiment
leftPWM=276000 at the
beginning and
192800 at steady state

## Slide 68: Understanding PID –a little summary for the I Integral term
When the measurement is below the set point (leftRPMset)
  The motor is slow
  The I Intergral term is +ve, pushing the speed higher
When the measurement is above the set point (leftRPMset)
  The motor is running too fast
  The I intergral term is -ve, lowering down the speed.
Increase in Igain (Ki) will result in
  It is similar to the P term (see above two points)
  So increase overshoot, settling time
  and decrease rise time
  Note: the main function of Integral control is to reduce steady state error

## Slide 69: PID Tuning (usually done by trail and error)
Tuning PID (adjust manually)
Adjust PID constants:
  Set motor to move from 0 to speed V1 ,
  step1) Pgain proportional_gain (Kp), record 5 seconds of the speed, plot result and evaluate performance
  step2) Dgain derivative_gain (Kd), record 5 seconds of the speed, plot result and evaluate performance
  step3) Igain integral_gain (Ki), record 5 seconds of the speed, plot result and evaluate performance
Repeat steps1,2,3 again until satisfied
Typical good performance we want:
  Short rise time
  Small overshoot/undershoot
  Short settling time
  Small steady state error
Right motor speed
Left motor speed
Desired speed (target)

## Slide 70: Application of
PID

## Slide 71: Exercise 16.7: Robot Turning (for smooth circular turns around 90-degree corners) http://micromouse.cannock.ac.uk/dynamics/smoothcorners.htm
Required speed V (meters per minute) – measure at center of the robot
Turning radius R (meters), from a point C to robot center
Wheel diameter = a (meters)
Use similar triangle
V1/(R+D/2)=V/R
V1=V+(VD)/2R
(a) Write V2 in terms of V,D, and R
(b) If wi=rotations per
minute of wheel I (i=1 or 2),
write w1 and w2 in terms of R,V,D,a
D/2 D/2
V1 V V2
R
a
D
C
smooth circular turn
C

## Slide 72: Exercise 16.8 (take home exercise)
Why PID control is good control method?
Describe a PID control system for keeping the water to be at 23 degrees Celsius.
Discus what are the uses of Proportional , Integration, and Derivation in the above application.

## Slide 73: Summary
Studies PID control theory and implementation
Learn how to tune PID systems

## Slide 74
Block diagram of our robot control system
Appendix

## Slide 75
The schematic of the robot control system