## Slide 1: CENG2400 Tutorial 1
Keil IDE

## Slide 2: Keil
Include C compilers
Assemblers
(uVision5)  Integrated Development Environment (IDE)
For ARM series
Notes: ~eclipse

## Slide 3: uVision5 IDE
Installed on all the PCs in SHB102
How to install in your own PC?
Download MDK524A.exe
  https://www.keil.com/demo/eval/arm.htm
Download legacy support for ARM7
  http://www2.keil.com/mdk5/legacy

## Slide 4: Open uVision5 IDE
Find this Shortcut from the desktop
  Double click to open it
If you cannot find it
  Go to “Start”  “All Programs”  “Keil uVision5”

## Slide 5: Open uVision5 IDE
You will see something like this

## Slide 6: Project Setup

## Slide 7: Create a new project
Select Project  New uVision Project

## Slide 8: Project working directory
In the Pop up Window
Type the project name and select the working directory
Project Name

## Slide 9: Choose the device
1. Select Legacy Device Database
3. Select NXP, LPC2131
2. Search LPC2131
4. Click “OK”

## Slide 10: Create the startup file
Click “Yes”

## Slide 11: Modify the Startup.s file
Open “Startup.s”

## Slide 12: Modify the Startup.s file
Comment out the line 430
“;” consider as comment

## Slide 13: Option
Right click “Target 1”in the project menu
Choose “Option for Target ‘Target 1’”

## Slide 14: Option
Go to “Linker” Tab
Tick “Use Memory Layout from Target Dialog”

## Slide 15: Program file

## Slide 16: Create a new source code file
Click “File”  “New”

## Slide 17: Create a new source code file
Enter the file name and click “save”
1. File Name
2. Click “Save”
Notes: .s file  Assembly source code

## Slide 18: Add the source code to your project
Click “Project”  “Manage”  “Project Items…”

## Slide 19: Add the source code to your project
Click “Add Files…”

## Slide 20: Add the source code to your project
Select the source code
1. Select “.s” file type
2. Select the source code

## Slide 21: Add the source code to your project
Click “OK” if the file is added to your Project

## Slide 22: Program code
Write some code

## Slide 23: Build the Program
Press “F7” key on your keyboard
Or click “Project”  “Build Target”

## Slide 24: Build the Program
Success if no error
Notes: You are now successfully compile the program and ready to run

## Slide 25: Using the Debug Mode

## Slide 26: Debug Mode
Ctrl+F5, Run debug Mode
Or Click “Debug”  “Start/Stop Debug Session”

## Slide 27: Debug Mode
Click “OK”

## Slide 28: Debug your program
Test your code “line by line”

## Slide 29: Debug your program
Select Any line you want to execute
Right Click and Click “Run to Cursor line”
Or Press “Ctrl+F10”

## Slide 30: Debug your program
View the current status of the system
  E.g. Register value, Program counter value

## Slide 31: Debug your program
Execute the code “line by line” by pressing “F11”

## Slide 32: Debug your program
The value of the Program Counter is changing

## Slide 33: Small exercise
Run the given source code
Check the register values in debug mode
  R0, R1, R2, PC(R15)

## Slide 34: Program code
; User Initial Stack & Heap
AREA |.text|, CODE, READONLY
EXPORT __main
__main
; Add the code HERE
START
MOV R0, #0x1
MOV R1, #0x2
ADD R2, R0, R1
END

## Slide 35: Useful Shortcut Key
Shortcut Key
  F7, Build Project (Compile)
  Ctrl+F5, Run debug Mode
  Ctril+F10, Run to Current Cursor Line
  F11, Next Step