## Slide 1: Arm board tutorial
Part 1
Using the ARM board
And start working with C
Tutorial 5 and 6

## Slide 2: Outline
Software
Hardware
Download the program to the board
The ARM7 board test program

## Slide 3: Materials distributed
Materials will be distributed:
  NXP LPC2131 x 1
  FT232BL x 1
  Power adapter x 1
  USB cable x 1
Please use them CAREFULLY
You MUST return all the materials at the end of this semester
  30 marks will be deduced if you lose or don’t return anyone of them

## Slide 4: Hints for the exercises
The User manual (UM10120.pdf) and the Schematic of the board are VERY usefully
You may need to check the lecture notes

## Slide 5: Software
Setup the uVision project …

## Slide 6: Start working with C
New Project
  Project  New μVision Project…
  Find somewhere to save you project
  choose NXP  LPC2131
  with Startup.s
  Edit Startup.s
    comment the line 430

## Slide 7: Start working with C
Project  Options for target1
  At "Linker" tab
    select “Use Memory Layout from Target Dialog”
  At "Output" tab
    select “Create HEX File”

## Slide 8: Start working with C
Create a C file
  File  New…
  File  Save
  Find a good place to save your code
    e.g. same folder as the project file
  End the file name with ".c"
    Some examples : main.c, test_c.c
    Bad examples: a.c, asd.c

## Slide 9: Start working with C
Add the code into your project
  Project  Manage  Components, Environment and Books  Add files
  Locate the C file you just saved
  Your project should look like this:

## Slide 10: Start working with C
Paste the following template to your code:
#include <lpc213x.h>
int main(){
while(1);
return 0;
}

## Slide 11: Start working with C
#include <lpc213x.h>
  tell the compiler to use the header file "lpc213x.h"
  lpc213x.h defines all the register address for the devices in LPC213x family
    IOPIN0 for GPIO0, U0THR for UART0

## Slide 12: Start working with C
int main(){ while(1); return 0; }
  the function "main" is the entry point of your program after the running the instructions in "Startup.s"
  "while(1);" is an infinite loop which keeps the processor busy

## Slide 13: Hardware
Introduction to the CUHK ARM7 board 2012

## Slide 14: CUHK ARM Board 2012
The latest version of the board

## Slide 15: CUHK ARM7 board 2012
A simple prototype board
Serial ↔ USB IC
NXP LPC2131
Connect to computer
Power
Reset

## Slide 16: CUHK ARM7 board 2012
A simple prototype board
Serial ↔ USB IC
NXP LPC2131
Always light up with power on
Press to reset
Connect to computer
Use Power Supply (9V)
OR
Use power adapter
A Slide switch (Pull right is the programming mode; Pull left is the normal mode)

## Slide 17: Install the Serial ↔ USB driver
After you power on and connect the board to computer, you may need to install the driver for the Serial ↔ USB chip
Please download the driver from BlackBoard, named “CDM20828_Setup.exe”
  You can also download the driver from this link http://www.ftdichip.com/Drivers/VCP.htm
Please install it, then, re-connect the board to computer
Now, go to Device Manager to check the board can be recognize by the computer or not

## Slide 18: Install the Serial ↔ USB driver
Your board is ready to use if this appear

## Slide 19: Flash the program to the board

## Slide 20: Download to the Board
Create a HEX file
Use the Flash Tools by Philips(LPC21XX)
  You can install it in your own computer
  Please download “Philips Flash Utility Installation.exe” and install it if you needed

## Slide 21: Check the project setting
Choose “Option for Target…”

## Slide 22: Check the project setting
Make sure “Create Hex File” in Output tab is selected

## Slide 23: Configure the Flash Tool
Click “Flash”, select “Configure Flash Tools…”

## Slide 24: Configure the Flash Tool
Make sure it is correspond to the COM device of the board (Mostly it is COM4)
You may need to check the Device Manager to confirm
Change to 57600
Make sure this part is same as follow
(If you install the tool in your own computer, the path will be different. Please find it from your installed directory)

## Slide 25: Check the Hardware connection
Connect the USB cable
Set the slide switch (SW2) to programming mode (Right)
Press the reset button
Please pull to Right

## Slide 26: Download

## Slide 27: Upload
Click “Upload to Flash” if not start automatically
On error, please check:
  Any other program using the serial port?
  Make sure the switch is connected
  Push the reset button

## Slide 28: Lab Exercise
Create a new project
  Please mark sure all the settings are correct
Download the “gpio.s” form BlackBoard
Add it to the project
Compile and download it to the board
Observe and test the result
Now, change the “BEQ” in line 23 to “BNE”
Compile and download to the board again
Observe the result, state the differences between the previous

## Slide 29: Lab Exercise
Remove the “gpio.s” in the project
Create a new file, called “gpio.c” and add it to the project
Re-write the previous two “gpio.s” in C
  The original one and the modified one
Compile and download to the board
Can you re-produce the previous two results?

## Slide 30: The ARM7 board Test program
You may use it to test out the board you make …

## Slide 31: Test program of the board
You can download a test program, named “TestProg.hex” from BlackBoard to test out your board

## Slide 32: To use this test program …
Connect the board to the computer
Pull the slide switch to the programming mode
Press the Reset button
Please go to “Start” -> “All Programs” -> “Philips Semiconductors” -> “Flash Utility” -> “Launch LPC210x_ISP.exe”
Click “Launch LPC210x_ISP.exe” to start the Flash Tool

## Slide 34: Setting the Flash Tool
Click this. Select the “TestProg.hex” file you downloaded
Select 57600
Select the corresponding the COM port (Mostly is COM4). You may need to check it for Device Manager
After the settings are finished, Click this to download the program to the board

## Slide 35: To use this test program …
Wait the download process is finished
  If it is not success, please redo the pervious steps again
Pull the switch back to the normal mode
Press the Reset button
Now, the test program is running. You may observe the LEDs are blink. Also, you can turn on/off those LEDs using the push buttons

## Slide 36: part 2

## Slide 37: Building LDR module
Building LDR module

## Slide 38: Supplementary…

## Slide 39: Change the COM Port Number
Select “Properties”

## Slide 40: Change the COM Port Number
Click “Advanced…”

## Slide 41: Change the COM Port Number
Select the COM Port Number which between COM2-COM5

## Slide 42: Change the COM Port Number
Click “Yes”

## Slide 43: Change the COM Port Number
Click “OK”

## Slide 44: Change the COM Port Number
Now, the COM Port Number is changed

## Slide 45: Using Hyper Terminal

## Slide 46: Using Hyper Terminal

## Slide 47: Using Hyper Terminal
Choose a name for your connection

## Slide 48: Using Hyper Terminal
Choose the com port connected to the device

## Slide 49: COM Properties
Choose a setting that match the board
  Baudrate
  Data Bit
    8
  Flow control
    None

## Slide 50: Communicate with ARM board
Connect
Disconnect

## Slide 51: Other way to open Hyper Terminal
Double click the shortcut in Desktop, named by baudrate value
  E.g 57600.ht, 115200.ht

## Slide 52: LDR Module

## Slide 53: LDR Module
LDR module
Vout
Vcc
GND
On the ARM board
Please don’t forget this resistor
Vout
Vcc
GND
47 ohm