## Slide 1: High Speed Logic
Power supply systems

## Slide 2: Part 1
High speed circuit

## Slide 3: 0.1 Frequency / time relation
Basic facts and tools for the analysis of the edge of a clock
  Rise time (Tr) = time to rise from 10% to 90% of the signal.
10%
90%
Tr
A slow
rising edge
A fast falling edge
V
t

## Slide 4: 0.1 Knee frequency calculation Convert rise-time edge (Tr) and frequency (Fknee)
Fknee=0.5/Tr
e.g. edge=5ns, what is the equivalent frequency.
Fknee==0.5/5ns=100MHz.
Period/2=Tr
Period of the equivalent
signal

## Slide 5: Analog / digital signal relation
Can a digital signal pass an analog circuit without distortion?
Use Fknee to quickly estimate if the signal can pass the clock edge or not.

## Slide 6
Short term (edge) response by F_knee method
Rising or falling edge=
short term behavior
Level 1 or 0 =
long term behavior

## Slide 7: Short term (edge) response by F_knee
At high frequency, a wire becomes an inductor. Then a high frequency signal (fast edge) is attenuated (or distorted).
F_knee0.5/Tr , where Tr= rise time
A long wire or PCB trace
I
L
R

## Slide 8: Frequency response of a low pass trace
Shorter rise time pushes frequency requirement higher. Important results:
  (1) A circuit has flat frequency response up to and including F_knee (0.5/Tr) will pass the digital signal with rise edge (Tr).
  (2) The behavior above F_knee of a digital circuit will have little effect on how it processes digital signals.
  (3) Frequency lower than F_knee will affect the long term behavior of the signal.

## Slide 9: How to apply the F_knee technique
Find or estimate Tr rise time of your signal.
Find F_knee  0.5/Tr
Now whether your circuit can pass this signal or not depends on whether the circuit has flat frequency up to F_knee or not.

## Slide 10: Example
Since F_knee =0.5/Tr, Tr=0.5/100MHz
Hence Tr should not be shorter than 5ns.
What would happen if Tr is shorter than 5NS (e.g. 3ns) ? Answer: distorted, edge smoothed
5ns
A PCB
TRACE
This circuit has flat frequency response up to 100MHZ
5ns
The output of a 3ns edge
3ns
5ns

## Slide 11: F_knee method is only an approximation
F_knee is only defined by the signal rise time and has no relation to other frequency domain parameters. It is easy to use and remember.
An imprecise measure of spectral contents, it cannot make precise prediction of circuit behavior.
Use Fourier transform if an accurate result is required.

## Slide 12: Power exercise 1
A circuit can pass signals of 200 MHz without distortion, what is the shortest rising edge that can pass this circuit?

## Slide 13: 0.2 The horror of large dI/dt
Since V =-L dI/dt , L=inductance.
Since the traces are inductive, Large dI/dt will create huge noise voltage V in the circuit.
Large dI/dt creates large voltage V here
V
dI/dt

## Slide 14: Speed dI/dt problem
Logic families having minimum switch times much faster than the propagation delay suffer an unnecessary penalty in system design. Large dI/dt creates problems.
Given two families with identical propagation delay statistics, the family with the slowest output switching time will be cheaper and easier to run.

## Slide 15: Speed dV/dt problems
Circuit response lower than Fknee may distort signal, circuit response higher than Fknee is not important in our design.
Shorter Tr (switch time) results in higher Fknee. So unnecessary short Tr is a problem.
So shorter Tr will not work in poorly designed circuits.
Shorter Tr will give larger dI/dt, which will cause ground bounce. (will be discussed later)

## Slide 16: How to find dI/dt from dV/dt
dI/dt creates problems.
Since dV/dt is easier to measure, so we try to find dI/dt from V (output voltage change),Tr(rise time) and C(load capacitance).
We will show that
max(dI/dt) =1.52 V C/(Tr)2

## Slide 17
Fig.2.14
of [1]
Max slope is (V/2)/(Tr/2)
= V/Tr
Max slope is
(V/Tr)/ (Tr/2)]
=2 V/(T2r )---(i)
-------------------------
More precisely:
consider voltage difference  0.76*V (from 10 % to 86%) in equ. (i).
Max slope is =0.75*{2 V/(Tr2)}
 1.52 V/(T2r )
T10-90Tr
=rise time
from 10 to 86 %
Tr/2
T10-90Tr

## Slide 18: Showed two important relations
(1/R)max(dV/dt)= (1/R)V/Tr
C*max(d2V/dt2)=C*1.52*V/(Tr)2

## Slide 19: Effect of dI/dt at output and at power supply is similar dI/dt is difficult to measure, so use dV/dt easier estimate, it is easier
to 1/T2r, big,
more significant
 1/Tr, smaller so ignored
R
Tr
L
VL
Power supply V
C

## Slide 20: Max(dIcapacitor/dt)  1/T10-902 Shorter Tr will give larger dI/dt, which will cause ground bounce.
C
dI/dt
Power supply
Same dI/dt
R
Tr
L
VL

## Slide 21: Exercise 2
5V step
1ns
R
Tr
L
VL
Power supply V
C

## Slide 22: Part 2
Power systems

## Slide 23: Power system
Fixed and variable power supply
  use 78xx chip
  Use power transistor 3055
Use of opto-coupler
Use capacitors to stabilize power

## Slide 24: Fixed and variable Power supply
Use power supply chips 78xx
  E.g. 7805 for supper isolation to reduce interference
E.g. Variable power supply design and usage, e.g. step down 5V --> 3V.
7805
1
2
3
7V or above
200uF
Fixed at 5V,
current limit 500mA
http://eddie.dyec.com.tw/diy-demo/audio-diy/cd_dvd_modify/cd-100_2/cd100_2image/7805.jpg
Output=V1[R2/(R1+R2)]
(0-5V)
R1
R2
Input power
V1(5V)
TIP3055
100uF

## Slide 25: Power exercise 3
If I have a power source 9 V and want to produce a power supply of 5V, R1=10K.
Suggest two methods to achieve this.
Answer:
R1
R2
Output=V1[R2/(R1+R2)]
Input power
V1
TIP3055

## Slide 26: Example: Use of 7805 power stabilizer and opto isolator
7.2V or above
Power supply
8031
Xilinx
3 Volts battery
Current driver
circuit
Left/Right motors
7805
7805
Optical
Isolators
4N35
Electrically Isolated
Low power
High power
light
2 systems has no
electrical linkage

## Slide 27: Board level Power supply sys.
Power systems
  provide stable voltage references
  distribute power to all devices
We will learn about how to find
  board level bypass capacitors
  capacitor array
Examples and pictures are from Reference :High speed digital design by HW Johnson and Graham, Prentice Hall

## Slide 28: Method (in single ended signaling) to reduce ground noise (low cost) for normal gates : return current is the same as the ground
Use better power distribution method:
  Rule 1: Low impedance ground
  Rule 2: Low impedance power (5V) lines
  Rule 3:Low impedance between power (5V) and ground (0V) -- use of bypass capacitors.

## Slide 29
Power Rule 1: Use low-impedance ground connections between gates -- use ground planes, power rails.
Reasons:
  Fig. 8.2 shows the hypothetical noise “N” in the ground loop, which is caused by the return current flowing through the ground inductance

## Slide 30
Power Rule 2: The impedance between power pins on the two gates should be as low as possible (fig. 8.3) --use power planes,etc. Reasons:
  common path inductance between power pins on any other gates is a problem even the ground is perfect.
  If N is large, gate A may receive a lower power supply or reference voltage.

## Slide 31: Voltage reference problems
Differential input= V1-N-R,
The ground wire has inductance and creates noise voltage N which should be as low as possible.
(2.5V)

## Slide 32: Power Exercise 4
R (internal reference voltage is 2.5V) i.e.
  gate_C_out =1(high) when the input of the gate C amplifier is positive
  Else gate_C_out=0 (low)
Now V1=2.8V, R (internal reference voltage is 2.5V,
What is Gate_C_out when
(i) noise N=0?
(ii) noise N=0.5?
(iii) Why there is noise N?
(2.5V)

## Slide 33
Power Rule 3: There must be a low-impedance path between power and ground (fig. 8.4)-- use by- pass-capacitors.
Reasons (Fig 8.3):
  The return current flows thru. the battery should create a voltage drop as low as possible to maintain a good reference. The impedance of the battery must be low.
  By pass capacitors provide such low impedance paths.
Board bypass
capacitor C2
Lpcable=100nH
LC2
Perfect
Power
supply
C3
C3
C3
Ltot=N number of LC3 in parallel
Cap.
array

## Slide 34: Use of power, ground planes and capacitor array
Rule1
Rule 2
Rule3

## Slide 35: Power system design techniques: Multi-layer Power distribution
Power supplies designed and sold usually have very low output impedance.
But the wiring to the board and devices may contain inductance.
To maintain a stable power to the circuits we have to solve it in 3 different levels:
  Power distribution wiring
  Board level filtering
  Local filtering at individual integrated circuits

## Slide 36: Level 1: Power distribution wiring
Resistance of power distribution wiring.
  Resistance proportional to inverse diameter wire, 40% increase of wire diameter reduces resistance by 1/2.
  Sense wire in new power supply designs corrects for resistance in power distribution wiring ( http://reprap.org/bin/view/Main/PCPowerSupply)
Inductance, a more difficult issue. (Section 8.2.1)
  Use low-inductance wiring -- wide-flat wires.
  Use differential logic Fig. 8.6 (not economical)
  Reduce power supply current change can minimize the effect of inductance -- using by pass capacitors.

## Slide 37: Level 2 :Board level filtering
Fig. 8.7, switching at output of gate A can create a large current change through the power supply.
For a 1ns edge (at high frequency) , the inductance blocks the current from the power supply to gate A.
Add C2 (board level by pass capacitor) in fig. 8.8 to reduce the current passing through the inductance.
Example 8.1 shows how to calculate the value of the board level by pass capacitor. This capacitor Cboard_bypass provides low impedance up to a Power-System-Wiring frequency FPSW.
Water
tanks
In
Germany
Mannheim

## Slide 38: Demo
Youtube
By-pass capacitor
10uF
+
TX
(Noisy)
Vcc
(Noisy)
TX
(Clean)
Vcc
(Clean)
No by-pass capacitor
using by-pass capacitor

## Slide 39: A PC mother board with board level by-pass filter (use parallel capacitors to make a big one: reduce leg inductance; save size and cost)
Board level by-pass capacitors(C2)
Power supply
and cable

## Slide 40
C2
to be
added

## Slide 41: Level 3: Local filtering at individual integrated circuits
However no capacitor is perfect, LC2 (at the legs of by pass capacitor C2) may cause its impedance to rise at high frequency.
The best way to get very low inductance is to use a lot of parallel small capacitors.
Use capacitor array to reduce the the problem of LC2 at high frequency.
See Example 8.2

## Slide 42: Analogous to the water delivery system
or
Capacitor
Array e.g. 0.01uF
Board level
By Capacitor
e.g. 10uF-200uF
Power supply
e.g. 10uF-200uF

## Slide 43: Multi-level by pass capacitors design
Power supply -> board --> individual Ics
Example:Fpsw Fboard Fc_array
below159KHz 159K->3.18M 3.18M->Fknee
10u-1000uF 32x0.016uF
A power supply provides low impedance at low frequency.
Board level by pass capacitors provide low impedance at higher frequency
Parallel a lot of small capacitors provide very low impedance up to a very high frequency Fknee(e.g. edge=5ns, Fknee=0.5/Tr=0.5/5ns=100MHz).

## Slide 44: Power supply bypass capacitor design
Design calculations, find

## Slide 45: Revision of important formulas (Remember them!!!!)
Impedance of C at freq.
Impedance of L at freq.
  current passing thru. a capacitor with changing voltage
  voltage across an inductor with changing current
Also when impedance is in terms of Fknee:

## Slide 46: Level 1 - Power distribution lines
Board level by pass capacitor(C2) design
Power
supply
Vcc
Ground
Digital circuit board
Board level
electrolytic
bypass capacitor
 10~500uF
Cap array(C3)
0.1 ~ 1uF

## Slide 47: Level 2 - bypass capacitor design
Board level by pass capacitor (C2) design
Power
supply
Vcc
Ground
Digital circuit board
Board level
electrolytic
bypass capacitor
 10~500uF
Cap array (c3)
0.1 ~ 1uF

## Slide 48: Capacitor array C3 (a number of surface mounted capacitors)
Old type

## Slide 49: Capacitor array C3 (a number of new type surface mounted capacitors)
Old type

## Slide 50: Board level filtering calculations Why board level by-pass cap. C2 is needed?

## Slide 51: Procedure for level 2 (board level) calculation
2-1. First find out the maximum change of current the circuit demands.
2-2. Then find the maximum tolerated impedance of the inductor
2-3. Find at what signal frequency (or edge using Tr=0.5/Fknee) this inductor has too much impedance
2-4. Find the value of the required bypass cap. C2

## Slide 52: Given:N=100 gates, C=10pF load in  t =5ns, supply voltage= E,inductance Lpcable= 100nH
Step2-1: find max. change of current the circuit demands
Assume max. tolerable noise  EN=0.1Volts
Perfect 5V
power supply
Digital circuit,
when 100 gates are
switching draws 1A
Lpcable=100nH
impedance <0.1 
Maximum noise allowed=0.1V
Ground

## Slide 53: Additional Explanation
Dear professor,
In the previous slide, we computer the maximum current change is 1A, then we use ohm’s law to calculate the impedance. But I am confuse that if we use the max current change to calculate, the result should be minimum impedance since the noise En is fix. So impedance should larger than 0.1 ohm.
Answer: Thanks for your question and I think it is a very good question on this topic. For your query, I think it is a naming problem; the explanation of calling it Xmax is as follows:
  We set the noise allowed (by noise margin) to be En=0.1 Volts. If the total required current is 1A
  The max impedance is Xmax=En/1A=0.1 Ohms. You are right to say that if the required current is less, say 0.9 A, Xmax will be 0.1/0.9=1.111 Ohms, it is higher than 0.1 Ohms. Then how can I say this is called Xmax. The reason is we call it Xmax because it is the X allowed for that situation, and you cannot allow a higher impedance X in the circuit, that means when I=0.9A, your Xmax is 0.11 Ohms.
  Or in my original slide , when I=1A, Xmax is 0.1 Ohms.
  Using another example, if the current is I= 1.1A (higher than 1A), En=0.1 is not changed because it is coming from the noise margin (you don’t want noise to be higher than that in your circuit) , Xmax=En/I=0.1/1.1=0.09 Ohms, so in this case Xmax is 0.09 Ohms. That means when you design a circuit, you cannot allow impedance inside the circuit higher than 0.09 Ohms.

## Slide 54: Step2-2:
Assume max. current change=1A, so I= from 0A to 1A is 1A
Impedance XLof power cable Lpcable
= EN /  I = 0.1
Perfect 5V
power supply
Digital circuit,
when 100 gates are
switching draws 1A
Lpcable=100nH
impedance <0.1 
Maximum noise allowed=0.1V
Ground

## Slide 55: Step2-3: Find at what signal frequency the inductor has too much impedance
(At a very slow edge, the power source is blocked by the inductor, let alone Tr=5ns that the circuit demands)
Perfect 5V
power supply
Digital circuit,
when 100 gates are
switching draws 1A
Lpcable=100nH
impedance <0.1 
Maximum noise allowed=0.1V
Ground

## Slide 56: Photos of the board and caps(board C2 and Cap array C3).
Power
supply
Vcc
Ground
Digital circuit board
Board level
Electrolytic C3
bypass capacitor
 10~500uF
Local filtering
Cap array C3
0.1 ~ 1uF

## Slide 57: Step2-4: Find board level by-pass cap. to give an alternative power path at high freq.
At what freq. Lpcable is too large(>0.1 )?
Below this Fpcable frequency, the power supply unit can supply current; above this the bypass C2 can supply current.
XL=2 FL

## Slide 58: Level 3 Local filtering
It is needed because of the inductance at the legs of the board level bypass capacitor
Local filtering using capacitor array

## Slide 59: Level 3 - Local filtering
Board level by-pass capacitor C2 design
Power
supply
Vcc
Ground
Digital circuit board
Board level
electrolytic
bypass capacitor
 10~500uF
Local filtering
C3

## Slide 60: When Freq. >159KHz, the power supply cannot supply current
But when freq. is too high, the inductance at bypass cap C2 may have problems.See next
Board bypass
capacitor C2
=10uF
LC2=5nH
Perfect
Power
supply
Lpcable=100nH
Digital circuit
When freq. >159KHz, the paths
are cut off by the large impedance

## Slide 61: But the board level by-pass cap has inductance 5nH at its legs
The maximum impedance at legs is 0.1 , so that noise is controlled under 0.1V.
So when freq. is higher than 3.18MHz, the legs of the by-pass capacitor will block current flow, so use an array of small capacitors to supply current.
Low freq, get power
from power supply
Mid. freq. Get power
from board level cap.
High freq.Get power
from cap. array
F1 =159KHz
F2=3.18MHz

## Slide 62: When Freq. F2 >3.18Mhz, the board bypass cap. cannot supply current
Freq.
Board bypass
capacitor C2
LC2=5nH
Perfect
Power
supply
Lpcable=100nH
Digital circuit
When freq.F2 >3.18MHz, these paths
are cut off by the large impedance

## Slide 63: Level 3 Design procedures
Step 3-1: Find the highest (F3 ) frequency of the system based on Tr3 (e.g. 5ns) .
Step 3-2: Find (Ltot3) total inductance tolerated.
Step3-3: Find (N) total number of cap used for the cap. array for the given serial inductance of each capacitor element. (e.g. 5ns).
Step 3-4 : Find (C3) the minimum value of each Cap. array element.

## Slide 64: Capacitor array number N calculations Ltot3=Max. tolerable induct. for all array capacitors Xmax= Max. tolerable impedance for all array capacitors
Step 3-1: Find highest F3 frequency: comes from clock edge 5ns , therefore
Board bypass
capacitor C2
Lpcable=100nH
LC2=5nH
Perfect
Power
supply
C3
C3
C3
Ltot3=LC3/32 (in parallel)
Cap.
array
Ctot3

## Slide 65: Capacitor array number N calculations Ltot3=Max. tolerable induct. for all array capacitors Xmax= Max. tolerable impedance for all array capacitors
Step 3-3: Find N
We will use an array of capacitors to provide alternative power source at high freq.
Given LC3=5nH (legs of each small caps. C3).
Board bypass
capacitor C2
Lpcable=100nH
LC2=5nH
Perfect
Power
supply
C3
C3
C3
Ltot3=LC3/32 (in parallel)
Cap.
array
Ctot3

## Slide 66: Step 3-4 Find (C3):the minimum value of each Cap. array element
Again Xmax=0.1 to provide current to gates,
Find minimum C3 value to do the job so use F2=3.18MHz (lower side)
C3
C3
C3
Ctot3=32 C3 in parallel
Cap.
array
Ctot3

## Slide 67: Note: Verify that when F2=3.18MHz or T2=157ns,
T2=157ns is the clock edge limit when LC2 blocks the current.
(LC2 pathway)
Or
(Ctot3 pathway)
X
0.1 
XLC2
XC3_array
F2s=3.18MHz

## Slide 68: Overall impedance X and Freq. plot
X
0.1 
XC2
XC3_array
Xpcable
XLC2
XLtot3
F1=159KHz
3.18MHz
100MHz
Current from
power supply
Current from C2
Current from
Cap. Array C3
No current
demand here
See
next
slide

## Slide 69: A summary of the steps :
Based on power line inductance, find max impedance Xmax
Based on Xmax, find the lowest effective freq.(F1) of the board-level bypass cap (C_bypass)
Based on F1, find C_bypass value.
To solve the problem caused by legs of C_bypass using capacitor array (C3_array).
  Find the minimum number (N) of array elements needed based on the inductance of the legs of elements in C3_array, and the maximum required frequency inside the board.
  From N find the value of individual element of C3_array (C3)
  Plot the frequency response curves of the whole span of frequencies.

## Slide 70: Power exercise 5
A hardware system has 500 digital outputs, each output is switching a 10-pF load at 5ns.
The power comes from a perfect voltage source of 5V via a power cable of inductance 200nH.
The maximum allowable supply voltage drop within the system is 0.1V.
The series inductance of each capacitor (for all types) is 5nH. Ignore the inductance of the traces in the system board. State any assumptions you used in the calculations.
Find board level bypass capacitor C2
Find the number N of elements in the capacitor array and its individual value C3.

## Slide 71: Power Exercise 6
A large PCB board contains two circuit areas groups, A and B. The overall power comes from a perfect voltage source of 5Volts. The maximum allowable supply voltage drop anywhere in the board is 0.1Volts.
Given that dI = |C (dV/dt)|, for dI is the change in current, C is the capacitance of the capacitor and dV/dt is the rate of change of the voltage. The board level bypass capacitors for serving both group A and B have a very small series inductance. State any assumptions you used in the calculations.
  Three large board level by-pass capacitors are provided, how do you place them? Copy the following diagram to your answer book and insert the bypass capacitors in your diagram.
Calculate the values required? Show your calculation
Power supply +
Ground
A large PCB
Circuit group A:
  100 outputs
each output has a capacitive load of 10pF.
switching time is 10ns
Circuit group B
  120 outputs
each output has a capacitive load of 5pF.
switching time is 15ns
Power cable with inductance =150nH
Circuit trace with inductance=60nH
Circuit trace with inductance=35nH

## Slide 72: Appendix
Answers to exercises

## Slide 73: Q&A on capacitor array
Should the impedance of inductance XLtot3 and capacitance XCtot3 (both are 0.1 ) be added together since they are in series? (The total equivalent Ctot3=0.5uF, LCtot3=5nH/32)
Ans: Yes they should be added together. But at 3.18MHz, XLtot3(3.18MHz) =2  3.18M (5nH/32)  3x10-3  (very low), while XCtot3(3.18MHz) = 1/[2  3.18M (0.5uF)]  0.1  .
On the other hand at 100MHz, XLtot3(100MHz) = 2  100M (5nH/32) 0.1  while X Ctot3(100MHz) =1/[2  100M (0.5uF)] 3x10-3  is low.
So between 3.18MHz and 100MHz, when XC and XL are added they will not be too much larger than 0.1 .
C3
C3
C3
Cap.
array
Ctot3

## Slide 74: Answers:
Answer1:
  Tr=2.5ns.
Answer2:
  (i) noise N=0? Ans: 2.8-0-2.5=0.3 positive, gateC out 1
  (ii) noise N=0.5? Ans:2.8-0.5-2.5=-0.2V neg. so gateC out is 0 (ii) Why there is noise N? ans: ground loop, long wire
Answer3:
  Exercise: When gate A is on , N=0.5V , what is Vdiff? ANS: V0=2.5(FIXED),V1=2.5: v0+v1-(V0-v1)=2.5+2.5-(2.5-2.5)=5V, N has no effect
  Exercise: When gate A is off , N=0.5V, what is Vdiff? ANS: V0=2.5(FIXED), V1=0: v0+v1-(V0-v1)=2.5+0-(2.5-0)= 0V, N has no effect
Answer4 : (verified on 29 March 2016)
  Board level bypass capciator(C2)=500uF
  Capacitor array totoal=C_total_array=12.5uF
  Number o capacyor in the cap. Array(N)=157
  Each element of the cap. array isC3 = 0.079uF.
Answer5 :
  C1=7.3uF
  C2=0.875uF
  C3=0.24uF

## Slide 75: Appendix

## Slide 76: Alternative method (differential signaling) to reduce ground noise (expensive) by using differential logic gates and transmission lines
Gate C sees V_diff
V0=2.5 (fixed),
When a gate is on, V1 =2.5 else V1=0
A method to remove ground connection noise
Differential signaling logic uses 3 wires (2 signals plus ground) to connect a stage to the next, while the usual non-differential signaling logic uses 2 wires (signal + ground) only.
=2.5-V1
=2.5+V1
V1
V0

## Slide 77: Signal propagation
http://en.wikipedia.org/wiki/Differential_signaling