## Slide 1: Tutorial 2: Introduction to ISE 14.6 (revised by khw)
CENG 3430

## Slide 2: Step 1: Start up the software
Double click the ISE icon in the desktop
Or start from the Start Menu

## Slide 3: Step 2: Create a new project
Click File->Select New Project->Type ‘tutorial’->Click Next->Fill in the properties->Click Next->Click Finish
♦ Evaluation Development Board: None Specified
♦ Product Category: All
♦ Family: Spartan3A and Spartan3AN
♦ Device: XC3S50AN
♦ Package: TQ144
♦ Speed: -4
♦ Top-Level Source Type : HDL
♦ Synthesis Tool: XST (VHDL/Verilog)
♦ Simulator: ISim (VHDL/Verilog)
♦ Preferred Language: VHDL

## Slide 4: Step 3: Create a VHDL Source
Left-top (view= Implementation)
Right-click xCs50an-4tqg144
->Select New source->Select VHDL Module->Type ‘counter’->Click Next->Fill in port information->Click Next->Click Finish

## Slide 5: Step 4: Add your code
use IEEE.STD_LOGIC_ARITH.ALL;
use IEEE.STD_LOGIC_UNSIGNED.ALL;
process (CLOCK)
begin
if CLOCK='1' and CLOCK'event then
if DIRECTION='1' then
count_int <= count_int + 1;
else
count_int <= count_int - 1;
end if;
end if;
end process;
COUNT_OUT <=count_int;
signal count_int : std_logic_vector(3 downto 0) := "0000";

## Slide 6: Step 5: Check the syntax
Select Implementation->Select counter source file->Select Synthesize->Double click the Check Syntax

## Slide 7: Step 6: Create a test bench
Click Simulation->Select Project->Select New Source->Select VHDL Test Bench->Type ‘counter_tb’->Click Next->Click Next->Click Finish

## Slide 8: Step 7: Enter your code
Modify the code and save
Set DIRECTION to be ‘1’
Set CLOCK_period to be ‘1 us’

## Slide 9: Step 8: Run the simulation
Select counter_tb->Right click Simulate Behavioral Model->Click Rerun All

## Slide 10: Step 8: Run the simulation
Press F11 3 times->Select Window->Select Tile Horizontally

## Slide 11: Step 8: Run the simulation
Select Restart->Press F11 10 times->Use Zoom in and Zoom out to adjust the scale

## Slide 12: Step 9: Implement Design
Select Implementation->Double click the generate Programming File

## Slide 13: Step 10: Pin Assignment
Click User Constraints->Double click the Floorplan Area/IO/Logic->Press ‘yes’->Press ‘close’->Click the ‘+’ next to the COUNT_OUT
COUNT_OUT[0] → P3
COUNT_OUT[1] → P4
COUNT_OUT[2] → P5
COUNT_OUT[3] → P6
CLOCK → P124
(make sure you use the correct pin for the clock)
DIRECTION → P110

## Slide 14: Step 10: Pin Assignment
Select File->Select Save constraints->Close the PlanAhead Window->
(left top window : View – implementation)
Double Click the counter.ucf->
Top-left window : Mouse over counter-Behavioral (counter.vhd)
Bottom-left window: mouse over/right click Generating Programming File (rerun all)

## Slide 15: Step 11: Download to the board
Refer to the Tutorial 1 (appendix) and finish this step
A revision of tutorial 1. The required voltage of USB JTAG is 3.3V but that of parallel is 5V.

## Slide 16: Run simulation without test bench
Force Clock

## Slide 17: Run simulation without test bench
Force Clock
Remember to enter the UNIT
e.g. 50 ns, 0.5us, 1ms
Leading Edge: the start value
Trailing Edge: the end value
e.g. Leading = 0, Trailing = 1 will make a

## Slide 18: Run simulation without test bench
Force Constant

## Slide 19: Run simulation without test bench
Force Constant

## Slide 20: Appendix

## Slide 21: Introduction to FPGA Board
Ceng 3430

## Slide 22: Collect your board
Come to collect your board
  CUHK CSE FPGA Board 2013
  Xilinx USB JTAG Cable
  DC 9V Adapter
Don’t forget to tick your name in the list form when collecting your board

## Slide 23: Overview diagram

## Slide 24: A test to your board: Step 1
Connect your board with PC using the USB JTAG cable

## Slide 25: Step 2
Configure DIP switch as follows

## Slide 26: Step 3
Connect your board with power

## Slide 27: Step 4
Double click the TestSpartan3AN.xise file icon in the TestSpartan3AN folder to open the TestSpartan3AN project.

## Slide 28: Step 5
Open iMPACT
  Implementation -> TestSpartan3AN -> double-click the Configure Target Device -> iMPACT -> File -> New Project

## Slide 29: Step 6
Build a new iMPACT project

## Slide 30: Step 7
Select testspartan3an.bit

## Slide 31: Step 8
Program flash and Load FPGA
  Right-click on the xc3s50an device image, and select Program Flash and Load FPGA

## Slide 32: Result
4 seven segment displays are lit and counting from ‘0’ to ‘F’

## Slide 33: End
Download the materials from Blackboard system.