## Slide 1: VHDL 2 Identifiers, data objects and data types
Chapter2
Identifiers
Data
objects
constants
Signals
Variables
Data types

## Slide 2: Identifiers It is about how to create names
Used to represent an object (constant, signal or variable)
Chapter2
Identifiers
Data
objects
constants
Signals
Variables
Data types

## Slide 3: Rules for Identifiers
Names for users to identify data objects: signals, variables etc.
First character must be a letter
last character cannot be an underscore
Not case sensitive
Two connected underscores are not allowed
Examples of identifiers: a, b, c, axy, clk ...

## Slide 4: Example: a,b,equals are Identifiers of signals
1 entity eqcomp4 is
2 port (a, b: in std_logic_vector(3 downto 0);
3 equals: out std_logic);
4 end eqcomp4;
5
6 architecture dataflow1 of eqcomp4 is
7 begin
8 equals <= '1' when (a = b) else '0’;
9-- “comment” equals is active high
10 end dataflow1;

## Slide 5: Data objects

## Slide 6: Data objects
Constant
Signals
variables
Chapter2
Identifiers
Data
objects
Constants
(Global)
Signals
(Global)
Variables
(Local)
Data types

## Slide 7: Data objects: 3 different objects
1 Constants: hold values that cannot be changed within a design.
  e.g. constant width: integer :=8
2 Signals: to represent wire connections
  e.g. signal count: bit_vector (3 downto 0)
  -- count means 4 wires; they are count(3),count(2), count(1), count(0).
3 Variables: internal representation used by programmers; do not exist physically.

## Slide 8: Recall: if a signal is used as input/output declared in port
It has 4 modes
Modes in port
in
out
inout
buffer
e.g.
entity eqcomp4 is
port (a, b: in std_logic_vector(3 downto 0 );
equals: out std_logic);
end eqcomp4;

## Slide 9: Syntax to create data objects
In entity declarations

## Slide 10: Constants with initialized values
constant CONST_NAME: <type_spec> := <value>;
-- Examples:
constant CONST_NAME: BOOLEAN := TRUE;
constant CONST_NAME: INTEGER := 31;
constant CONST_NAME: BIT_VECTOR (3 downto 0) := "0000";
constant CONST_NAME: STD_LOGIC := 'Z';
constant CONST_NAME: STD_LOGIC_VECTOR (3 downto 0) := "0-0-"; -- ‘-’ is don’t care

## Slide 11: Signals with initialized values
signal sig_NAME: type_name [: init. Value];
-- examples
  signal s1_bool : BOOLEAN; -- no initialized value
  signal xsl_int1: INTEGER :=175;
  signal su2_bit: BIT :=‘1’;

## Slide 12: Variables with initialized values
variable V_NAME: type_name [: init. Value];
-- examples
  variable v1_bool : BOOLEAN:= TRUE;
  variable val_int1: INTEGER:=135;
  variable vv2_bit: BIT; -- no initialized value

## Slide 13: Signal and variable assignments
SIG_NAME <= <expression>;
VAR_NAME :=<expression>;

## Slide 14: Exercise 2.1: On signals
1-- 4-bit parallel load register with asynchronous reset
2-- CLK, ASYNC ,LOAD, : in STD_LOGIC;
3-- DIN: in STD_LOGIC_VECTOR(3 downto 0);
4-- DOUT: out STD_LOGIC_VECTOR(3 downto 0);
5 process (CLK, ASYNC)
6 begin
7 if ASYNC='1' then
8 DOUT <= "0000";
9 elsif CLK='1' and CLK'event then
10 if LOAD='1' then
11 DOUT <= DIN;
12 end if;
13 end if;
14 end process
Fill in the blanks.
Identifiers are:
  __________
  __________
  __________
  __________
  __________
Input signals are:
  __________
  __________
  __________
Signal arrays are:
  __________
  __________
Signal type of DIN:
  __________
Mode of DOUT
  __________
Student ID: __________________ Name: ______________________ Date:_______________
(Submit this at the end of the lecture.)

## Slide 15: Data types
Different types of wires
Each type has a certain range of logic levels

## Slide 16: Data types
Chapter2
Identifiers
Data
objects
Constants
(Global)
Signals
(Global)
Variables
(Local)
Data types

## Slide 17: Data types
User can design the type for a data object.
  E.g. a signal can have the type ‘bit’
  E.g. a variable can have the type ‘std_logic’
Only same type can interact.

## Slide 18: Types must match
1 entity test is port (
2 in1: in bit;
3 out1: out std_logic );
4 end test;
5 architecture test_arch of test is
6 begin
7 out1<=in1;
8 end test_arch;
Different types :
bit and std_logic
Not allowed

## Slide 19: Exercise 2.2: (a) Declare a signal “signx” with type bit in line 2 (b) Can you assign an IO mode to this signal (Yes or No) , and why? Answer:______________________________
1 Architecture test2_arch of test2
2 ?_________________
3 begin
4 ...
5 …
6 end test_arch

## Slide 20: Exercise 2.3: (a) Where do you specify the types for signals? (b) Draw the schematic of this circuit.
1 entity nandgate is
2 port (in1, in2: in STD_LOGIC;
3 out1: out STD_LOGIC);
4 end nandgate;
5 architecture nandgate_arch of nandgate is
6 signal connect1: STD_LOGIC;
7 begin
8 connect1 <= in1 and in2;
9 out1<= not connect1;
10 end nandgate_arch;
Answer for (a) : Specify types of signals in
(i)____________________
(ii)____________________
Answer for (b)

## Slide 21: Revision (so far we learned) (w3 begins)
Data object
  Constants, signal, Variables
Signal in port (external pins)
  In
  Out
  Inout
  Buffer
Data type
  Many types: integer, float, bit, std_logic, etc.
Chapter2
Identifiers
Data
objects
Constants
(Global)
Signals
(Global)
Variables
(Local)
Data types

## Slide 22: Exercise: 2.4:
1 entity nandgate is
2 port (in1, in2: in STD_LOGIC;
3 out1: out STD_LOGIC);
4 end nandgate;
5 architecture nandgate_arch of nandgate is
6 signal connect1: STD_LOGIC;
7 begin
8 connect1 <= in1 and in2;
9 out1<= not connect1;
10 end nandgate_arch;
(a) Underline the IO signal
(b) Underline the Internal Signal

## Slide 23: Different data types

## Slide 24
Chapter2
Identifiers
Data
objects
Constants
(Global)
Signals
(Global)
Variables
(Local)
Data types
Data types
Enumeration:
Red, blue
Boolean:
“TRUE”,
”FALSE”
Bit:
0,1
Character
‘a’,’b’
String:
“text”
Integer:
13234,23
Float:
0.124
standard logic:
Resolved,
Unresolved
Different data types

## Slide 25: Examples of some common types
Type BOOLEAN is (FALSE, TRUE)
type bit is (‘0’ ,’1’);
type character is (-- ascii string)
type INTEGER is range of integer numbers
type REAL is range of real numbers
Type Standard logic( with initialized values):
  signal code_bit : std_logic := ‘1’; --for one bit , init to be ‘1’, or ‘0’
  signal codex : std_logic_vector (1 downto 0) :=“01”; -- 2-bit
  signal codey : std_logic_vector (7 downto 0) :=x“7e”; --8-bit hex 0x7e
  Note:
    Double quote “ ” for more than one bit
    Single quote ‘ ’ for one bit

## Slide 26: Boolean, Bit Types
Boolean (true/false), character, integer, real, string, these types have their usual meanings. In addition, VHDL has the types: bit, bit_vector,
The type “bit” can have a value of '0' or '1'. A bit_vector is an array of bits.
See VHDL Quick Reference http://www.doulos.com/knowhow/vhdl_designers_guide/

## Slide 27: Integer type (depends on your tool; it uses large amount of logic circuits for the implementation of integer/float operators) E.g.
Range from -(2^31) to (2^31)-1

## Slide 28: Floating type
-3.4E+38 to +3.4E+38
For encoding floating numbers, but usually not supported by synthesis tools of programmable logic because of its huge demand of resources.

## Slide 29: Enumeration types:
How to input an abstract concept into a circuit ?
E.g.1 color: red, blue, yellow, orange etc, we need 2 bits
E.g.2
Language type: Chinese, English, Spanish, Japanese, Arabic. How many bits needed?
Answer: 5 different combinations: 3 bits
中文字, Chinese characters, caracteres chinos,漢字,الأحرف الصينية ,
exercise

## Slide 30: Enumeration types:
An enumeration type is defined by listing (enumerating) all possible values
Examples:
type COLOR is (BLUE, GREEN, YELLOW, RED);
type MY_LOGIC is (’0’, ’1’, ’U’, ’Z’);
-- then MY_LOGIC can be one of the 4 values

## Slide 31: Exercises 2.5
Example of the enumeration type of the menu of a restaurant:
  type food is (hotdog, tea, sandwich, cake, chick_wing);
(a) Declare the enumeration type of the traffic light.
  Answer: _______________________________________
(b) Declare the enumeration type of the outcomes of rolling a dice.
  Answer: _______________________________________
(c) Declare the enumeration type of the 7 notes of music.
  Answer: _______________________________________

## Slide 32: Define
Array or a bus

## Slide 33: Std_logic_vector (array of bits) for bus implementation
To turn bits into a bus
‘bit’ or ‘std_logic’ is ‘0’, ‘1’ etc.
Std_logic_vector is “000111”etc.
1 entity eqcomp3 is
2 port (a, b: in std_logic_vector(2 downto 0);
3 equals: out std_logic);
4 end eqcomp3;
So a, b are 3-bit vectors:
a(2), a(1), a(0), b(2), b(1), b(0),
Bit_vector
bit
bit

## Slide 34: Exercise 2.6 Difference between “to” and “downto”
(a) Given: signal a : std_logic_vector( 2 downto 0);
Create a 3-bit bus c using “to”instead of “downto” in the declaration.
Answer: ______________________________
(b) Draw the circuit for this statement: c<=a;

## Slide 35: An advanced topic
Resolved, Unresolved logic
(Concept of Multi-value logic)

## Slide 36: Resolved logic concept (Multi-value Signal logic)
Can the outputs be connected together to drive a device ?
The connected output is driving a device (e.g. a buffer) to produce an output. A device is usually having high input impedance (e.g. 10M)
C1
C2
??
Rin=Input impedance 10M
Rin
output

## Slide 37: Resolved signal concept
Signal c1,c2, b1: bit;
b1<=c1;
c1
b1
no problem
A device

## Slide 38: Resolved signal concept
Signal c1,c2, b1: bit;
b1<=C1;
b1<=C2;
C1
b1
??
illegal
C2
??
We need "resolved type"
to resolve this problem
A device

## Slide 39: Type Std_logic and std_ulogic
Std_logic is a type of resolved logic, that means a signal can be driven by 2 inputs
std_ulogic: (the “u”: means unresolved) Std_ulogic type is unresolved logic, that means a signal cannot be driven by 2 inputs
A device

## Slide 40: Although VHDL allows resolved types, but Xilinx has not implemented it
Error message # 400
Signal 'name' has multiple drivers.
The compiler has encountered a signal that is being driven in more than one process.
Note that it is legal VHDL to have a signal with multiple drivers if the signals type is a resolved type (i.e. has a resolution function) such as 'std_logic' (but not 'std_ulogic'). (Metamor, Inc.)

## Slide 41: Standard logic type and resolved logic (Multi-Value Signal Types)
The IEEE_1164 library -- the industrial standard And some of its essential data types

## Slide 42: To use the library, add the two lines at the front
Library IEEE
use IEEE.std_logic_1164.all
entity
architecture

## Slide 43: The 9-valued logic standard logic system of IEEE_1164, It specifies the possible states of a signal(Multi-Value Signal Types)
‘U’ Uninitialized
‘X’ Forcing Unknown
‘0’ Forcing 0
‘1’ Forcing 1
‘Z’ High Impedance=float
‘W’ Weak Unknown
‘L’ Weak 0
‘H’ Weak 1
‘-’ Don’t care
?
state

## Slide 44: Resolved rules of the 9-level logic
There are weak unknown, weak 0, weak 1 and force unknown, force 0, force 1
when 2 signals tight together, the forcing signal dominates.
It is used to model the internal of a device.
In our applications here, the subset of the IEEE forcing values ‘X’ ‘0’ ‘1’ ‘Z’ are used.

## Slide 45: Exercise 2.7: Resolution table when two std_logic signals S1,S2 meet (X=forcing unknown, Z=float)
Fill in the blanks “?”

## Slide 46: From: http://zeus.phys.uconn.edu/wiki/index.php/VHDL_tutorial
‘U’ Uninitialized
‘X’ Forcing Unknown
‘0’ Forcing 0
‘1’ Forcing 1
‘Z’ Float
‘W’ Weak Unknown
‘L’ Weak 0
‘H’ Weak 1
‘-’ Don’t care

## Slide 47: Understanding multi-level logic using Ohms law
Driving voltage
Level (Vi)
Driving voltage
Level (Vj)
Level type | Ri or Rj (vraiable resistor dpends on the level-type) | Driving Voltage Vi or Vj (in Voltage)
‘U’ Uninitialized | unknown | Unknown
‘X’ Forcing Unknown | 50 :(low R for forcing) | Unknown
‘0’ Forcing 0 | 50 :(low R for forcing) | 0
‘1’ Forcing 1 | 50 :(low R for forcing) | 5
‘Z’ Float | 10M (Very high R for float) | Not connected
‘W’ Weak Unknown | 100 K :(high R for weak) | Unknown
‘L’ Weak 0 | 100 K :(high R for weak) | 0
‘H’ Weak 1 | 100 K :(high R for weak) | 5
‘-’ Don’t care | unknown | Unknown
Connection junction
Ri
Rj
output
The junction is driving a device
Rin=10M

## Slide 48: Calculation Example
Proof Vc  5V
Answer: using Kirchhoff law at junction: i1+i2+i3=0
i1=(5-Vc)/50
i2=(0-Vc)/100K
i3=(0-Vc)/10M, so
(5-Vc)/50+(0-Vc)/100K+(0-Vc)/10M=0, since 50<<100K &10M
5-Vc  0, hence Vc  5
Driving voltage
Level (Vi=L)
Weak Low
Output=
Driving voltage
Level (Vj=1=5V)
Forcing high
Connection
Junction (Vc)  5V=high
Ri=100K
Rj=50
output
Rin=10M
i1
i2
i3
Vc

## Slide 49: Examples (you can use Ohms and Kirchhoff laws to verify results)
Example1
Example 2
Example3
Driving voltage
Level (Vi=L=0v)
Weak Low
Output=
Driving voltage
Level (Vj=1=5V)
Forcing high
Connection
Junction  5V=high
Ri=100K
Rj=50
Driving voltage
Level (Vi=H=5v)
Weak high
Driving voltage
Level (Vj=0=0V)
Forcing low
Connection
Junction0v=low
Ri=100K
Rj=50
Driving voltage
Level (Vi=0)
Forcing low
Driving voltage
Level (Vj=1=5V)
Forcing high
Connection
Junction2.5V=X (forcing unknown) ,
current is high
Ri=50
Rj=50
output
Rin=10M

## Slide 50: More examples
Example 4
Example 5a
Example 5b
Driving voltage
Level (Vi=0)
Forcing Low
Driving voltage
Level (Vj=Z,
not connected)
Connection
Junction0=0V (Low) ,
Ri=50
Rj=10M
Driving voltage
Level (Vi=L=0V)
Weak Low
Driving voltage
Level (Vj=H=5V),
Weak High
Connection
Junction0V=Low,
Ri1=100K
Rj=100K
Driving voltage
Level (Vi=L=0V)
Forcing Low
Ri2=50
Driving voltage
Level (Vi=L=0V)
Weak Low
Driving voltage
Level (Vj=H=5V),
Weak High
Connection
Junction2.5V=W, weak unknown
Ri1=100K
Rj=100K

## Slide 51: Exercise 2.8: use Ohms and Kirchhoff laws to verify results
Calculate Vc for the following 2 cases:
Ex2.8A: for example5a in lecture note2
Ex2.8B: for example5b in lecture note2
Driving voltage
Level (Vi=L=0V)
Weak Low
Driving voltage
Level (Vj=H=5V),
Weak High
Connection
Junction0V=Low,
Ri1=100K
Rj=100K
Driving voltage
Level (Vi=L=0V)
Forcing Low
Ri2=50
Driving voltage
Level (Vi=L=0V)
Weak Low
Driving voltage
Level (Vj=H=5V),
Weak High
Connection
Junction2.5V=W, weak unknown
Ri1=100K
Rj=100K
Vc
Vc

## Slide 52: Answer 2.8A
Exercise2.8A (for exercise 2.8B students need to produce the answer on their own)
Answer: using Kirchhoff law at junction: i1+i2+i3=0
i1=(5-Vc)/100K
i2=(0-Vc)/100K
i3=(0-Vc)/10M, so
(5-Vc)/100K+(0-Vc)/100K+(0-Vc)/10M=0, since 100K << 10M
5-Vc+(0-Vc)=5-2*Vc  0, hence Vc  2.5 (unknown but is weak)
Why it is weak because I1=(5-Vc)/100K=2.5/100K=0.025mA
current is weak.
Driving voltage
Level (Vi=L=0v)
Weak Low
Output=
Driving voltage
Level (Vj=H=5V),
Weak High
Connection
Junction (Vc)  5V=high
Ri1=100K
Rj=100K
output
Rin=10M
i1
i2
i3
Vc

## Slide 53: Alternative answers for exercise 2.8
For example 5a
  5V---100K  -----junction------100K  ----0V
  Junction is 2.5 is an unknown level but is weak.
For example 5b
  5V---100K -----junction------100K  ----0V
^---------50 ----0V
Equivalent to
  5V---100K -----junction------100K//50 ----0V
  Or (when 100K is in parallel to 50 , the equivalent resistance is very close to 50 ), so the circuit becomes
  5V---100K -----junction------50 ----0V
  So junction is low (nearly 0 Volt)

## Slide 54: Appendix 1 Example of using IEEE1164
library IEEE;
use IEEE.std_logic_1164.all; -- defines std_logic types
--library metamor;
entity jcounter is
port (
clk : in STD_LOGIC;
q : buffer STD_LOGIC_VECTOR (7 downto 0)
);

## Slide 55: Quick Revision
You should have learnt
  Identifier and usage
  Different data objects (constant, signals, variables)
  Different data types (Boolean , bit, stad_logic, std_logic_vector integer etc)
  Resolved logic