## Slide 1: VHDL 3 Basic operators and Architecture Body
Design descriptions & Design constructions
examples are taken from foundation series examples

## Slide 2: We will learn
Operators and
Different architecture design methods
  1) Structural
  2) Data flow
  3) Behavioral
Use of signals and variables

## Slide 3: VHDL operators
And their usage

## Slide 4: Typical Operators
Operators
Logical /
Relation
E.g and/or
Shift,
e.g.
SLR
Basic
+,-,&
Abs,**

## Slide 5: Logical / relation operators
And, or, nand, nor, xor, xnor, not -- have their usual meanings.
But nand is not associative :
  A nand B nand C is illegal.
  Exercise 3.1: Draw the truth table to show
  (A nand B) nand C ≠ A nand (B nand C)
Relation operators
= equal ; /= not equal
< <= > >= smaller, bigger , equal etc.

## Slide 6: Exercise 3.1: Fill in “?__”. It shows the NAND-gate is not associative , so A nand B nand C is illegal. (A nand B) nand C ≠ A nand (B nand C)
A | B | C | A nand B | (A nand B) nand C | B nand C | A nand (B nand C)
0 | 0 | 0 | 1 | 1 | 1 | 1
0 | 0 | 1 | 1 | ?__ | 1 | 1
0 | 1 | 0 | 1 | 1 | 1 | 1
0 | 1 | 1 | 1 | 0 | ?__ | 1
1 | 0 | 0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 0 | 1 | ?__
1 | 1 | 0 | 0 | 1 | 1 | 0
1 | 1 | 1 | 0 | 1 | ?__ | 1
Student ID: __________________ Name: ______________________ Date:_______________
(Submit this at the end of the lecture.)

## Slide 7: Shift operators see VHDL for Engineers – (Google books) Kenneth L. Short - 2008 - Computers – 685 see http://www.csee.umbc.edu/portal/help/VHDL/numeric_std.vhdl
Logical shift and rotate
Sll (shift left logical, fill blank with 0);
srl (shift right logical, fill blank with 0)
rol(rotate left logical ); ror(rotate right logical) circular operation.
E.g. “10010101” rol 3 is “10101100”
Arithmetic shift (http://en.wikipedia.org/wiki/Arithmetic_shift)
  sla (shift left arithmetic) fill blank with 0,same as sll (shift left logical)
  sra (shift right arithmetic), fill blank with sign bit (MSB)

## Slide 8: Exercise 3.2 on shift and rotate
A <= “10010101”;
A sll 2 =__________
A srl 3 =__________
A sla 3 =__________
A sra 2 =__________
A rol 3=__________
A ror 5 =__________

## Slide 9: Shift and rotate in Xilinx ISE or Vivado 14.4 http://stackoverflow.com/questions/15885390/vhdl-programming and http://www.csee.umbc.edu/portal/help/VHDL/numeric_std.vhdl use IEEE.numeric_std.all;
--using shift_left,shift_right, rotate_left,rotate_right functions in VHDL (use IEEE.numeric_std.all;)
--ISE complied ok
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
use IEEE.numeric_std.all;
entity EXAMPLE is
Port (
clk : in STD_LOGIC; -- master clock
enable : in std_logic; -- when '1' --> rotate
dir : in STD_LOGIC; -- when '1': right, when '0': left
nr : in STD_LOGIC_VECTOR (1 downto 0); -- number of steps to rotate
din : in STD_LOGIC_VECTOR (7 downto 0); -- in vector
dout : out STD_LOGIC_VECTOR (7 downto 0)); -- out vector
end EXAMPLE;
architecture Behavioral of EXAMPLE is
begin
shifter: process(clk)
begin
if rising_edge(clk) then
if enable='1' then
if dir='0' then -- right
dout<=std_logic_vector(rotate_right(unsigned(din),to_integer(unsigned(nr))));
-- dout<=std_logic_vector(shift_right(unsigned(din),to_integer(unsigned(nr))));
else -- left
dout<=std_logic_vector(rotate_left(unsigned(din), to_integer(unsigned(nr))));
-- dout<=std_logic_vector(shift_left(unsigned(din), to_integer(unsigned(nr))));
end if;
end if;
end if;
end process shifter;
end Behavioral;

## Slide 10: Some basic operators
‘+’ arithmetic add, for integer, float.
‘-’ arithmetic subtract, for integer, float.
‘&’ concatenation: ‘0’ & ‘1’ is “01”, Notice the use of “&”.

## Slide 11: Some basic operators
‘*’ multiplication
‘/’ division
‘mod’ =modulus=
  E.g. A mod B= A-(B*N) -- N is an integer
‘abs’ = absolute value
‘**’ = exponentiation

## Slide 12: Architecture body
Design methods
W4 begins

## Slide 13: 3 types of design description
1. Structural
(parallel)
Use port map
2. Data Flow
(parallel)
Use concurrent
statements
3. Behavioral
(serial)
Use process
Design
description

## Slide 14: (1) Structural design description method
1. Structural
(parallel)
Use port map
2. Data Flow
(parallel)
Use concurrent
statements
3. Behavioral
(serial)
Use process
Design
description

## Slide 15: Structural :Like a circuit but describe it by text.
Component A
Component B
Component C
Related by port map
in architecture

## Slide 16: Structural :Like a circuit but describe it by text.
Step1: Create entities
Step2: create components from entities
Step3: create “port map” to relate the components

## Slide 17: A working example
--Demo_component.vhdl (ok vivado 2014.4)
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
-------------------------------------------
entity and2 is
port (a,b: in STD_LOGIC;
c: out STD_LOGIC ); end;
architecture and2_arch of and2 is
begin
c <= a and b;
end and2_arch;
--entity xnand2 is
-------------------------------------------
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
entity or2 is
port (a,b: in STD_LOGIC;
c: out STD_LOGIC ); end;
architecture or2_arch of or2 is
begin
c <= a or b;
end or2_arch;
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
entity test is --
port ( in1: in STD_LOGIC; in2: in STD_LOGIC;--
in3: in STD_LOGIC; out1: out STD_LOGIC--
); end test;
architecture test_arch of test is
component and2 --create components--
port (a,b: in std_logic; c: out std_logic); --
end component ;
component or2-- Port ( );
port (a,b: in std_logic; c: out std_logic); --
end component ;
signal con1_signal: std_logic;
begin
label1: and2 port map (in1, in2, con1_signal);
label2: or2 port map (con1_signal, in3, out1);
end test_arch;

## Slide 18: Step1 of Structural Description Create the and2 chip :an entity and2
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
-------------------------------------------
entity and2 is
port (a,b: in STD_LOGIC;
c: out STD_LOGIC ); end;
architecture and2_arch of and2 is
begin
c <= a and b;
end and2_arch;
--entity xnand2 is
-------------------------------------------
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
entity or2 is
port (a,b: in STD_LOGIC;
c: out STD_LOGIC ); end;
architecture or2_arch of or2 is
begin
c <= a or b;
end or2_arch;
a
b
c
AND
a
b
c
OR

## Slide 19: Step 2 : Create component “and2” based on “entity and2”
architecture test_arch of test is
component and2 --create components--
port (a,b: in std_logic; c: out std_logic); --
end component ;
component or2-- Port ( );
port (a,b: in std_logic; c: out std_logic); --
end component ;
Exercise: Use the same method to create a component “NOR2”.
Component “and2”
a = input
c= output
b = input

## Slide 20: Step 3 : connect components using port map
begin
label1: and2 port map (in1, in2, con1_signal);
label2: or2 port map (con1_signal, in3, out1);
end test_arch;
in1
in3
Con1_signal
out1
in2
What will happen if these 2 lines (23,24) are interchanged ?

## Slide 21: Core of the structural design
begin
label1: and2 port map (in1, in2, con1_signal);
label2: or2 port map (con1_signal, in3, out1);
end test_arch;
Label1,label2 are line labels
“port map” are reserved words
lines can be interchanged
in1
in3
Con1_signal
out1
in2
It is still this circuit even the two lines are interchanged

## Slide 22: Exercise: 3.3:
(a) When will line i) and (ii) be executed?
  Answer: ___________________________________________
(b) Draw the schematic diagram if a VHDL program has lines
  (i) label_u0:and2 port map (a, c, x);
  (ii) label_u1:or2 port map (b,x,y);
(c) Complete line (i) and (ii) if the circuit is
  (i) label_u0: ?_______________
  (ii) label_u1:?_________________
a
c
x
y
b

## Slide 23
entity test_andor2 is – Another detailed example
port ( in1: in STD_LOGIC; in2: in STD_LOGIC;
in3: in STD_LOGIC; out1: out STD_LOGIC
); end test_andor2;
architecture test_andor2_arch of test_andor2 is
component and2
port (a,b:in std_logic; c: out std_logic);
end component ;
component or2
port (a,b:in std_logic; c: out std_logic);
end component ;
signal con1_signal: std_logic;
begin
label1: and2 port map (in1, in2, con1_signal);
label2: or2 port map (con1_signal, in3, out1);
end test_andor2_arch;
in1
in3
Con1_signal
out1
in2

## Slide 24: Example: half-adder
library IEEE; --Vivado 14.4 ok
use IEEE.STD_LOGIC_1164.ALL;
-------------------------------------------
entity and2 is
port (a,b: in STD_LOGIC;
c: out STD_LOGIC ); end;
architecture and2_arch of and2 is
begin
c <= a and b;
end and2_arch;
--entity xnand2 is
-------------------------------------------
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
entity xor2 is
port (a,b: in STD_LOGIC;
c: out STD_LOGIC ); end;
architecture xor2_arch of xor2 is
begin
c <= a xor b;
end xor2_arch;
-------------------------------------------
library IEEE; --Vivado 14.4 ok
use IEEE.STD_LOGIC_1164.ALL;
entity half_adder is -- another example
port ( x: in bit; y: in bit;
sum: out bit; carry: out bit );
end half_adder;
architecture half_adder_arch of half_adder is
component xor2 port(a,b: in bit; c: out bit);
end component;
component and2 port( a,b: in bit; c: out bit);
end component;
begin
label1: xor2 port map (x,y,sum);
label2: and2 port map (x,y, carry);
end half_adder_arch;

## Slide 25
Exercise 3.4
Draw the schematic diagram of the half-adder shown on the right.
library IEEE; --Vivado 14.4 ok
use IEEE.STD_LOGIC_1164.ALL;
entity half_adder is -- another example
port ( x: in bit; y: in bit;
sum: out bit; carry: out bit );
end half_adder;
architecture half_adder_arch of half_adder is
component xor2 port(a,b: in bit; c: out bit);
end component;
component and2 port( a,b: in bit; c: out bit);
end component;
begin
label1: xor2 port map (x,y,sum);
label2: and2 port map (x,y, carry);
end half_adder_arch;

## Slide 26: (3) Dataflow method {Using concurrent statements}
1. Structural
(parallel)
Use port map
2. Data Flow
(parallel)
Use concurrent
statements
3. Behavioral
(serial)
Use process
Design
description

## Slide 27: Data flow: concurrent execution (no need to use “port map”)
library IEEE; %Vivado2014.4 tested ok
use IEEE.STD_LOGIC_1164.ALL;
entity eqb_comp4 is
port (a, b: in std_logic_vector(3 downto 0);
equals,bigger: out std_logic);
end eqb_comp4;
architecture dataflow4 of eqb_comp4 is
begin
equals <= '1' when (a = b) else '0';--concurrent
bigger <='1' when (a > b) else '0';--concurrent
end dataflow4;

## Slide 28: Exercise: 3.5: Exercise based on entity eqb_comp4
library IEEE; --Vivado 14.4
use IEEE.STD_LOGIC_1164.ALL;
entity eqb_comp4 is
port (a, b: in std_logic_vector(3 downto 0);
equals,bigger: out std_logic);
end eqb_comp4;
architecture dataflow4 of eqb_comp4 is
begin
equals <= '1' when (a = b) else '0';--concurrent
bigger <='1' when (a > b) else '0';--concurrent
end dataflow4;
(a) When will lines
equals <= '1' when (a = b) else '0';
bigger <='1' when (a > b) else '0';
Answer: ___________________________________

## Slide 29: Exercise3.6 : Draw the schematic of this code
library IEEE; --Vivado 14.4
use IEEE.STD_LOGIC_1164.ALL;
entity abc is
port (a, b,c: in std_logic;
y: out std_logic);
end abc;
architecture abc_arch of abc is
signal x : std_logic;
begin
x <= a nor b;
y <=x and c;
end abc_arch;

## Slide 30: (3) Behavioral design description method {Using Process( ) }
1. Structural
(parallel)
Use port map
2. Data Flow
(parallel)
Use concurrent
statements
3. Behavioral
(serial)
Use process
Design
description

## Slide 31: Behavioral design is sequential the keyword is ‘process’
Sequential, inside a process
Just like a sequential program
the main character is
  ‘process(sensitivity list)’

## Slide 32
library IEEE; --vivado14.4
use IEEE.STD_LOGIC_1164.ALL;
entity eqcomp4 is port(
port (a, b: in std_logic;_vector(3 downto 0)
equals: out std_logic);
end eqcomp4;
architecture behavioral of eqcomp4 is
begin
comp: process (a, b)
begin
if a = b then
equals <= '1';
else
equals <= '0';
end if;
end process;
end behavioral;
Behavioral design:
It is sequential,
the keyword
is ‘process’
sequential execution
like a sequential
software program

## Slide 33: Exercise 3.7: Exercise based on eqcomp4
(a) When will the line containing process( ), be executed?
  Answer:
  ________________
  ________________
(b) When will lines after process ( ) begin be executed?
  Answer:
  _______________
library IEEE; --vivado14.4 ok
use IEEE.STD_LOGIC_1164.ALL;
entity eqcomp4 is port(
a,b:in std_logic_vector(3 downto 0);
equals: out std_logic);
end eqcomp4;
architecture behavioral of eqcomp4 is
begin
comp: process (a, b)
begin
if a = b then
equals <= '1';
else
equals <= '0';
end if;
end process; end behavioral;

## Slide 34: Concurrent VS sequential
Every statement inside the architecture body is executed concurrently, except statements enclosed by a process.
Process
  Statements within a process are executed sequentially. Result is known when the whole process is complete.
  You may treat a process as one concurrent statement in the architecture body.
  Process(sensitivity list): when one or more signals in the sensitivity list change state, the process executes once.

## Slide 35: DESIGN CONSTRUCTIONS
Concurrent and sequential

## Slide 36: Design constructions
Concurrent: statements that can be stand-alone
  When-else
  With-select-when
Sequential: statements that can only live inside processes
  Case-when
  for–in-to-loop
  If-then-else
sequential -- with processes
Concurrent sequential -- NO process

## Slide 37: Design constructions Concurrent statements
Design
constructions
Concurrent
stand-alone
  (No process)
Sequential
statements live in
processes( )
when else
with select when
  Case-when
for-in-to-loop
  if-then-else

## Slide 38: Concurrent: statements that can stand-alone
(concurrent 1) when-else
(concurrent 2) with-select-when
concurrent -- no process

## Slide 39: When-else : example ‘and-gate’
library IEEE; --vivado14.4 ok
use IEEE.STD_LOGIC_1164.ALL;
entity when_ex is
port (in1, in2 : in std_logic;
out1 : out std_logic);
end when_ex;
architecture when_ex_a of when_ex is
begin
out1 <= '1' when in1 = '1' and in2 = '1' else '0';
end when_ex_a;
concurrent - 1-(when)
And-gate
in1
in2
out

## Slide 40: With-select-when : example ‘and-gate’ again
library IEEE; --vivado14.4 ok
use IEEE.STD_LOGIC_1164.ALL;
entity with_ex is
port (in1, in2 : in std_logic;
out1 : out std_logic);
end with_ex;
-------------------------------------------------
architecture with_ex_a of with_ex is
begin
with in1 select
out1 <= in2 when '1',--means when in1='1'
'0' when others;--means other cases out1 <='0'
end with_ex_a;
concurrent - 2(with)
And-gate
in1
in2
out

## Slide 41: Design constructions Sequential statements
Design
constructions
Concurrent
stand-alone
  (No process)
Sequential
statements live in
processes( )
when else
with select when
  Case-when
for-in-to-loop
  if-then-else

## Slide 42: Process( sensitivity list of signals) for sequential execution
library IEEE; --vivado14.4 ok
use IEEE.STD_LOGIC_1164.ALL;
entity conc_ex is
port (in1, in2 ,in3: in std_logic;
out1,out2 : inout std_logic);
end conc_ex;
architecture for_ex_arch of conc_ex is
begin
process (in1, in2) -- execute once when the signals
--in the sensitivity list (I.e. in1 or in2) change state
begin
out1 <= in1 and in2;
-- : can add more lines here if you wish to
end process;
out2 <= out1 and in3; -- concurrent statement
end for_ex_arch;
**the process (9-14) and line 15 are concurrent
in1
in2
in3
out1
out2

## Slide 43: Sequential: statements that can only live inside processes
  (Sequential 1) Case-when
  (Sequential 2) for-in-to-loop
  (Sequential 3) if-then-else
A very important question:
When should a process be executed?
sequential
– within a process

## Slide 44
library IEEE; --tested ise, vivado14.4 ok
use IEEE.STD_LOGIC_1164.ALL;
entity test_case is
port ( in1, in2: in std_logic;
out1,out2 : out std_logic);
end test_case;
architecture case_arch of test_case is
signal b : std_logic_vector (1 downto 0);
begin
process (b)
begin case b is
when "00"|"11" => out1 <= '0';
out2 <= '1';
when others => out1 <= '1';
out2 <= '0';
end case;
end process;
b <= in1 & in2;
end case_arch;
Exercise 3.8
List the line numbers of the concurrent lines.
Answer: ___________
(b) List the line numbers of the Sequential lines.
Answer: ___________
(c ) Fill in the truth table
Means
implies
-- “00”| “11” means
case “00” or “11”,
b(1) | b(0) | Out1 | Out2
0 | 0 | ?__ | ?__
0 | 1 | ?__ | ?__
1 | 0 | ?__ | ?__
1 | 1 | ?__ | ?__

## Slide 45: Things to remember for Case-when:
Remember:
“=>” means “implies” not “bigger”
all cases must be present, use others to complete all cases
ans:
b(0)
b(1)
out1
out2
Ex-nor

## Slide 46: For-in-to-loop (example invert 4 inputs)
library IEEE; --%ISE tested ok, vivado 14.4 ok
use IEEE.STD_LOGIC_1164.ALL;
entity for_ex is
port (in1: in std_logic_vector(3 downto 0);
out1: out std_logic_vector(3 downto 0));
end for_ex;
architecture for_ex_arch of for_ex is
begin
process (in1)
begin
label_for0 : for i in 0 to 3 loop
out1 (i) <= not in1(i);
end loop;
end process;
end for_ex_arch;
in(3:0)
out(3:0)

## Slide 47: Exercise 3.9 : use of FOR
Rewrite arch1 without a process( ).
1 architecture arch1 of ex1 is
2 begin
3
4
5
6
7
8
9 end for_ex_arch;
1 architecture arch1 of ex1 is
2 begin
3 process (in1)
4 begin
5 lab0 : for i in 0 to 3 loop
6 out1 (i) <= not in1(i);
7 end loop;
8 end process;
9 end for_ex_arch;
?

## Slide 48: If-then-else: example ‘and’
library IEEE; --%ISE tested ok
use IEEE.STD_LOGIC_1164.ALL;
entity if_ex is
port (in1,in2: in std_logic;
out1: out std_logic);
end if_ex;
architecture if_ex_a of if_ex is
begin
process (in1, in2)
begin
if in1 = '1' and in2 = '1' then
out1 <= '1';
else
out1 <= '0';
end if;
end process;
end if_ex_a;
And-gate
in1
out
in2
sequential - 3
if--then-else

## Slide 49: Use of signals and variables
Signals (global)
Variable (live inside processes only)
We will learn more about this in Finite state machines design

## Slide 50: Signal assignment <= Global, concurrent execution
<= signal assignment. Do not confused with the relation operator <= equal or smaller
A1<= B1 or C1
A1 signal must be declared outside a process,
It is a signal representing an internal wire or an in/out/buffer signal in port.
B1
C1
A1

## Slide 51: Variable assignment := Local, sequential execution
Variables can only be declared and used in the sequential part (inside process) of VHDL
local to a process.
:= variable assignment.
A2 := B2 and C2
similar to signal assignment but A2 must be a variable.

## Slide 52: Quick revision
You should know
  Operators and usage
  Architecture design methods
    1) Structural (port map)
    2) Data flow (concurrent statements)
    3) Behavioral (process)
  Use of signals and variables
    Signals assignment use ‘<=‘, Can be used in concurrent and sequential statements
    Variable assignment use ‘:=‘. Can only be used in sequential statements -- inside process() only

## Slide 53: Exercise 3.10, Demo_component.vhdl Design method 1 (structural method): Given the following program a) Draw the circuit diagram of this design b) How many components? c) What are the components and line numbers for them?
--Demo_component.vhdl (ok for ise and vivado v2014.4)
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
-------------------------------------------
entity xxnand2 is
port ( xxin1: in STD_LOGIC; xxin2: in STD_LOGIC;
xxout1: out STD_LOGIC
); end;
architecture xxnand2_arch of xxnand2 is
begin
xxout1 <= xxin1 nand xxin2;
end xxnand2_arch;
--entity xnand2 is
-------------------------------------------
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
entity xxnor2 is
port ( xxin1: in STD_LOGIC; xxin2: in STD_LOGIC;
xxout1: out STD_LOGIC
); end;
architecture xxnor2_arch of xxnor2 is
begin
xxout1 <= xxin1 nor xxin2;
end xxnor2_arch;
--------------------------
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
entity xnandnor2 is --
port ( in1: in STD_LOGIC; in2: in STD_LOGIC;-- arithmetic functions with Signed or Unsigned values
in3: in STD_LOGIC; out1: out STD_LOGIC--use IEEE.NUMERIC_STD.ALL;
); end xnandnor2;
architecture xnandor2_arch of xnandnor2 is
component xxnand2 --create components--library UNISIM;
port (xxin1,xxin2: in std_logic; xxout1: out std_logic); --use UNISIM.VComponents.all;
end component ;
component xxnor2-- Port ( );
port (xxin1,xxin2: in std_logic; xxout1: out std_logic);
end component ;
signal con1_signal: std_logic;
begin
label1: xxnand2 port map (in1, in2, con1_signal);
label2: xxnor2 port map (not con1_signal, in3, out1);
end xnandor2_arch;
-------------------ccccccccccccccccc-------------------------------

## Slide 54: Exercise 3.11
How many signal lines are in “equals”?
How many signal lines are in a and b?
In line 9, comp: process (a, b), describe the meaning of each word.
List the sensitivity list of process:comp
When will the process be executed?
Originally a =b=“000”, then a=“001”, what will the hardware do?
library IEEE; %vivado 2014.4 tested
use IEEE.STD_LOGIC_1164.ALL;
entity eqcomp4 is port(
a, b:in std_logic_vector(2 downto 0);
equals: out std_logic);
end eqcomp4;
architecture behavioral of eqcomp4 is
begin
comp: process (a, b)
begin
if a = b then
equals <= '1';
else
equals <= '0';
end if;
end process;
end behavioral;

## Slide 55: Exercise 3.12 Design constructions Concurrent statements Fill in the Blanks
Design
constructions
Concurrent
stand-alone
  (No process)
Sequential
statements live in
processes( )
?______
?_____
  ?____
?______
  ?_____
Key words you may choose from
:
for-in-to-loop
with select when
when else
Case-when
if-then-else

## Slide 56: Exercise 3.13:When-else : example ‘and-gate’ Fill in the blank in line 8 using when else
1 entity when_ex is
2 port (in1, in2 : in std_logic;
3 out1 : out std_logic);
4 end when_ex;
5
6 architecture when_ex_a of when_ex is
7 begin
8____________________________? Using when -else
9 end when_ex_a;
concurrent - 1-(when)
in1
in2
out

## Slide 57: Exercise 3.14 : State which lines are concurrent and which lines are sequential
architecture for_ex_arch of for_ex is
begin
outx1 < = out1 and in3;
process (in1, in2) -- execute once when the signals
begin
out1 <= in1 and in2;
:
end process;
outx2 < = out1 or in3;
end for_ex_arch;