## Slide 1: Omni-wheel Car Additional Documentation

## Slide 2: Purpose
To help student bridging their knowledge in the lecture to the car they have to build
To provide a clear documentation of all necessary details to students + teaching assistants + mentors

## Slide 3: Contents
Mechanism of the Car
Overview of the Skeleton Code
State Diagram
State Transition Conditions
Receiving Joystick Input
Receiving Light Input
Debug board
TODO list for students

## Slide 4: Mechanism of the Car (1)
We always use top view to present the car in this set of slides
When view from outside of the card, each motor can be controlled to move:
  Clockwise (-ve speed)
  Counter-clockwise (+ve speed)
M2
M1
M3

## Slide 5: Mechanism of the Car (2)
To simplify handling [1], the controls are:
Linear movement of six directions:
Self-rotations:
[1] The formal way to control a omni-wheel car involves computing the compound force and the total torque from each motor.
M2
M1
M3

## Slide 6: Mechanism of the Car (3)
As an example, moving forward would means:
  M1.set(-255);
  M2.set(0);
  M3.set(255);
M2
M1
M3
NO MOVE
CLOCKWISE
ANTI- CLOCKWISE
The speed: -255 to 255

## Slide 7: Mechanism of the Car (4)
How should the wheels move for each of these movements?
M2
M1
M3
M2
M1
M3
M2
M1
M3
M2
M1
M3
M2
M1
M3
M2
M1
M3
M2
M1
M3
M2
M1
M3
Check Lab7 material
Pls do these 2 on your own

## Slide 8: Overview of the Skeleton Code (1) Work-sharing between functions
setup() – initialize what the program requires
loop() – main loop of the car
  BluetoothCom() – read a command from the bluetooth
  SetDevice() – interpret the command read
  StateMachine() – state machine when the car is in remote control mode
  LightControl() – state machine when the car is in light control mode
  setLED() – change the LED by setting values into pLEDpattern[]
  updateMotor() – internal-state management of the motor interface
  updateLED() – read pLEDpattern[] and send hardware commands
    getCode() – convert character to 7-segment on/off values
  slowDown() – a fixed delay for the car to execute the motor moves for some time
Students are allowed to edit the bold-typed functions

## Slide 9: Overview of the Skeleton Code (2) Motor interface
To prevent bad things due to sudden change of speed[2], a motor interface is provided.
Initialize (already done before setup())
  setProperties() – set the minimum, maximum speed and the “step” value, which is the limit of change of speed per time-step.
Functions Exposed to the Students
  set() – set the speed we want it to have
  getSpeed() – get the speed the motor currently is running at
Other Function
  update() – declare a time-step to the interface.
[2] such as skidding, burn of parts due to back EMF, etc.

## Slide 10: Remote Control
Your remote control looks like this (unless you are using the Android app)
Joystick
Power Switch
9 buttons
Dec Max Speed | Dec Acceleration | Inc Acceleration
Inc Max Speed | Light Following Mode START | Light Following Mode STOP
Stop Robot | CCW Rotation | CW Rotation

## Slide 11: Receiving Joystick Input (1)
We want to map joystick input into regions
Each region corresponds to one linear movement or STOP
0 y 255
0 x 255
1
0
2
3
6
5
4

## Slide 12: Receiving Joystick Input (2)
The X-Y axis given by the remote control is different from the X-Y axis used inside StateMachine(). Search for the following lines of code and see how this is handled:
Inside loop()
StateMachine(MotorY, MotorX);
Inside StateMachine(int X, int Y)
X = X-128; if(X==0)X=1; // X cannot be 0.
Y = Y-128; if(Y==0)Y=1;

## Slide 13: Receiving Light Input
Students can add at most 6 LDRs[3]. LDR receives more light gets a higher value from the analogRead().
In LightControl(), the voltage of all LDRs are read into Ai and the maximum is found. If is larger than some threshold, then it corresponds to linear movement towards that direction. Otherwise the car should stop.
The skeleton code gives , which is always true (except when all s are equal). Students may want to change this. Otherwise the car would move randomly when there is no obvious light source.
[3] Reducing the number of LDR needed while still keeping the light control function work well is consider as a bonus task.

## Slide 14: State Diagram
Upon receiving the commands, students are expected to follow the state diagram in the next page.
A textual description of the state transition conditions will also be given after the state diagram.

## Slide 15
STOP (Also initial state)
7 states provided in
StateMachine(int X, int Y)
J = 1
J = 1
J = 1
J = 0
J = 0
J = 0
J = 0
J = 0
J = 0
J = 2
J = 4
J = 4
J = 4
J = 3
J = 3
J = 3
J = 2
J = 6
J = 5
J = 5
J = 6
J = 6
J = 2
J = 5
CCW rotation button pressed and all motors have speed 0
CW rotation button pressed and all motors have speed 0
Stop rotation button pressed
Stop rotation button pressed
J: Joystick Input

## Slide 16: State transition conditions
For transitions between linear movements and STOP:
  Joystick stays in the required region
For transitions from STOP to self-rotations:
  The ball is stationary (i.e., getSpeed() of each motor are ZERO)
  The relevant button has been pressed (checking the RobotRot variable)
For transitions from self-rotations to STOP:
  The relevant button has been pressed (checking the RobotRot variable)
Reminder: No direct transitions in-between the two self-rotation states

## Slide 17: “DEBUG” board
To facilitate students’ troubleshooting effort, a debug board is given to the students.
Students could change pLEDpattern[] in setLED(). updateLED() will be called by loop() to display the message onto the debug board.

## Slide 18: TODO list for students
Students will have to do the following:
  JoyStick control – StateMachine()
    Implement the self-rotation states
  Light control
    Test and Find the range of the LDR values
    Implement the details of the FSM for light control