## Slide 1: ENGG1100 Ch6: Introduction To Engineering Design (Digital Logic)
Part 2 of digital logic
KH WONG

## Slide 2: Part 2
  Implementations of logic functions in programs
  Method1: Logic Formula (use of IF-Then-Else)
  Method2: Truth table (Use of Switch-case)
  Examples
  **For both methods, you don’t need to write the full programs, you only need to understand and modify the examples given.
Video link http://www.youtube.com/channel/UCjlkiXFReY2Ubv6WX8m4F8A?feature=watch

## Slide 3: Method 1: to implement logic operations in a program using
  Logic Formula (use of IF-Then-Else)

## Slide 4: Sensors of our robot
Sensors
  S1,S2,S3 each can be ‘1’ or ‘0’
  Magnetic field detected =>Si=0
  No Magnetic field detected =>Si=1
4
S2 S3 S1
The robot is facing you

## Slide 5: Motors of our robot
Motors: LM1, LM2, RM1 and RM2
  Instruction LM1(0) sets LM1 to be 0
  Instruction LM1(1) sets LM1 to be 1
Motor control method
  {LM1=1 and LM2=0}=> Left-motor moves forward
  {LM1=0 and LM2=1} => Left-motor moves backward
  {LM1=0 and LM2=0} => Left-motor stops
  Similar for the right-motor
5
RM1
RM2
LM1
LM2
The robot is facing you

## Slide 6: In the lab : use switches to simulate sensors; use LEDs to simulate motors
Testing hardware setup in our robot system
LM1 is an output for a Light Emitting Diode LED
  When LM1=1 it is on
  When LM1=0 it is off
  Same for LM2,RM1 and RM2 etc
S1 is a switch
  When depressed S1=0
  When released S1=1
  Same for S2,S3 and S4
Simulate sensors S1,S2 etc
Simulate
Motors
LM1,LM2
RM1,EM2

## Slide 7: Programing procedures
Details in the document
  “Document B: A tutorial of how to use the controller board”, of Engg1100 Lab manual 5 from elearninghttps://elearn.cuhk.edu.hk/webapps/login/
Edit program
Compile
Download to the SMART-car-board
Run the program
Demo video in http://www.youtube.com/channel/UCjlkiXFReY2Ubv6WX8m4F8A?feature=watch

## Slide 8: Method 1 (Use of If-then-else): This program will enable the robot to follow the magnetic path
The program segment:
Void loop()
{
LM1(0);LM2(0);RM1(0);RM2(0);
//comment :LM1 =S1 AND S2
If (S1()==1 && S2()==1) LM1(1);
Else LM1(0);
//comment :LM2 = S3 OR S4
If (S3()==1 || S4()==1) LM2(1);
Else LM2(0);
}
Notations used in the program
Void Loop= repeated the execution of the lines
LM1(0) sets the digital output LM1 to 0
LM1(1) sets the digital output LM1 to 1
== means condition
&&= logic operation AND
|| = Logic OR
// comment, for you to put in notes
S2 S1
RM1
RM2
LM1
LM2

## Slide 9: How to use “If” in a program
IF (condition) then output is result 1, else output is result 2
Example1: //just to illustrate the idea, not a runnable program
  If (“you_eat” and “you_drink”) you _can_live;
  Else “you_die”;
Example2: // && means “AND”
  If (S1()==1 && S2()==1) LM1(1);
  Else LM1(0);
  The above program means if S1 is 1 AND S2 is 1, the LM1 will be 1 else LM1 is 0
Example3: // || means “OR”
  If (S3()==1 || S4()==1) LM2(1);
  Else LM2(0);
  The above program means if S3 is 1 OR S4 is 1, the LM2 will be 1 else LM2 is 0

## Slide 10: Exercise1
//LM2 = S3 OR S4
If (S3()==1 || S4()==1) LM2(1);
Else LM2(0);
If (S4()==0 && S1()==1) LM1(0);
Else LM1(1);
Explain in English the meaning of the above statements
  ??

## Slide 11: Method 2 : to implement logic operation in a program using
truth table (Use of Switch-Case)

## Slide 12: Using two sensors S2,S1 to follow a magnetic stripe
Sensors: S2 S1
Magnetic sensors
S1, S2
Terminal
12
S2 S1

## Slide 13: Robot specifications of the sensor input and motor outputs
Inputs:
  S1 S2 are magnetic sensors
    S1 =‘1’ if it detects no magnetic material
    S1 =‘0’ if it detects magnetic material
Outputs for left motor (similar to right motor) :
  LM1, LM2=“10” left motor moves forward
  LM1, LM2=“01” left motor moves backward
  LM1, LM2=“00” or “11” left motor stops
Magnetic sensors
S1, S2
Magnetic stripe
Robot car
Terminal

## Slide 14: Motor control
Motor control outputs for both motors
  Robot forward: LM1, LM2, RM1, RM2=“1010”
  Robot turns right: LM1, LM2, RM1, RM2=“1000”
  Robot turns left: LM1, LM2, RM1, RM2=“0010”

## Slide 15: Exercise2: Truth table example to make our robot follow the magnetic strip
Case
  S2=1, S1=1 (on both sides of magnetic strip): Robot should move forward
  S2=0, S1=1 (robot on the left side of the magnetic strip): Robot should turn right
  S2=1, S1=0 (robot on the right side of the magnetic strip): Robot should turn left
  S2=0,S1=0 (robot reaches the terminal) : Robot should stop
Case | Inputs |  | Outputs |  |  | 
 | S2 | S1 | LM1 | LM2 | RM1 | RM2
1) | 1 | 1 | 1 | 0 | 1 | 0
2) | 0 | 1 | ?__ | ?__ | ?__ | ?__
3) | 1 | 0 | ?__ | ?__ | ?__ | ?__
4) | 0 | 0 | ?__ | ?__ | ?__ | ?__
Magnetic strip
S1 S2
S1 S2
S1 S2
forward:LM1, LM2, RM1, RM2=“1010”
turn right:LM1, LM2, RM1, RM2=“1000”
turn left:LM1, LM2, RM1, RM2=“0010”
S1 S2
Fill in the table
Robot

## Slide 16: Add another sensor at the front to detect the target object
Sensors: S2 S1 facing the ground for following the to follow the magnetic stripe
S3 is used to detect the target object
  S3=1 if no object is detected
  S3=0 if an object is detected
Magnetic sensors
S1, S3 S2
16
S2 S3 S1

## Slide 17: Use of “Switch – case” in a program
You may treat it as a table lookup method
In English it means:
  If INPUT is code1, result 1 will occur
  If INPUT is code2, result 2 will occur
  If INPUT is code3, result 3 will occur
  Etc……
switch (INPUT)
{
case code1 : result 1;
break;
case code2 : result 2;
break;
case code3 : result 3;
break;
:
}

## Slide 18: Program example for our robot You only need to edit the program to change the desired truth table
The program segment that produces the truth table on the right
void LogicTable()
{
// S4,S3,S2,S1 are the least significant 4 bits of IN_sensor in the program
switch (IN_sensor) // 0b00FEDCBA
{
case 0bxxxxxx11 : LM1(1);LM2(0);RM1(1);RM2(0);
break;
case 0bxxxxxx10 : LM1(1);LM2(0);RM1(0);RM2(0);
break;
case 0bxxxxxx01 : LM1(0);LM2(0);RM1(1);RM2(0);
break;
  default : LM1(0);LM2(0);RM1(0);RM2(0);
break;
}
}
Inputs |  | Outputs |  |  | 
S2 | S1 | LM1 | LM2 | RM1 | RM2
0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 1 | 0
Magnetic sensors
S1, S3 S2
S2 S3 S1

## Slide 19: To be done in the lab : Lab5.ino from https://elearn.cuhk.edu.hk/webapps/login/
Experiment 1.3: Fill in the truth table of the AND logic function after you completed the following procedures. (Hardware experiment is required for this and the following exercises)
//program segment in the main loop of Lab5.ino
void loop()
{ // Experiment 1.3 OUT1=S1 AND S3
if(Din1() && Din3()) Out1(1);
else Out1(0);
:
}
Din1 () , Din(3)
LED to represent OUT1()
Inputs |  |  |  | Outputs Q | 
S3 | S1 | LED3 | LED1 | LED7 | Out1
0 | 0 | ON | ON |  | 
0 | 1 | ON | OFF |  | 
1 | 0 | OFF | ON |  | 
1 | 1 | OFF | OFF |  | 

## Slide 20: Appendix1: Answer for the exercise1
//LM2 = S3 OR S4
If (S3()==1 || S4()==1) LM2(1);
Else LM2(0);
If (S4()==0 && S1()==1) LM1(0);
Else LM1(1);
Explain in English the meaning of the above statements
  ?? ans: if S3 is 1 OR S4 is 1 LM2 is 1, else LM2 is 0
  ans: if S4 is 0 AND S1 is 1 LM1 is 0, else LM2 is 1

## Slide 21: Appendix2: Answer: Exercise 2:Truth table example to make our robot follow the magnetic strip
Case
  S2=1, S1=1 (on both sides of magnetic strip): Robot should move forward
  S2=0, S1=1 (robot on the left side of the magnetic strip): Robot should turn right
  S2=1, S1=0 (robot on the right side of the magnetic strip): Robot should turn left
  S2=0,S1=0 (robot reaches the terminal) : Robot should stop
Case | Inputs |  | Outputs |  |  | 
 | S2 | S1 | LM1 | LM2 | RM1 | RM2
1) | 1 | 1 | 1 | 0 | 1 | 0
2) | 0 | 1 | 1 | 0 | 0 | 0
3) | 1 | 0 | 0 | 0 | 1 | 0
4) | 0 | 0 | 0 | 0 | 0 | 0
Magnetic strip
S1 S2
S1 S2
S1 S2
forward:LM1, LM2, RM1, RM2=“1010”
turn right:LM1, LM2, RM1, RM2=“1000”
turn left:LM1, LM2, RM1, RM2=“0010”
S1 S2
Fill in the table
Robot

## Slide 22: Appendix 3: Reference Main loop of experiment5(lab5.ino) from https://elearn.cuhk.edu.hk/webapps/login/
void loop()
{
// Experiment 1.3 OUT1=S1 AND S3
if(Din1() && Din3()) Out1(1);
else Out1(0);
// Experiment 1.4 OUT3=S1 OR S3
if(Din1() || Din3()) Out3(1);
else Out3(0);
// Experiment 2.1 OUT2=(S2 AND S3) AND S4
if((Din2() && Din3()) && Din4()) Out2(1);
else Out2(0);
// Experiment 2.2 OUT4=(S2 AND S3) OR S4
if((Din2() && Din3()) || Din4()) Out4(1);
else Out4(0);
}

## Slide 23: Appendix 4 Truth table example to make our robot follow the magnetic strip
Inputs |  |  |  | Outputs |  |  | 
S4 | S3 | S2 | S1 | LM1 | LM2 | RM1 | RM2
0 | 0 | 0 | 0 |  |  |  | 
0 | 0 | 0 | 1 |  |  |  | 
0 | 0 | 1 | 0 |  |  |  | 
0 | 0 | 1 | 1 |  |  |  | 
0 | 1 | 0 | 0 |  |  |  | 
0 | 1 | 0 | 1 |  |  |  | 
0 | 1 | 1 | 0 |  |  |  | 
0 | 1 | 1 | 1 |  |  |  | 
1 | 0 | 0 | 0 |  |  |  | 
1 | 0 | 0 | 1 |  |  |  | 
1 | 0 | 1 | 0 |  |  |  | 
1 | 0 | 1 | 1 |  |  |  | 
1 | 1 | 0 | 0 |  |  |  | 
1 | 1 | 0 | 1 |  |  |  | 
1 | 1 | 1 | 0 |  |  |  | 
1 | 1 | 1 | 1 |  |  |  | 
Table 1: Truth Table of Smart car control logic