## Slide 1: ENGG1100 Ch7: Introduction To Engineering Design (Digital Logic)
Part 3 of digital logic
KH WONG

## Slide 2: Part3
Use a finite state machine to control the robot

## Slide 3: Overview
Understanding finite state machines
3a) A simple finite state machine (no sensor)
  E.g.: The dancing robot
3b) An finite state machine uses 2 sensors
  E.g. The robot that follows the magnetic strip
3c) A finite state machine uses 3 sensors
  E.g. Follow the magnetic strip, find the CAN and stop

## Slide 4: Understanding finite state machines
Example of a door
  State
  Transition
  Transition condition
  Entry action
http://en.wikipedia.org/wiki/State_diagram

## Slide 5: Example in life
State of a student at CUHK
Start: go to state 1
State 1=Year 1:
  entry action: register 12 courses
  Transition: go to state 2 after 1 year
State 2=Year 2:
  entry action: register 12 courses
  Transition: go to state 3 after 1 year
State 3=Year 3:
  entry action: register 12 courses
  Transition: go to state 4 after 1 year
State 4=Year 4:
  entry action: register 8 courses and Final_year_project
  Transition: go to stop after 1 year
Stop: Graduation

## Slide 6: 3a) The simple state machine (no transition condition )
The robot that dances with a pattern
  Forward 2 seconds, turn left 2 seconds and turn right 2 seconds, stops and repeat the pattern again
Video demo:
http://youtu.be/iyakbVyoafI

## Slide 7: Simple finite state machine for (3a) : No sensor input (no transition condition)
Entry action:
Move
Forward
Output: LM1,LM2,RM1,RM2=1010
E: Turn
Left
Output: LM1,LM2,RM1,RM2=0010
E:Turn
Right
Output: LM1,LM2,RM1,RM2=1000
Transition: After 2 seconds
E:Stop
Output: LM1,LM2,RM1,RM2=0000
After 2 seconds
After 2 seconds
Transition: After 2 seconds
State1
State2
State3
State4
Start
Entry actions
Transition
Flow diagram
Baisc form

## Slide 8: Implementation of the finite state machine for (3a)
Part of the sample source code is shown below:
switch(state)
{
case STATE1:
LM1=1;LM2=0;RM1=1;RM2=0;SPEED=200; //entry action
DELAY_TIME=2000; // transition :delay 2 seconds
motors(LM1,LM2,RM1,RM2,SPEED,SPEED,DELAY_TIME);
state=STATE2; // next state will be state2
break; //end of the current state
case STATE2:
LM1=0;LM2=0;RM1=1;RM2=0;SPEED=200;DELAY_TIME=2000; // delay 2 seconds
motors(LM1,LM2,RM1,RM2,SPEED,SPEED,DELAY_TIME);
state=STATE3; //next state will be state3
break; //end of the current state
// to be continued on next page
Use of DELAY:
DELAY_TIME=2000
motors(LM1,LM2,RM1,RM2,SPEED,SPEED,DELAY_TIME);
Set motor to run forward with speed=200
System call to ask the motor to work
Exercise: explain the meaning of state 2

## Slide 9: Continue from last page
case STATE3:
LM1=1;LM2=0;RM1=0;RM2=0;DELAY_TIME=2000;
motors(LM1,LM2,RM1,RM2,SPEED,SPEED,DELAY_TIME);
state=STATE4;
break;
case STATE4:
LM1=0;LM2=0;RM1=0;RM2=0;SPEED=200;DELAY_TIME=2000;
motors(LM1,LM2,RM1,RM2,SPEED,SPEED,DELAY_TIME);
state=STATE1;
break;
default: //none of above will be forced to run state4
state=STATE4;
break;
}
Exercises: explain the meaning of state 3 and 4

## Slide 10: 3b) A finite state machine uses 2 sensors (with transition condition)
E.g. The robot that follows the magnetic strip

## Slide 11: Example in life (with transition condition : study hard)
State of a student at CUHK
Start：go to state1
State 1=Year 1:
  entry action: register 12 courses
  Transition: if (study hard) promote to state2 (year2) else go back to state 1
State 2=Year 2:
  entry action: register 12 courses
  Transition: if (study hard) promote to state3 (year3) else go back to state 2
State 3=Year 3:
  entry action: register 12 courses
  Transition: if (study hard) promote to state4 (year4) else go back to state 3
State 4=Year 4:
  entry action: register 12 courses
  Transition: if (study hard) promote to stop(graduation) else back go to state4
Stop: Graduation

## Slide 12: Demo 3b) An finite state machine uses 2 sensors
The robot can follow the magnetic strip
Video Demo:
http://youtu.be/NWHjWrq_VoY
Please refer to the program of demo 3c, Demo 3b and demo3c are using the same program.

## Slide 13: 3c) A finite state machine uses 3 sensors E.g. Follow the magnetic strip, find the CAN and stop
Video Demo : http://youtu.be/JEQkuax7lKE
  The robot finds the CAN using the magnetic strip placed under the testing board and stops
S2
S3
S1
Obstacle
End point
RM1,RM2
LM1,LM2
Start point

## Slide 14: Finite state machine using 3 sensors (s1, s2, s3)with transition conditions for (3c)
Flow diagram
Basic form

## Slide 15: Program 3c (S1, S2, S3 are used) S1, S2 for following the magnetic strip S3 for detecting the CAN
The sample source code (program_segment3) is shown below:
switch(state)
{
case STATE1: // forward for 1 second
LM1=1;LM2=0;RM1=1;RM2=0;
SPEED=200;DELAY_TIME=10;
motors(LM1,LM2,RM1,RM2,SPEED,DELAY_TIME);
//
if ( S3()==1 && S2()==1 && S1()=0 ) state=STATE2;
else if(S3()==1 && S2()==0 && S1()=1) state=STATE3;
else if((S3==0) || (S3()==1 && S2()==0 && S1()=0)) state=STATE4;
break;
case STATE2: //robot turns left
LM1=0;LM2=0;RM1=1;RM2=0;SPEED=200;DELAY_TIME=10;
motors(LM1,LM2,RM1,RM2,SPEED,DELAY_TIME);
//
if ( S3()==1 && S2()==1 && S1()=1 ) state=STATE1; //back to state 1
else if(S3()==1 && S2()==0 && S1()=1) state=STATE3;
else if((S3==0) || (S3()==1 && S2()==0 && S1()=0)) state=STATE4;
break;
If S3=0, a CAN is detected, next state is state4
Move forward for 1 second
Robot Deviated right, goto state 2
Robot Deviated left
goto state 3

## Slide 16
case STATE3: //robot turns right
LM1=1;LM2=0;RM1=0;RM2=0;
SPEED=200;DELAY_TIME=10;
motors(LM1,LM2,RM1,RM2,SPEED,DELAY_TIME);
//
if ( S3()==1 && S2()==1 && S1()=1 ) state=STATE1;
else if(S3()==1 && S2()==1 && S1()=0) state=STATE2;
else if((S3==0) || (S3()==1 && S2()==0 && S1()=0)) state=STATE4;
break;
case STATE4: //stop
  LM1=0;LM2=0;RM1=0;RM2=0;
  SPEED=200;DELAY_TIME=10;
motors(LM1,LM2,RM1,RM2,SPEED,DELAY_TIME);
break;
default: //none of above states
state=STATE4;
LM1=0;LM2=0;RM1=0;RM2=0;
SPEED=200;DELAY_TIME=10;
motors(LM1,LM2,RM1,RM2,SPEED,DELAY_TIME);
break;
}
State4 is the stop state, the robot stops
If S3=0,a CAN is detected
Next state is state4

## Slide 17: Summary
In digital logic part 1,2 & 3, we learned
  What is digital logic
  Digital logic operations represented by
    Digital logic formula method
    Truth table method
    Their implementation methods using programs
  Final state machines
    Theory and implementations
  Use the above to control a robot for specific tasks

## Slide 18: End