## Slide 1: Stem6: smart farming DIY
K.H. Wong
CUHK
Web: http://www.cse.cuhk.edu.hk/~khwong/
Email: khwong@cse.cuhk.edu.hk

## Slide 2: Introduction
What is smart farming?
  Open space
  Lab/factor based
How to build a smart farming lab?
  Equipment
  Techniques
  Cost
  Open sources
Training
Conclusion

## Slide 3: Use of Wifi/Internet
Centralize smart sensing and control
http://www.shop-wifi.com/wireless-sensors/wireless-agriculture

## Slide 4: Case study 1
Saving water, increasing efficiency and reducing the environmental impacts of ornamental plant production practices!
http://www.smart-farms.net/

## Slide 5: Case study 2
Use of
  Ardunio
  Sensors: Rain ,soil moisture
  Electronic valve
  To a feedback system
https://aisel.aisnet.org/isd2014/proceedings2017/ISDevelopment/7/

## Slide 6: Equipment: water drip irrigation
farm water drip irrigation 6v dc solenoid valve
https://www.alibaba.com/product-detail/farm-water-drip-irrigation-6v-dc_60255165815.html

## Slide 7: Equipment: Moisture sensor
Moisture and nutrient status in the root zone
Rapid monitoring of growing conditions
Calibrations for many soils and substrates
https://www.delta-t.co.uk/product/wet-2/
Click for video

## Slide 8: Combine Solar power with farming
Saving space and fossil fuel
https://cleantechnica.com/2017/11/24/combining-solar-panels-agriculture-makes-land-productive/

## Slide 9: Lab/factory based
http://emag.directindustry.com/article-long/smart-farming-the-cloud-brings-more-than-rain-to-japanese-farmers/

## Slide 10: Lab/factory based: vertical farming
Vertical farming is becoming important
http://emag.directindustry.com/article-long/smart-farming-the-cloud-brings-more-than-rain-to-japanese-farmers/
https://spectrum.ieee.org/energy/environment/the-green-promise-of-vertical-farms

## Slide 11: LED based farming
LED (Light-emitting diode)
https://sg.rs-online.com/web/generalDisplay.html?id=i/led-lighting

## Slide 12: How to build a smart farming lab?
  Equipment
  Techniques
  Cost
  Open sources

## Slide 13: Equipment
Sensors
  Moisture sensor
LED
  Use of Arduino
Bump
Computer Arduino
https://www.delta-t.co.uk/product/wet-2/
https://learn.sparkfun.com/tutorials/sik-experiment-guide-for-arduino---v32/experiment-4-driving-multiple-leds
https://www.lelong.com.my/mini-diaphragm-water-pump-2l-min-6-to-12v-iot-arduino-littlecraft-183609909-2019-10-Sale-P.htm
  https://en.wikipedia.org/wiki/Arduino
Arduino and LEDs

## Slide 14: Case study 1: Hacker farm
Hacker farm
https://hackerfarm.jp/event/hackerfarm-agriculture-tech-series-vol-2-urban-farming/

## Slide 15: Training
Learn Arduino software
Learn Arduino hardware interface
Learn control methods (algorithms)

## Slide 16: Arduino software
Easy to program , C-like
  Important steps:
    For loop
      void loop() { for (int i=0; i <= 255; i++){ analogWrite(PWMpin, i); delay(10); } }
    Input/output
      analogWrite(PWMpin, i);
    Use “Delay” to control timing
      delay(10);
https://www.arduino.cc/en/Main/Software
With tutorial

## Slide 17: Arduino hardware
Use the development kit to learn hardware/software ,35 USD only (can be cheaper in Taobo)
Use of Breadboard
https://www.amazon.com/Arduino-Ultimate-Starter-Circuit-Learning/dp/B00BT0NDB8

## Slide 18: Arduino driving multiple LEDs
One Arduino computer can driving many LEDs using transistors.
Need to tune the colors to achieve the best farming result
Breadboard
Transistor
LED
resistor

## Slide 19: Arduino driving a water bump
driving a motorized water bump
https://eeenthusiast.com/arduino-plant-watering-drip-feed-system/
A water bump

## Slide 20: Arduino sensor: Water level sensor
Liquid Level Controller Module Water Level Detection Sensor
Circuit Diagram of water level detector
https://www.banggood.com/
http://microcontrollerslab.com
https://www.dhgate.com/

## Slide 21: Control theory
Feedback control theory
E.g,. Control water level
https://en.wikipedia.org/wiki/Control_theory
Required
Water level
R
Motorized bump
Water level sensor: S
Arduino water bump control
Error
Err= R-S

## Slide 22: Example for speed control: PID (proportional-integral-derivative) control
Required speed=
leftRPMset
wheel
Speed
encoder
LeftRPM
+
-
leftRPM
Motor
&
generates PWM
for driver L293
leftPWM
integral control
Igain* leftErr dt
Proportional control
Pgain*leftErr
Derivative control
Dgain*[d(leftErr)/dt]
sum
leftErr
leftPWM
http://www.cse.cuhk.edu.hk/~khwong/www2/ceng2400/2400_16_pid.pptx
Integration in software = addition of two sequential values
Derivation in software = subtraction of two sequential values

## Slide 23: Introduction
Control for better performance
Use PID, choose whatever response you want
Good performance
Criteria depends
on users and
applications
Too much overshoot/undershoot, not stable
Response too slow
time
Motor speed (w)
required

## Slide 24: Exercise 2: Values to evaluate a control system
Describe the terms in the following diagram
Do you want them to be large or small?
Typically
value=10%
Depends
on application
Rise time
Settling time
0
time
Target
value
overshoot
Steady
state
error
undershoot

## Slide 25: Choosing a computer
Arduino
Raspberry pie

## Slide 26: Choosing a computer
Simple student starter projects, use Arduino
More serious projects use Raspberry pie
New Raspberry 3 has Wifi and Blue tooth
Prices of these products are similar
TV
monitor
Arduino
has more interface channels
For heavy computing
For simple computing
Arduino Raspberry Pie
https://www.instructables.com/id/Arduino-Vs-Raspberry-Pi-Which-Is-Better-For-You/
https://hk.element14.com

## Slide 27: Open DIY Projects
Smart farming based agriculture IoT stick is regarded as IoT gadget focusing on live monitoring of environmental data in terms of temperature, moisture and other types depending on sensors integrated with it. Agricultural IoT stick provides the concept of "plug & sense" in which farmers can directly implement smart farming by as such putting the stick on the field and getting live data feeds on various devices like smartphones, tablets etc. and data generated via sensors can be easily shared anywhere and viewed by agriculture consultants remotely via cloud computing technology.
  Smart monitoring only
  Give enough construction steps
  s://www.instructables.com/id/IoT-Based-Smart-Farming-Stick-Using-Arduino-and-Cl/

## Slide 28: Other DIY projects
https://www.kickstarter.com/projects/sunair/smartplant-pi-smart-garden-with-your-raspberry-pi
https://create.arduino.cc/projecthub/projects/tags/agriculture
https://www.banggood.com/
  2pcs Automatic Drip Irrigation Water Seepage Device Watering System Sprinklers Self Watering
  Intelligent Automatic Flowers Watering Timer House Garden Water Timer
  DIY 12V Automatic Watering Module Kit Soil Moisture Sensor With Time Delay (HKD25)

## Slide 29: Suggestions from https://www.amazon.com/
Learn Arduino
  E.g. Elegoo EL-KIT-008 Mega 2560 Project The Most Complete Ultimate Starter Kit w/TUTORIAL for Arduino UNO Nano (from or raspberry pie
  E.g. reenove Ultimate Starter Kit for Raspberry Pi | Beginner Learning | Model 3B+ 3B 2B 1B+ 1A+ Zero W | Python, C, Java, Processing | 57 Projects, 401 Pages Detailed Tutorials, 220+ Components
    Many comparable products elsewhere and may be cheaper
  Learn basic electronics: Ohms law (Voltage = Current X Resistor), power, have a good sense of current and power relation.
  Follow the tutorial study how to use them
  Warning: safe when using batteries, be careful if you are using the 220V main power.

## Slide 30: Suggested projects
Build a moisture monitor system
  Generate plots of data vs time
Build an irrigation system
  Grow something using solid or water
Build an LED based smart farming system
  Change LED color composition (mixing 3 different color LEDs (Red, green, blue) by using pulse-width-modulation PWM method) and see the farming results.

## Slide 31: Experiments test6.1 Soil Moisture Sensor
// test6.1.ino
#include <LiquidCrystal.h> //2020.6.17 khw
//lcd display is optional, use serial com to monitor outout
///https://www.electronicshub.org/interfacing-soil-moisture-sensor-with-arduino/
const int rs = 7, en = 6, d4 = 5, d5 = 4, d6 = 3, d7 = 2;
LiquidCrystal lcd(rs, en, d4, d5, d6, d7);
int j=0;
int prev=0;
int pres=0;
void setup()
{
lcd.begin(16, 2);
lcd.setCursor(0,0);
lcd.print(" Soil Moisture ");
Serial.begin(9600);
}
void loop()
{
j=analogRead(A0);
j=map(j,0,982,148,0);
pres=j;
if(j>100)
j=100;
else if(j<0)
j=0;
lcd.setCursor(6,1);
lcd.print(j);
lcd.print("% ");
prev=j;
Serial.println(j);
delay(500);
}

## Slide 32: End
Thank you!