## Slide 1: Chapter 3: Image processing and computer vision Edge detection and image filtering
by K.H. Wong,
Computer Science and Engineering Dept. CUHK
khwong@cse.cuhk.edu.hk

## Slide 2: Introduction:
You will learn
Edge detection by differentiation and threshold
The Convolution math tool
Edge mask : edge detection by convolution
Image Filtering: smoothing, high pass etc.
Laplacian method : 2nd order derivative method.
  Laplacian of Gaussian :LOG smoothing and edge detection together
Canny Edge Detection: Most popular method

## Slide 3: Topics
Edge detection
  First order derivative G(I)
  Second order derivative 2I
A gray level image I
has many sharp edges

## Slide 4: What are edges and why we need them?
Features have many applications: recognition, tracking etc.
The most common are
  Point edges
    Shape intensity change positions
  Boundary edges
    Shape intensity changing lines

## Slide 5: Sobel Demo
http://www.youtube.com/watch?v=z_a6e30aOXo

## Slide 6: Edge detection
Demo
https://www.youtube.com/watch?v=UMsJNC3dCIA

## Slide 7: Application of edges
Lane detection
http://www.youtube.com/watch?v=Al4DnNkZUeA&feature=related
http://www.youtube.com/watch?v=9F3_6xL8hEY&feature=related

## Slide 8: How to obtained edges?
Use gradient G of intensity [I(x,y)] change, two methods
First order gradient
  I(x,y) is an edge if
Second order gradient (Laplacian operator)
  I(x,y) is an edge if
x
y
I(x,y)
I(x,y+1) I(x+1,y+1)
I(x,y) I(x+1,y)
Notes: \documentclass{article}
\usepackage{amsmath}
\begin{document}
edge, Slide 8\\
\begin{flalign}
\label{eq4}
\begin{aligned}
\sqrt{nm}\\
|G(x,y)|&= \sqrt{ \frac{\partial I(x,y)}{\partial x} + \frac{\partial I(x,y)}{\partial x} }
\geq \text{Threshold}\\
\nabla^2I(x,y)&= \frac{\partial I(x,y)}{\partial x} + \frac{\partial I(x,y)}{\partial x}=0
%%%%%%%%%%%%
%|G(I(x,y)|=\sqrt(\left( \frac{\partial I(x,y)}{\partial x} = \frac{\partia I(x,y)}{\partial y} \right) ))
%|G(I(x,y)|=\sqrt(\left( \frac{\partial I(x,y)}{\partial x} = \frac{\partia I(x,y)}{\partial y} \right) ))
%G(I(x,y)=\sqrt((Z\right) )
\end{aligned}
\end{flalign}
\end{document}

## Slide 9: Edge detection using First order gradient G > threshold
Edges are at positions of rapid change of intensity levels
If (intensity gradient G(I(x,y))> threshold)
{
pixel(x,y) is an edge point;
}
First order derivative
I(x,y)
G[I(x,y)] > threshold, Pixel position (x,y) has an edge

## Slide 10: Edge detection using second order gradient 2I=0
Edges are at 2I =0
If (intensity gradient 2I =0)
{
pixel(x,y) is an edge point;
}
I(x,y)
G[I(x,y)]> threshold is an edge
2I(x,y)= 0 is an edge
First order derivative
(gradient of I(x,y))
Second order derivative
(gradient of gradient of I(x,y))
x
I(x,y)
x
x

## Slide 11: Practical computational methods (discrete method for finding first order gradient)
First order gradient operators
  Roberts operator
  Prewiit operator
  Sobel operator

## Slide 12: Convolution method
Convolution is an important and popular technique in signal processing
Edges can be found by convoluting an image with a mask

## Slide 13: Gradient calculation by convolution*
Differentiate an image I w.r.t x
G(I)=gradient of I= dI/dx
It is the same as
dI/dx  (d/dx)*I
*=Convolution operator
Gradient mask
Or filter mask

## Slide 14: Assume Gx,Gy are separable, the total gradient Gm becomes
Horizontal gradient =Gx(i,j)= h_x * I(i,j)
vertical gradient= Gy(i,j)= h_y * I(i,j),
* is the
convolution operator
Horizontal
direction
vertical
direction
An edge is found
and direction is tan-1(Gy/Gx)=e
e

## Slide 15: What is convolution ? Discrete convolution C=I*h
By definition (http://en.wikipedia.org/wiki/Convolution)
X=multiplication
*=convolution
Notes: \begin{flalign}
\label{eq:convolution_01}
\begin{aligned}
C(m,n)=
\sum_{j=-\infty}^{j=\infty}
\sum_{k=-\infty}^{j=\infty}
h(m-j,n-k) \times I(j,k)
%%%%%%%%%%%%
\end{aligned}
\end{flalign}\\

## Slide 16: Convolution is
Commutative : g(n)*h(n)=h(n)*g(n)
associative: {x(n)*g(n)}*h(n)=x(n)*{h(n)*g(n)}
Distributive
x(n)*{g(n)+h(n)}=x(n)*g(n)+x(n)*h(n)
Application: edge finding
In practice : only accept convoluted values obtained when edge mask and image are fully overlapped.

## Slide 17: 1-D convolution examples
Example 1
Example 2
http://en.wikipedia.org/wiki/Convolution

## Slide 18: Another demo
http://www.fourier-series.com/fourierseries2/flash_programs/Convolution/index.html

## Slide 19: We first learn discrete (cross) correlation
h=[1 3 4
2 7 1
0 5 2]
F=[4 1
2 7]
G =
convulve(h*F)
7 23 34 8
15 60 37 18
2 50 53 8
0 5 22 8
1*4+2*2+3*1+7*7=60
0*1=0
4*0+5*1=5
4*5+2*1=22
https://www.youtube.com/watch?app=desktop&v=C3EEy8adxvc
1 | 3 | 4
2 | 7 | 1
0 | 5 | 2
4 | 1
2 | 7
4 | 1
2 | 7
4 | 1
2 | 7
4 | 1
2 | 7

## Slide 20: Discrete convolution: Correlation is more intuitive
so we use correlation of the flipped version of h to implement convolution[1]
correlation
convolution
Flipped h
Notes: \documentclass{article}
\usepackage{amsmath}
\begin{document}
edge, Slide 20\\
\begin{flalign}
\label{eqxx}
\begin{aligned}
C(m,n)=\sum_{j=-\infty}^{j=\infty}\sum_{k=-\infty}^{k=\infty}{h(m-j,n-k)\times I(j,k)}\\
=\sum_{j=-\infty}^{j=\infty}\sum_{k=-\infty}^{k=\infty}{h^{(flip)}(-m+j,-n+k)\times I(j,k)}
\end{aligned}
\end{flalign}
\end{document}

## Slide 21: Matlab (octave) code for convolution
I=[1 4 1;
2 5 3]
h=[1 3 ;
2 -4]
conv2(I,h)
pause
disp('It is the same as the following');
conv2(h,I)
pause
disp('It is the same as the following');
xcorr2(I,fliplr(flipud(h)))
-4 | 2
3 | 1
Flipped h=h(flip)=

## Slide 22: Steps to find C(m,n)
Step1:
C(0,0)
=2x2=4
Step 2:
C(1,0)
= -4*2+2*5=2
Step 3:
C(2,0)
= -4*5+2*3
=-14
Step 4:
C(3,0)
= -4*3
=-12
1 | 4 | 1
2 | 5 | 3
1 | 4 | 1
2 | 5 | 3
-4 | 2
3 | 1
1 | 4 | 1
2 | 5 | 3
1 | 4 | 1
2 | 5 | 3
-4 | 2
3 | 1
C(m,n)=
C(0,0) | C(1,0) | C(2,0) | C(3,0)
C(0,0) | C(1,0) | C(2,0) | C(3,0)
C(0,0)=4 | C(1,0)=2 | C(2,0)=-14 | C(3,0)=-12
Flipped h
-4 | 2
3 | 1
-4 | 2
3 | 1

## Slide 23: Steps continue
Step 5:
C(0,1)
=1*2+2*1
=4
Step 6:
C(1,1)
= 1*-4+2*3+4*2+5*1
=15
Step 7:
C(2,1)
= -4*4+5*3+1*2+3*1
=4
Step 8:
C(3,1)
= -4*1+3*3
=5
1 | 4 | 1
2 | 5 | 3
-4 | 2
3 | 1
1 | 4 | 1
2 | 5 | 3
-4 | 2
3 | 1
1 | 4 | 1
2 | 5 | 3
-4 | 2
3 | 1
1 | 4 | 1
2 | 5 | 3
-4 | 2
3 | 1
C(m,n)=
C(0,2) | C(1,2) | C(2,2) | C(3,2)
C(0,1)=4 | C(1,1)=15 | C(2,1)=4 | C(3,1)=5
C(0,0)=4 | C(1,0)=2 | C(2,0)=-14 | C(3,0)=-1

## Slide 24: Find all elements
m
n
m
n
C(m,n)
1 | 4 | 1
2 | 5 | 3
-4 | 2
3 | 1
1 | 4 | 1
2 | 5 | 3
-4 | 2
3 | 1
1 | 4 | 1
2 | 5 | 3
-4 | 2
3 | 1
1 | 4 | 1
2 | 5 | 3
-4 | 2
3 | 1

## Slide 25: Cmsc5711, Worksheet 3.1
x=[2 6 7;
4 6 9
1 3 2]
h=[1 -2
-3 4]
Z=x*h ; % * is the convolution operator
Find z. (Fully overlapping and half overlapping of x and h are considered, this is the formal definition of convolution)
What is the size of Z?
What is the value of h*x?
Multiple choice question
Answer 1: Z=
1 2 -5 -14
-2 -12 0 10
-11 -1 -7 32
-3 -5 6 8
Answer 2: Z=
2 2 -5 -14
-2 -12 0 10
-11 -1 -7 32
-3 -5 6 8
Answer 3: Z=
3 5 -5 -14
-2 -12 0 10
-11 -1 -7 32
-3 -5 6 8
Hints:
h after 2D flip is
flipud(fliplr(h))=
4 -3
-2 1
Which answer is correct?

## Slide 26: Answer 3.1
Z=x*h
Find z. (Fully overlapping and half overlapping of x and h are considered, this is the formal definition of convolution):
ANSWER (2) is correct: Z=
2 2 -5 -14
-2 -12 0 10
-11 -1 -7 32
-3 -5 6 8
What is the size of Z? : answer: 4x4
What is the value of h*x (reversed order of h,x)?
Same as z
%Matlab
x=[2 6 7;
4 6 9
1 3 2]
h=[1 -2
-3 4]
flipud(fliplr(h))
conv2(x,h)
conv2(h,x)
Answer 2 is correct:
ans =
2 2 -5 -14
-2 -12 0 10
-11 -1 -7 32
-3 -5 6 8
Hints:
h after 2D flip is
flipud(fliplr(h))=
4 -3
-2 1

## Slide 27: Worksheet 3.2: Find edge image Gx, Gy using filter masks h_x Horizontal edge mask, h_y Vertical edge mask MC question
h
Answer (1)
Gx=conv2(J,h_x)
%horizonatal edge image
= 0 0 0 0 0 0
0 0 0 0 0 0
0 0 0 0 0 0
0 0 -1 -1 1 1
0 0 -1 -1 1 1
0 0 0 0 0 0
Gy=conv2(J,h_y)
%vertical edge image
ans =
0 0 0 0 0 0
0 0 0 0 0 0
0 0 0 1 1 0
0 0 0 1 1 0
0 0 0 -1 -1 0
0 0 0 -1 -1 0
Answer (2)
Gx=conv2(J,h_x)
%horizonatal edge image
= 0 0 0 0 0 0
0 0 0 0 0 0
0 0 0 0 0 0
0 0 1 -1 1 1
0 0 -1 -1 1 1
0 0 0 0 0 0
Gy=conv2(J,h_y)
%vertical edge image
ans =
0 0 0 0 0 0
0 0 0 0 0 0
0 0 0 -1 1 0
0 0 0 1 1 0
0 0 0 -1 -1 0
0 0 0 -1 -1 0

## Slide 28: Answer5711, 3.2
J=[0 0 0 0
0 0 0 0
0 0 1 1
0 0 1 1]
h_x=[0 0 0
-1 0 1
0 0 0]
h_y=[0 1 0
0 0 0
0 -1 0]
conv2(J,h_x)
conv2(J,h_y)
Answer (1) is correct
Gx=conv2(J,h_x)
%horizonatal edge image
= 0 0 0 0 0 0
0 0 0 0 0 0
0 0 0 0 0 0
0 0 -1 -1 1 1
0 0 -1 -1 1 1
0 0 0 0 0 0
Gy=conv2(J,h_y)
%vertical edge image
ans =
0 0 0 0 0 0
0 0 0 0 0 0
0 0 0 1 1 0
0 0 0 1 1 0
0 0 0 -1 -1 0
0 0 0 -1 -1 0

## Slide 29: Edge direction
Θ(x,y) = tan-1(Gy(x,y) / Gx(x,y))

## Slide 30: Edge mask
Convolution is useful in many image processing applications
For each application what you need is to design a mask for that task
You can use different masks for various applications
  E.g. Edge detection masks
    Prewitt, Sobel etc.
  Image smoothing
  High pass: Edge highlighting

## Slide 31: Other simple 3x3 gradient operators (In practice : only accept convoluted values obtained when edge mask and image are fully overlapped. The size of the image is usually much bigger than the masks)
Two popular operators

## Slide 32: Convolution of a mask to a picture
In theory all overlapped and non-overlapped areas are considered.
But in practice: Non-fully-overlapped areas are usually ignored. Only fully overlapped mask and Image I is considered.
  The effect of this is small
  Size of the convolution result of a 3x3 mask and I1024x768 is (1024-2)x(768-2)
I1024x768 =a 1024x768 image
Mask=3x3
* I

## Slide 33: Edge detection procedure
Input: Image I() , h_A, h_B
Output: edge_image edge()
For m=1,..,M
For n=1,…,N
  Find Horizontal gradient =Gx(m,n)= h_A * I(m,n)
  Find vertical gradient =Gy(m,n)= h_B * I(m,n)
  Find overall_edge(m,n)=Gt(m,n)=sqrt{Gx(m,n)2+Gy (m,n)2}
  If ( overall_edge(m,n)>threshold )
edge(m,n) is an edge
  Else
    edge(m,n) is not an edge.
End
End

## Slide 34: Example to find edges, e.g. use Prewitt edge filter on image I
In practice outside or at m=1 and m=M-1 are not considered, because it is where image/mask are not fully overlapped. Same for n.
For m=2..,M-2
For n=2..,N-2
  Gx(m,n)=h_A*I(m,n)
  Gy(m,n)=h_B*I(m,n)
  Gt(m,n)=sqrt{Gx(m,n)2+Gy(m,n)2}
  If Gt(m,n)>Threshold
  Edge(m,n)=1, else =0
End
End
done

## Slide 35: Sobel masks
Sobel mask approximation
of a horizontal edge
Sobel mask approximation
of a vertical edge

## Slide 36: Using Sobel edge masks
Example

## Slide 37: Another example

## Slide 38: Find edge of real images (tested on octave too)
%ws3_3b.m find edge image of a real image, (2022.1.19)
%put test.jpg in c:\images\ ,tested ok on octave
clear
ii=imread('c:\\images\\test.jpg');
prew_x=[1 1 1; 0 0 0; -1 -1 -1]
ex=conv2(ii, prew_x);
prew_y=[1 1 1; 0 0 0; -1 -1 -1]
ey=conv2(ii, prew_y);
%If edge image is required:
etemp=sqrt(ex.*ex+ey.*ey);
e=etemp;
threshold=mean(mean(etemp))% set threshold
e(e<=threshold)=0; %< threshold, set to 0
e(e>threshold)=255;%> threshold, set to 255
figure(1),clf
subplot(2,2,1)
colormap(gray(256))
image(ii)
ylabel('real image')
subplot(2,2,3)
colormap(gray(256))
image(e)
ylabel('edge image')

## Slide 39
G(x,y)
GI(x,y) =
0 0 70.7107 60.8276 78.1025 14.1421
0 0 219.2442 465.7403 422.3423 367.7635
0 0 315.7847 612.1511 444.9326 574.8261
0 0 384.0000 765.0000 384.0000 765.0000
0 0 286.2167 637.8001 460.6788 570.1973
0 0 181.0193 460.1239 403.8230 360.6245 Find a formula to relate G(x,y) and ex and ey using the results as shown above
Answer:__________________________?
Question 3.3a)MC question
G(x,y)=sqrt(|ex|+|ey|)
G(x,y)=sqrt(ex^2+ey^2)
G(x,y)=sqrt(ex^0.5+ey^0.5)
Question 3.3a)MC question
Write the edge image (255= edge, 0=no edge) if the threshold is 500.
%Worksheet 3.3: Intensity gradient of an image
ii=[ 0 0 50 10
0 0 128 255
0 0 128 255
0 0 128 255]
prewitt_x =[1 1 1
0 0 0
-1 -1 -1]
prewitt_y =[1 0 -1
1 0 -1
1 0 -1]
ex=conv2(ii, prewitt_x )
ey=conv2(ii, prewitt_y )
ex =
0 0 50 60 60 10
0 0 128 383 383 255
0 0 78 323 323 245
0 0 0 0 0 0
0 0 -128 -383 -383 -255
0 0 -128 -383 -383 -255
ey =
0 0 50 10 -50 -10
0 0 178 265 -178 -265
0 0 306 520 -306 -520
0 0 384 765 -384 -765
0 0 256 510 -256 -510
0 0 128 255 -128 -255
Answer (1) e=
0 0 0 0 0 0
0 0 0 0 0 0
0 0 0 255 0 255
0 0 0 255 0 255
0 0 0 255 0 255
0 0 0 0 0 0
Answer (2) e=
0 0 0 0 0 0
0 0 0 0 0 0
0 0 0 255 255 255
0 0 0 255 255 255
0 0 0 255 255 255
0 0 0 0 0 0

## Slide 40
G(x,y)
GI(x,y) =
0 0 70.7107 84.8528 84.8528 14.1421
0 0 181.0193 541.6438 541.6438 360.6245
0 0 110.3087 456.7910 456.7910 346.4823
0 0 0 0 0 0
0 0 181.0193 541.6438 541.6438 360.6245
0 0 181.0193 541.6438 541.6438 360.6245
Find a formula to relate G(x,y) and ex and ey using the results as shown above
Q3.3a ,anwer2 is correct:_G(x,y)=sqrt(ex^2+ey^2)
Write the edge image (255 =edge, 0= no edge) if the threshold is 500.
Answer:? __
Answer:? __
etemp=sqrt(ex.*ex+ey.*ey);
e=etemp;
threshold=500
e
%threshold=mean(mean(etemp))% set threshold
e(e<=threshold)=0; %< threshold, set to 0
e(e>threshold)=255;%> threshold, set to 255
e=
%Answer: Worksheet 3.3: Intensity gradient of an image
ii=[ 0 0 50 10
0 0 128 255
0 0 128 255
0 0 128 255]
prewitt_x =[1 1 1
0 0 0
-1 -1 -1]
prewitt_y =[1 1 -1
1 0 -1
1 0 -1]
ex=conv2(ii, prewitt_x )
ey=conv2(ii, prewitt_y )
ex =
0 0 50 60 60 10
0 0 128 383 383 255
0 0 78 323 323 245
0 0 0 0 0 0
0 0 -128 -383 -383 -255
0 0 -128 -383 -383 -255
ey =
0 0 50 10 -50 -10
0 0 178 265 -178 -265
0 0 306 520 -306 -520
0 0 384 765 -384 -765
0 0 256 510 -256 -510
0 0 128 255 -128 -255
Q3.3a ,
Answer1 is correct, e=
0 0 0 0 0 0
0 0 0 0 0 0
0 0 0 255 0 255
0 0 0 255 0 255
0 0 0 255 0 255
0 0 0 0 0 0

## Slide 41: Image filtering You may design a mask for Low pass filtering (smoothing filter)
Low pass

## Slide 42: Other image processing operators
Low pass (or called smoothing filter, blurring filter pixel or averaging filter)
This term is to normalize the pixel value after the operation
Notes: \documentclass{article}
\usepackage{amsmath}
\begin{document}
edge, Slide 42\\
\begin{flalign}
\label{eq4}
\begin{aligned}
h_{low_{pass}}=\frac{1}{9}\left[\begin{matrix}1&1&1\\1&1&1\\1&1&1\\\end{matrix}\right],\\
or\ h_{low_pass}=\frac{1}{10}\left[\begin{matrix}1&1&1\\1&2&1\\1&1&1\\\end{matrix}\right],etc
\end{aligned}
\end{flalign}
\end{document}

## Slide 43
Low pass filtering result

## Slide 44
Low pass filtering result

## Slide 45: Smooth an image kernal size is 11x11
%smooth an image ws3_5.m,
%put test.jpg in c:\images\
clear
ii=imread('c:\\images\\test.jpg');
%smooth_kernal=[1 1 1 ; 1 2 1; 1 1 1];
%smooth_kernal=[0.1 0.1 0.1 ; 0.1 0.1 0.1; 0.1 0.1 0.1 ]
smooth_kernal=ones(11,11)
%optional:trust middle element more
%smooth_kernal(5,5)=11*11;
%this is to normalize the pixels
smooth_kernal=smooth_kernal/sum(sum(smooth_kernal))
smooth_ii=conv2(ii, smooth_kernal);
figure(1),clf
colormap(gray(256))
subplot(2,2,1)%----------------------
image(ii)
ylabel('real image')
subplot(2,2,3)%--------------------
image(smooth_ii)
ylabel('smoothed image')

## Slide 46: Worksheet 3.4:Can you comment on what is the function of this convolution?
I*hlp=
0 0 10.0000 20.0000 20.0000 10.0000
0 0 22.0000 54.0000 54.0000 22.0000
0 0 42.0000 96.0000 96.0000 42.0000
0 0 57.5000 135.0000 135.0000 57.5000
0 0 45.5000 116.5000 116.5000 45.5000
0 0 25.5000 51.0000 51.0000 25.5000
MC question:
Find the edge
Smooth the image
Extract features
Notes: \documentclass{article}
\usepackage{amsmath}
\begin{document}
edge, Slide 46\\
\begin{flalign}
\label{eq4}
\begin{aligned}
I=\left[\begin{matrix}0&0&100&100\\0&0&120&120\\0&0&200&200\\0&0&255&255\\\end{matrix}\right],h_{lp}=\left(\frac{1}{10}\right)\left[\begin{matrix}1&1&1\\1&2&1\\1&1&1\\\end{matrix}\right]
\end{aligned}
\end{flalign}
\end{document}

## Slide 47: Answer 3.4:Can you comment on what is the function of this convolution?
I*hlp=
0 0 10.0000 20.0000 20.0000 10.0000
0 0 22.0000 54.0000 54.0000 22.0000
0 0 42.0000 96.0000 96.0000 42.0000
0 0 57.5000 135.0000 135.0000 57.5000
0 0 45.5000 116.5000 116.5000 45.5000
0 0 25.5000 51.0000 51.0000 25.5000
ANSWER2 s correct : It is low pass filtering; the function is to smooth (or blur) the image.
%Matlab
I=[ 0 0 100 100
0 0 120 120
0 0 200 200
0 0 255 255]
h_low_pass=0.1*[1 1 1
1 2 1
1 1 1]
conv2(I,h_low_pass)

## Slide 48: Worksheet 3.5: Example for intensity gradient calculation
Q3.5a: Write a formula to find the direction of the edge image at pixel (x,y).
////// Question 3.5a , MC question /////
Answer1:Θ(x,y) = tan-1(ex(x,y) / ey(x,y))
Answer2 :Θ(x,y) = tan-1(ey(x,y) / ex(x,y))
Q3.5b: Find the edge direction at (x1,y1)
/////// Question 3.5b , MC question ////
Answer1 :Θ(x,y) = atan(265/383)
Answer2 :Θ(x,y) = acos(265/383)
%Given
ii=[ 0 0 50 10
0 0 128 255
0 0 128 255
0 0 128 255]
prewitt_x =[1 1 1
0 0 0
-1 -1 -1]
prewitt_y =[1 0 -1
1 0 -1
1 0 -1]
ex=conv2(ii, prew_x)
ey=conv2(ii, prew_y)
ex=ii*prewitt_x=
0 0 50 60 60 10
0 0 128 383 383 255
0 0 78 323 323 245
0 0 0 0 0 0
0 0 -128 -383 -383 -255
0 0 -128 -383 -383 -255
ey=ii*prewitt_y =
0 0 50 10 -50 -10
0 0 178 265 -178 -265
0 0 306 520 -306 -520
0 0 384 765 -384 -765
0 0 256 510 -256 -510
0 0 128 255 -128 -255
At (x1,y1)
Underlined
cell

## Slide 49: Answer :Worksheet 3.5: Example for intensity gradient calculation
Q3.5a: Write a formula to find the direction of the edge image at pixel (x,y).
////// Question 3.5a , MC question /////
Answer2 :Θ(x,y) = tan-1(ey(x,y) / ex(x,y))
Is correct
Q3.5b: Find the edge direction at (x1,y1)
/////// Question 3.5b , MC //////////////
Answer1 :Θ(x,y) = atan(265/383)= 0.605 rad
Is correct
%Given
ii=[ 0 0 50 10
0 0 128 255
0 0 128 255
0 0 128 255]
prewitt_x =[1 1 1
0 0 0
-1 -1 -1]
prewitt_y =[1 0 -1
1 0 -1
1 0 -1]
ex=conv2(ii, prewitt_x)
ey=conv2(ii, prewitt_y )
ex=ii*prewitt_x=
0 0 50 60 60 10
0 0 128 383 383 255
0 0 78 323 323 245
0 0 0 0 0 0
0 0 -128 -383 -383 -255
0 0 -128 -383 -383 -255
ey=ii*prewitt_y =
0 0 50 10 -50 -10
0 0 178 265 -178 -265
0 0 306 520 -306 -520
0 0 384 765 -384 -765
0 0 256 510 -256 -510
0 0 128 255 -128 -255
At (x1,y1)
Underlined
cell

## Slide 50: A small summary
If you convolve an image I with an edge mask, you get an edge image.
If you convolve an image I with a smoothing mask, you get a smoothed image.

## Slide 51: A more formal smoothing filter is the Gaussian filter
Smoothing_image(I)= Gaussian (I)
= Gaussain_mask*I
How to get the Gaussian mask?
  See following slides
http://en.wikipedia.org/wiki/Normal_distribution
Standard Normal distribution:
Red line, when mean()=0, Sigma ()=1)
Probability density function

## Slide 52: Properties of Gaussian (Normal) distribution
Standard Normal distribution (1-dimension):
Red line, when mean()=0, Sigma ()=1
  At (x-)=0,  =1
  G(x) =1/sqrt(2*pi)=0.3989
At x=1*, drops off to
  (1/sqrt(2*pi))*exp(-1^1/2)=0.2420
  Area covered 68.2%
At x=2*, drops off to
  (1/sqrt(2*pi))*exp(-2^2/2)= 0.0540
  Area covered 95.44%
At x=3*, drops off to
  (1/sqrt(2*pi))*exp(-2^2/2)= ?? (exercise)
  Area covered 99.73%
http://en.wikipedia.org/wiki/Normal_distribution
Probability density function
Standard Normal distribution
Area covered
(total=
100%)
G
G
sets the horizontal shift
Controls the shape
So called 95% confident value µ(+/-)2

## Slide 53: Gaussian (Normal) functions 1D,2D
G(x)
x
y
x

x
y
1-D Gaussian
2-D Gaussian
Notes: %%%%%%%%%%%% slide 54 %%%%%%%%%%%%%%%%%%%%
%%% eeeeee eq:filtering_01A eeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeee
%%%
1st order (A) Gaussian
\begin{flalign}
\label{eq:filtering_01a}
\begin{aligned}
G(x) = \frac{1}
{\sqrt{2\pi{\sigma^2 }}}
e^{-
\frac{(x-\mu)^2}
{2\sigma^2}
}
\end{aligned}
\end{flalign}
%%% eeeeee eq:filtering_01B eeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeee
1st order (B) Gaussian\\
\begin{flalign}
\label{eq:filtering_01b}
\begin{aligned}
G(x) = \frac{1}
{\sqrt{2\pi{\sigma^2 }}}
exp\left({-
\frac{(x-\mu)^2}
{2\sigma^2}
}\right)
\end{aligned}
\end{flalign}
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
%%% eeeeee eq:filtering_02A eeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeee
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
2nd order (A) Gaussian\\
\begin{flalign}
\label{eq:filtering_02A}
\begin{aligned}
G(x,y) =G(x)G(y)= \frac{1}
{{2\pi{\sigma^2 }}}
e^{-
\frac{(x-\mu_x)^2+(y-\mu_y)^2}
{2\sigma^2}
}
\end{aligned}
\end{flalign}
%%%
2nd order (B) Gaussian
%%% eeeeee eq:filtering_02B eeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeee
\begin{flalign}
\label{eq:filtering_02B}
\begin{aligned}
G(x,y) =G(x)G(y)= \frac{1}
{{2\pi{\sigma^2 }}}
exp\left({-
\frac{(x-\mu_x)^2+(y-\mu_y)^2}
{2\sigma^2}
}\right)
\end{aligned}
\end{flalign}

## Slide 54: Intuition of Gaussian (Normal) distribution?
Like you play dart many times (e,g, 1000)
  Aim at (mean_x,mean_y)
  If you are good player , standard deviation () is small. If you are bad, deviation () is large.
  The distribution is the counts of your dart landed at (x,y)
  The distribution is Gaussian --It is governed by mean and Standard Deviation (SD)
http://www.youtube.com/watch?v=2-EPvfFK1zw
x
y
Mean_x
mean_y
Standard
Deviation (SD) ()
(mean_x,mean_y)
Week3

## Slide 55: To generate a discrete (2N+1)x(2N+1) Gaussian mask
Knowing that at +/-3  it drops off to 0.1%
Set Sigma=SD= =N/4 will give a useful Gaussian Mask (it drops off to 0 at borders)
Example: N=10, mask size= (2N+1)x(2N+1) =21x21
=10/4=2.5; Peak2D is at 1/(2*pi*2.5^2)=0.0255
Sum_all_elements=1
function demo_gauss_mask1 %matlab code
clear, N=10
[X,Y]=meshgrid(-N:N,-N:N);sigma =N/4;
G=1/(2*pi*sigma^2)*exp(-(X.^2+Y.^2)/(2*sigma^2));
G=G./sum(G(:)) %normalise it
'sigma is ', sigma
'sum(G(:)) is ',sum(G(:))
'max(max(G(:))) is',max(max(G(:)))
figure(1), clf
surfc(G)

## Slide 56: Example: Gaussian Masks calculated by Matlab
function demo_gauss_mask1b %matlab code
clear, N=2
[X,Y]=meshgrid(-N:N,-N:N);sigma =N/4;
G=1/(2*pi*sigma^2)*exp(-(X.^2+Y.^2)/(2*sigma^2));
G=G./sum(G(:)) %normalise it
'sigma is ', sigma
'sum(G(:)) is ',sum(G(:))
'max(max(G(:))) is',max(max(G(:)))
figure(2), clf
surfc(G)
title ('mask size is 5x5')
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
clear, N=3
[X,Y]=meshgrid(-N:N,-N:N);sigma =N/4;
G=1/(2*pi*sigma^2)*exp(-(X.^2+Y.^2)/(2*sigma^2));
G=G./sum(G(:)) %normalise it
'sigma is ', sigma
'sum(G(:)) is ',sum(G(:))
'max(max(G(:))) is',max(max(G(:)))
figure(3), clf
surfc(G)
title ('mask size is 7x7')
[X,Y]=meshgrid(-2:2,-2:2);sigma =0.5;
5x5 Gussian Mask
[X,Y]=meshgrid(-3:3,-3:3);sigma =0.75;
7x7 Gussian Mask

## Slide 57: Worksheet 3.6
For the 5x5 2-D, Gaussian mask ,
 =0.5
  Calculate the value of G(x,y) when x= y=0 and
    X=-3*,y=0,G(x,y)=_____?
    MC question3.6
    Answer 1: G(x,y)=0.0071
    Answer 2: G(x,y)=0.0862
    Answer 3: G(x,y)=0.3861
    X=-2*,y=0,G(x,y)=_____?
    X=-1*,y=0,G(x,y)=_____?
    X=0*,y=0,G(x,y)=_____?
    X=1*,y=0,G(x,y)=____?
    X=2*,y=0,G(x,y)=____?
    X=3*,y=0,G(x,y)=____?
  Sketch G(x,y=0), assume y=0
-3 -2 -1 0 1 2 3
x
G(x,y=0)
Notes: %%%%%%%%%%%% slide 54 %%%%%%%%%%%%%%%%%%%%
%%% eeeeee eq:filtering_01A eeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeee
%%%
1st order (A) Gaussian
\begin{flalign}
\label{eq:filtering_01a}
\begin{aligned}
G(x) = \frac{1}
{\sqrt{2\pi{\sigma^2 }}}
e^{-
\frac{(x-\mu)^2}
{2\sigma^2}
}
\end{aligned}
\end{flalign}
%%% eeeeee eq:filtering_01B eeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeee
1st order (B) Gaussian\\
\begin{flalign}
\label{eq:filtering_01b}
\begin{aligned}
G(x) = \frac{1}
{\sqrt{2\pi{\sigma^2 }}}
exp\left({-
\frac{(x-\mu)^2}
{2\sigma^2}
}\right)
\end{aligned}
\end{flalign}
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
%%% eeeeee eq:filtering_02A eeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeee
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
2nd order (A) Gaussian\\
\begin{flalign}
\label{eq:filtering_02A}
\begin{aligned}
G(x,y) =G(x)G(y)= \frac{1}
{{2\pi{\sigma^2 }}}
e^{-
\frac{(x-\mu_x)^2+(y-\mu_y)^2}
{2\sigma^2}
}
\end{aligned}
\end{flalign}
%%%
2nd order (B) Gaussian
%%% eeeeee eq:filtering_02B eeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeee
\begin{flalign}
\label{eq:filtering_02B}
\begin{aligned}
G(x,y) =G(x)G(y)= \frac{1}
{{2\pi{\sigma^2 }}}
exp\left({-
\frac{(x-\mu_x)^2+(y-\mu_y)^2}
{2\sigma^2}
}\right)
\end{aligned}
\end{flalign}

## Slide 58: Answer: 3.6
For the 5x5
2-D Gaussian mask ,
 =0.5
  %Calculate the value of G(x,y) when x= y=0,
%matlab, assume y is always at 0 (becomes 2D)
Clear, sigma=0.5 , mean_x=0 , mean_y=0
for (i=1:7)
x=(i-4)*sigma
%will make x=-3,-2,-1,0, 1 ,2 ,2, 3
g(i)=(1/(2*pi*sigma^2))*...
exp(-(x- mean_x)^2/(2*sigma^2))
end
image (1),clf, plot(g)
    Asnwer g(x=-3), g(x=-2), g(x=-1 ), g(x=0), g(x=1 ), g(x=2), g(x=3), =
    g = 0.0071 0.0862 0.3861 0.6366 0.3861 0.0862 0.0071 (left / right mirror image)
58
-3 -2 -1 0 1 2 3
G(x,y) in 2D
MC 3.6
Answer 1: G(x,y)=0.0071
Is correct

## Slide 59: Worksheet 3.7
Fill in the blanks of this Gaussian mask of size 9x9 , sigma ()=2
MC question 3.7
G(mx ,my)= 0.0351
G(mx ,my)= 0.0398
G(mx ,my)= 0.0213
Sketch the function
G(x,y)=
0.0007 0.0017 0.0033 0.0048 0.0054 0.0048 0.0033 0.0017 0.0007
0.0017 0.0042 0.0078 0.0114 0.0129 0.0114 0.0078 0.0042 0.0017
0.0033 0.0078 0.0146 0.0213 0.0241 0.0213 0.0146 0.0078 0.0033
0.0048 0.0114 0.0213 0.0310 0.0351 0.0310 0.0213 0.0114 0.0048
0.0054 0.0129 0.0241 0.0351 ____? ____? 0.0241 0.0129 0.0054
0.0048 0.0114 0.0213 0.0310 0.0351 ____? 0.0213 0.0114 0.0048
0.0033 0.0078 0.0146 0.0213 0.0241 0.0213 0.0146 0.0078 0.0033
0.0017 0.0042 0.0078 0.0114 0.0129 0.0114 0.0078 0.0042 0.0017
0.0007 0.0017 0.0033 0.0048 0.0054 0.0048 0.0033 0.0017 0.0007
x=mx
y=my
x=1+mx
y=my

## Slide 60: Answer: Worksheet 3.7 M.C. 3.7: answer 2: G(mx ,my)= 0.0398 is correct
Fill in the blanks Gaussian mask of size the 9x9 , sigma ()=2
0.0007 0.0017 0.0033 0.0048 0.0054 0.0048 0.0033 0.0017 0.0007
0.0017 0.0042 0.0078 0.0114 0.0129 0.0114 0.0078 0.0042 0.0017
0.0033 0.0078 0.0146 0.0213 0.0241 0.0213 0.0146 0.0078 0.0033
0.0048 0.0114 0.0213 0.0310 0.0351 0.0310 0.0213 0.0114 0.0048
0.0054 0.0129 0.0241 0.0351 0.0398 0.0351 0.0241 0.0129 0.0054
0.0048 0.0114 0.0213 0.0310 0.0351 0.0310 0.0213 0.0114 0.0048
0.0033 0.0078 0.0146 0.0213 0.0241 0.0213 0.0146 0.0078 0.0033
0.0017 0.0042 0.0078 0.0114 0.0129 0.0114 0.0078 0.0042 0.0017
0.0007 0.0017 0.0033 0.0048 0.0054 0.0048 0.0033 0.0017 0.0007
clear %matlab
sigma=2 % in matlab , no -ve index for looping, so shift center to (5,5)
mean_x=5 , mean_y=5
for y=1:9
for x=1:9
g(x,y)=(1/(2*pi*sigma^2))*exp(-((x-mean_x)^2+(y-mean_y)^2) /(2*sigma^2))
end
end
mesh(g)
title('2D Gaussian function')
1/(2*pi*2^2)
1/(2*pi*2^2)*exp(-1/8)
1/(2*pi*2^2)*exp(-2/8)
x=mx
y=my
x=1+mx
y=my

## Slide 61: Result of smoothing an image by a Gaussian filter
Gaussain_filter * I = Guassian_filter (I)
Image I
Guassian_filter (I)

## Slide 62: Laplacian filter
Second order derivative method

## Slide 63: Second order edge detection method
We use gradient G of intensity [I(x,y)] change
First order gradient
I(x,y) is an edge if
Second order gradient (Laplacian operator), I(x,y) is an edge if
x
y
I(x,y)
I(x,y+1) I(x+1,y+1)
I(x,y) I(x+1,y)
Notes: Slide 62 \\
Laplacian method\\
edge, Slide 62\
\begin{flalign}
\label{eq:laplacian_62}
\begin{aligned}
|G(x,y)|&= \sqrt{ \frac{\partial I(x,y)}{\partial x} + \frac{\partial I(x,y)}{\partial x} }
\geq \text{Threshold}\\
\nabla^2I(x,y)&= \frac{\partial I(x,y)}{\partial x} + \frac{\partial I(x,y)}{\partial x}=0\\
\nabla^2I(x,y)&=0
\end{aligned}
\end{flalign}

## Slide 64: Edge detection using second order gradient 2I=0
Edges are at 2I =0
If (intensity gradient 2I =0)
{
pixel(x,y) is an edge point;
}
I(x,y)
G[I(x,y)]> threshold is an edge
2I(x,y)= 0 is an edge
First order derivative
(gradient of I(x,y))
Second order derivative
(gradient of gradient of I(x,y))
x
I(x,y)
x
x

## Slide 65: Result of applying second order filter (Laplacian filter)
Top left: Orginal image. Top right: After Gaussian blur filter. Bottom Left: Apply Laplacian filter on the blurred image. Bottom right: Edge after zero crossing

## Slide 66: 2I calculation by convolution*
Second order derivative of an image I w.r.t x and y
Similar to using a 2nd-order-derivative filter to I
Or convolves a 2nd-order-derivative filter mask with I
  That means: 2I =2*I
When 2I(x,y) =0, it is an edge
=
2nd-order-derivative filter : http://homepages.inf.ed.ac.uk/rbf/HIPR2/log.htm
Notes: %%%%% eq 65 eeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeee
edge, Slide 65\\
\begin{flalign}
\label{eq:laplacian_65}
\begin{aligned}
\nabla^2I(x,y)&=\nabla^2*I(x,y)=\frac{\partial I(x,y)}{\partial x} + \frac{\partial I(x,y)}{\partial y}=\left( \frac{\partial^2}{\partial x^2} \right)*I(x,y) +\left( \frac{\partial^2}{\partial y^2} \right)*I(x,y)\\
&=\begin{bmatrix}
0 &0 &0\\
1 &-2 &1\\
0 &0 &0\end{bmatrix}*I+
\begin{bmatrix}
0 &1 &0\\
0 &-2 &0\\
0 &1 &0\end{bmatrix}*I\\
&=\begin{bmatrix}
0 &1 &0\\
1 &-4 &1\\
0 &1 &0\end{bmatrix}\\
\end{aligned}
\end{flalign}

## Slide 67: Noise removal using Gaussian
2I(x,y) =0 is sensitive to noise (is a problem), so we use 2G(I(x,y)) =0 , smooth first then find edge
In convolution you can
  2G(I(x,y)) = (2G)*I(x,y) =0
  Convolve a Laplacian operator (2G) with I
Idea: Second order differentiation of Gaussian distribution. Combine 2 and G together
  Application: smoothing and edge finding at one go

## Slide 68: LoG (Laplacian of Gaussian) Put smoothing and edge detection together for better performance. Second order differentiation of Gaussian Application: smoothing and edge finding at one go
Gaussian G
First order differentiation of G (Divergence of G) G
Second order differentiation of G (Laplacian of G LOG) 2G
G(x)
x
m
x
G(x)
G(x)
2G(x)
x

## Slide 69: How to get the LOG (Laplacian of Gaussian) mask?
G(x)
x
y
x

x
y
1-D Gaussian
2-D Gaussian
Notes: %%%%%%%%%%%% slide 54/68 %%%%%%%%%%%%%%%%%%%%
%%% eeeeee eq:filtering_01A eeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeee
%%%
1st order (A) Gaussian
\begin{flalign}
\label{eq:filtering_01a}
\begin{aligned}
G(x) = \frac{1}
{\sqrt{2\pi{\sigma^2 }}}
e^{-
\frac{(x-\mu)^2}
{2\sigma^2}
}
\end{aligned}
\end{flalign}
%%% eeeeee eq:filtering_01B eeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeee
1st order (B) Gaussian\\
\begin{flalign}
\label{eq:filtering_01b}
\begin{aligned}
G(x) = \frac{1}
{\sqrt{2\pi{\sigma^2 }}}
exp\left({-
\frac{(x-\mu)^2}
{2\sigma^2}
}\right)
\end{aligned}
\end{flalign}
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
%%% eeeeee eq:filtering_02A eeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeee
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
2nd order (A) Gaussian\\
\begin{flalign}
\label{eq:filtering_02A}
\begin{aligned}
G(x,y) =G(x)G(y)= \frac{1}
{{2\pi{\sigma^2 }}}
e^{-
\frac{(x-\mu_x)^2+(y-\mu_y)^2}
{2\sigma^2}
}
\end{aligned}
\end{flalign}
%%%
2nd order (B) Gaussian
%%% eeeeee eq:filtering_02B eeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeee
\begin{flalign}
\label{eq:filtering_02B}
\begin{aligned}
G(x,y) =G(x)G(y)= \frac{1}
{{2\pi{\sigma^2 }}}
exp\left({-
\frac{(x-\mu_x)^2+(y-\mu_y)^2}
{2\sigma^2}
}\right)
\end{aligned}
\end{flalign}

## Slide 70: 2nd derivative of G (x,y)=2G(x,y) =Laplacian of Gaussian (LoG)
=
Notes: %%%%%%%%%%%% slide 69 %%%%%%%%%%%%%%%%%%%%%
%%% eeeeee eq:filtering_02A eeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeee
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
2nd order (A) Gaussian\\
\begin{flalign}
\label{eq:filtering_02A}
\begin{aligned}
G(x,y) =G(x)G(y)= \frac{1}
{{2\pi{\sigma^2 }}}
e^{-
\frac{(x-\mu_x)^2+(y-\mu_y)^2}
{2\sigma^2}
}
\end{aligned}
\end{flalign}
%%%
2nd order (B) Gaussian
%%% eeeeee eq:filtering_02B eeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeee
\begin{flalign}
\label{eq:filtering_02B}
\begin{aligned}
G(x,y) =G(x)G(y)= \frac{1}
{{2\pi{\sigma^2 }}}
exp\left({-
\frac{(x-\mu_x)^2+(y-\mu_y)^2}
{2\sigma^2}
}\right)
\end{aligned}
\end{flalign}
%%%%% eq 69 eeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeee
%%% eeeeee eq:filtering_69A LOG eeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeee
\begin{flalign}
\label{eq:filtering_69A_LoG}
\begin{aligned}
LoG(x,y) = \frac{1}
{\pi \sigma^4}
\left[1-\frac{x^2+y^2}{2 \sigma^2} \right]
e^{\left({-
\frac{(x)^2+(y)^2}
{2\sigma^2}
}\right)}
\end{aligned}
\end{flalign}
%%% eeeeee eq:filtering_69B LOG eeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeee
\begin{flalign}
\label{eq:filtering_69B_LoG}
\begin{aligned}
LoG(x,y) = \frac{1}
{\pi \sigma^4}
\left[1-\frac{x^2+y^2}{2 \sigma^2} \right]
exp\left({-
\frac{(x)^2+(y)^2}
{2\sigma^2}
}\right)
\end{aligned}
\end{flalign}

## Slide 71: Laplacian of Gaussian (LoG) method -- LoG = 2nd order differentiation mask
2-D Mask
Laplacian of Gaussian (LoG) mask
Looks like a Mexican Hat

## Slide 72: Laplacian of Gaussian (LOG) by excel (cut and paste to excel to view plot)

## Slide 73: Method to reduce noise: Laplacian of Gaussian (LOG) method
Second derivative is sensitive to noise , so smooth it with a Gaussian smoothing filter first
It is like first blurring the image to remove noise then extract edges
LOG mask
http://homepages.inf.ed.ac.uk/rbf/CVonline/LOCAL_COPIES/OWENS/LECT6/node2.html

## Slide 74: Canny Edge Detector
A practical non-linear filtering method
Very popular

## Slide 75: Motivation
Using 1st derivative and 2nd derivative alone are not good enough to locate edges
  1st derivate method gives “thick” edges.
  2nd derivate method gives too much noise--“rings”.
First order method with thresholding is good but too simple. It cannot handle a wide range of images.
  A threshold works for one image usually won’t work for another image.

## Slide 76: Goal
Mark as many real edges as possible.
The detected edges should be as close as the real edges.
All edges are of one pixel width.
Ref: http://en.wikipedia.org/wiki/Canny_edge_detector
Good result obtained by the canny-edge-detector
Source image

## Slide 77: Canny Edge Detector
It is first proposed by John F. Canny in 1986.
Use multiple stages to detect a wide range of edges.
It uses the 1st derivative of an image.
It takes a gray-level image as input.
Still one of the most used edge detectors in the world.

## Slide 78: 1st stage: Noise Reduction
Since it uses the 1st derivative of an image, it would be better to smooth the image first.
Usually, we convolve the image with a Gaussian filter to smooth the image.
*
=
Gaussian filter
Original Image
Smoothed Image
Notes: \documentclass{article}
\usepackage{amsmath}
\begin{document}
edge, Slide 78\\
\begin{flalign}
\label{eq4}
\begin{aligned}
\frac{1}{159}\left[\begin{matrix}2&4&5&4&2\\4&9&12&9&4\\5&12&15&12&5\\4&9&12&9&4\\2&4&5&4&2\\\end{matrix}\right]
\end{aligned}
\end{flalign}
\end{document}

## Slide 79: 2nd stage: Find intensity gradient
Use some gradient operators (e.g. Prewitt, Sobel) to find Gx and Gy using the first order method, which requires a threshold set by the user.
*The image are scaled to show negative value for display purposes. You should notice that Gx responses to the vertical edges while Gy for horizontal edges.
Gx
Gy

## Slide 80: 2nd stage: Find intensity gradient
Find the magnitude G and direction Θ of the gradient by:
That is: G = |Gx| + |Gy| Θ = tan-1(Gy / Gx)
G
Θ (4 different colors)
Θ is rounded to 4 directions!!
0°, 45°, 90° and 135°!!!
0
0
90
45
135
135
90
45

## Slide 81: 3rd stage: Non-maximum suppression
The gradient magnitude G gives us the edges of the image. But they are thick.
Let’s thin the lines in G.

## Slide 82: 3rd stage: Non-maximum suppression
Real edges are located at the maximum of the lines in G.
For each point (x,y), we compare the G(x,y) with its two neighbors along the Gradient Vector direction.
  E.g. 25, 50, 17 in this example
The gradient vector direction is perpendicular to the edge direction.
Edge
direction
Gradient Vector
direction
G(x,y)
25
-----
50
-----
17
Along gradient vector
direction

## Slide 83: 3rd stage: Non-maximum suppression
If G(x,y) is greater than its two neighbors along the gradient direction, then (x,y) is set to remain. Non-maximum points are removed (suppressed ) in this process.
E.g we know G(x,y)’s direction (gradient vector direction) from Θ(x,y) and it is 90° because Gy is much bigger than Gx, Θ=tan-1(Gy/Gx)90 °. Note:Θ is rounded to 4 directions!! : 0°, 45°, 90° and 135°
Then, we have to compare G(x,y) values along (the gradient vector direction) 25,50,17. G(x,y) =50 is found because 50 > 25 and 50 > 17.
Set the edge for position (x,y) as ‘1’. The others are ‘0’, so this edge is thin (one pixel wide) .
G(x,y)
25
-----
50
------
17
Along gradient vector
direction

## Slide 84: 3rd stage: Non-maximum suppression
The lines are thinned into 1 pixel.
Before after non-maximum

## Slide 85: 4th stage: Hysteresis Thresholding
We do thresholding (set in stage1) on the image twice with two different thresholds, tHigh and tLow.
tHigh is applied first to remove edges that produced by noise (G(x,y)>THigh). Only edges with high gradient magnitude can survive. So many long edges are broken
Threshold
with tHigh
Many broken edges
here

## Slide 86: 4th stage: Hysteresis Thresholding
For each remaining edges after threshold with tHigh, we trace along the EDGE direction (perpendicular to gradient vector direction) and check whether its two neighbors are above tLow, (G(x,y)>Tlow).
If any of the neighbors is above tLow, we mark this neighbor as an edge point and recursively check its neighbor using the same logic.
Edge
direction
Gradient Vector
direction

## Slide 87: 4th stage: Hysteresis Thresholding
Tracing along the edge with tLow will connect the broken edges or restore segments removed by tHigh.
Final result of Canny edge detection: one-pixel edges and few broken edges
After high thresholding

## Slide 88: OpenCV
Since Canny edge detector is so popular, Intel’s Computer Vision library, namely OpenCV, has included this detector.
You can just call the build-in function Canny() and put corresponding parameters (e.g. the two thresholds) in it.
It is highly optimized and can be run in real time with a normal PC and Webcam.
More information: http://opencv.willowgarage.com/documentation/cpp/feature_detection.html?highlight=canny#Canny
http://www.pages.drexel.edu/~weg22/can_tut.html
Demos:
  https://www.youtube.com/watch?v=GIAa3ETmUpU
  Real-time Canny edge detection using OpenCV and CUDA – YouTube

## Slide 89: Writing your own Canny edge detector
If you want to implement it yourself, you can still use OpenCV since it provides a lot of useful functions like Sobel() and gaussianBlur().

## Slide 90: Worksheet 3.8
What are the features of the Canny edge detector?
MC question.
Output one-pixel wide edges, easy to implement, cannot run in real time by a common personal computer.
Output one-pixel wide edges, easy to implement, can run in real time by a common personal computer.
Output one-pixel wide edges, difficult to implement, can run in real time by a common personal computer.
Can you describe what is a Gaussian distribution?
Answer:_____________________
Write the algorithm for the Canny edge detector.
Answer:___________________

## Slide 91: Answer: Worksheet 3.8
Why the Canny edge detector is so popular in image processing? MC question.
  Answer 2 is correct: Output one-pixel wide edges, easy to implement, can run in real time by a common personal computer.
Can you describe what is a Gaussian distribution?
Answer:_in lecture notes
Write the algorithm for the Canny edge detector.
Answer:_in lecture notes

## Slide 92: Conclusion
Studied first order and second order edge detection techniques
Studied the Gaussian operator
Studied the Canny edge detection algorithm

## Slide 93: Appendix

## Slide 94: 1d and 2d

## Slide 95: Latex 5711 ch03 edge
\documentclass{article} %for testing formulas ppt cam, dec8, 2019
\usepackage{amsmath}
\begin{document}
5711 03 edge\\
Convolution method\\
\begin{flalign}
\label{eq:convolution_01}
\begin{aligned}
C(m,n)=
\sum_{j=-\infty}^{j=\infty}
\sum_{k=-\infty}^{j=\infty}
h(m-j,n-k) \times I(j,k)
%%%%%%%%%%%%
\end{aligned}
\end{flalign}\\
%%% eeeeee eq:filtering_01A eeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeee
%%%
1st order (A) Gaussian
\begin{flalign}
\label{eq:filtering_01a}
\begin{aligned}
G(x) = \frac{1}
{\sqrt{2\pi{\sigma^2 }}}
e^{-
\frac{(x-\mu)^2}
{2\sigma^2}
}
\end{aligned}
\end{flalign}
%%% eeeeee eq:filtering_01B eeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeee
1st order (B) Gaussian\\
\begin{flalign}
\label{eq:filtering_01b}
\begin{aligned}
G(x) = \frac{1}
{\sqrt{2\pi{\sigma^2 }}}
exp\left({-
\frac{(x-\mu)^2}
{2\sigma^2}
}\right)
\end{aligned}
\end{flalign}
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
%%% eeeeee eq:filtering_02A eeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeee
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
2nd order (A) Gaussian\\
\begin{flalign}
\label{eq:filtering_02A}
\begin{aligned}
G(x,y) =G(x)G(y)= \frac{1}
{{2\pi{\sigma^2 }}}
e^{-
\frac{(x-\mu_x)^2+(y-\mu_y)^2}
{2\sigma^2}
}
\end{aligned}
\end{flalign}
%%%
2nd order (B) Gaussian
%%% eeeeee eq:filtering_02B eeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeee
\begin{flalign}
\label{eq:filtering_02B}
\begin{aligned}
G(x,y) =G(x)G(y)= \frac{1}
{{2\pi{\sigma^2 }}}
exp\left({-
\frac{(x-\mu_x)^2+(y-\mu_y)^2}
{2\sigma^2}
}\right)
\end{aligned}
\end{flalign}
\end{document}

## Slide 96: Obtain a LOG mask by DoF Difference of Gaussian
Want to remove noise with low frequency (low fluctuation) and high frequency (high fluctuation).
That means band pass filtering
Solution
  Difference of Gaussians DoG=
  (Blurred version of I) – (Less blurred version of I)
  DoG=G(k)- G()

## Slide 97: Intuition DoG (Difference of Gaussian) and LoG (Laplacian of Gaussian)
Using difference of 2 Gaussians to approx. 2nd derivative of G
Consider
  G()   G(k)
DoG=G(k) - G()
 G(k)-  G(k)
 2 G(k) (2nd derivative)
G(x)
x
m
 (less blurred)
k (blurred)
1-D DoG
See http://www.cse.yorku.ca/~kosta/CompVis_Notes/DoG_vs_LoG.pdf

## Slide 98: Applying DOG Difference of Gaussian
Example
Using 2 Gaussian masks of standard deviations (=1 and k= 1.6) for the two blurred versions

## Slide 99
High pass filtering result

## Slide 100: Use excel to plot a Gaussian distribution (cut and paste to excel to view plot)

## Slide 101: Edge detection: essential Formulas
1st order edge gradient .
: