## Slide 1: Digital Logic (Part 1)
Prof. Kin Hong Wong
Department of Computer Science and Engineering

## Slide 2: Overview
Part 1: Introduction
  1.1 What is Digital logic?
  1.2 Digital operations (AND, OR, NOT)
  1.3 Truth table
  1.4 Robot Hardware
  1.5 Software implementation of digital operations
Part 2 (next week): Hardware/software Implementation
  2.1 Robot system
  2.1 Use of If-then-else (software method 1)
  2.2 Use of switch case (software method 2)
  2.3 Finite state machines

## Slide 3: Motivations and plans
The brain of our robot is a set of digital logic functions
We will introduce three techniques in digital logic design
  Logic formula
  Truth table
  Finite state machine
We will use a program in a micro-controller system to implement these techniques

## Slide 4: Example
How to keep the robot to move forward? Method:
  If the robot deviates to the left, turn right
  If the robot deviates to the right, turn left
The above rules are logic functions and operations.
Magnetic sensors
S1 S2
Terminal
Magnetic
strip following robot
(2013-4)
Light following robot
(2014-5)

## Slide 5: 1.1 What is digital logic?
Understanding the difference between Digital and Analog operations

## Slide 6: Analog and digital signals
Analog signals: the signal can be any values within the valid range
  Example: Range =0  10 Volts
  E.g. The signal can be 1.356 Volts or 2.432 Volts
Digital signals: It can only be HIGH (or called ‘1’ )or LOW (or called ‘0’). Examples:
  In TTL Transistor-transistor-logic standard:
    High=‘1’  5 volts, Low=‘0’  0 Volt
  Usually more than one digital bit is used to represent a number
    E.g. 8-bit to represent a value from 0 to 28-1 =255, or 32-bit to represent a value from 0 to 232-1
Voltage
Time (ms)
Voltage
Time (ms)
5 V
0 V
10 V
0 V
1
1
Analog
One Digital Bit

## Slide 7: What is the meaning of digital logic?
A signal is represented by ‘1’ or ‘0’
  Advantages:
    Easy to be implemented in a circuit.
    Less likely to be interfered by noise, temperature and radiation.
Application, digital music
Analog to Digital conversion (ADC)
Digital data saved in CDs
Digital to Analog conversion (DAC)

## Slide 8: 1.2 Digital Operations
AND, OR, NOT

## Slide 9: Digital Operations
Study how to combine inputs to generate outputs
  In arithmetic operations: 2 Add 3= 5, result is 5
  In digital operations: we need a truth table to see the result
3 popular digital operations you will learn here
  AND
  OR
  NOT (Negation)
Digital operation
Digital
Input1
Digital
Input2
Digital
Output

## Slide 10: Exercises
Multiple choice questions
Are these values digital or analog?
  Temperature : Ans: _________?
  Humidity : Ans: _________?
Are you a Chinese Univ. student,
  the answer is : Ans_____?
  Is the above answer Analog or digital? : Ans:_________?
Do you have a mobile phone in your pocket,
  the answer is : Ans:______?
  Is the above answer Analog or digital? Ans: ________?
What is the temperature in this room,
  the answer is Ans:___?
  Is the above answer Analog or digital? Ans: ________?
Answers: 1) Analog, analog 2) Yes, digital 3) Yes, digital 4) 20 Degrees, analog

## Slide 11: AND operation, example in real life
You get a Degree from CUHK if you take 123 units and your GPA is greater than 1.5
  You may write a formula
    (X=take 123 units) AND (Y=GPA>1.5) then you can get a Degree from CUHK (W)
You must eat and drink in order to live
  You may write a formula
    (X=eat ) AND (Y=drink) then you can live (W)
X
Y
W=X AND Y
Notation

## Slide 12: OR operation, example in real life
If you live in Mongkok, you either take a bus or train to come to the Chinese University
  You may write a formula
    (X=take bus) or (Y=take train) then you can come to the University (W)
You can ride on a bus if you pay cash or pay using octopus
  You may write a formula
    (X=pay by cash) or (Y=pay by octopus) then you can ride on the bus (W)
X
Y
W=X OR Y
Notation

## Slide 13: NOT operation, example in real life
I don’t love you = Not (I love you)
  You may write a formula
    NOT (X=I love you) means I don’t love you (W)
You are not rich = NOT (you are rich)
  You may write a formula
    NOT(X=you are rich) that means you are poor (W)
X
W=NOT X
Notation

## Slide 14: Exercise for robot control to follow the magnetic path
Sensors: S2 S1
If S2 detects the magnetic strip, but not S1, has the robot deviated to the right or left of the path?
Answer (right or left) : ______?
Answer: left
Magnetic sensors
S1 S2
Terminal
S2 S1

## Slide 15: 1.3 Truth table
A method to represent logic functions for digital signals

## Slide 16: Truth table
The idea is to have all different combinations of inputs arranged in a table
Each combination gives one output
For n digital inputs , there will be 2n different combinations
The truth table has 2n rows
Example:
  n=2 (X and Y as inputs), so there are 2n=4 rows
  You can see that no two rows have the same combination of inputs
Example
Input: X | Input: Y | W= Output For the operation
0 | 0 | ?
0 | 1 | ?
1 | 0 | ?
1 | 1 | ?
? = depends on the operation

## Slide 17: Truth table example for “AND” operation
X , Y are 2 digital input signals
We can use a “Truth table” to find the output
Because there are n=2 inputs: X,Y
So there are 2n=4 rows in the truth table
Steps to fill in the table
  Fill in Y: 0,1,0,1 (from top)
  Fill in X: 0,0,1,1
  Fill in the outputs
  Compute output:
    Output=1 only when both inputs are 1
Input : X=eat | Input: Y=drink | Output W= X AND Y =live
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
X
Y
W=
X AND Y

## Slide 18: Truth table example for “OR” operation
X , Y are 2 digital input signals
We can use a “Truth table” to find the output
Because there are n=2 inputs: X,Y
So there are 2n=4 rows in the truth table
Steps:
  Fill in Y: 0,1,0,1(from top)
  Fill in X: 0,0,1,1
  Fill in the outputs
  Compute output:
    Output=1 only when either input is 1
Input: X(pay by cash) | Input: Y (pay by Octopus) | Output W= X OR Y= (ride on a bus)
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
X
Y
W=
X OR Y

## Slide 19: NOT (or called negation)
X is a digital input signal
We can use a “Truth table” to find the output
Because there are n=1 input: X
So there are 2n=2 rows in the truth table
Step:
  Fill in X: 0,1
  Fill in the outputs
  Compute output:
    Output=Reverse the input
X= you are rich | NOT X (you are not rich)
0 | 1
1 | 0
X
W=
NOT X

## Slide 20: Exercises
How many rows are required in the truth table for 3 inputs?
Give examples of
  AND
  OR
  NOT
Answer: 23=8 rows

## Slide 21: Combinational logic (Combine NOT, AND, OR)
X , Y , Z are 3 digital input signals
We can use a “Truth table” to find the output
Because there are n=3 inputs: X,Y,Z
So there are 2n=8 rows in the truth table
Fill in Z: 0,1,0,1,0,1,0,1
Fill in Y: 0,0,1,1,0,0,1,1
Fill in X: 0,0,0,0,1,1,1,1

## Slide 22: Truth table
We want to find : W=X OR (NOT (Y) AND Z)
Step 1: fill in different combinations of inputs
2 inputs, so 23=8 rows
X | Y | Z |  |  | W=X OR (NOT ( Y) AND Z)
0 | 0 | 0 |  |  | ?
0 | 0 | 1 |  |  | ?
0 | 1 | 0 |  |  | ?
0 | 1 | 1 |  |  | ?
1 | 0 | 0 |  |  | 
1 | 0 | 1 |  |  | 
1 | 1 | 0 |  |  | 
1 | 1 | 1 |  |  | 
W

## Slide 23: We can solve it step by step
Step2
W
X | Y | Z | NOT(Y)
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Produce NOT (Y)
from Y first.
X,Z are not used in this step.
input
output

## Slide 24: We can solve it step by step
Step 3
W
X | Y | Z | NOT(Y) | Z AND (NOT(Y))
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0
input
output
input
Then, produce
[Z AND (NOT (Y))].
X , Y are not used directly in this step.

## Slide 25: We can solve it step by step
Step 4
X | Y | Z | NOT(Y) | Z AND (NOT(Y) | W=X OR (Z AND (NOT(Y)))
0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0 | 1
1 | 1 | 1 | 0 | 0 | 1
input
input
output
W=X OR (Z AND (NOT(Y)))

## Slide 26: Exercise 1.1
Use a truth table to find the output of
NOT( X AND Y ) OR Z

## Slide 27: Exercise1.1: NOT( X AND Y ) OR Z
Fill the blanks in X,Y, Z columns
X | Y | Z | X AND Y | NOT (X AND Y) | W=(NOT (Z AND Y)) OR Z
0 |  | 0 |  |  | 
 |  | 1 |  |  | 
 |  | 0 |  |  | 
 |  | 1 |  |  | 
 |  | 0 |  |  | 
 |  | 1 |  |  | 
 |  | 0 |  |  | 
 |  | 1 |  |  | 

## Slide 28: Exercise1.1: NOT( X AND Y ) OR Z
Fill the blanks
The answer is in the appendix
X | Y | Z | X AND Y | NOT (X AND Y) | W=(NOT (Z AND Y)) OR Z
0 | 0 | 0 |  |  | 
0 | 0 | 1 |  |  | 
0 | 1 | 0 |  |  | 
0 | 1 | 1 |  |  | 
1 | 0 | 0 |  |  | 
1 | 0 | 1 |  |  | 
1 | 1 | 0 |  |  | 
1 | 1 | 1 |  |  | 

## Slide 29: Robot Hardware

## Slide 30: Robot Hardware
  Controlled by an Arduino computer
    Write programs and download to run
  The robot will be put in a sphere, it has
    LED display Board
    7-segment display
    Light seeking sensors
    Magnetic sensor for power on/off

## Slide 31
The Intelligent Robot system
Arduino board
(programs to be run in the Arduino computer):
:
void Loop
{
If ….
then….
else….
}
Inputs
Outputs
Motor drivers
Magnetic on/off sensor
Programmer to update the program
Bluetooth
H-bridge
motors
Light sensors
S1 S2
S3 S4
S5 S6
Light source

## Slide 32: Light following design
You need to design the robot to follow a light source
Your work: Program the motor actions responding to which light sensor receives the strongest light energy
You learn magnetic strip following method here then find out how to do light following yourself
Light sensors (Si)
S1 S2
S3 S4
S5 S6
Light sensors

## Slide 33: 1.5 Software Implementation

## Slide 34: Software Implementation
Document about the use of Arduino
  E-learning https://elearn.cuhk.edu.hk/webapps/login/
Edit program
Compile
Download to the Arduino board of the robot
Run the program

## Slide 35: How to use “If-then-else”
IF (condition) then output is result 1, else output is result 2
//Example1: //just to illustrate the idea, not a runnable program
  If (“you_eat” and “you_drink”) you _can_live;
  Else “you_die”;
//Example2: // && means “AND”
if(Din1() && Din3()) Out1(1); // same as if(Din1()==1 && Din3()==1) Out1(1);
else Out1(0);
The above program means: if Din1 is 1 AND Din3 is 1, then Out1 is 1. Else Out1 is 0
//Example3: // || means “OR”
If (Din1() || Din3()) Out3(1); // same as if(Din1()==1 || Din3()==1) Out1(1);
Else Out3(0));
The above program means: if Din1 is 1 OR Din3 is 1, then Out3 is 1. Else Out3 is 0

## Slide 36: You will learn this in Lab6.
You are given: An Arduino computer with the debug board
In here, inputs are represented as In1=A, In3=B and output Out1=Q.
//program segment in the main loop of Lab6.ino
void loop()
{ // Experiment 1.3 Out1=In1 AND In3
//that means if In1 and In3 are ‘1’, Out1 is ‘1’. Otherwise Out1 is ‘0’
if(Din1() && Din3()) Out1(1); //&& means logic function AND
else Out1(0);
:
}
In1
In3
Out1

## Slide 37: A more complex function You will test it in Lab 6.
//Program segment in the main loop of Lab6.ino
void loop()
{ :
// Experiment 2.1 Out2=(NOT(In2) AND In3) AND In4
if((!(Din2()) && Din3()) && Din4()) Out2(1);
else Out2(0);
:
}

## Slide 38: Summary
Learned
  Digital logic
  The use of the truth table
  Our robot system design
  To implement logic functions using if-then-else

## Slide 39: END

## Slide 40: Appendix Part 1.A:
ANSWER1.1: W=(NOT( X AND Y )) OR Z
Fill the blanks
X | Y | Z | X AND Y | NOT (X AND Y) | W=(NOT (X AND Y)) OR Z
0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1
1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1
1 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0 | 1