## Slide 1
Lecture 4: Measurement and Instrumentation
Professor Hon Ki Tsang
Department of Electronic Engineering
February 10, 2014
ENGG 1100 Introduction to Engineering Design

## Slide 2: Measurement, units and uncertainty
Reference
Halliday Resnick and Walker, Principles of Physics, (9th edition)
Chapter 1, and sections 18.2, 38.8, Appendix A1

## Slide 3: SI Base System of Units
Every measurement may be quantified in units that can be derived from the 7 Base units of Système international d'unites (SI System of units):
Dimension | unit | 
Mass | kilogram | kg
Length | meter | m
Time | second | s
Temperature | kelvin | K
Electric Current | ampere | A
Amount of substance | mole | mol
Luminous intensity | candela | cd

## Slide 4: Example: Some common derived units
Let M=mass, T=time, L = Length, A= current, K=temperature
Force = mass x acceleration = M LT-2
  Hence 1 newton = 1 kg m/ s2
Energy = force x distance = ML2T-2
  1 joule = 1 kg m2/ s2
Electric potential = energy per coulomb = ML2T-2/(AT)= ML2A-1T-3
  1 volt = 1 kg m2 s-3A-1
Question: Express the units of electrical resistance, electrical power and capacitance in terms of the SI base units
1 ohm= 1 volt/ampere = 1 kg m2 s-3A-2
1 watt = 1 joule/second = 1 kg m2/ s3
1 farad = 1 coulomb/volt = (A s) / (kg m2 s-3A-1)=A2 s4 kg-1 m-2

## Slide 5: Dimensional Analysis
Dimensional analysis is a technique to analyze experiments or physical phenomena in terms of the dimensions of its parameters, and to simplify the analysis by grouping parameters together to form dimensionless parameters.
Grouping of parameters to dimensional variables can help reduce the number of unknown variables: Buckingham’s pi theorem: A function F(a1, a2, … , an) = 0 may be converted to f(k1, k2, … kr < n) = 0
where, F = function of dimensional variables, and f is the function in terms of dimensionless parameters ki; if m = number of relevant dimensions, n = number of dimensional variables, then r = n – m .
  Useful in analysis of experiments and modeling of experiments

## Slide 6: Example: Period of a pendulum
q
L
m
How does the period of the pendulum T depend on its length and mass?
Guess that T will depend on gravity acceleration g, mass m, length L and intial angle q
where a, b and c are unknown integers
Consider the dimensions
Equation must have same dimensions on both sides
Hence: a=0, c=-1/2 , b=-c=1/2

## Slide 7: More examples on dimensional analysis
For some interesting examples of applications of dimensional analysis to problems such as cooking time for a turkey, estimating the energy in an atomic bomb explosion refer to: preview of the examples are available by searching books.google.com)

## Slide 8: Uncertainty in measurements: errors

## Slide 9: Measurement Uncertainty and Errors
Every measurement M has some uncertainty, which is usually described by an error range M where has the same units as M and is an estimate of the uncertainty in the measurement (or it may be defined in terms of one standard deviations from the mean of a set of the same measurement repeated a number of times)
Repeating the same measurements Mi at different time and taking the average of n measurements may help to reduce the uncertainty by a factor
  CAUTION: Taking the average does not reduce systematic errors from mis-calibration of the instrument and assumes that the parameter being measured does not change from one observation to the next
Sources of measurement uncertainty in electronic instrumentation comes from electrical noise, finite resolution of analog to digital converters, deviations from linear response of electrical amplifiers, and ageing of electronic components (affecting instrumentation calibration).

## Slide 10: Example: Resistor Ageing
Improved stability of thin-film resistors
Reiner W. Kuehl, Vishay Draloric, EDN June 15, 2011
http://www.edn.com/design/components-and-packaging/4368133/Improved-stability-of-thin-film-resistors

## Slide 11: Electrical ageing of transistors
No stress
After 216 hours @ 60mA
N. Toufik, Active and Passive Elec. Comp., 2001, Vol. 24, pp. 155-163

## Slide 12: Electrical Noise
Thermal Noise (also called Johnson noise) is due to random thermal motion of electric charge in conductors
Similar at all frequencies ie “white noise” and hence noise power scales with bandwidth of the measurement
Mean of the square of the noise current (variance of the noise) is
Where
k= Boltzman constant =1.38x10-23 m2 kg s-2 K-1
T = Temperature (kelvin), B= bandwidth (Hz), R = resistance of the conductor

## Slide 13: Ground Loops
Ground loops exist when there is more than one connection to “ground” and the ground currents are not equal leading to small voltage differences between the local grounds
I1
I2

## Slide 14: Measurements affect system being measured
Voltage across the resistor and the current in the cicuit is not changed by the measurement only if the volmeter has infinite resistance and ammeter has zero resistance. In practice the voltmeter may have ~10Mohm resistance and ammeter may have a few ohms resistance

## Slide 15
HEISENBERG UNCERTAINTY PRINCIPLE
Cannot make precise measurement of both “conjugate” parameters such as position and momenta, energy and time.
HEISENBERG UNCERTAINTY PRINCIPLE.

## Slide 16: Example: Double slit experiment and interference of matter waves
Wave particle duality: wavelength of electrons
p = momentum
h = 6.6x10-34Js
Interference pattern of electrons
Young’s double slit interference with electrons
http://www.hitachi.com/rd/portal/research/em/doubleslit.html

## Slide 17: Quantum Teleportation

## Slide 18: Electronic Instrumentation: OSCILLOSCOPE

## Slide 19: Oscilloscope
The oscilloscope measures voltage (vertical) against time (horizontal).
Measurement is periodic and starts from a trigger signal
  Trigger input may be from the signal itself (internal trigger) or external trigger input
Trigger input is at back panel of this model

## Slide 20: Oscilloscope – working principle
Digital Oscilloscope
  Analogue to Digital converter (ADC) samples the input voltage and stores it as a number (quantization error may be present because of finite number of discrete levels)
  Number is stored in memory and processed digitally (DSP_
Source:
“Oscilloscope Fundamentals” by Agilent Technology

## Slide 21
Aliasing

## Slide 22: Aliasing
Aliasing may be prevented by sampling above the Nyquist frequency (2x Fmax)
Spatial aliasing on oscilloscope display may be seen if the time scale is too slow

## Slide 23: Oscilloscope probes
x10 Probe reduces loading of probe on circuit

## Slide 24: Printed Circuit Boards (PCB)
Vias - connecting tracks from one layer to another
Multilayer PCB – for making more
complicated circuits
Via