## Slide 1: Computer-aided Drafting (SolidWorks)
Tutorial (Basics in SolidWorks)
小明 in ERB106

## Slide 2: Today’s Outline
Modeling
  2D
    Sketching
    Dimensioning
    Mirror/Pattern
    Trim/Extend
    Fillet/Chamfer
  3D
    Extruded/ Extruded Cut
    Revolved
    Fillet/Chamfer

## Slide 3: Getting Started
Open Software
  Start > All programs > SolidWorks 2011 > SolidWorks 2011
New Document
Choose “Part‟ and then “OK‟ / ”Enter”
Create parts (File format -.sldprt)Assembly parts (File format -.sldasm)2D Engineering Draws (File format -.slddrw)

## Slide 4: Basic Interface
Drawing tools
Design tree
Drawing region

## Slide 5: Basic procedures on sketching
Select plane for sketch
  Invisible planes, planer surface on parts
Create sketch(2-D)
Draw features on sketch(3-D)

## Slide 6: Basic steps
Sketch on the plane
Select a plane
Dimensioning
Create features (extrude)
Finish a feature
Nothing

## Slide 7: Basic steps [Con’t]
Create more features
Select other planes
Assemble with other parts
Assembly done, or modify if necessary
Create more sketches
Create engineering drawing

## Slide 8: Control
Standard View -Right click and hold
  (View>Toolbars>Standard View)
Shading and background
Others
  Rotating –Middle click and hold
  Panning –Ctrl + Middle click and hold
  Zooming –Scroll Wheel
  Fast views –Ctrl + 1,2,3,4,5,6,7
Many others…….(this tutorial covers only the basics)

## Slide 9: 2-D sketch
Select a plane and right click.
In dialog box, click “sketch”
Or click “sketch” and select a plane
Exit the sketch before you move on. (at the top of the right side)
Confirm
Discard
Debug: if you stuck somewhere, check this!!

## Slide 10: 2-D
Basic sketching
  Lines
  Circles
  Rectangles
  Arcs
Modifications
  Dimensions (many types)
  Fillets/Chamfers
  Mirrors
  Patterns
    Linear
    Circular
  Trims

## Slide 11: 2-D lines
Enter / Create Sketch
Click line
ESC : leave the current command
Delete elements: select the elements and click delete button
button
As sketch: click to define arbitrary first point, second point,…etc
Horizontal:click to draw horizontal line only
Vertical:click to draw vertical line only
Angle:click to draw line by defining angle with respect to horizontal line
For construction: can change the elements for reference
Infinite length: can draw line with infinite length
Usually use this and further define the line by dimension
Sometimes useful for later drawings

## Slide 12: 2-D lines
Tell you its existing relation/the relation with other elements
You can add relations here
Modify options (normally you can set “for construction” after all necessary lines are drawn
Define parameter of current element. E.g. length of line
Intersections
Horizontal

## Slide 13: 2-D lines (dimensions)
Click Smart Dimension
  Click on the line: define the line by length only
    Pull the dimension to different directions
      Along line
      Vertical
      horizontal
    Then type in the value to modify the line
    Click ‘tick’ when done
  Click on 2 points: define the line by 2 end points (similar)

## Slide 14: 2-D circles
Select circle
  Click a point(center), then click another point(radius)
Select Perimeter circle
  Select three points to define a circle
Radius and Center
Useful when you want to draw tangent circle

## Slide 15: 2-D circles (dimensions)
Usually it is defined by its center and radius
Not yet fully defined (blue)
Fully defined (Black)
Or use the mouse to force set the relations of the center with some reference (e.g. the origin)

## Slide 16: 2-D rectangles
Select rectangle
  Click 2 more points to define it
Usually it is defined by 2 sides
Not yet fully defined (blue)
Fully defined (Black)

## Slide 17: 2-D Trim (cutting lines)
Click trim and select “trim to closest”
Trim the line between 2 (intersecting) points

## Slide 18: 2-D fillets / chamfers
Click fillet
  Fillet the corner at the intersection of two sketch (choose a corner)
Click chamfer
Set corner radius

## Slide 19: 3-D
Extrude / extrude cut
Revolve / revolve cut
Fillets / chamfers
Mirror
Patterns
  Linear
  Circular
Many others
  Loft base
  Sweep base
  Etc.

## Slide 20: 3-D extrudes
Select a sketch (must be close-loop)
Click
Extrude type
Extrude thickness

## Slide 21: 3-D extrudes
Frequently used

## Slide 22: 3-D extrude-cut
Select a plane on feature
Sketch on that plane
Click Features >Extruded Cut
Select this plane and sketch first!!!

## Slide 23: 3-D fillets
Select edge/face of feature and click
Constant radius
Radius

## Slide 24: Assembly
Assemble virtually before manufacturing!

## Slide 25: Assembly
Open new assembly
Insert new component
Browse a new part

## Slide 26: Assembly
Open the first (fixed) component
Click to place the component
In the “Assembly” tab, click “Insert Components” and browse more components

## Slide 27: Assembly
Take one part for each component (totally 5 more parts)
Duplicate parts: Press Ctrl + mouse (left) key on the motor (yellow part), pull away from it.

## Slide 28: Assembly
The prefixes:
(f) Fixed: position of this component is fixed,
i.e., it CANNOT be moved / rotated.
(-) Float: position of this component has NOT been defined,
i.e., it can be moved / rotated freely.
You can right-click it, and set to float if necessary

## Slide 29: Assembly
Adding relations, click Mate

## Slide 30: Assembly
Standard Mates
Coincident
  configure two items(faces, edges or planes) so that they touch each other.
Parallel
  configure two items so that they remain a specified distance from one another.
Perpendicular
  configure two items so that they’re 90 degrees from one another.
Tangent:
  configure a curve and another item so that they meet at a single point. One of the selected items must be a cylindrical, conical or spherical face.
Concentric:
  configure two items so that they share the same center axis.
Distance:
  configure two items at a specified distance from one another.
Angle:
  configure two items at a specified angle to one another.
Most commonly used!
Mate can only handle 2 features each time!!!

## Slide 31: Assembly (omni-wheel)
Click “Mate”, select 2 faces

## Slide 32: Assembly (omni-wheel)
Reverse mating directions

## Slide 33: Assembly (omni-wheel)
Mate (coincident), click 2 surfaces, then “Mate”, finally click “tick”

## Slide 34: Assembly (screw rods)
Mate (coincident) with all 4 surfaces,
Mate (concentric) the rods and the holes on the chassis,

## Slide 35: Assembly (screw rods)
Mate (coincident) with 2 surfaces,
Mate (concentric) the holes on the “omni-wheel” with the 4 rods, (either 2 holes are enough in this case)
Mate (coincident) the head of the rods with the flat surface on the omni-wheel

## Slide 36: Rapid Prototyping (RP)
Flows of RP:
  1. Design some parts
  2. Save as “part_name.stl” format
  3. Send to RP machine for fabrication
  4. Post-treatment such as supporting materials removal
Demonstration of the rapid prototyping process:
  http://www.youtube.com/watch?feature=player_embedded&v=bpcwBQKUqK4

## Slide 37
Thank you!
Good luck with your study!