## Slide 1: Repair Pipelining for Erasure-Coded Storage
Runhui Li, Xiaolu Li, Patrick P. C. Lee, Qun Huang
The Chinese University of Hong Kong
USENIX ATC 2017

## Slide 2: Introduction
Fault tolerance for distributed storage is critical
  Availability: data remains accessible under failures
  Durability: no data loss even under failures
Erasure coding is a promising redundancy technique
  Minimum data redundancy via “data encoding”
  Higher reliability with same storage redundancy than replication
  Reportedly deployed in Google, Azure, Facebook
    e.g., Azure reduces redundancy from 3x (replication) to 1.33x (erasure coding)  PBs saving

## Slide 3: Erasure Coding
Divide file data to k blocks
Encode k (uncoded) blocks to n coded blocks
Distribute the set of n coded blocks (stripe) to n nodes
Fault-tolerance: any k out of n blocks can recover file data
Nodes
(n, k) = (4, 2)
File
encode
divide
A
B
C
D
A+C
B+D
A+D
B+C+D
A
B
C
D
A+C
B+D
A+D
B+C+D
A
B
C
D
Remark: for systematic codes, k of n coded blocks are the original k uncoded blocks

## Slide 4: Erasure Coding
Practical erasure codes satisfy linearity and addition associativity
  Each block can be expressed as a linear combination of any k blocks in the same stripe, based on Galois Field arithmetic
  e.g., block B = a1B1 + a2B2 + a3B3 + a4B4
  for k = 4, coefficients ai’s, and blocks Bi’s
Also applicable to XOR-based erasure codes
Examples: Reed-Solomon codes, regenerating codes, LRC

## Slide 5: Erasure Coding
Good: Low redundancy with high fault tolerance
Bad: High repair penalty
  In general, k blocks retrieved to repair a failed block
Mitigating repair penalty of erasure coding is a hot topic
  New erasure codes to reduce repair bandwidth or I/O
    e.g., Regenerating codes, LRC, Hitchhiker
  Efficient repair approaches for general erasure codes
    e.g., lazy repair, PPR

## Slide 6: Conventional Repair
Single-block repair:
  Retrieve k blocks from k working nodes (helpers)
  Store the repaired block at requestor
Repair time = k timeslots
  Bottlenecked by requestor’s downlink
  Uneven bandwidth usage (e.g., links among helpers are idle)
k = 4 helpers
requestor
Network
R
N1
N2
N3
N4
Bottleneck

## Slide 7: Partial-Parallel-Repair (PPR)
Exploit linearity and addition associativity to perform repair in a “divide-and-conquer” manner
[Mitra, EuroSys’16]
k = 4 helpers
requestor
Network
R
N1
N2
N3
N4
Repair time = ceil(log2(k+1)) timeslots
Timeslot 1:
N1 sends a1B1 to N2  a1B1+a2B2
N3 sends a3B3 to N4  a3B3+a4B4
Timeslot 2:
N2 sends a1B1+a2B2 to N4  a1B1+a2B2+a3B3+a4B4
Timeslot 3:
N4  R  repaired block

## Slide 8: Open Question
Repair time of erasure coding remains larger than normal read time
  Repair-optimal erasure codes still read more data than amount of failed data
Erasure coding is mainly for warm/cold data
  Repair penalty only applies to less frequently accessed data
  Hot data remains replicated
Can we reduce repair time of erasure coding to almost the same as the normal read time?
  Create opportunity for storing hot data with erasure coding

## Slide 9: Our Contributions
Repair pipelining, a technique to speed up repair for general erasure coding
  Applicable for degraded reads and full-node recovery
  O(1) repair time in homogeneous settings
Extensions to heterogeneous settings
A prototype ECPipe integrated with HDFS and QFS
Experiments on local cluster and Amazon EC2
  Reduction of repair time by 90% and 80% over conventional repair and partial-parallel-repair (PPR), respectively

## Slide 10: Repair Pipelining
Goals:
  Eliminate bottlenecked links
  Effectively utilize available bandwidth resources in repair
Key observation: coding unit (word) is much smaller than read/write unit (block)
  e.g., word size ~ 1 byte; block size ~ 64 MiB
  Words at the same offset are encoded together in erasure coding
…
n blocks of a stripe
words at the same offset are encoded together
word
Notes:     Eliminate bottleneck links: no link transmits more traffic than others
    Utilize bandwidth resources Links should not be idle for most times

## Slide 11: Repair Pipelining
Idea: slicing a block
  Each slice comprises multiple words (e.g., slice size ~ 32 KiB)
  Pipeline the repair of each slice through a linear path
Single-block repair:
Repair time = 1 + (k-1)/s  1 timeslot if s is large
time
k = 4
s = 6 slices
N1
N2
N3
N4
R
N1
N2
N3
N4
R
N1
N2
N3
N4
R
N1
N2
N3
N4
R
N1
N2
N3
N4
R
N1
N2
N3
N4
R
a1b1
a1b1+a2b2
a1b1+a2b2
+a3b3
a1b1+a2b2
+a3b3+a4b4

## Slide 12: Repair Pipelining
Two types of single-failure repair (most common case):
  Degraded read
    Repairing an unavailable block at a client
  Full-node recovery
    Repairing all lost blocks of a failed node at one or multiple nodes
    Greedy scheduling of multiple stripes across helpers
Challenge: repair degraded by stragglers
  Any repair of erasure coding faces similar problems due to data retrievals from multiple helpers
Our approach: address heterogeneity and bypass stragglers

## Slide 13: Extension to Heterogeneity
Heterogeneity: link bandwidths are different
Case 1: limited bandwidth when a client issues reads to a remote storage system
  Cyclic version of repair pipelining: allow a client to issue parallel reads from multiple helpers
Case 2: arbitrary link bandwidths
  Weighted path selection: select the “best” path of helpers for repair

## Slide 14: Repair Pipelining (Cyclic Version)
Requestor receives repaired data from k-1 helpers
Repair time in homogeneous environments  1 timeslot for large s
N1
N2
N3
N4
N2
N3
N4
N1
N3
N4
N1
N2
R
N4
N1
N2
N1
N2
N3
N4
N2
N3
N4
N1
N3
N4
N1
N2
Send to requestor
R
N4
N1
N2
Send to requestor
Group 1
Group 2

## Slide 15: Weighted Path Selection
Goal: Find a path of k + 1 nodes (i.e., k helpers and requestor) that minimizes the maximum link weight
  e.g., set link weight as inverse of link bandwidth
  Any straggler is associated with large weight
Brute-force search is expensive
  (n-1)!/(n-1-k)! permutations
Our algorithm:
  Apply brute-force search, but avoid search of non-optimal paths
    If link L has weight larger than the max weight of the current optimal path, any path containing L must be non-optimal
  Remain optimal, with much less search time

## Slide 16: Implementation
  Requestor implemented as a C++/Java class
  Each helper daemon directly reads local blocks via native FS
  Coordinator access block locations and block-to-stripe mappings
ECPipe is integrated with HDFS and QFS, with around 110 and 180 LOC of changes, respectively
Helper
Node
Helper
Node
Helper
Node
Coordinator
Requestor
control flow
datal flow
ECPipe: a middleware atop distributed storage system

## Slide 17: Evaluation
ECPipe performance on a 1Gb/s local cluster
Single-block repair time vs. slice size for (n,k) = (14,10)
Trade-off of slice size:
  Too small: transmission overhead is significant
  Too large: less parallelization
  Best slice size = 32 KiB
Repair pipelining (basic and cyclic) outperforms conventional and PPR by 90.9% and 80.4%, resp.
Only 7% more than direct send time over a 1Gb/s link  O(1) repair time

## Slide 18: Evaluation
ECPipe performance on a 1Gb/s local cluster
Full-node recovery rate vs. number of requestors for (n,k) = (14,10)
Recovery rate increases with number of requestors
Repair pipelining (RP and RP+scheduling) achieves high recovery rate
Greedy scheduling balances repair load across helpers when there are more requestors (i.e., more resource contention)

## Slide 19: Evaluation
ECPipe performance on Amazon EC2
Weighted path selection reduces single-block repair time of basic repair pipelining by up to 45%

## Slide 20: Evaluation
Single-block repair performance on HDFS and QFS
ECPipe significantly improves repair performance
  Conventional repair under ECPipe outperforms original conventional repair inside distributed file systems (by ~20%)
    Avoid fetching blocks via distributed storage system routine
  Performance gain is mainly due to repair pipelining (by ~90%)
QFS: slice size
QFS: block size
HDFS: (n,k)

## Slide 21: Conclusions
Repair pipelining, a general technique that enables very fast repair for erasure-coded storage
Contributions:
  Designs for both degraded reads and full-node recovery
  Extensions to heterogeneity
  Prototype implementation ECPipe
  Extensive experiments on local cluster and Amazon EC2
Source code:
  http://adslab.cse.cuhk.edu.hk/software/ecpipe