## Slide 1: Elastic Parity Logging for SSD RAID Arrays
Yongkun Li*, Helen Chan#, Patrick P. C. Lee#, Yinlong Xu*
*University of Science and Technology of China #The Chinese University of Hong Kong
DSN 2016

## Slide 2: SSD Storage
Solid-state drives (SSDs) are widely deployed in desktops and data centers
  Extensive field studies by Facebook [Meza, Sigmetrics’15], Google [Schroeder, FAST’16]
Better performance, shock resistance, and power efficiency than harddisks

## Slide 3: How SSDs Work?
Basic operations:
  Read and write: per-page basis (e.g., 4KB, 8KB)
  Erase: per-block basis (e.g., 64 or 128 pages)
Out-of-place write for updates:
  Write to a clean page and mark it as valid
  Mark the original page as stale
Garbage collection (GC) reclaims stale pages
  Erase blocks and relocate any valid page

## Slide 4: Challenges
Reliability
  Flash errors are commonplace
  Error-correcting codes aren’t bullet-proof
Endurance
  Blocks allow only limited P/E cycles
Performance
  Poor random write performance
  GC overhead

## Slide 5: SSD RAID
RAID provides fault tolerance
  Each stripe contains data chunks and parity chunks
Challenge:
  Parity updates aggravate small writes
   degrade performance and endurance
m1
m4
m7
SSD1
m2
m5
c3
SSD2
c1
m6
m9
SSD4
m3
c2
m8
SSD3
c1 = m1 + m2 + m3 ‘+’ means XOR
…
…
…
…

## Slide 6: Our Contributions
EPLog: a new RAID design for SSD RAID arrays via elastic parity logging
  Redirects writes to separate log devices
  Constructs “elastic” stripes by new writes only
  Maintains high reliability, endurance, performance
Prototype implementation
  General fault tolerance with erasure coding
  Deployable on commodity hardware
Reliability analysis + testbed experiments

## Slide 7: Related Work
Improve parity updates for SSD RAID
  Parity caching: requires non-volatile memory [HotDep’09,TC’11,SAC’11]
  Elastic striping: incurs RAID-level GC [DSN’13,DSN’15]
  Parity logging: needs pre-read and per-stripe computation [ISCA’93]
EPLog extends parity logging with two optimizations

## Slide 8: Parity Logging
Original parity logging
  Requests: {, , }, {, , }, {, , }
Drawbacks:
  Pre-read: Extra reads
  Per-stripe basis: Extra log chunks; Partial parallelism

## Slide 9: EPLog
Performs out-of-place updates at system level
Computes a log chunk based on new writes
Elastic parity logging:
  No pre-reads of existing chunks
  A log chunk may span across stripes

## Slide 10: EPLog Architecture
User-level block device layer
  SSD main array + harddisk log devices
Parity commit

## Slide 11: Design Issues
Limitations:
  Extra footprints for log devices
  Extra space for multiple versions of chunks
  Slow recovery before parity commit
Issues:
  Write processing
  Parity commit
  Caching
  Metadata management

## Slide 12: Write Processing
Full-stripe new writes
  Write directly data/parity chunks to SSD main array
  Use k-of-n erasure coding
    e.g., RAID-5: k = n - 1
Partial-stripe writes or updates
  Write data chunks to SSD main array
  Write log chunks to log devices in append-only mode
  Log chunks: parity chunks for elastic stripes
    Formed by k’-of-n’ erasure coding
    k’ = number of data chunks in an elastic stripe
    n’ – k’ = number of tolerable failed devices

## Slide 13: Parity Commit
Commit latest updates to main array
  Identify data stripes
  Read latest versions of data chunks from SSDs
  Re-compute parity chunks
  Write back to SSDs
  Release space
Performed regularly or during idle time
No need to access log devices

## Slide 14: Caching
EPLog offers an optional caching feature
  Stripe buffer: New writes
  Device buffers: Updates
Notes: Supports in-place updates

## Slide 15: Implementation
Persistent metadata management
  Full checkpoint: flushes all metadata
  Incremental checkpoint: flushes modified metadata since the last checkpoint
Persistent metadata storage on SSDs
  Separate data and metadata on SSDs
  RAID-10 for metadata partitions
Multi-threaded writes for performance gains

## Slide 16: Reliability Analysis
Question:
  Reduced writes to SSDs slow down wearing  improves reliability
  Extra harddisk log devices  degrades reliability
    Reduced to SSDs slows down the wearing of SSDs and so improves reliability
Compare EPLog and conventional SSD RAID via Markov MTTDL analysis
Our key findings:
  EPLog improves reliability in common settings

## Slide 17: Experiments
Testbed
  Linux Ubuntu 14.04 LTS with kernel 3.13
  Plextor M5 Pro 128GB SSDs
  Seagate ST1000DM003 7200RPM 1TB SATA HDDs
Four public block-level traces
  Write-intensive; dominated by small random writes
Three schemes
  Linux software RAID mdadm (MD)
  Original parity logging (PL)
  EPLog

## Slide 18: Write Size to SSDs
EPLog has ~50% less writes than MD
(6+2)-RAID-6

## Slide 19: GC Overhead
EPLog has 77% fewer GC requests than MD
  Slightly fewer GCs than PL due to better sequentiality
(6+2)-RAID-6
Notes: Blktrace utilty
Feed into SSD simulator

## Slide 20: I/O Performance
EPLog outperforms MD by 30-120% and PL by 190-300%
  No pre-reads
  Fewer log chunks
(6+2)-RAID-6

## Slide 21: Caching
Caching reduces write size to SSDs with small cache
(6+2)-RAID-6

## Slide 22: Parity Commit
Parity commit has limited overhead if it’s performed in groups of writes
(6+2)-RAID-6

## Slide 23: Conclusions
EPLog is a new SSD RAID design with reliability, endurance, and performance in mind
  Elastic parity logging
EPLog design is backed by implementation, reliability analysis, extensive experiments
Source code:
  http://ansrlab.cse.cuhk.edu.hk/software/eplog