## Slide 1: An In-Depth Analysis of Cloud Block Storage Workloads in Large-Scale Production
Jinhong Li*, Qiuping Wang*, Patrick P. C. Lee*, Chao Shi#
*The Chinese University of Hong Kong (CUHK) #Alibaba Group

## Slide 2
Trace analysis are important in storage workload optimizations
Several field studies have analyzed the I/O behaviors of Microsoft Research Cambridge (MSRC) traces
However, it may have different patterns with cloud applications
Background

## Slide 3
Requirements in cloud storage systems
  Quality-of-services guarantees
  Efficient resource utilizations
Design considerations of cloud block storage systems
  Load balancing: Balance the traffic in different volumes and time intervals
  Cache efficiency: Improve cache hit ratios and boost I/O performance
  Storage cluster management: Improve performance and endurance of flashes
Motivation

## Slide 4
Volume: Each volume is perceived by an upper-layer application
Storage Cluster: Provide the physical space for users
…
…
Block Storage
Storage Cluster
Storage Cluster
Volume
OS
Volume
Web
Volume
DB
Volume
KV
…
Volume
Desktop
Architecture

## Slide 5
An in-depth study on the block-level I/O traces collected from a cloud block storage system at Alibaba Cloud
We analyze two traces from a high-level perspective to compare their basic characteristics
We provide 15 findings on the I/O characterization in terms of
  Load intensity
  Spatial patterns
  Temporal patterns
We release our block-level traces, with billions of I/O requests and hundreds of terabytes of I/O traffic
Our Contribution

## Slide 6
AliCloud:
  Traces collected from a product of Alibaba Cloud
  1000 volumes
  Starts from January 1st 2020 and ends with January 31st 2020
  Fields
    Volume ID, request type, request offset, request size, and timestamp
MSRC:
  Microsoft Research Cambridge traces from a data center of Windows servers
  36 volumes
  One week in February 2007
  Fields
    Volume ID, request type, request offset, request size, timestamp, and response time
Traces

## Slide 7
AliCloud has a larger scale.
  Duration: 4.3x
  I/O requests: 46.6x
  Volumes: 27.8x
  Traffic: 54.1x
  Working set size (WSS): 10.3x
Reads span small working sets in AliCloud.
Most AliCloud volumes are write-dominant.
High-level Analysis
Notes: Reads span only 34.3% of WSS in AliCloud, but 98.4% in MSRC
Writes span 89.4% of WSS in AliCloud
Write-to-read ratio: the number of writes divided by the number of reads.
The write-to-read ratio of AliCloud (MSRC) is 3:1 (0.42:1)
91.5% of AliCloud volumes are write-dominant, while only 53% of volumes are write dominant in MSRC
42.4% volumes have write-to-read ratios larger than 100

## Slide 8
Small I/Os dominate in both traces.
  Left: Request sizes
    AliCloud: 75% of reads (writes) are no larger than 32 KiB (16 KiB).
    MSRC: 75% of reads (writes) are no larger than 64 KiB (20 KiB)
  Right: Average request sizes of volumes
    AliCloud: 75% of the average read (write) sizes are less than 39.1 KiB (34.4 KiB)
    MSRC: 75% of the average read (write) sizes are less than 50.8 KiB (15.3 KiB)
High-level Analysis

## Slide 9
A non-negligible fraction of volumes in AliCloud are active in short time periods.
  A volume is said to be active if it has at least one I/O request.
  We measure the active days of the volumes:
    AliCloud: 15.7% of volumes are active for only one day.
    MSRC: All volumes are active in 7 days.
High-level Analysis

## Slide 10
Commonality:
  Small I/Os are dominant
Differences from MSRC:
  A larger scale, in terms of duration, traffic, working set size, and the number of I/O requests
  Smaller read working sets
  Some volumes are active in short time
  Larger write-to-read ratios
High-level Analysis - Summary

## Slide 11
Finding 1: Both traces have similar load intensities of volumes
Load intensities (req/s):
  Average intensity: The traffic divided by the duration of all requests
  Peak intensity: The maximum traffic in each minute of each volume
  The average intensity and peak intensity is similar in both traces.
Findings on Load Intensity

## Slide 12
Finding 2: Both traces have high burstiness in some volumes.
Burstiness ratios:
  The peak intensity divided by the average intensity
  The overall burstiness ratios are 2.11 (7.39) for AliCloud (MSRC).
Finding 3: AliCloud has more diverse burstiness across volumes.
Findings on Load Intensity

## Slide 13
Finding 4: Both traces have high short-term burstiness from the perspective of inter-arrival times of requests.
Inter-arrival time:
  The elapsed time between two adjacent requests
  The 25th, 50th, and 75th percentiles are lower than 1.3 ms (equivalent to at least 700 req/s)
Findings on Load Intensity

## Slide 14
Finding 5: Most of the volumes in both traces are active throughout the trace periods, while AliCloud is more active than MSRC.
  We divide the traces into 10-minute intervals and examine the activeness in each interval.
  At least 59.4% of the traces are active all the time
  72.2% (55.6%) volumes are active in 95% trace periods of AliCloud (MSRC).
Findings on Load Intensity

## Slide 15
Finding 6: Writes are the dominant factor in determining activeness in both AliCloud and MSRC.
Finding 7: Removing write requests shows drastic decreases in activeness in both AliCloud and MSRC.
  After removing write requests, the number of active volumes drops by more than 58.3% in AliCloud, and 24.6% in MSRC
Findings on Load Intensity

## Slide 16
Finding 8: Random I/Os are common in both traces. The volumes in AliCloud see more random I/Os than those in MSRC.
Randomness: Measured by the minimum distance between offsets of the current request and previous 32 requests
  The request is a random request if the distance is smaller than 128 KiB
  The randomness ratios in top-10 volumes of AliCloud is higher.
Findings on Spatial Patterns

## Slide 17
Finding 9: Reads and writes aggregate in small working sets for a non-negligible fraction of volumes in both AliCloud and MSRC.
  Writes are more aggregated than reads.
Finding 10: Reads and writes tend to aggregate in read-mostly and write-mostly blocks in AliCloud, respectively.
  MSRC shows stronger aggregation in reads, but weaker in writes.
Finding 11: AliCloud generally has higher update coverage than MSRC. The update coverage also varies across volumes.
Findings on Spatial Patterns

## Slide 18
Finding 12: Both traces have large read-after-write (RAW) time, but small write-after-write (WAW) time.
  The median of RAW time in AliCloud (MSRC) is 3.0 hours (16.2 hours).
  The median of WAW time in AliCloud (MSRC) is 1.4 hours (0.2 minutes).
Findings on Spatial Patterns

## Slide 19
Finding 13: Most of the read-after-read (RAR) and write-after-read (WAR) requests in AliCloud have large elapsed time.
  AliCloud: Most of the RAR and WAR times are larger than 1 minute
  MSRC: There exist non-negligible fractions of RAR and WAR times (35.6% and 29.2%, respectively) that are less than 1 minute.
Findings on Spatial Patterns

## Slide 20
Finding 14: Written blocks have varying update intervals.
  Update interval: The elapsed time between two consecutive writes to the same block.
  The update intervals distributes in different values in different percentiles.
Findings on Spatial Patterns

## Slide 21
Finding 15: AliCloud shows higher reduction in miss ratios than MSRC when the cache size increases.
  Cache sizes as the 1% or 10% of WSS of each volume, LRU policy
  In AliCloud, the absolute reduction of the 25th percentile read or write miss ratios is 36.7% and 22.1%
  In MSRC, the corresponding number is only 22.8% and 14.1%
Findings on Spatial Patterns

## Slide 22
Load balancing:
  Writes dominate in the activeness, and the load balancing on writes is more important in AliCloud.
Cache efficiency:
  It is viable to allocate limited cache resources to improve the I/O throughput.
  It is possible to identify read-mostly and write-mostly blocks in the workloads.
  The cloud storage systems may benefit from disk-based write caching.
Storage cluster management:
  Building log structures or upper-layer FTLs may optimize the performance on small and random I/Os and deal with the variation of the update patterns
Implications of Findings

## Slide 23: Conclusion
We provide 15 findings on the I/O characterization in terms of
  Load intensity, spatial patterns, and temporal patterns
We provide important insights from the findings on how to solve problems in
  load balancing, cache efficiency, and storage cluster management
Our traces: https://github.com/alibaba/block-traces

## Slide 24: Thank You! Q & A
Notes: This is all I got. Thanks for your watching.