## Slide 1: Toward I/O-Efficient Protection Against Silent Data Corruptions in RAID Arrays
Mingqiang Li and Patrick P. C. Lee
The Chinese University of Hong Kong
MSST ’14

## Slide 2: RAID
RAID is known to protect data against disk failures and latent sector errors
  How it works? Encodes k data chunks into m parity chunks, such that the k data chunks can be recovered from any k out of n=k+m chunks
[Patterson et al., SIGMOD ’88]

## Slide 3: Silent Data Corruptions
Silent data corruptions:
Data is stale or corrupted without indication from disk drives  cannot be detected by RAID
Generated due to firmware or hardware bugs or malfunctions on the read/write paths
More dangerous than disk failures and latent sector errors
[Kelemen, LCSC ’07; Bairavasundaram et al., FAST ’08; Hafner et al., IBM JRD 2008]

## Slide 4: Silent Data Corruptions
Lost write:
Torn write:
Misdirected writes/reads:
Stale
Stale
(a) Misdirected writes
(b) Misdirected reads
updated

## Slide 5: Silent Data Corruptions
Consequences:
User read:
  Corrupted data propagated to upper layers
User write:
  Parity pollution
Data reconstruction
  Corruptions of surviving chunks propagated to reconstructed chunks

## Slide 6: Integrity Protection
Protection against silent data corruptions:
  Extend RAID layer with integrity protection, which adds integrity metadata for detection
  Recovery is done by RAID layer
Goals:
  All types of silent data corruptions should be detected
  Reduce computational and I/O overheads of generating and storing integrity metadata
  Reduce computational and I/O overheads of detecting silent data corruptions

## Slide 7: Our Contributions
A taxonomy study of existing integrity primitives on I/O performance and detection capabilities
An integrity checking model
Two I/O-efficient integrity protection schemes with complementary performance gains
Extensive trace-driven evaluations

## Slide 8: Assumptions
At most one silently corrupted chunk within a stripe
If a stripe contains a silently corrupted chunk, the stripe has no more than m-1 failed chunks due to disk failures or latent sector errors
Otherwise, higher-level RAID is needed!
D0
D1
D2
D3
D4
D5
P0
P1
m-1=1

## Slide 9: How RAID Handles Writes?
Full-stripe writes:
  Parity chunks are computed directly from data chunks to be written chunks (no disk reads needed)
Partial-stripe writes:
  RMW (Read-modify-writes)  for small writes
    Read all touched data chunks and all parity chunks
    Compute the data changes and the parity chunks
    Write all touched data chunks and parity chunks
  RCW (Reconstruct-writes)  for large writes
    Read all untouched data chunks
    Compute the parity chunks
    Write all touched data chunks and parity chunks

## Slide 10: Existing Integrity Primitives
Self-checksumming / Physical identity
Data and metadata are read in a single disk I/O
Inconsistency implies data corruption
Cannot detect stale or overwritten data
[Krioukov et al., FAST ’08]

## Slide 11: Existing Integrity Primitives
Version Mirroring
Keep a version number in the same data chunk and m parity chunks
Can detect lost writes
Cannot detect corruptions
[Krioukov et al., FAST ’08]

## Slide 12: Existing Integrity Primitives
Checksum Mirroring
[Hafner et al., IBM JRD 2008]
Keep a checksum in the neighboring data chunk (buddy) and m parity chunks
Can detect all silent data corruptions
High I/O overhead on checksum updates

## Slide 13: Comparisons
Question: How to integrate integrity primitives into I/O-efficient integrity protection schemes?
Additional I/O overhead
No additional I/O overhead

## Slide 14: Integrity Checking Model
Two types of disk reads:
  First read: sees all types of silent data corruptions
  Subsequent reads: see a subset of types of silent data corruptions
Observation: A simpler and lower-overhead integrity checking mechanism is possible for subsequent-reads

## Slide 15: Checking Subsequent-Reads
Subsequent-reads can be checked by self-checksumming and physical identity without additional I/Os
Integrity protection schemes to consider:
  PURE (checksum mirroring only), HYBRID-1, and HYBRID-2
Seen by subsequent-reads
No additional I/O overhead
15

## Slide 16: Integrity Protection Schemes
Hybrid-1
  Physical identity + self-checksumming + version mirroring
  A variant of the scheme in [Krioukov et al., FAST ’08]

## Slide 17: Integrity Protection Schemes
Hybrid-2
  Physical identity + self-checksumming + checksum mirroring
  A NEW scheme

## Slide 18: Additional I/O Overhead for a Single User Read/Write
Both Hybrid-1 and Hybrid-2 outperform Pure in subsequent-reads
Hybrid-1 and Hybrid-2 provide complementary I/O advantages for different write sizes
Switch point:

## Slide 19: Choosing the Right Scheme
If choose Hybrid-1
If choose Hybrid-2
= average write size of a workload (estimated through measurements)
= RAID chunk size
The chosen scheme is configured in the RAID layer (offline) during initialization

## Slide 20: Evaluation
Computational overhead for calculating integrity metadata
I/O overhead for updating and checking integrity metadata
Effectiveness of choosing the right scheme

## Slide 21: Computational Overhead
Implementation:
  GF-Complete [Plank et al., FAST’13] and Crcutil libraries
Testbed:
  Intel Xeon E5530 CPU @ 2.4GHz with SSE4.2
Overall results:
  ~4GB/s for RAID-5
  ~2.5GB/s for RAID-6
RAID performance is bottlenecked by disk I/Os, rather than CPU

## Slide 22: I/O Overhead
Trace-driven simulation
  12 workload traces from production Windows servers
  RAID-6 with n=8 for different chunk sizes
[Kavalanekar et al., IISWC ’08]

## Slide 23: I/O Overhead
Pure can have high I/O overhead, by up to 43.74%
I/O overhead can be kept at reasonably low (often below 15%) using the best of Hybrid-1 and Hybrid-2, due to I/O gain in subsequent reads
More discussions in the paper
43.74%

## Slide 24: Choosing the Right Scheme
Accuracy rate: 34/36 = 94.44%
For the two inconsistent cases, the I/O overhead difference between Hybrid-1 and Hybrid-2 is small (below 3%)

## Slide 25: Implementation Issues
Implementation in RAID layer:
  Leverage RAID redundancy to recover from silent data corruptions
Open issues:
  How to keep track of first reads and subsequent reads?
  How to choose between Hybrid-1 and Hybrid-2 based on workload measurements?
  How to integrate with end-to-end integrity protection?

## Slide 26: Conclusions
A systematic study on I/O-efficient integrity protection schemes against silent data corruptions in RAID systems
Findings:
  Integrity protection schemes differ in I/O overheads, depending on the workloads
  Simpler integrity checking can be used for subsequent reads
Extensive evaluations on computational and I/O overheads of integrity protection schemes