## Slide 1: SketchLearn: Relieving User Burdens in Approximate Measurement with Automated Statistical Inference
Qun Huang, Patrick P. C. Lee, Yungang Bao

## Slide 2: Typical Approximate Measurement
Measurement
Algorithm
Configuration
Expected errors
Query thresholds
Domain knowledge
Measurement
Results
Network traffic
Query
Network statistics
Our goal: identify and relieve user burdens for approximate measurement

## Slide 3: User Burden 1
Measurement
Algorithm
Configuration
Expected errors
Query thresholds
Domain knowledge
Measurement
Results
Network traffic
Query
Network statistics
1: Hard to specify
Errors need to be specified:
bias: an answer deviates true answer by ε
failure probability: fail to produce small-error answer with a probability δ

## Slide 4: User Burden 2
Measurement
Algorithm
Configuration
Expected errors
Query thresholds
Domain knowledge
Measurement
Results
Network traffic
Query
Network statistics
1: Hard to specify
2: Hard to know in advance
Large-threshold configurations fail to work for small-threshold queries
No guideline for sufficiently small threshold
Vary across management operations and traffic characteristics

## Slide 5: User Burden 3
Measurement
Algorithm
Configuration
Expected errors
Query thresholds
Domain knowledge
Measurement
Results
Network traffic
Query
Network statistics
1: Hard to specify
2: Hard to know in advance
3: Hard to follow theory to tune
Domain knowledge is not always available
Theories usually show worst-case results
Configuration for worst case not practically efficient

## Slide 6: User Burden 4
Measurement
Algorithm
Configuration
Expected errors
Query thresholds
Domain knowledge
Measurement
Results
Network traffic
Query
Network statistics
1: Hard to specify
2: Hard to know in advance
3: Hard to follow theory to tune
4: Hard to redefine flow-keys
Algorithm works on a particular flow-key
Flow-key definition must be fixed in deployment

## Slide 7: User Burden 5
Measurement
Algorithm
Configuration
Expected errors
Query thresholds
Domain knowledge
Measurement
Results
Network traffic
Query
Query Results
1: Hard to specify
2: Hard to know in advance
3: Hard to follow theory to tune
4: Hard to redefine flow-keys
5: Hard to quantify actual errors
Infeasible to track errors for a particular flow
Configuration only tells worst-case and overall errors

## Slide 8: All User Burdens
Measurement
Algorithm
Configuration
Expected errors
Query thresholds
Domain knowledge
Measurement
Results
Network traffic
Query
Query Results
1: Hard to specify
2: Hard to know in advance
3: Hard to follow theory to tune
4: Hard to redefine flow-keys
5: Hard to quantify actual errors

## Slide 9: Our Work
Relieve five user burdens
Performance
  Catch up with underlying packet forwarding speed
Memory efficiency
  Consume only limited memory
Accuracy
  Preserve high accuracy of sketches
Generality
  One design and one configuration for multiple tasks
  Deployable in both software and hardware
SketchLearn: Sketch-based measurement system with limited user burdens

## Slide 10: Root Cause: Resource Conflicts
Previous work: perfect configuration to eliminate conflicts
  Determined by many factors
Algorithm
Flow definition
Query parameters
Resource conflicts
Input data
Configuration

## Slide 11: High-Level Idea
Not pursue perfect configurations to mitigate resource conflicts
  Hard to identify right trade-offs
Characterize resource conflicts in an “imperfect” configuration
Network queries
Data structure with
imperfect configuration
Conflict model
Statistical
Properties
Expected errors
Query parameters
Flow definitions
Not necessary
Domain knowledge

## Slide 12: How to Realize?
Network queries
Data structure with
imperfect configuration
Conflict model
Statistical
Properties

## Slide 13: Design Data Structure
Network queries
Data structure with
imperfect configuration
Conflict model
Statistical
Properties

## Slide 14: Multi-level Sketch [Cormode, ToN 05]
L: # of bits considered
Data structure: L+1 levels (from 0 to L), each of which is a counter matrix
Level 0 is always updated
Level k is updated iff k-th bit in a flowkey is 1
All levels share same hash functions

## Slide 15: Statistical Properties of Resource Conflicts
Network queries
Conflict model
Statistical
Properties
Multi-level
Sketch

## Slide 16: Properties
Does a flow update level k?
  Depends on inherent distribution of flow keys
Does a flow update bucket (i, j)?
  Depends on hash functions of sketch
A theory should characterize the above two factors

## Slide 17: Main Theorem
Main Theorem: if no large flows, follows Gaussian distribution with mean p[k]
p[k]: probability that k-th bit is 1
: counter of bucket (i,j)
: counter of bucket (i,j)
random variable

## Slide 18: Build Conflict Model
Network queries
Conflict model
Main
Theorem
Multi-level
Sketch

## Slide 19: Statistical Model Inference
Goals
  Extract all large flows
  Guarantee remaining flows in sketches are small
  Estimate Gaussian distributions for each level
Challenges
  No guidelines to distinguish large and small flows

## Slide 20: Self-Adaptive Inference Algorithm
Multi-Level
Sketch
Imperfect
Gaussian Distribution
Large Flows
Estimate Gaussian distributions
Extract large flows
Remove extracted large flows （Flow extracted）
Use smaller threshold （No flow extracted）

## Slide 21: Self-Adaptive Inference Algorithm
Multi-Level
Sketch
Imperfect
Gaussian Distribution
Large Flows
Estimate Gaussian distributions
Extract large flows
Remove extracted large flows （Flow extracted）
Use smaller threshold （No flow extracted）

## Slide 22: Large Flow Extraction
Intuition: a large flow
  (i) results in extremely (large or small) , or
  (ii) at least deviates from its expectation p[k] significantly
Key idea: examine and its difference from p[k], then
  Determine k-th bit of a large flow (assuming it exists)
  Estimate frequency
  Associate flow confidence
More details in paper!

## Slide 23: Guarantee
Theorem: w is sketch width, flows exceeding 1/w of total must be extracted
  Empirical results: even flows that are smaller than 1/w can also be extracted！
64KB: flows above 0.6% of total traffic can be extracted (by theorem)
Practice: >99% flows exceeding 0.3% are also extracted with 64KB

## Slide 24: How to Perform Network-wide Queries?
Multi-level
Sketch
Self-adaptive
Model Inference
Decoupled
Components
Extracted Large Flows
Residual
Sketch
Conflict Characteristics
Flow
Confidence
Gaussian
Distributions
Main
Theorem
Network queries

## Slide 25: Supported Network Queries
Per-flow byte count
Heavy hitter detection
Heavy changer detection
Cardinality estimation
Flow size distribution estimation
Entropy estimation

## Slide 26: Extended Query Model
Allow query for arbitrary flowkeys
  Only use corresponding levels
Estimate actual query errors
  Use attached errors for each large flow
  Use Gaussian distributions

## Slide 27: Putting It Together
Multi-level
Sketch
Self-adaptive
Model Inference
Decoupled
Components
Extracted Large Flows
Residual
Sketch
Conflict Characteristics
Flow
Confidence
Gaussian
Distributions
Network-wide
Query Runtime
Main
Theorem

## Slide 28: (Slight) User Burdens
Users now just need to configure the multi-level sketch
Expected errors
Query parameters
Flow definitions
Domain knowledge
Multi-level
Sketch
Not necessary
One row suffices
Columns: based on minimum flow or memory budget
Example:
400 KB memory
Require flows exceeding 0.1%
1000 columns

## Slide 29: Implementation
Challenge: updating L+1 levels is time consuming
Solution: parallel updating
  L+1 levels are independent
Software
  Based on OpenVSwitch + DPDK
  Parallelism with SIMD
Hardware
  Based on P4 programmable switches
  Parallelism with P4 pipeline stages

## Slide 30: Evaluation
Platforms
  Software: OpenVSwitch + DPDK
  Hardware: Tofino swtich
  Large-scale simulation
Traces
  Caida 2017
  Data center traffic (IMC 2010)

## Slide 31: Fitting Theorem
Guaranteed boundary of flow extraction
Flows that are guaranteed to be extracted
Flows that are not guaranteed (but are likely) to be extracted

## Slide 32: Arbitrary Flow Keys
Query for three flow keys
Heavy hitter detection
Traffic size distribution

## Slide 33: More Experiments
Resource consumption
Generality for various measurement tasks
Efficiency of attached query errors
Network-wide measurement

## Slide 34: Conclusion
Analyze 5 user burdens in existing approximate measurement
SketchLearn framework
  Multi-level data structure design
  Theory: counters follow Gaussian distributions when no large flows
  Self-adaptive model inference algorithm
  Extended query models
Prototype and evaluations
Source code available at: https://github.com/huangqundl/SketchLearn

## Slide 35: Limitations and Future Work
Less pipeline consumptions
Quantify Gaussian distributions and convergence rate
More applications