## Slide 1: Stochastic Modeling of Large-Scale Solid-State Storage Systems: Analysis, Design Tradeoffs and Optimization
Yongkun Li, Patrick P. C. Lee and John C.S. Lui
The Chinese University of Hong Kong, Hong Kong
Sigmetrics’13

## Slide 2: SSD Storage is Emerging
Solid-state drives (SSDs) are widely adopted in data centers
  Examples: EMC XtremIO Array, NetApp Sandisk, Micron P420m
Pros of SSDs:
  High I/O throughput, low power, high reliability
Cons of SSDs:
  Wear-out
EMC XtremIO [Source: http://www.crn.com]

## Slide 3: How SSDs Work?
Organized into blocks
Each block has 64 or 128 pages of size 4KB each
Three basic operations: read, write, erase
  Read, write: per-page basis
  Erase: per-block basis
Out-of-place write for updates:
  Write to a clean page and mark it as valid
  Mark original page as invalid

## Slide 4: How SSDs Work?
Garbage collection (GC) needed to reclaim clean pages
  Choose a block to erase
  Move valid pages to another clean block
  Erase the block
Challenges:
  Blocks can only be erased a finite number of times
    SLC: 100K; MLC: 10K; 3-bit MLC: several K to several hundred
  When a block reaches the limit, it wears out
  Bit error rates increase as blocks wear down
2
1
0
Block A
Block B
Block B
1. write
2. erase
0
2
Block A
Before GC
After GC

## Slide 5: Motivation
Design tradeoff of GC algorithms
  Minimizing cleaning cost
    reclaim the block with smallest number of valid pages
    improve I/O throughput and minimize write amplification
  Maximizing wear-leveling
    erase all blocks as evenly as possible
    improve durability
Problems
  How to model the performance-durability tradeoff of GC algorithms?
  How to parameterize a GC algorithm to adapt to different tradeoff requirements?

## Slide 6: Our Work
Develop a Markov model to characterize I/O dynamics
Use mean-field analysis to derive asymptotic steady state
Develop an optimization framework to analyze the tradeoff
Propose a tunable GC algorithm which operates along the optimal tradeoff curve
Conduct trace-driven simulations on DiskSim with SSD add-ons
Construct an analytical model that characterizes tradeoff between cleaning cost and wear-leveling for a general class of GC algorithms

## Slide 7: Related Work on GC
  Empirical analysis:
    Agrawal et al. (USENIX ATC08) addressed tradeoff between cleaning cost and wear-leveling in GC
  Theoretical analysis on GC: focus on write amplification
  Hu et al. (SYSTOR09), Bux et al. (Performance10), Desnoyers (SYSTOR12): model different greedy algorithms on GC
  Benny Van Houdt (Sigmetrics13) also models write amplification of GC algorithms using mean field technique
  Our work analyzes performance tradeoff of different GC algorithms, with more general access pattern and address mapping; also conducts trace-driven simulations

## Slide 8: Markov Model
Consider an SSD containing physical blocks, each with pages
  Classify blocks into different types
    : type of block at time
    A block is of type iff it has valid pages ()
  System state:
Transformation:
  : number of type blocks at time
0
1
2
Block
valid pages 

## Slide 9: I/O Dynamics
Read
  Does not change
GC
  Always reallocate valid pages to a new (clean) block
  Does not change
2
1
0
Block A
Block B
Block B
1. write
2. erase
0
2
Block A
Before GC
After GC
Notes: Note: In our work, we assume that when reclaim a block, the valid pages in the block are reallocated to a NEW block
PS: For page level address mapping, even if there is a write frontier, and all writes are
directed to the frontier, which makes the system evolves in a deterministic way, in a long term, we can still analyze it in probabilistic way.

## Slide 10: I/O Dynamics
Program (write data to flash)
  Changes a block from type to
Invalidate (mark the data as invalid)
  Changes a block from type to
2
1
0
Before
2
1
0
3
After
2
1
0
Before
2
1
0
After
Notes: We focus on the flash level I/O here

## Slide 11: State Transition
Only consider program and invalidate requests
  Arrive as a Poisson process with rate
  Uniform access pattern:
    each block has the same probability of being accessed
    probability of the requested page being invalidated is proportional to number of valid pages in the block
What about the state transition of an SSD?
State transition of a block
Notes: We consider accesses in physical address space.

## Slide 12: State Transition
State space of is huge
  Cardinality =
  For 256GB SSD,  huge state space!
Resort to mean-field analysis to make the model tractable
Occupancy measure
  : fraction of type blocks at time
  Stochastic process
Notes: NOTE:
The state space of n^N(t) is large, so it is difficult to derive n^N(t), we use mean field analysis.
When we use mean field analysis, our goal is to derive the occupancy measure
M^N(t) instead of n^N(t). The occupancy measure M^N(t) is a continuous vector.

## Slide 13: Mean Field Analysis
Stochastic process converges to a deterministic process (mean field limit) as N is large
  : fraction of type blocks at time
  ODEs:
Proof in technical report.

## Slide 14: Steady-State Solution
Deterministic process converges to a steady-state solution (fixed point)
  (uniform case)
approximates the steady-state solution of the occupancy measure
The SSD contains fraction of type blocks in steady state
Proof in technical report.

## Slide 15: General Access Pattern
Define as the transition probability of a type block being transited to state for each request
ODEs:
Fixed point can be derived accordingly
See our validation results in the paper

## Slide 16: Performance Metrics
Formalize GC algorithms
  Define as the weight of selecting a type block for each GC
  Constraint:
Performance metrics
  Cleaning cost:
    Average number of valid pages that are reallocated
  Wear-leveling:
    How evenly each block is reclaimed
Prob. of choosing any type block
Prob. of choosing a particular type block
Notes: Using pi as input, choose w_i that minimizes cleaning cost or maximizes wear leveling

## Slide 17: Tradeoff Analysis
Maximizing wear-leveling
Solution
  for all
  (for uniform case)
  Choose every block with the same probability in each GC
  Random algorithm

## Slide 18: Tradeoff Analysis
Minimizing cleaning cost
Solution
  for all
  (for uniform case)
  Choose the block with smallest number of valid pages in each GC
  Greedy algorithm

## Slide 19: Tradeoff Analysis
Optimal tradeoff
Solution
Greedy algorithm
minimizes cleaning cost
Random algorithm
maximizes wear-leveling
tradeoff
Notes: Identify the full design space of GC algorithms
NOTE: Due to the symmetric nature, we are not interested in the cases when C^* > \sumi\pi_i . So random and greedy stand for two extreme points in the tradeoff curve.
The symmetric phenomenon can be viewed from the figure shown in our paper.

## Slide 20: Randomized Greedy Algorithm
Randomized Greedy Algorithm (RGA)
  Random step: Randomly choose (window size) blocks
  Greedy step: Choose the block that has the smallest number of valid pages among the blocks for GC
  If : random algorithm
  If : greedy algorithm
Performance
  Cleaning cost:
  Wear-leveling:
MD Mitzenmacher, “The Power of Two Choices in Randomized Load Balancing”, 1996

## Slide 21: Numerical Results
Performance tradeoff
Tradeoff indeed exists for GC algorithms
RGA operates along the optimal tradeoff curve

## Slide 22: Experimental Results
Environment: DiskSim with SSD add-ons
System configuration
  32GB SSD with 8 flash chips, with 16,384 physical blocks each
  GC is performed independently in each chip
  Each block has 64 pages of size 4KB each
  15% storage space preserved
  Threshold for triggering GC: free blocks less than 5%
Datasets
  Financial, Webmail, Online and Webmail+Online
  Write intensive (around 80% write requests)

## Slide 23: Cleaning Cost & Wear-leveling
Greedy algorithm has the lowest cleaning cost and random algorithm achieves the highest wear-leveling
RGA balances the tradeoff
See our paper for I/O throughput and durability results
Notes: Note: Reason why the cleaning cost could be so small: In this simulation, the address space is much smaller than the SSD capacity (the whole logical space), and the locality of the workload is also high (which means that only a small fraction of addresses are
accessed very frequently), so when GC is triggered every time, the block which is selected by GC contains very small number of valid pages (0 in many times).
Workload statistics:
All are write intensive (around 80% write requests).
Financial is random write dominant (sequential ratio is less than 1%)
Other three are sequential write dominant (sequential ratio is bigger than 70%)

## Slide 24: Summary
Propose a stochastic model that characterizes tradeoff between cleaning cost (performance) and wear-leveling (durability) of GC algorithms in SSDs
  Random algorithm and greedy algorithm stand for the two extreme points in the tradeoff curve
Propose a randomized greedy algorithm that operates on the optimal tradeoff curve
Conduct extensive trace-driven simulations
Future work:
  Hot/cold separation, address mapping, RAID reliability