## Slide 1: Face pose tracking using the four-point algorithm
Ho Yin Funga, Kin Hong Wonga, Ying Kin Yu , Kwan Pang Tsuib, and Ho Chuen Kama
a Department of Computer Science and Engineering,
The Chinese University of Hong Kong
b Department of Mechanical Engineering,
The Chinese University of Hong Kong
Tuesday, 2 May 2017
Objective
Motivation
Our proposal
Perspective-Four-Point
Expr. & Results
Conclusion

## Slide 2: Contents
Objective
Motivation
Our proposal
Perspective-Four-Points
Experiments and Results
Conclusion
Objective
Motivation
Our proposal
Perspective-Four-Point
Conclusion
Expr. & Results

## Slide 3: Contents
Objective
Motivation
Our proposal
Perspective-Four-Points
Experiments and Results
Conclusion
Objective
Motivation
Our proposal
Perspective-Four-Point
Conclusion
Expr. & Results

## Slide 4: Objective
We would like to develop a head pose tracking device for virtual reality application.
Objective
Motivation
Our proposal
Perspective-Four-Point
Conclusion
Expr. & Results

## Slide 5: Objective
We would like to develop a head pose tracking device for virtual reality applications.
Face tracking system and the four-point algorithm are proposed and developed.
6 DOF of face pose can then be found.
Objective
Motivation
Our proposal
Perspective-Four-Point
Exp. & Results
Conclusion

## Slide 6: Contents
Objective
Motivation
Our proposal
Perspective-Four-Points
Experiments and Results
Conclusion
Conclusion
Objective
Motivation
Our proposal
Perspective-Four-Point
Conclusion
Expr. & Results

## Slide 7: Motivation
Head pose tracking is useful in various applications.
Can be used as interactive inputs for users, even for the disabled.
Objective
Motivation
Our proposal
Perspective-Four-Point
Conclusion
Expr. & Results

## Slide 8: Motivation
Using Inertial Measurement Unit alone can only output relative positions only.
It also has a drift problem, i.e. accumulated error from integration.
Objective
Motivation
Our proposal
Perspective-Four-Point
Conclusion
Expr. & Results

## Slide 9: Contents
Objective
Motivation
Our proposal
Perspective-Four-Points
Experiments and Results
Conclusion
Objective
Motivation
Our proposal
Perspective-Four-Point
Conclusion
Expr. & Results

## Slide 10: Our proposal
Our system has two components , namely
  Face detection tool
  Pose estimation
First a face detection library called “DLib” is used to extract the human face and locate facial features.
Then four of the features are selected, and are passed to the next step for pose estimation.
Objective
Motivation
Our proposal
Perspective-Four-Point
Conclusion
Expr. & Results

## Slide 11: Face Detection & Feature Extraction
DLib library can automatically detect and track faces.
By using 68 landmark points we get features
Our proposal only uses 4 of them.
Objective
Motivation
Our proposal
Perspective-Four-Point
Conclusion
Expr. & Results

## Slide 12: Contents
Objective
Motivation
Our proposal
Perspective-Four-Points
Experiments and Results
Conclusion
Objective
Motivation
Our proposal
Perspective-Four-Point
Conclusion
Expr. & Results

## Slide 13: Perspective-Four-Point
Perspective-Four-Point (four-point) is an iterative algorithm.
If we know the model of four 3-D feature points, and their correspondence image points, pose of the object relative to the camera can be found.
Objective
Motivation
Our proposal
Perspective-Four-Point
Conclusion
Expr. & Results

## Slide 14: Perspective-Four-Point
Suppose we have four model points defined as t=0:
Their image projection points can be detected as:
Objective
Motivation
Our proposal
Perspective-Four-Point
Conclusion
Expr. & Results

## Slide 15: Perspective-Four-Point
As this is a rigid body, the relative distance among these model points at any time can be known.
Objective
Motivation
Our proposal
Perspective-Four-Point
Conclusion
Expr. & Results
||A(1,t)-A(4,t)||
D(1,4)=

## Slide 16: Perspective-Four-Point
With the above information + focal length ,we can determine the length between the camera center and model points.
Objective
Motivation
Our proposal
Perspective-Four-Point
Conclusion
Expr. & Results

## Slide 17: Perspective-Four-Point
Now we can relate the 3-D Model with the length by the following vector:
Where is the unit vector.
Objective
Motivation
Our proposal
Perspective-Four-Point
Conclusion
Expr. & Results

## Slide 18: Problem Formulation
Aim: Find the Length l.
What we have:
  Image measurements:
  The model ( )i=1,2,3,4
  Focal length
Objective
Motivation
Our proposal
Perspective-Four-Point
Conclusion
Expr. & Results

## Slide 19: Forming Constraints
By using the distances among four points and using cosine law:
The predicted form is:
Objective
Motivation
Our proposal
Perspective-Four-Point
Conclusion
Expr. & Results

## Slide 20: Forming Constraints
From the above formulae, the generalized error function:
With four points, we have 6 combinations of I and J.
Objective
Motivation
Our proposal
Perspective-Four-Point
Conclusion
True
Predicted
Expr. & Results

## Slide 21: Extra Constraint
Using the above 6 constraints is not enough. (Liu & Wong 1999).
One more constraint is added to ensure unique solution.
The difference of true and guessed:
Objective
Motivation
Our proposal
Perspective-Four-Point
Conclusion
Expr. & Results

## Slide 22: Iterative Processing
After developing 7 error functions/constraints, now we minimized the error using a Gauss-Newton method.
At Initialization:
Initial Guess:
Iteration from k = 0 to Kmax :until L is very small
Objective
Motivation
Our proposal
Perspective-Four-Point
Conclusion
Where J is a Jacobian matrix:
Expr. & Results
meter

## Slide 23: Contents
Objective
Motivation
Our proposal
Perspective-Four-Points
Experiments and Results
Conclusion
Objective
Motivation
Our proposal
Perspective-Four-Point
Conclusion
Expr. & Results

## Slide 24: Simulations
We performed a simulation to prove our proposed method.
  4 feature points on 3-D space were created w.r.t features on face.
  Points were moved for 50 time-steps with randomness. (Model)
  Random image noise with normal distribution was also added (Measurement)
  Finally they are fed into the four-point algorithm to recover the pose.
Objective
Motivation
Our proposal
Perspective-Four-Point
Conclusion
Expr. & Results

## Slide 25: Simulation Results
Translation
Rotation
Objective
Motivation
Our proposal
Perspective-Four-Point
Conclusion
Legend:
‘o’: By Four-point algorithm
‘+’: Ground Truth
Expr. & Results

## Slide 26: Simulation Result - Error
For 1000 trials:
Objective
Motivation
Our proposal
Perspective-Four-Point
Conclusion
Expr. & Results

## Slide 27: Real Experiments - Video
Demo video
Objective
Motivation
Our proposal
Perspective-Four-Point
Conclusion
Expr. & Results
https://www.youtube.com/watch?v=XqvpIsX7XRg

## Slide 28: Contents
Objective
Motivation
Our proposal
Perspective-Four-Points
Experiments and Results
Conclusion
Objective
Motivation
Our proposal
Perspective-Four-Point
Conclusion
Expr. & Results

## Slide 29: Discussion & Conclusion
We successfully built a system to integrate face detection algorithm ‘dLib’ to a pose estimation.
10 frames per second.
Effective in tracking the face pose.
Still need to improve “lost-tracking” issues.

## Slide 30: References
[1] Davis E. King. Dlib-ml: A machine learning toolkit. Journal of Machine Learning Research, 10:1755{
1758, 2009.
[2] Man Lee Liu and Kin HongWong. Pose estimation using four corresponding points. Pattern Recognition
Letters, 20(1):69{74, 1999.
[3] Pengfei Sun, Changku Sun, Wenqiang Li, and Peng Wang. A new pose estimation algorithm using a
perspective-ray-based scaled orthographic projection with iteration. PloS one, 10(7):e0134029, 2015.
[4] Zimiao Zhang, Shihai Zhang, and Qiu Li. Robust and accurate vision-based pose estimation algorithm
based on four coplanar feature points. Sensors, 16(12):2173, 2016.
[5] Alfredo Liverani, Alessandro Ceruti, and Gianni Caligiana. Tablet-based 3d sketching and curve reverse
modelling. Int. Journ. of Comp. Aided Engineering and Technology 8, 5(2-3):188{215, 2013.
[6] Zimiao Zhang, Bin Liu, and Yongxiang Jiang. A two-step pose estimation method based on four
non-coplanar points. Optik-Int. Journ. for Light and Electron Optics, 126(17):1520{1526, 2015.
[7] Zhe Zhang and Kin HongWong. A novel geometric approach for camera calibration. In Image Processing
(ICIP), 2014 IEEE Int. Conf. on, pages 5806{5810. IEEE, 2014.

## Slide 31: Thank You!
Q & A
Objective
Motivation
Our proposal
Perspective-Four-Point
Experiments & Results
Conclusion