## Slide 1: Arduino experiments
http://www.cse.cuhk.edu.hk/~khwong/www2/stem/stem.html
http://www.cse.cuhk.edu.hk/~khwong/www2/stem/test_code_ino.zip
KH Wong

## Slide 2: Teaching plan
Class | Theory & tutorials (30 mins) | Experiments ( 2 hours)
1 | Digital logic: AND/OR gates | Arduino IDE: use it for logic calculation. Test 1 Digital logic and LED, Input on/off switch
2 | Number systems | Test 2 : Pulse width modulation; Test 3: Temperature sensing
3 | Basic electronic systems, resistors, capacitor etc. | Test 4: LCD display; Humidity sensor, Test 5: Motors
4 | Ohms law: Voltage current calculation | Test 6: Servo motor Test 7: Stepping motor; Test 8: LDR sensor, Test 9: Real Time clock RTC
5 | Digital sampling theory and techniques | Test 10: Radio Frequency Identification (RFID); Test 11: IR remote control and relay, Test 12: L298 H-bridge drives
6 | Project development methods | Test 13: 2-axis gyroscope Test 14: Self balancing robot theory Test 15: Clap sound detection; Test 16: Ultrasonic range sensor, Test 17: Inertial measurement unit (IMU) & display

## Slide 3: Arduino Uno configuration
Reference
From : https://store.arduino.cc/arduino-uno-rev3
Use ATmega328P (datasheet).
It has 14 digital input/output pins (of
which 6 can be used as PWM outputs), 6 analog inputs,
a 16 MHz quartz crystal, a USB connection,
a power jack, an ICSP header and a reset button.Mixed signal (analog and digital)

## Slide 4: Some good projects by others
Top 10 Best Arduino Projects - Maker Tutor
https://www.youtube.com/watch?v=nfm3qQoZIuo
TOP 10 Arduino Projects Of All Time | 2018
https://www.youtube.com/watch?v=-p_8u_0GNZE
Inside an Autonomous Self Balancing Robot #1 (Tutorial)
https://www.youtube.com/watch?v=s5m-DTn8jyw
7 Pro Arduino Projects with DIY Instructions
https://www.youtube.com/watch?v=XxmD70Wvmdw
13 NEW Arduino Projects for Beginners in 2023!
https://www.youtube.com/watch?v=LwZ35wZJreU
Top 10 Arduino Projects 2023 | DIY Arduino Ideas
https://www.youtube.com/watch?v=qeKgDYf8wKM

## Slide 5: Experiments
http://www.cse.cuhk.edu.hk/~khwong/www2/stem/stem.html
http://www.cse.cuhk.edu.hk/~khwong/www2/stem/test_code_ino.zip
Using the Arduino Uno board

## Slide 6: Overview of experiments in stem2.ppt
Test2.1: LED blink
Test2.2: PWM control LED lighting, serial interface, echoing
Test2.3: Temperature sensing
Test2.4: LCD display
Test2.5: LCD display of humidify and temperature
Test2.5: Humidify and temperature sensors
Test2.6: servo motor --use PC-python to control servo motor
Test2.7: Stepping motor
Test2.8: LDR Light dependent resistor
Test2.9: RTC Real time clock
Test2.10: RFID
Test2.11: test11_IRremote_relay
Test2.12: L298 H-bridge drives 2 Direct Current D.C. motors
Test2.13: 2-axis Gyroscope
Test2.14: self balance robot, test14_self_bal.ino
Test2.15: clap_sound_detection
Test2.16: Ultrasonic range sensor
Test2.17: IMU GY-801 IMU BMP180 ADXL345
Test2.18: OLED display panel 0.96” 128x32
Test19: Keypad

## Slide 7: Classifications of experiments in stem2.ppt
Digital output
  Test2.1: LED blink
  Test2.2: PWM control LED lighting, serial interface, echoing
Digital input
  Test19: Keypad
Analog Input
  Test2.3: Temperature sensing
  Test2.5: Humidify and temperature sensors
  Test2.8: LDR Light dependent resistor
Display
  Test2.4: LCD display
  Test2.18: OLED display panel 0.96” 128x32
  Test2.5: LCD display of humidify and temperature
Motor control
  Test2.6: servo motor --use PC-python to control servo motor
  Test2.7: Stepping motor
  Test2.12: L298 H-bridge drives 2 Direct Current D.C. motors
Digital devices
  Test2.9: RTC Real time clock
  Test2.10: RFID
  Test2.13: 2-axis Gyroscope
  Test2.15: clap_sound_detection
Remote control
  Test2.11: test11_IRremote_relay
Projects:
  Test2.17: IMU GY-801 IMU BMP180 ADXL345
  Test2.14: self balance robot, test14_self_bal.ino
  Test2.16: Ultrasonic range sensor

## Slide 8: Use of breadboard
https://learn.sparkfun.com/tutorials/how-to-use-a-breadboard/all
Connected horizontally
Connected horizontally
Connected horizontally
Connected vertically

## Slide 9: Test1: LED blink test1_LED.ino
int ledPin = 12; // LED (light emitted diode) pin assignment
void setup() //== comment, for user only, system will ignore it
{ // select output port for LED
pinMode(ledPin, OUTPUT);
}
void loop()
{
digitalWrite(ledPin, HIGH); //Rurn on LED
delay(1000); //delay for 1000ms
digitalWrite(ledPin, LOW); //Turn off LED
delay(1000); //delay for 1000ms
}
Pin12
GND
(ground)
1K resistor
LED
Figure 1
+
-
Video demo1 LED
https://youtu.be/PiTh_vDWLf8

## Slide 10: The LED circuit
LED Long leg
LED
short leg
LED
short leg
LED Long leg
pin12
+
-
5V
GND
ground
pin12
10K Ohms
resistor
1KΩ Color code
Brown, black, red, gold(+/- 5%)
http://www.circuitstoday.com/resistor-color-code-chart

## Slide 11: Tutorial exercise 2.1
What is the output pin number?
How to double the blinking rate ?
What is the color code for a 1K Ohms resistor?
Voltage drop of the red LED is 1.8V, calculate the current passing through the LED. See https://en.wikipedia.org/wiki/LED_circuit

## Slide 12: Answer: Tutorial exercise 2.1
What is the output pin number?
Answer: Pin 12
How to double the blinking rate ?
Answer: Changes:
Line 9) delay(500); //delay for 500ms
Line 11) delay(500); //delay for 500ms
What is the color code for a 1K Ohms resistor?
Answer: Brown, black, red, gold
Voltage drop of the red LED is 1.8V, calculate the current passing through the LED.
Answer : (5-1.8)/1000=3.2mA. If you want to make the LED brighter, use a smaller resistor to increase the current (not less than 100, otherwise, the large current will damage the LED).

## Slide 13: Test 2.2a: PWM control LED lighting, serial interface test 2.2a_PWM_LED.ino
int potpin=0;//Input pin
int ledpin=12;//output pin for LED
int val=0;//variable
void setup()
{pinMode(ledpin,OUTPUT);//define LED outpiin pin
Serial.begin(9600);//set Serial port transfer rate 9600 bit per second
}
void loop()
{digitalWrite(ledpin,HIGH);//turn on LED
delay(val+25);//time delay depends on val
digitalWrite(ledpin,LOW);// turn off LED
delay(val+25); //time delay depends on val
val=analogRead(potpin);//read variable resistor = val
Serial.println(val);//send this to computer for display
} // val is controlled by the variable resistor
A0
Figure 2
Add this to Figure 1
Video demo2 PWM LED
https://youtu.be/N7AkSPDNMr0
Add this circuit
to test1

## Slide 14: PWM_test1 by interrupt using TimerOne
//https://www.arduino.cc/reference/en/libraries/timerone/
//IDE/Examples/Timerone/Fanspeed
#include <TimerOne.h>
// This example creates a PWM signal with 25 kHz carrier.
//
// Arduino's analogWrite() gives you PWM output, but no control over the
// carrier frequency. The default frequency is low, typically 490 or
// 3920 Hz. Sometimes you may need a faster carrier frequency.
//
// The specification for 4-wire PWM fans recommends a 25 kHz frequency
// and allows 21 to 28 kHz. The default from analogWrite() might work
// with some fans, but to follow the specification we need 25 kHz.
//
// http://www.formfactors.org/developer/specs/REV1_2_Public.pdf
//
// Connect the PWM pin to the fan's control wire (usually blue). The
// board's ground must be connected to the fan's ground, and the fan
// needs +12 volt power from the computer or a separate power supply.
const int fanPin = 9;
void setup(void) {
Timer1.initialize(40); // 40 us = 25 kHz
Serial.begin(115200);
}
void loop(void) {
// slowly increase the PWM fan speed
float min_speed = 50.0; // can find this by trial-and-error
for (float dutyCycle = min_speed; dutyCycle < 100.0; dutyCycle++) {
Serial.print("PWM Fan, Duty Cycle = ");
Serial.println(dutyCycle);
Timer1.pwm(fanPin, (dutyCycle / 100) * 1023);
delay(500);
}
}

## Slide 15: PWM test2: drive motor , speed controlled (one side) by V.R. thru. A0, based on timerOne (interrupt)
//https://www.arduino.cc/reference/en/libraries/timerone/
//IDE/Examples/Timerone/Fanspeed
#include <TimerOne.h>
// This example creates a PWM signal with 25 kHz carrier.
//
// Arduino's analogWrite() gives you PWM output, but no control over the
// carrier frequency. The default frequency is low, typically 490 or
// 3920 Hz. Sometimes you may need a faster carrier frequency.
//
// The specification for 4-wire PWM fans recommends a 25 kHz frequency
// and allows 21 to 28 kHz. The default from analogWrite() might work
// with some fans, but to follow the specification we need 25 kHz.
//
// http://www.formfactors.org/developer/specs/REV1_2_Public.pdf
//
// Connect the PWM pin to the fan's control wire (usually blue). The
// board's ground must be connected to the fan's ground, and the fan
// needs +12 volt power from the computer or a separate power supply.
const int fanPin = 9;
void setup(void) {
Timer1.initialize(40); // 40 us = 25 kHz
Serial.begin(115200);
}
void loop(void) {
// slowly increase the PWM fan speed
// float min_speed = 50.0; // can find this by trial-and-error
/*
for (float dutyCycle = 70; dutyCycle < 100.0; dutyCycle++) {
Serial.print("PWM Fan, Duty Cycle = ");
Serial.println(dutyCycle);
Timer1.pwm(fanPin, (dutyCycle / 100) * 1023);
delay(500);
}
*/
// float input = analogRead(A0);//convet to 0-99, analogRead range 0-1023, from 0 to 5V
// float dutyCycle=(input/1024)*100;
float dutyCycle=((float)analogRead(A0)/1024)*100;//convet to 0-99,analogRead :0-1023
Serial.print("PWM Fan, Duty Cycle in % = ");
Serial.println(dutyCycle);
Timer1.pwm(fanPin, (dutyCycle / 100) * 1023);
}
A0
GPIO9
5V
GND
IN1
IN2
H-bridge
L298
GND
DC
Motor
Arduino
UNO
10K B

## Slide 16: PWM test3: drive motor (clockwise, anticlockwise) , speed controlled by V.R. thru. A0, based on timerOne (interrupt), (added deadband)
//https://www.arduino.cc/reference/en/libraries/timerone/
//based on IDE/Examples/Timerone/Fanspeed
#include <TimerOne.h>
// This example creates a PWM signal with 25 kHz carrier.
//
// Arduino's analogWrite() gives you PWM output, but no control over the
// carrier frequency. The default frequency is low, typically 490 or
// 3920 Hz. Sometimes you may need a faster carrier frequency.
//
// The specification for 4-wire PWM fans recommends a 25 kHz frequency
// and allows 21 to 28 kHz. The default from analogWrite() might work
// with some fans, but to follow the specification we need 25 kHz.
//
// http://www.formfactors.org/developer/specs/REV1_2_Public.pdf
//
// Connect the PWM pin to the fan's control wire (usually blue). The
// board's ground must be connected to the fan's ground, and the fan
// needs +12 volt power from the computer or a separate power supply.
const int fanPin1 = 9;
const int fanPin2 = 10;
void setup(void) {
Timer1.initialize(40); // 40 us = 25 kHz
Serial.begin(115200);
}
void loop(void) {
float reading = ((float)analogRead(A0) - 511.5) / 5.115; // adjusted middle =0, can be fanged from -513 or +513; reading from -100 to 100
float dutyCycle;
Serial.print("reading (-100 to 100) = ");
Serial.println(reading); // for testing
if (abs(reading) < 10) //%deadband, within teh deadnabd motor is not moving
{
Serial.print("inside deadband, reading = ");
Serial.println(reading); // for testing
Timer1.pwm(fanPin1, 0);
digitalWrite(fanPin2, 0);
} else {
if (reading > 0) //assume working range of pwm of the 1.5V motor is in the range of 70-80
{ //dutyCycle = (reading / 512) * 100; //convet to 0-99,analogRead :0-1023
dutyCycle = reading * (80 - 70) / 100 + 70;
Serial.print("PWM Fan (++++ normal rotation), Duty Cycle in % = ");
Serial.println(dutyCycle);
Timer1.pwm(fanPin1, (dutyCycle / 100) * 1023);
digitalWrite(fanPin2, 0);
} else {
dutyCycle = -1 * reading * (80 - 70) / 100 + 70;
Serial.print("PWM Fan (---- reverse rotation), Duty Cycle in % = ");
Serial.println(dutyCycle);
Timer1.pwm(fanPin2, (dutyCycle / 100) * 1023);
digitalWrite(fanPin1, 0);
}
}
delay(100);
}
A0
GPIO9
GPIO10
5V
GND
IN1
IN2
H-bridge
L298
DC
Motor
Arduino
UNO
10K B

## Slide 17: Serial monitor
You may use
IDE/Tools/Serial_monitor to view the variable (val)
Make sure
  (line6) Serial.begin(9600);
  And the serial port serial is the same.
Actual com port number
depends on your system
See this in your monitor
When you turn the variable resistor, this number changes

## Slide 18: Answer: Tutorial exercise 2.2a
If in line 1) int potpin=1;//Input pin
Discuss how to change the hardware to accommodate the change

## Slide 19: Tutorial exercise 2.2a
If in line 1) int potpin=1;//Input pin
Discuss how to change the hardware to accommodate the change
Answer: Change the connection from A0 to A1
A0A1

## Slide 20: Test 2.2b: serial communication with PC, echo a character
//serial communication with PC, echo a character
void setup()
{
Serial.begin(9600);
}
void loop()
{
if (Serial.available() > 0)
{
char c = Serial.read();
Serial.print( c );
}
delay(10);
}

## Slide 21: Test 2.2c: serial communication with PC, echo a string of characters
//from https://forum.arduino.cc/index.php?topic=66621.0
String readString; //echo program
void setup() {
Serial.begin(9600);
Serial.println("echo program: serial test , you type a string of characters, this program echo back"); // so I can keep track of what is loaded
}
void loop() {
while (Serial.available()) {
delay(10);
if (Serial.available() > 0) {
char c = Serial.read();
readString += c;
}
}
if (readString.length() > 0) {
Serial.println(readString);
readString = "";
}
}
Enter a sentence here

## Slide 22: Test 2.2d: Serial communication with PC(python), send data from Arduino to PC (Python)
REF: https://www.instructables.com/id/Arduino-Python-Communication-via-USB/
#run this on python, PPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPP
import serial # pip install pyserial (not pip install serial ) # if needed
arduino = serial.Serial('COM6', 9600, timeout=.1)
while True:
data = arduino.readline()[:-2] #the last bit gets rid of the new-line chars
if data:
print (data)
//run this on Arduino, AAAAAAAAAAAAAAAAAAAAA
void setup() {
Serial.begin(9600); // use the same baud-rate as the python side
}
void loop() {
Serial.println("Hello world from Ardunio!"); // write a string
delay(1000);
}

## Slide 23: Test2.2e: Serial communication with PC(python), data sent from PC-python to Arduino and echo back to PC-python for printing
REF: https://www.instructables.com/id/Arduino-Python-Communication-via-USB/
# run on PC-python
import serial, time
arduino = serial.Serial('COM6', 9600, timeout=.1)
time.sleep(1) #give the connection a second to settle
#arduino.write(b"Hello from Python!")
while True:
#arduino.write("Hello from Python!")
arduino.write("Hello from Python!".encode())
time.sleep(1)
data = arduino.readline()
# print(data)
if data:
#print(data.rstrip('\n'))
print(data)
#strip out the new lines for now
# (better to do .read()
#in the long run for this
/// run on Arduino -uno
void setup() {
Serial.begin(9600);}
void loop() {
if (Serial.available() > 0) {
char data = Serial.read();
char strx[2];
strx[0] = data;
strx[1] = '\0';
Serial.print(strx);
}
}
}

## Slide 24: Test2.2f : Simple send data from Arduino to python
/// run on Arduino -uno
void setup() {
Serial.begin(9600);}
int i=0;
void loop() {
Serial.print(i,OCT);
i++;
delay(1000);
}
# run on PC-python
import serial, time
arduino = serial.Serial('COM4', 9600, timeout=.1)
time.sleep(1) #give the connection a second to settle
#arduino.write(b"Hello from Python!")
while True:
#time.sleep(1)
data = arduino.readline()
# print(data)
# if data:
#print(data.rstrip('\n'))
#print(data)
print(data.decode('utf-8'))

## Slide 25: Test 2.3a: Temperature sensing test3_temperature.ino using LM35
int val;
int tempPin = 0;
void setup()
{Serial.begin(9600);
}
void loop()
{val = analogRead(tempPin);
float cel=(val*0.48828125);
float farh = (cel*9)/5 + 32;
Serial.print("TEMPRATURE = ");
Serial.print(cel);
Serial.print("*C, or ");
Serial.print(farh);
Serial.print("*F");
Serial.println();
delay(1000);
}
https://www.theengineeringprojects.com/2019/01/introduction-to-lm35.html
Vcc, Out, GND
Vcc, Out, GND

## Slide 26: Test 2.3b: sensing using: Temperature and Humidity sensor DHT11 https://www.circuitbasics.com/how-to-set-up-the-dht11-humidity-sensor-on-an-arduino/
#include <DFRobot_DHT11.h>
DFRobot_DHT11 DHT;
#define DHT11_PIN 10
//https://github.com/DFRobot/DFRobot_DHT11 void setup(){
Serial.begin(115200);
} void loop(){
DHT.read(DHT11_PIN);
Serial.print("temp:");
Serial.print(DHT.temperature);
Serial.print(" humi:");
Serial.println(DHT.humidity);
delay(1000);
}
// will how temperature and
//humidity in IDE/tools/serial monitor
Install https://github.com/DFRobot/DFRobot_DHT11
IDE/tools/manage libraries/ add this library
Search for DHT11, lib name /DFRobot_DHT11
/*!
* @file readDHT11.ino
* @brief DHT11 is used to read the temperature and humidity of the current environment.
*
* @copyright Copyright (c) 2010 DFRobot Co.Ltd (http://www.dfrobot.com)
* @license The MIT License (MIT)
* @author [Wuxiao](xiao.wu@dfrobot.com)
* @version V1.0
* @date 2018-09-14
* @url https://github.com/DFRobot/DFRobot_DHT11
*/
Vcc out ground
DHT11

## Slide 27: Test 2.4: LCD display test4_LCD
Circuit Diagram
http://wiki.sunfounder.cc/index.php?title=I%C2%B2C_LCD1602
GND
VCC
SDA
SCL

## Slide 28: Drivers for LCD display
//2019.5.2 by khwong, test5_LCD_DHT.ino
//1.1) If you are using the lcd module 1602, 16x2 and you will receive the error message of no LiquidCrystal_I2C.h not found.
// FIX: in Arduino IDE/Sketch/Include library/Add Zip file, select the file from
// // https://github.com/johnrickman/LiquidCrystal_I2C //(bug fixed)
// if you are using the lcd module 1602, 16x2 and no LiquidCrystal_I2C.h found in your system
//1.2) the control code may be 0x3f, or 0x27, try it yourself
//1.3) //Note: https://www.geeetech.com/Documents/LiquidCrystal_I2Cv1-1.rar has bug don't use it because it can only print one character per line.
// this zip file // https://github.com/johnrickman/LiquidCrystal_I2C //(bug fixed), bug fix of cpp
// ardunio-IDE can read this LiquidCrystal_I2C.cpp and function correctly.

## Slide 29: If you have problems when importing zip libraries
Question1: If you received error message like: “dht.h: No such file or directory”, what to do?
Answer:1 (i) Find the .zip file from the web, e.g. download http://www.circuitbasics.com/wp-content/uploads/2015/10/DHTLib.zip to a directory. (ii) In IDE/Sketch/Inlcude_library/Add_Zip_library, add the Zip file. (iii) You may also use IDE/Sketch/Inlcude_library/Manage_Libraries to add Zip libraries.
Question 2: Some zip libraries do not work for you, then you may need to find another alternative library with the same name. But when you import the new zip library, you received an error :”A library named xxxx (e.g. DHTLib) already exists”
Answer2: Go to IDE/File/Preference/Sketch_book_location, under /libraries , delete the old zip file directory, e.h. DHTLib, you can install the new zip library again.

## Slide 30: Code test2.4_lcd.ino
#include <Wire.h>
#include <LiquidCrystal_I2C.h>
//LiquidCrystal_I2C lcd(0x27,20,2);
// set the LCD address to 0x27 for a 16 chars and 2 line display
LiquidCrystal_I2C lcd(0x3F,20,2); // set the LCD address to 0x27 for a 16 chars and 2 line display
//LiquidCrystal_I2C lcd(0x3F,16,2); // set the LCD address to 0x27 for a 16 chars and 2 line display
void setup()
{ Serial.begin(9600);
lcd.init(); // initialize the lcd
lcd.backlight();
lcd.setCursor(3,0); //first row: line 0,cursor index 3. first postion is index 0
lcd.print("Hello, world!");
lcd.setCursor(2,1); //second row : line 1, position index 2
lcd.print("from KH WONG");
delay(3000);
lcd.clear ();}
void loop() {
void loop() {
int i = 0;
while (1)//loop for ever
{ i = 0;
while (i < 20)
{ // print line 1
lcd.setCursor(0, 0);
lcd.print("Line 1");//line 1
lcd.setCursor(10, 0);
lcd.print(i);
// print line 2
lcd.setCursor(0, 1);
lcd.print("Line 2");//line 1
lcd.setCursor(10, 1);
lcd.print(i + 1);
i++;
delay(2000);
lcd.setCursor(10, 0);
lcd.print(" "); //line 1: clear 2 places from 10
lcd.setCursor(10, 1);
lcd.print(" "); //line 2: clear 2 places from 10
}
}
}

## Slide 31: Test 2.5a: LCD display of humidity and temperature
Circuit Diagram
http://wiki.sunfounder.cc/index.php?title=I%C2%B2C_LCD1602
GND
VCC
SDA
SCL

## Slide 32: Test 2.5b: Humidify and temperature sensors (I2c)
ds
http://www.circuitbasics.com/how-to-set-up-the-dht11-humidity-sensor-on-an-arduino/
https://www.arduinolibraries.info/libraries/dht-sensor-library
C:\Users\khwon\Documents\Arduino\libraries\

## Slide 33: Install drivers for LCD and DHT sensor test5_LCD_DHT.ino
//2019.5.2 by khwong, test5_LCD_DHT.ino
//1.1) If you are using the lcd module 1602, 16x2 and you will receive the error message of no LiquidCrystal_I2C.h not found.
// FIX: in Arduino IDE/Sketch/Include library/Add Zip file, select the file from
// // https://github.com/johnrickman/LiquidCrystal_I2C //(bug fixed)
// if you are using the lcd module 1602, 16x2 and no LiquidCrystal_I2C.h found in your system
//1.2) the control code may be 0x3f, or 0x27, try it yourself
//1.3) //Note: https://www.geeetech.com/Documents/LiquidCrystal_I2Cv1-1.rar has bug don't use it because it can only print one character per line.
// this zip file // https://github.com/johnrickman/LiquidCrystal_I2C //(bug fixed), bug fix of cpp
// ardunio-IDE can read this LiquidCrystal_I2C.cpp and function correctly.
//2)see http://www.circuitbasics.com/how-to-set-up-the-dht11-humidity-sensor-on-an-arduino/
// download http://www.circuitbasics.com/wp-content/uploads/2015/10/DHTLib.zip
//in Arduino IDE/Sketch/Include library/Add Zip file,

## Slide 34: Code test2.5_LCD_DHT.ino
#include <Wire.h>
#include <LiquidCrystal_I2C.h>
#include <dht.h>//tested ok.
dht DHT ;//DHT DHT;
#define DHT11_PIN 4
//LiquidCrystal_I2C lcd(0x27,20,2);
// set the LCD address to 0x27 for a 16 chars and 2 line display
LiquidCrystal_I2C lcd(0x3F,20,2); // set the LCD address to 0x27 for a 16 chars and 2 line display
//LiquidCrystal_I2C lcd(0x3F,16,2); // set the LCD address to 0x27 for a 16 chars and 2 line display
void setup()
{ Serial.begin(9600);
lcd.init(); // initialize the lcd
lcd.backlight();
lcd.setCursor(3,0); //first row: line 0,cursor index 3. first postion is index 0
lcd.print("Hello, world!");
lcd.setCursor(2,1); //second row : line 1, position index 2
lcd.print("from KH WONG");
delay(3000);
lcd.clear ();
}
void loop() {
//send himidity and tenmeprature to tool: serial monitor
int chk = DHT.read11(DHT11_PIN);
Serial.print("Temperature = ");
Serial.println(DHT.temperature);
Serial.print("Humidity = ");
Serial.println(DHT.humidity);
delay(2000); //need longer delay otherwise the senor cannot read correctly
// read humidity
float h = DHT.humidity;
//read temperature
float f = DHT.temperature;
if (isnan(h) || isnan(f)) {
lcd.print("ERROR");
return;
}
lcd.setCursor(0, 0);
lcd.print("Humidity=");
lcd.setCursor(10, 0); //first row is humidity
lcd.print(h);
lcd.setCursor(0, 1);
lcd.print("Temperat=");
lcd.setCursor(10, 1); //first row is humidity
lcd.print(f);
}

## Slide 35: Test 2.5e: Humidify and temperature sensors (I2c), see code in next slide
ds
http://www.circuitbasics.com/how-to-set-up-the-dht11-humidity-sensor-on-an-arduino/
https://www.arduinolibraries.info/libraries/dht-sensor-library
C:\Users\khwon\Documents\Arduino\libraries\
RTC
DHT11_PIN 7

## Slide 36: Real time Clock (RTC) ,LCD, and temp/humidity sensor (#define DHT11_PIN 7)
// khwong 2020 July 11,See http://misclab.umeoce.maine.edu/boss/Arduino/bensguides/DS3231_Arduino_Clock_Instructions.pdf
/* khwong 2020 march 22, cimbining DS3231+LCD+serail-port display
using DS3231 library, by Andrew Wickert, Eric Ayars, Jean-Claude Wippler version 1.02
installation: //Sketch/inlucde_library/manage librray/type DS3231,
Can try examples : Files/Exaples/DS3231/
Reference :DS3231_test.pde
Eric Ayars
4/11
Test/demo of read routines for a DS3231 RTC.
Turn on the serial monitor after loading this to check if things are
working as they should.
*/
/*
DS3231_test.pde
Eric Ayars
4/11
Test/demo of read routines for a DS3231 RTC.
Turn on the serial monitor after loading this to check if things are
working as they should.
*/
//////////////////////// LCD //////////////////////
//#include <Wire.h>
#include <Wire.h>
//#include <LiquidCrystal_I2C.h>
#include <dht.h>//tested ok.
dht DHT ;//DHT DHT;
#define DHT11_PIN 7
#include <LiquidCrystal_I2C.h>
LiquidCrystal_I2C lcd(0x27, 16, 2);
// set the LCD address to 0x27 for a 16 chars and 2 line display
//LiquidCrystal_I2C lcd(0x3F,20,2); // set the LCD address to 0x27 for a 16 chars and 2 line display
//LiquidCrystal_I2C lcd(0x3F,16,2); // set the LCD address to 0x27 for a 16 chars and 2 line display
void setup()
{ Serial.begin(9600);
lcd.init(); // initialize the lcd
lcd.backlight();
lcd.setCursor(3, 0); //first row: line 0,cursor index 3. first postion is index 0
lcd.print("Hello, world!");
lcd.setCursor(2, 1); //second row : line 1, position index 2
lcd.print("from KH WONG");
delay(500);
lcd.clear ();
////////////////////////////////
//setup_RTC_DS3231();// if you want to change the time////////////////
}
#include <DS3231.h>
#include <Wire.h>
DS3231 Clock;
bool Century = false;
bool h12;
bool PM;
byte ADay, AHour, AMinute, ASecond, ABits;
bool ADy, A12h, Apm;
void setup_RTC_DS3231() {
// Start the I2C interface
Wire.begin();
// Start the serial interface
Serial.begin(9600);
// See http://misclab.umeoce.maine.edu/boss/Arduino/bensguides/DS3231_Arduino_Clock_Instructions.pdf
Clock.setSecond(50);//Set the second
Clock.setMinute(07);//Set the minute
Clock.setHour(17); //Set the hour
Clock.setDoW(3); //Set the day of the week
Clock.setDate(22); //Set the date of the month
Clock.setMonth(2); //Set the month of the year
Clock.setYear(22); //Set the year (Last two digits of the year)
}
int count;
//////////////////////////////////////////////////////////////
void loop() {
int chk = DHT.read11(DHT11_PIN);
//send himidity and tenmeprature to tool: serial monitor
if (count >= 3) // read at a period
{
Serial.print("Temperature = ");
Serial.println(DHT.temperature);
Serial.print("Humidity = ");
Serial.println(DHT.humidity);
count = 0;
}
lcd.setCursor(9, 1);
lcd.print(DHT.temperature);
lcd.setCursor(11, 1);
lcd.print("C");
lcd.setCursor(12, 1);
lcd.print(" ");
lcd.setCursor(13, 1); //
lcd.print(DHT.humidity);
lcd.setCursor(15, 1); //
lcd.print("%");
count++; //since the loop is executed once in 1 second
// send what's going on to the serial monitor.
// Start with the year
Serial.print("2");
/// print LCD prot ////////////////////////////////////////////////////////////
lcd.setCursor(0, 0); lcd.print("2");
if (Century) { // Won't need this for 89 years.
Serial.print("1");
lcd.setCursor(1, 0); lcd.print("1");
} else {
Serial.print("0");
lcd.setCursor(1, 0); lcd.print("0");
}
Serial.print(Clock.getYear(), DEC);
lcd.print(Clock.getYear()); lcd.print(Clock.getYear());
Serial.print(' '); lcd.setCursor(4, 0); lcd.print("-");
// then the month
Serial.print(Clock.getMonth(Century), DEC); lcd.setCursor(5, 0);
switch (Clock.getMonth(Century)) {
case 1: lcd.print("Jan"); break;
case 2: lcd.print("Feb"); break;
case 3: lcd.print("Mar"); break;
case 4: lcd.print("Apr"); break;
case 5: lcd.print("May"); break;
case 6: lcd.print("Jun"); break;
case 7: lcd.print("Jul"); break;
case 8: lcd.print("Aug"); break;
case 9: lcd.print("Sept"); break;
case 10: lcd.print("Oct"); break;
case 11: lcd.print("Nov"); break;
case 12: lcd.print("Dec"); break;
default: lcd.print("???"); break;
}
Serial.print(' '); lcd.setCursor(8, 0); lcd.print("-");
// then the date
Serial.print(Clock.getDate(), DEC); lcd.setCursor(9, 0); lcd.print(Clock.getDate());
Serial.print(' '); lcd.setCursor(11, 0); lcd.print(",");
// and the day of the week
Serial.print(Clock.getDoW(), DEC); lcd.setCursor(12, 0);
switch (Clock.getDoW()) {
case 1: lcd.print("Mon"); break;
case 2: lcd.print("Tue"); break;
case 3: lcd.print("Wed"); break;
case 4: lcd.print("Thu"); break;
case 5: lcd.print("Fri"); break;
case 6: lcd.print("Sat"); break;
case 7: lcd.print("Sun"); break;
default: lcd.print("???"); break;
}
Serial.print(' ');
// Finally the hour, minute, and second
Serial.print(Clock.getHour(h12, PM), DEC); lcd.setCursor(0, 1); lcd.print(Clock.getHour(h12, PM));
Serial.print(' '); lcd.setCursor(2, 1); lcd.print(":");
Serial.print(Clock.getMinute(), DEC); lcd.setCursor(3, 1); lcd.print(Clock.getMinute());
Serial.print(' '); lcd.setCursor(5, 1); lcd.print(":");
Serial.print(Clock.getSecond(), DEC); lcd.setCursor(6, 1); lcd.print(Clock.getSecond());
// Add AM/PM indicator
if (h12) {
if (PM) {
Serial.print(" PM ");
} else {
Serial.print(" AM ");
}
} else {
Serial.print(" 24h ");
}
// Display the temperature
Serial.print("T=");
Serial.print(Clock.getTemperature(), 2);
// Tell whether the time is (likely to be) valid
if (Clock.oscillatorCheck()) {
Serial.print(" O+");
} else {
Serial.print(" O-");
}
// Indicate whether an alarm went off
if (Clock.checkIfAlarm(1)) {
Serial.print(" A1!");
}
if (Clock.checkIfAlarm(2)) {
Serial.print(" A2!");
}
// New line on display
Serial.print('\n');
// Display Alarm 1 information
Serial.print("Alarm 1: ");
Clock.getA1Time(ADay, AHour, AMinute, ASecond, ABits, ADy, A12h, Apm);
Serial.print(ADay, DEC);
if (ADy) {
Serial.print(" DoW");
} else {
Serial.print(" Date");
}
Serial.print(' ');
Serial.print(AHour, DEC);
Serial.print(' ');
Serial.print(AMinute, DEC);
Serial.print(' ');
Serial.print(ASecond, DEC);
Serial.print(' ');
if (A12h) {
if (Apm) {
Serial.print('pm ');
} else {
Serial.print('am ');
}
}
if (Clock.checkAlarmEnabled(1)) {
Serial.print("enabled");
}
Serial.print('\n');
// Display Alarm 2 information
Serial.print("Alarm 2: ");
Clock.getA2Time(ADay, AHour, AMinute, ABits, ADy, A12h, Apm);
Serial.print(ADay, DEC);
if (ADy) {
Serial.print(" DoW");
} else {
Serial.print(" Date");
}
Serial.print(' ');
Serial.print(AHour, DEC);
Serial.print(' ');
Serial.print(AMinute, DEC);
Serial.print(' ');
if (A12h) {
if (Apm) {
Serial.print('pm');
} else {
Serial.print('am');
}
}
if (Clock.checkAlarmEnabled(2)) {
Serial.print("enabled");
}
// display alarm bits
Serial.print('\nAlarm bits: ');
Serial.print(ABits, BIN);
Serial.print('\n');
Serial.print('\n');
delay(1000);
}

## Slide 37: Test2.6a: servo motor, test6_servo.ino (using timer 1)
#include <Servo.h>
int servoPin = 3; // Declare the Servo pin
// Create a servo object
Servo Servo1;
void setup() {
Servo1.attach(servoPin);
}
void loop(){
// Make servo go to 0 degrees
Servo1.write(0);
delay(1000);
// Make servo go to 90 degrees
Servo1.write(90);
delay(1000);
// Make servo go to 180 degrees
Servo1.write(180);
delay(1000);
}
http://www.sharetechnote.com/html/Arduino_ServoMotor.html
https://www.instructables.com/id/Arduino-Servo-Motors/
Use pin 3
Video demo6 servo
https://youtu.be/AeSN7NFGm0w

## Slide 38: Test2.6b: use PC-python to control servo motor
Ref: https://stackoverflow.com/questions/56316443/how-to-send-an-int-from-python-to-an-arduino-in-order-to-use-it-as-an-argument-f
# run on PC-python
import serial #pip install pyserial #if needed
ser = serial.Serial("COM6", 9600)
while True:
input_value = input('Enter servo position 0-180: ')
ser.write(input_value.encode())
//run on Arduino
#include <Servo.h>
int servoPin = 3;
Servo Servo1;
void setup() {
Servo1.attach(servoPin);
Serial.begin(9600);
}
void loop()
{
if (Serial.available())
{
String a = Serial.readString();
Serial.print("Received Value: ");
Serial.println(a);
int b = a.toInt();
Servo1.write(b);
//delay(1000);
}
}

## Slide 39: Test 2.6c: servo using timer2 to avoid conflict with timer1 https://create.arduino.cc/projecthub/ashraf_minhaj/how-to-use-servotimer2-library-simple-explain-servo-sweep-512fd9
//Sometime timer is being used by other program, so the previous approach does not work. This approach uses timer2 instead
#include"ServoTimer2.h"
ServoTimer2 servo1;
void setup()
{
servo1.attach(3);
}
void loop()
{ // put your main code here, to run repeatedly:
servo1.write(750); //min pulse width for 0 degree
delay(1000);
servo1.write(1500); //pulse width for 90 degree
delay(1000);
servo1.write(2250); //max pulse width for around 180 degree
delay(1000);
}
Use pin 3

## Slide 40: Tutorial
How to change the motor shaft to 45 degrees?

## Slide 41: Tutorial
How to change the motor shaft to 45 degrees?
Answer:
#include <Servo.h>
int servoPin = 3; // Declare the Servo pin
// Create a servo object
Servo Servo1;
void setup() {
Servo1.attach(servoPin);
}
void loop(){
// Make servo go to 45 degrees
Servo1.write(45);
delay(1000);
}

## Slide 42: Test2.7: Stepping motor, test7_stepper.ino
//https://github.com/arduino-libraries/Stepper/blob/master/src/Stepper.h
#include <Stepper.h>
#define STEPS 100
//stepper connection pins
Stepper stepper(STEPS, 8, 9, 10, 11);
int previous = 0;
void setup()
{
stepper.setSpeed(90);
}
void loop()
{
//int val = analogRead(0);
stepper.step(100);
delay(30);
//previous = val;
}
Video Demo7 stepper
https://youtu.be/0Ak9Ckyl09o
https://circuitdigest.com/microcontroller-projects/arduino-stepper-motor-control-tutorial

## Slide 43: Stepper code
//https://docs.arduino.cc/learn/electronics/stepper-motors
#include <Stepper.h> const int stepsPerRevolution = 200; // change this to fit the number of steps per revolution
// for your motor
// initialize the stepper library on pins 8 through 11:
Stepper myStepper(stepsPerRevolution, 8, 9, 10, 11);
int stepCount = 0; // number of steps the motor has taken
void setup() {
// initialize the serial port:
Serial.begin(9600);
}
void loop() {
// step one step:
myStepper.step(1);
Serial.print("steps:");
Serial.println(stepCount);
stepCount++;
delay(50);
}

## Slide 44: Tutorial
Project: How to use a stepping motor to make a clock that the arm will rotate 360 degrees in one minute?
Answer: To be left for students.

## Slide 45: Test2.8: LDR Light dependent resistor test8_LDR_display.ino
//LDR Light Dependent Resistor
int photocellPin = 2; // LDR connected to pin2
int photocellVal = 0; // photocell variable
void setup() {
Serial.begin(9600);
}
void loop() {
// reading LDR and send to serial port
photocellVal = analogRead(photocellPin);
Serial.println(photocellVal);
delay(100);
}
Video demo 8 LDR
https://youtu.be/HZ1qXmEj25s
10K Ohms resistor
GND
5V
A2
Arduino Uno

## Slide 46: Projects
Design and build a light tracking device.
May get inspirations from demo by others:
  https://stigern.wordpress.com/2009/05/06/how-to-make-a-light-tracker-using-photoresistors/
  https://www.instructables.com/id/Arduino-Solar-Tracker/

## Slide 47: Test 2.9 (Real time clock (DS3231) + LCD: share same i2c bus), and serial display
// khwong 2022.2.22, 2020 July 11,See http://misclab.umeoce.maine.edu/boss/Arduino/bensguides/DS3231_Arduino_Clock_Instructions.pdf
/* khwong 2020 march 22, cimbining DS3231+LCD+serail-port display
using DS3231 library, by Andrew Wickert, Eric Ayars, Jean-Claude Wippler version 1.02
installation: //Sketch/inlucde_library/manage librray/type DS3231,
Can try examples : Files/Exaples/DS3231/
Reference :DS3231_test.pde
Eric Ayars
4/11
Test/demo of read routines for a DS3231 RTC.
Turn on the serial monitor after loading this to check if things are
working as they should.
*/
/*
DS3231_test.pde
Eric Ayars
4/11
Test/demo of read routines for a DS3231 RTC.
Turn on the serial monitor after loading this to check if things are
working as they should.
*/
//////////////////////// LCD //////////////////////
//#include <Wire.h>
#include <Wire.h>
//#include <LiquidCrystal_I2C.h>
#include <dht.h>//tested ok.
dht DHT ;//DHT DHT;
#define DHT11_PIN 7
#include <LiquidCrystal_I2C.h>
LiquidCrystal_I2C lcd(0x27, 16, 2);
// set the LCD address to 0x27 for a 16 chars and 2 line display
//LiquidCrystal_I2C lcd(0x3F,20,2); // set the LCD address to 0x27 for a 16 chars and 2 line display
//LiquidCrystal_I2C lcd(0x3F,16,2); // set the LCD address to 0x27 for a 16 chars and 2 line display
void setup()
{ Serial.begin(9600);
lcd.init(); // initialize the lcd
lcd.backlight();
lcd.setCursor(3, 0); //first row: line 0,cursor index 3. first postion is index 0
lcd.print("Hello, world!");
lcd.setCursor(2, 1); //second row : line 1, position index 2
lcd.print("from KH WONG");
delay(500);
lcd.clear ();
////////////////////////////////
setup_RTC_DS3231();// if you want to change the time////////////////
}
#include <DS3231.h>
#include <Wire.h>
DS3231 Clock;
bool Century = false;
bool h12;
bool PM;
byte ADay, AHour, AMinute, ASecond, ABits;
bool ADy, A12h, Apm;
void setup_RTC_DS3231() {
// Clock.setSecond(50);//Set the second
// Clock.setMinute(21);//Set the minute
// Clock.setHour(17); //Set the hour
// Clock.setDoW(2); //Set the day of the week
// Clock.setDate(22); //Set the date of the month
// Clock.setMonth(2); //Set the month of the year
// Clock.setYear(22); //Set the year (Last two digits of the year)
}
int count;
//////////////////////////////////////////////////////////////
void loop() {
int chk = DHT.read11(DHT11_PIN);
//send himidity and tenmeprature to tool: serial monitor
if (count >= 3) // read at a period
{
Serial.print("Temperature = ");
Serial.println(DHT.temperature);
Serial.print("Humidity = ");
Serial.println(DHT.humidity);
count = 0;
}
lcd.setCursor(9, 1);
lcd.print(DHT.temperature);
lcd.setCursor(11, 1);
lcd.print("C");
lcd.setCursor(12, 1);
lcd.print(" ");
lcd.setCursor(13, 1); //
lcd.print(DHT.humidity);
lcd.setCursor(15, 1); //
lcd.print("%");
count++; //since the loop is executed once in 1 second
// send what's going on to the serial monitor.
// Start with the year
Serial.print("2");
/// print LCD prot ////////////////////////////////////////////////////////////
lcd.setCursor(0, 0); lcd.print("2");
if (Century) { // Won't need this for 89 years.
Serial.print("1");
lcd.setCursor(1, 0); lcd.print("1");
} else {
Serial.print("0");
lcd.setCursor(1, 0); lcd.print("0");
}
Serial.print(Clock.getYear(), DEC);
lcd.print(Clock.getYear()); lcd.print(Clock.getYear());
Serial.print(' '); lcd.setCursor(4, 0); lcd.print("-");
// then the month
Serial.print(Clock.getMonth(Century), DEC); lcd.setCursor(5, 0);
switch (Clock.getMonth(Century)) {
case 1: lcd.print("Jan"); break;
case 2: lcd.print("Feb"); break;
case 3: lcd.print("Mar"); break;
case 4: lcd.print("Apr"); break;
case 5: lcd.print("May"); break;
case 6: lcd.print("Jun"); break;
case 7: lcd.print("Jul"); break;
case 8: lcd.print("Aug"); break;
case 9: lcd.print("Sept"); break;
case 10: lcd.print("Oct"); break;
case 11: lcd.print("Nov"); break;
case 12: lcd.print("Dec"); break;
default: lcd.print("???"); break;
}
Serial.print(' '); lcd.setCursor(8, 0); lcd.print("-");
// then the date
Serial.print(Clock.getDate(), DEC); lcd.setCursor(9, 0); lcd.print(Clock.getDate());
Serial.print(' '); lcd.setCursor(11, 0); lcd.print(",");
// and the day of the week
Serial.print(Clock.getDoW(), DEC); lcd.setCursor(12, 0);
switch (Clock.getDoW()) {
case 1: lcd.print("Mon"); break;
case 2: lcd.print("Tue"); break;
case 3: lcd.print("Wed"); break;
case 4: lcd.print("Thu"); break;
case 5: lcd.print("Fri"); break;
case 6: lcd.print("Sat"); break;
case 7: lcd.print("Sun"); break;
default: lcd.print("???"); break;
}
Serial.print(' ');
// Finally the hour, minute, and second
Serial.print(Clock.getHour(h12, PM), DEC); lcd.setCursor(0, 1); lcd.print(Clock.getHour(h12, PM));
Serial.print(' '); lcd.setCursor(2, 1); lcd.print(":");
int minute = Clock.getMinute();
//lcd print minute
Serial.print(minute, DEC);
if (minute <= 9)
{ lcd.setCursor(3, 1);
lcd.print("0");
lcd.setCursor(4, 1);
lcd.print(Clock.getMinute());
}
else
{ lcd.setCursor(3, 1);
lcd.print(Clock.getMinute());
}
Serial.print(' '); lcd.setCursor(5, 1); lcd.print(":");
Serial.print(Clock.getSecond(), DEC); lcd.setCursor(6, 1); lcd.print(Clock.getSecond());
// Add AM/PM indicator
if (h12) {
if (PM) {
Serial.print(" PM ");
} else {
Serial.print(" AM ");
}
} else {
Serial.print(" 24h ");
}
// Display the temperature
Serial.print("T=");
Serial.print(Clock.getTemperature(), 2);
// Tell whether the time is (likely to be) valid
if (Clock.oscillatorCheck()) {
Serial.print(" O+");
} else {
Serial.print(" O-");
}
// Indicate whether an alarm went off
if (Clock.checkIfAlarm(1)) {
Serial.print(" A1!");
}
if (Clock.checkIfAlarm(2)) {
Serial.print(" A2!");
}
// New line on display
Serial.print('\n');
// Display Alarm 1 information
Serial.print("Alarm 1: ");
Clock.getA1Time(ADay, AHour, AMinute, ASecond, ABits, ADy, A12h, Apm);
Serial.print(ADay, DEC);
if (ADy) {
Serial.print(" DoW");
} else {
Serial.print(" Date");
}
Serial.print(' ');
Serial.print(AHour, DEC);
Serial.print(' ');
Serial.print(AMinute, DEC);
Serial.print(' ');
Serial.print(ASecond, DEC);
Serial.print(' ');
if (A12h) {
if (Apm) {
Serial.print('pm ');
} else {
Serial.print('am ');
}
}
if (Clock.checkAlarmEnabled(1)) {
Serial.print("enabled");
}
Serial.print('\n');
// Display Alarm 2 information
Serial.print("Alarm 2: ");
Clock.getA2Time(ADay, AHour, AMinute, ABits, ADy, A12h, Apm);
Serial.print(ADay, DEC);
if (ADy) {
Serial.print(" DoW");
} else {
Serial.print(" Date");
}
Serial.print(' ');
Serial.print(AHour, DEC);
Serial.print(' ');
Serial.print(AMinute, DEC);
Serial.print(' ');
if (A12h) {
if (Apm) {
Serial.print('pm');
} else {
Serial.print('am');
}
}
if (Clock.checkAlarmEnabled(2)) {
Serial.print("enabled");
}
// display alarm bits
Serial.print('\nAlarm bits: ');
Serial.print(ABits, BIN);
Serial.print('\n');
Serial.print('\n');
delay(1000);
}
demo:
https://www.youtube.com/watch?v=9-BqlcY1Bsw
RTC
Using SCL, SDA
https://microcontrollerslab.com/ds3231-rtc-module-pinout-interfacing-with-arduino-features/

## Slide 48: Test2.10: RFID test10_RFID.ino
You can obtain the driver from
IDE/Tools/Library_Manager/In_Filter_your_search: type: RFID 522
https://randomnerdtutorials.com/security-access-using-mfrc522-rfid-reader-with-arduino/
Circuit

## Slide 49: New Infrared code https://github.com/Arduino-IRremote/Arduino-IRremote (solved many IR control problems)
// modified from /SimpleReceiver.cpp, check 2 types of IR code NEC and Panasonic. see loop(), khwong 230704
/* https://github.com/Arduino-IRremote/Arduino-IRremote (install IRremote, see /examples/IRremote/SimpleReciver) )
Arduino
Uno
GND
5V
Pin4
Infrared light
Remote Controller
Pin2
GND
Vcc (5V)
or
IR receiver module
KY-022, HX1838B, or vs1838
Out Vcc, GND
Use Pin2 as default but can be changed to pin11 by modifying the default of PinDefinitionsAndMore.h
. Or simply add
#define IR_SEND_PIN 11
In your main.ino
https://electronoobs.com/eng_arduino_tut34

## Slide 50: New Infrared code example Can use NEC and Panasonic code together in one program(library IRremote) https://github.com/Arduino-IRremote/Arduino-IRremote (solved many IR control problems)
// modified from /SimpleReceiver.cpp, check 2 types of IR code NEC and panasonic. see loop(), khwong 230704
/* https://github.com/Arduino-IRremote/Arduino-IRremote (install IRremote, see /examples/IRremote/SimpleReciver) )
* SimpleReceiver.cpp
*
* Demonstrates receiving NEC IR codes with IRremote
*
* This file is part of Arduino-IRremote https://github.com/Arduino-IRremote/Arduino-IRremote.
*
************************************************************************************
* MIT License
*
* Copyright (c) 2020-2022 Armin Joachimsmeyer
*
* Permission is hereby granted, free of charge, to any person obtaining a copy
* of this software and associated documentation files (the "Software"), to deal
* in the Software without restriction, including without limitation the rights
* to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
* copies of the Software, and to permit persons to whom the Software is furnished
* to do so, subject to the following conditions:
*
* The above copyright notice and this permission notice shall be included in all
* copies or substantial portions of the Software.
*
* THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR IMPLIED,
* INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY, FITNESS FOR A
* PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE AUTHORS OR COPYRIGHT
* HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER LIABILITY, WHETHER IN AN ACTION OF
* CONTRACT, TORT OR OTHERWISE, ARISING FROM, OUT OF OR IN CONNECTION WITH THE SOFTWARE
* OR THE USE OR OTHER DEALINGS IN THE SOFTWARE.
*
************************************************************************************
*/
/*
* Specify which protocol(s) should be used for decoding.
* If no protocol is defined, all protocols (except Bang&Olufsen) are active.
* This must be done before the #include <IRremote.hpp>
*/
//#define DECODE_DENON // Includes Sharp
//#define DECODE_JVC
//#define DECODE_KASEIKYO
//#define DECODE_PANASONIC // alias for DECODE_KASEIKYO
//#define DECODE_LG
//#define DECODE_NEC // Includes Apple and Onkyo
//#define DECODE_SAMSUNG
//#define DECODE_SONY
//#define DECODE_RC5
//#define DECODE_RC6
//#define DECODE_BOSEWAVE
//#define DECODE_LEGO_PF
//#define DECODE_MAGIQUEST
//#define DECODE_WHYNTER
//#define DECODE_FAST
//#define DECODE_DISTANCE_WIDTH // Universal decoder for pulse distance width protocols
//#define DECODE_HASH // special decoder for all protocols
//#define DECODE_BEO // This protocol must always be enabled manually, i.e. it is NOT enabled if no protocol is defined. It prevents decoding of SONY!
//#define DEBUG // Activate this for lots of lovely debug output from the decoders.
//#define RAW_BUFFER_LENGTH 180 // Default is 112 if DECODE_MAGIQUEST is enabled, otherwise 100.
#include <Arduino.h>
#include "PinDefinitionsAndMore.h" // Define macros for input and output pin etc.
#include <IRremote.hpp>
void setup() {
Serial.begin(115200);
/*
#define DECODE_PANASONIC
IrReceiver.begin(IR_RECEIVE_PIN, ENABLE_LED_FEEDBACK);
delay(100);
*/
// Just to know which program is running on my Arduino
// Serial.println(F("START " __FILE__ " from " __DATE__ "\r\nUsing library version " VERSION_IRREMOTE));
// Start the receiver and if not 3. parameter specified, take LED_BUILTIN pin from the internal boards definition as default feedback LED
// #define DECODE_NEC // Includes Apple and Onkyo
// IrReceiver.begin(IR_RECEIVE_PIN, ENABLE_LED_FEEDBACK);
// Serial.print(F("Ready to receive IR signals of protocols: "));
// printActiveIRProtocols(&Serial);
//Serial.println(F("at pin " STR(IR_RECEIVE_PIN)));
}
//we will do 2 checks< : 1) NEC (2) panasoic, need delay 300ms in betwwen to achive that
void loop() {
/// check 1//////////////////////////////////
#define DECODE_NEC
IrReceiver.begin(IR_RECEIVE_PIN, ENABLE_LED_FEEDBACK);
delay(300);
/*
* Check if received data is available and if yes, try to decode it.
* Decoded result is in the IrReceiver.decodedIRData structure.
*
* E.g. command is in IrReceiver.decodedIRData.command
* address is in command is in IrReceiver.decodedIRData.address
* and up to 32 bit raw data in IrReceiver.decodedIRData.decodedRawData
*/
if (IrReceiver.decode()) {
/*
* Print a short summary of received data
*/
IrReceiver.printIRResultShort(&Serial);
IrReceiver.printIRSendUsage(&Serial);
if (IrReceiver.decodedIRData.protocol == UNKNOWN) {
Serial.println(F("Received noise or an unknown (or not yet enabled) protocol"));
// We have an unknown protocol here, print more info
IrReceiver.printIRResultRawFormatted(&Serial, true);
}
Serial.println();
/*
* !!!Important!!! Enable receiving of the next value,
* since receiving has stopped after the end of the current received data packet.
*/
IrReceiver.resume(); // Enable receiving of the next value
/*
* Finally, check the received data and perform actions according to the received command
*/
if (IrReceiver.decodedIRData.command == 0x10) {
// do something
} else if (IrReceiver.decodedIRData.command == 0x11) {
// do something else
}
}
/// check 2//////////////////////////////////
#define DECODE_PANASONIC
IrReceiver.begin(IR_RECEIVE_PIN, ENABLE_LED_FEEDBACK);
delay(300);
/*
* Check if received data is available and if yes, try to decode it.
* Decoded result is in the IrReceiver.decodedIRData structure.
*
* E.g. command is in IrReceiver.decodedIRData.command
* address is in command is in IrReceiver.decodedIRData.address
* and up to 32 bit raw data in IrReceiver.decodedIRData.decodedRawData
*/
if (IrReceiver.decode()) {
/*
* Print a short summary of received data
*/
IrReceiver.printIRResultShort(&Serial);
IrReceiver.printIRSendUsage(&Serial);
if (IrReceiver.decodedIRData.protocol == UNKNOWN) {
Serial.println(F("Received noise or an unknown (or not yet enabled) protocol"));
// We have an unknown protocol here, print more info
IrReceiver.printIRResultRawFormatted(&Serial, true);
}
Serial.println();
Serial.print("\n ^^^^^^ You may perform conmmand control based on these (NEC or Panasonic) codes^^");
Serial.print("\n -------------address (HEX): 0x");
Serial.print((unsigned int)IrReceiver.decodedIRData.address, HEX);
Serial.print("\n ****************command (HEX): 0x");
Serial.print((unsigned int)IrReceiver.decodedIRData.command, HEX);
Serial.println("\n ^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^\n");
/*
* !!!Important!!! Enable receiving of the next value,
* since receiving has stopped after the end of the current received data packet.
*/
IrReceiver.resume(); // Enable receiving of the next value
/*
* Finally, check the received data and perform actions according to the received command
*/
if (IrReceiver.decodedIRData.command == 0x10) {
// do something
} else if (IrReceiver.decodedIRData.command == 0x11) {
// do something else
}
}
}

## Slide 51
/* You can obtain the driver from
IDE/Tools/Library_Manager/In_Filter_your_search: type: RFID 522
All the resources for this project: http://randomnerdtutorials.com/
Modified by Rui Santos
Created by FILIPEFLOP
https://randomnerdtutorials.com/security-access-using-mfrc522-rfid-reader-with-arduino/
*/
#include <SPI.h>
#include <MFRC522.h>
#define SS_PIN 10
#define RST_PIN 9
MFRC522 mfrc522(SS_PIN, RST_PIN); // Create MFRC522 instance.
void setup()
{
Serial.begin(9600); // Initiate a serial communication
SPI.begin(); // Initiate SPI bus
mfrc522.PCD_Init(); // Initiate MFRC522
Serial.println("Approximate your card to the reader...");
Serial.println();
}
void loop()
{ // Look for new cards
if ( ! mfrc522.PICC_IsNewCardPresent())
{ return; }
// Select one of the cards
if ( ! mfrc522.PICC_ReadCardSerial())
{ return; }
//Show UID on serial monitor
Serial.print("UID tag :");
String content = "";
byte letter;
for (byte i = 0; i < mfrc522.uid.size; i++)
{ Serial.print(mfrc522.uid.uidByte[i] < 0x10 ? " 0" : " ");
Serial.print(mfrc522.uid.uidByte[i], HEX);
content.concat(String(mfrc522.uid.uidByte[i] < 0x10 ? " 0" : " "));
content.concat(String(mfrc522.uid.uidByte[i], HEX));
}
Serial.println();
Serial.print("Message : ");
content.toUpperCase();
// UID tag : 52 FA BF 10 (white card)
// UID tag : B5 E8 FD C2 (blue ring)
if (content.substring(1) == "52 FA BF 10") //change here the UID of the card/cards that you want to give access
{ Serial.println("Authorized access yes, yes, yes, yes, yes, yes");
Serial.println();
delay(3000);
}
else {
Serial.println(" Access denied, NO");
delay(3000);
}
}

## Slide 52: Test2.11a: test11_IRremote_relay
: required GitHub - Arduino-IRremote/Arduino-IRremote: Infrared remote library for Arduino: send and receive infrared signals with multiple protocols
Arduino
Uno
-
+
S
open
common
close
GND
5V
Pin4
Infrared light
Relay
Remote Controller
Pin11
GND
Vcc (5V)
or
IR receiver module
KY-022, HX1838B, or vs1838
Out Vcc, GND
https://electronoobs.com/eng_arduino_tut34

## Slide 53: Test2.11a_IRremote_relay.ino (OLD method)
/* from: https://github.com/z3t0/Arduino-IRremote * IRremote: IRrecvDemo - demonstrates receiving IR codes with IRrecv
* An IR detector/demodulator must be connected to the input RECV_PIN.
* Version 0.1 July, 2009
* Copyright 2009 Ken Shirriff
* http://arcfn.com
*/
#include <IRremote.h>
int RECV_PIN = 11;
int RELAY_PIN = 4;
IRrecv irrecv(RECV_PIN);
decode_results results;
// Dumps out the decode_results structure.
// Call this after IRrecv::decode()
// void * to work around compiler issue
//void dump(void *v) {
// decode_results *results = (decode_results *)v
void dump(decode_results *results) {
int count = results->rawlen;
if (results->decode_type == UNKNOWN) {
Serial.println("Could not decode message");
}
else { if (results->decode_type == NEC) {
Serial.print("Decoded NEC: "); }
else if (results->decode_type == SONY) {
Serial.print("Decoded SONY: "); }
else if (results->decode_type == RC5) {
Serial.print("Decoded RC5: "); }
else if (results->decode_type == RC6) {
Serial.print("Decoded RC6: "); }
Serial.print(results->value, HEX);
Serial.print(" (");
Serial.print(results->bits, DEC);
Serial.println(" bits)"); }
Serial.print("Raw (");
Serial.print(count, DEC);
Serial.print("): ");
for (int i = 0; i < count; i++) {
if ((i % 2) == 1) {
Serial.print(results->rawbuf[i]*USECPERTICK, DEC); }
else {
Serial.print(-(int)results->rawbuf[i]*USECPERTICK, DEC); }
Serial.print(" ");
}
Serial.println("");
}

## Slide 54
/////////////////////////////////////////////////////
void setup()
{ pinMode(RELAY_PIN, OUTPUT);
pinMode(13, OUTPUT);
Serial.begin(9600);
irrecv.enableIRIn(); // Start the receiver
}
int on = 0;
unsigned long last = millis();
/////////////////////////////////////////////////////
void loop() {
if (irrecv.decode(&results)) {
// If it's been at least 1/4 second since the last
// IR received, toggle the relay
if (millis() - last > 250) {
on = !on;
digitalWrite(RELAY_PIN, on ? HIGH : LOW);
digitalWrite(13, on ? HIGH : LOW);
dump(&results);
}
last = millis();
irrecv.resume(); // Receive the next value
}}

## Slide 55: Code: required GitHub - Arduino-IRremote/Arduino-IRremote: Infrared remote library for Arduino: send and receive infrared signals with multiple protocols test11a_IRremote_mechanical_relay
/* from: https://github.com/z3t0/Arduino-IRremote * IRremote: IRrecvDemo - demonstrates receiving IR codes with IRrecv
An IR detector/demodulator must be connected to the input RECV_PIN.
Version 0.1 July, 2009
Copyright 2009 Ken Shirriff
http://arcfn.com
*/
#include <IRremote.h>
int RECV_PIN = 11;
int RELAY_PIN = 4;
IRrecv irrecv(RECV_PIN);
decode_results results;
// Dumps out the decode_results structure.
// Call this after IRrecv::decode()
// void * to work around compiler issue
//void dump(void *v) {
// decode_results *results = (decode_results *)v
void dump(decode_results *results) {
int count = results->rawlen;
if (results->decode_type == UNKNOWN) {
Serial.println("Could not decode message");
}
else {
if (results->decode_type == NEC) {
Serial.print("Decoded NEC: ");
}
else if (results->decode_type == SONY) {
Serial.print("Decoded SONY: ");
}
else if (results->decode_type == RC5) {
Serial.print("Decoded RC5: ");
}
else if (results->decode_type == RC6) {
Serial.print("Decoded RC6: ");
}
Serial.print(results->value, HEX);
Serial.print(" (");
Serial.print(results->bits, DEC);
Serial.println(" bits)");
}
Serial.print("Raw (");
Serial.print(count, DEC);
Serial.print("): ");
for (int i = 0; i < count; i++) {
if ((i % 2) == 1) {
Serial.print(results->rawbuf[i]*USECPERTICK, DEC);
}
else {
Serial.print(-(int)results->rawbuf[i]*USECPERTICK, DEC);
}
Serial.print(" ");
}
Serial.println("");
}
/////////////////////////////////////////////////////
void setup()
{ pinMode(RELAY_PIN, OUTPUT);
pinMode(13, OUTPUT);
Serial.begin(9600);
irrecv.enableIRIn(); // Start the receiver
}
int on = 0;
unsigned long last = millis();
/////////////////////////////////////////////////////
void loop() {
if (irrecv.decode(&results)) {
// If it's been at least 1/4 second since the last
// IR received, toggle the relay
if (millis() - last > 250) {
on = !on;
digitalWrite(RELAY_PIN, on ? HIGH : LOW);
digitalWrite(13, on ? HIGH : LOW);
dump(&results);
}
last = millis();
irrecv.resume(); // Receive the next value
}
}

## Slide 56: Code : test11b_IRremote_mechanical_relay //IR control (17-key RC pad from TAOBO), IR-recive pin11, relay pin4 //Protocol=NEC Data=0xFF18E7(32 xxx bits) //17 key ID Rc control, this is arrow_up //Protocol=NEC Data=0xFF4AB5(32 xxx bits) // this is arrow_up
// test11b_IRremote_mechanical_relay
//IR control (17-key RC pad from TAOBO), IR-recive pin11, relay pin4
//Protocol=NEC Data=0xFF18E7(32 xxx bits) //17 key ID Rc control, this is arrow_up
//Protocol=NEC Data=0xFF4AB5(32 xxx bits) // this is arrow_up
//------------------------------------------------------------------------------
// Include the IRremote library header
//
#include <IRremote.h>
//------------------------------------------------------------------------------
// Tell IRremote which Arduino pin is connected to the IR Receiver (TSOP4838)
int IR_RECEIVE_PIN = 11;
int RELAY_PIN = 4;
IRrecv IrReceiver(IR_RECEIVE_PIN);
//+=============================================================================
// Configure the Arduino
//
void setup() {
pinMode(RELAY_PIN, OUTPUT); //must inlcude this, otherwise relay won't work
pinMode(LED_BUILTIN, OUTPUT); //optional
Serial.begin(9600); // Status message will be sent to PC at 9600 baud
#if defined(__AVR_ATmega32U4__) || defined(SERIAL_USB) || defined(SERIAL_PORT_USBVIRTUAL)
delay(2000); // To be able to connect Serial monitor after reset and before first printout
#endif
// Just to know which program is running on my Arduino
Serial.println(F("START " __FILE__ " from " __DATE__));
IrReceiver.enableIRIn(); // Start the receiver
IrReceiver.blink13(true); // Enable feedback LED
Serial.print(F("Ready to receive IR signals at pin "));
Serial.println(IR_RECEIVE_PIN);
}
//+=============================================================================
// Dump out the decode_results structure.
//
void dumpInfo() {
// Check if the buffer overflowed
if (IrReceiver.results.overflow) {
Serial.println("IR code too long. Edit IRremoteInt.h and increase RAW_BUFFER_LENGTH");
return;
}
// if (IrReceiver.results.value == 0x3D9AE3F7)
// {digitalWrite(RELAY_PIN, HIGH);
// }
// if (IrReceiver.results.value == 0x1BC0157B )
// {digitalWrite(RELAY_PIN, LOW);
// }
//Protocol=NEC Data=0xFF18E7 (32 xxx bits)
//Protocol=NEC Data=0xFFFFFFFF R (0 xxx bits)
//Protocol=NEC Data=0xFF4AB5(32 xxx bits)
if (IrReceiver.results.value == 0xFF18E7) //17-key RC arrow_up
{
// digitalWrite(RELAY_PIN, HIGH);
digitalWrite(4, HIGH);
// Serial.print("^^ key depressed\n");
// delay(1000);
}
if (IrReceiver.results.value == 0xFF4AB5)//17-key RC arrow_up
{
//digitalWrite(RELAY_PIN, LOW);
digitalWrite(RELAY_PIN, LOW);
// Serial.print("VV key depressed\n");
// delay(1000);
}
IrReceiver.printResultShort(&Serial);
Serial.print(" (");
Serial.print(IrReceiver.results.bits, DEC);
Serial.println(" xxx bits)");
}
//+=============================================================================
// The repeating section of the code
//
void loop() {
if (IrReceiver.decode()) { // Grab an IR code
dumpInfo(); // Output the results
// if you need more info. uncomment the following lines
// IrReceiver.printIRResultRawFormatted(&Serial); // Output the results in RAW format
// Serial.println(); // blank line between entries
// IrReceiver.printIRResultAsCArray(&Serial); // Output the results as source code array
// IrReceiver.printIRResultAsCVariables(&Serial); // Output address and data as source code variables
// IrReceiver.printIRResultAsPronto(&Serial);
// Serial.println(); // 2 blank lines between entries
// Serial.println();
IrReceiver.resume(); // Prepare for the next value
}
}
56
Arduino
Uno
GND
5V
Pin4
Infrared light
17-key RC type
Arrow_up (on_replay)
Arrow_down (off relay)
Pin11
GND
Vcc (5V)
or
IR receiver module
KY-022
Out Vcc, GND
-
+
S
GND
5V
Pin4
Relay
Old code method

## Slide 57: Test 11b_Use one IR controller to control another IR controller
/* from: https://github.com/z3t0/Arduino-IRremote * IRremote: IRrecvDemo - demonstrates receiving IR codes with IRrecv
An IR detector/demodulator must be connected to the input RECV_PIN.
Version 0.1 July, 2009
Copyright 2009 Ken Shirriff
http://arcfn.com
*/
// IR control rely, use 1 reciver to recive IR and send to another IR remote controller, 2020 April 23
#include <IRremote.h>
IRsend irsend;
/// the black remote controls: 17 kets
#define B_01 0xFFA25D
#define B_02 0xFF629D
#define B_03 0xFFE21D
#define B_04 0xFF22DD
#define B_05 0xFF02FD
#define B_06 0xFFC23D
#define B_07 0xFFE01F
#define B_08 0xFFA857
#define B_09 0xFF906F
#define B_00 0xFF9867
#define B_STAR 0xFF6897
#define B_HASH 0xFFB04F
#define B_LEFT 0xFF10EF
#define B_RIGHT 0xFF5AA5
#define B_UP 0xFF18E7
#define B_DOWN 0xFF4AB5
#define B_OK 0xFF38C7
//My_TV_Super= MTS, NEC:
#define MTS_UP 0xFB0058A7
#define MTS_LEFT 0xFB00E21D
#define MTS_RIGHT 0xFB00E01F
#define MTS_DOWN 0xFB0012ED
#define MTS_OK 0xFB00609F
#define MTS_POWER 0xFB0038C7
#define MTS_MTS_VOD 0xFB0020DF
#define MTS_HOME 0xFB0050AF
#define MTS_RETURN 0xFB00926D
#define MTS_INFO 0xFB0018E7
#define MTS_PLAY 0xFB00807F
#define MTS_STOP 0xFB00FA05
#define MTS_REW 0xFB009867
#define MTS_FFW 0xFB001AE5
#define MTS_SILENT 0xFB003AC5
#define MTS_BACKSPACE 0xFB0008F7
#define MTS_KEY0 0xFB0030CF
#define MTS_KEY1 0xFB002AD5
#define MTS_KEY2 0xFB006897
#define MTS_KEY3 0xFB00A857
#define MTS_KEY4 0xFB000AF5
#define MTS_KEY5 0xFB0048B7
#define MTS_KEY6 0xFB008877
#define MTS_KEY7 0xFB0032CD
#define MTS_KEY8 0xFB00708F
#define MTS_KEY9 0xFB00B04F
#define SIGNAL_DELAY1 150 // at least 120
#define SIGNAL_DELAY2 0 // at least 0
#define REC_DELAY 10 // typical 250 , 10-100 is ok for slow key-press action
/////////////////////////////////////////////////
int RECV_PIN = 11;
int RELAY_PIN = 4;
IRrecv irrecv(RECV_PIN);
long unsigned int irCode;
decode_results results;
// Dumps out the decode_results structure.
// Call this after IRrecv::decode()
// void * to work around compiler issue
//void dump(void *v) {
// decode_results *results = (decode_results *)
//////////////////////////////////////////////////////////////
void send_code_to_TV( long unsigned int irCode_recieved)
{
switch (irCode_recieved) {
case B_UP:
irCode = MTS_UP; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_DOWN:
irCode = MTS_DOWN; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_OK:
irCode = MTS_OK; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_LEFT:
irCode = MTS_LEFT; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_RIGHT:
irCode = MTS_RIGHT; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_STAR:
irCode = MTS_HOME; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_00:
irCode = MTS_RETURN; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_HASH:
irCode = MTS_INFO; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_01:
irCode = MTS_PLAY; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_02:
irCode = MTS_REW; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_03:
irCode = MTS_FFW; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_04:
irCode = MTS_STOP; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_07:
irCode = MTS_SILENT; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_09:
irCode = MTS_BACKSPACE; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
}
}
//////////////////////////////////////////////////
void dump(decode_results *results) {
int count = results->rawlen;
if (results->decode_type == UNKNOWN) {
Serial.println("Could not decode message");
}
else {
if (results->decode_type == NEC) {
Serial.print("Decoded NEC: ");
}
else if (results->decode_type == SONY) {
Serial.print("Decoded SONY: ");
}
else if (results->decode_type == RC5) {
Serial.print("Decoded RC5: ");
}
else if (results->decode_type == RC6) {
Serial.print("Decoded RC6: ");
}
Serial.print(results->value, HEX);
send_code_to_TV(results->value); /////////////////////////////////
Serial.print(" (");
Serial.print(results->bits, DEC);
Serial.println(" bits)");
}
Serial.print("Raw (");
Serial.print(count, DEC);
Serial.print("): ");
for (int i = 0; i < count; i++) {
if ((i % 2) == 1) {
Serial.print(results->rawbuf[i]*USECPERTICK, DEC);
}
else {
Serial.print(-(int)results->rawbuf[i]*USECPERTICK, DEC);
}
Serial.print(" ");
}
Serial.println("");
}
//////////////////////////////////////////////////////////////
void send_IR_code(long unsigned int irCode_to_sent)
{
Serial.println(irCode_to_sent, HEX);
Serial.println("--------------");
delay(SIGNAL_DELAY1);
irsend.sendNEC(irCode_to_sent, 32);
delay(SIGNAL_DELAY2);
irrecv.enableIRIn(); //fix rec freeze after sent, see https://forum.arduino.cc/index.php?topic=192472.0
}
/////////////////////////////////////////////////////
void setup()
{ pinMode(RELAY_PIN, OUTPUT);
pinMode(13, OUTPUT);
Serial.begin(9600);
irrecv.enableIRIn(); // Start the receiver
}
int on = 0;
unsigned long last = millis();
/////////////////////////////////////////////////////
void loop() {
if (irrecv.decode(&results)) {
// If it's been at least 1/4 second since the last
// IR received, toggle the relay
if (millis() - last > REC_DELAY) {
on = !on;
digitalWrite(RELAY_PIN, on ? HIGH : LOW);
digitalWrite(13, on ? HIGH : LOW);
dump(&results); // this is to send the recived code to the TV
}
last = millis();
irrecv.resume(); // Receive the next value
}
}
Remote controller
IR receiver (pin11)
IR emitter(pin3)
Reason to make it: use any controller to control any devices.
50 Ohms
Out GND 5V
or
IR receiver module
KY-022
Out Vcc, GND

## Slide 58: Test 2.11c: combine IR receiver, keypad for TV box control (//MTVS_controller_by_4x3keypad200708a.ino)
//MTVS_controller_by_4x3keypad200708a.ino
/* from: https://github.com/z3t0/Arduino-IRremote * IRremote: IRrecvDemo - demonstrates receiving IR codes with IRrecv
An IR detector/demodulator must be connected to the input RECV_PIN.
Version 0.1 July, 2009
Copyright 2009 Ken Shirriff
http://arcfn.com
*/
//////////////for keypad /////////////////////////////
//<script src="https://gist.github.com/francis2110/f04237b04c94218028e3.js"></script>
//https://gist.github.com/francis2110/f04237b04c94218028e3
//application for send infrared codes to LG tv with arduino
//irEmitterApp
#include <IRremote.h>
IRsend irsend;
////tv super box, NEC: FB0058A7 (32 bits)
//#define UP 0xFB0058A7
//#define LEFT 0xFB00E21D
//#define RIGHT 0xFB00E01F
//#define DOWN 0xFB0012ED
//#define OK 0xFB00609F
//
//#define POWER 0xFB0038C7
//#define TV_VOD 0xFB0020DF
//
//#define HOME 0xFB0050AF
//#define RET 0xFB00926D
//#define INFO_ 0xFB0018E7
//
//#define PLAY 0xFB00807F
//#define STOP 0xFB00FA05
//#define REW 0xFB009867
//#define FFW 0xFB001AE5
//
//#define SILENT 0xFB003AC5
//#define BACK_SPACE 0xFB0008F7
//
//#define KEY0 0xFB0030CF
//#define KEY1 0xFB002AD5
//#define KEY2 0xFB006897
//#define KEY3 0xFB00A857
//#define KEY4 0xFB000AF5
//#define KEY5 0xFB0048B7
//#define KEY6 0xFB008877
//#define KEY7 0xFB0032CD
//#define KEY8 0xFB00708F
//#define KEY9 0xFB00B04F
static int cero = 0;
long unsigned int irCode;
int cmdReceived;
//////////////for keypad /////////////////////////////
#include <Keypad.h> //keypad by mark standley
const byte ROWS = 4; // Four rows
const byte COLS = 3; // Three columns
// Define the Keymap
char keys[ROWS][COLS] = {
{'1', '2', '3'},
{'4', '5', '6'},
{'7', '8', '9'},
{'*', '0', '#'}
};
// Connect keypad ROW0, ROW1, ROW2 and ROW3 to these Arduino pins.
byte rowPins[ROWS] = { 9, 8, 7, 6 };
//byte rowPins[ROWS] = { 5, 4, 3, 2 };
// Connect keypad COL0, COL1 and COL2 to these Arduino pins.
byte colPins[COLS] = { 12, 11, 10 };
//byte colPins[COLS] = { 8, 7, 6};
// Create the Keypad
Keypad kpd = Keypad( makeKeymap(keys), rowPins, colPins, ROWS, COLS );
#define ledpin 13
////////////////////////////////////////////////////////////////
// IR control rely, use 1 reciver to recive IR and send to another IR remote controller, 2020 April 23
//include <IRremote.h>
//IRsend irsend;
/// the black remote controls: 17 kets
#define B_01 0xFFA25D
#define B_02 0xFF629D
#define B_03 0xFFE21D
#define B_04 0xFF22DD
#define B_05 0xFF02FD
#define B_06 0xFFC23D
#define B_07 0xFFE01F
#define B_08 0xFFA857
#define B_09 0xFF906F
#define B_00 0xFF9867
#define B_STAR 0xFF6897
#define B_HASH 0xFFB04F
#define B_LEFT 0xFF10EF
#define B_RIGHT 0xFF5AA5
#define B_UP 0xFF18E7
#define B_DOWN 0xFF4AB5
#define B_OK 0xFF38C7
//My_TV_Super= MTS, NEC:
#define MTS_UP 0xFB0058A7
#define MTS_LEFT 0xFB00E21D
#define MTS_RIGHT 0xFB00E01F
#define MTS_DOWN 0xFB0012ED
#define MTS_OK 0xFB00609F
#define MTS_POWER 0xFB0038C7
#define MTS_MTS_VOD 0xFB0020DF
#define MTS_HOME 0xFB0050AF
#define MTS_RETURN 0xFB00926D
#define MTS_INFO 0xFB0018E7
#define MTS_PLAY 0xFB00807F
#define MTS_STOP 0xFB00FA05
#define MTS_REW 0xFB009867
#define MTS_FFW 0xFB001AE5
#define MTS_SILENT 0xFB003AC5
#define MTS_BACKSPACE 0xFB0008F7
#define MTS_KEY0 0xFB0030CF
#define MTS_KEY1 0xFB002AD5
#define MTS_KEY2 0xFB006897
#define MTS_KEY3 0xFB00A857
#define MTS_KEY4 0xFB000AF5
#define MTS_KEY5 0xFB0048B7
#define MTS_KEY6 0xFB008877
#define MTS_KEY7 0xFB0032CD
#define MTS_KEY8 0xFB00708F
#define MTS_KEY9 0xFB00B04F
#define SIGNAL_DELAY1 150 // at least 120
#define SIGNAL_DELAY2 0 // at least 0
#define REC_DELAY 10 // typical 250 , 10-100 is ok for slow key-press action
/////////////////////////////////////////////////
int RECV_PIN = 5 ; //11;
//int RELAY_PIN = 4;
IRrecv irrecv(RECV_PIN);
//long unsigned int irCode;
decode_results results;
// Dumps out the decode_results structure.
// Call this after IRrecv::decode()
// void * to work around compiler issue
//void dump(void *v) {
// decode_results *results = (decode_results *)
//////////////////////////////////////////////////////////////
void send_code_to_TV( long unsigned int irCode_recieved)
{
switch (irCode_recieved) {
case B_UP:
irCode = MTS_UP; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_DOWN:
irCode = MTS_DOWN; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_OK:
irCode = MTS_OK; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_LEFT:
irCode = MTS_LEFT; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_RIGHT:
irCode = MTS_RIGHT; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_STAR:
irCode = MTS_HOME; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_00:
irCode = MTS_RETURN; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_HASH:
irCode = MTS_INFO; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_01:
irCode = MTS_PLAY; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_02:
irCode = MTS_REW; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_03:
irCode = MTS_FFW; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_04:
irCode = MTS_STOP; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_07:
irCode = MTS_SILENT; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_09:
irCode = MTS_BACKSPACE; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
}
}
//////////////////////////////////////////////////
void dump(decode_results *results) {
int count = results->rawlen;
if (results->decode_type == UNKNOWN) {
Serial.println("Could not decode message");
}
else {
if (results->decode_type == NEC) {
Serial.print("Decoded NEC: ");
}
else if (results->decode_type == SONY) {
Serial.print("Decoded SONY: ");
}
else if (results->decode_type == RC5) {
Serial.print("Decoded RC5: ");
}
else if (results->decode_type == RC6) {
Serial.print("Decoded RC6: ");
}
Serial.print(results->value, HEX);
send_code_to_TV(results->value); /////////////////////////////////
Serial.print(" (");
Serial.print(results->bits, DEC);
Serial.println(" bits)");
}
Serial.print("Raw (");
Serial.print(count, DEC);
Serial.print("): ");
for (int i = 0; i < count; i++) {
if ((i % 2) == 1) {
Serial.print(results->rawbuf[i]*USECPERTICK, DEC);
}
else {
Serial.print(-(int)results->rawbuf[i]*USECPERTICK, DEC);
}
Serial.print(" ");
}
Serial.println("");
}
//////////////////////////////////////////////////////////////
void send_IR_code(long unsigned int irCode_to_sent)
{
Serial.println(irCode_to_sent, HEX);
Serial.println("--------------");
delay(SIGNAL_DELAY1);
irsend.sendNEC(irCode_to_sent, 32);
delay(SIGNAL_DELAY2);
irrecv.enableIRIn(); //fix rec freeze after sent, see https://forum.arduino.cc/index.php?topic=192472.0
}
/////////////////////////////////////////////////////
void setup()
{ //pinMode(RELAY_PIN, OUTPUT);
pinMode(13, OUTPUT);
Serial.begin(9600);
irrecv.enableIRIn(); // Start the receiver
}
int on = 0;
unsigned long last = millis();
/////////////////////////////////////////////////////
void loop() {
////////////// check IR-code recived from IR-controller //////////
if (irrecv.decode(&results)) {
// If it's been at least 1/4 second since the last
// IR received, toggle the relay
if (millis() - last > REC_DELAY) {
on = !on;
// digitalWrite(RELAY_PIN, on ? HIGH : LOW);
digitalWrite(13, on ? HIGH : LOW);
dump(&results); // this is to send the recived code to the TV
}
last = millis();
irrecv.resume(); // Receive the next value
}
/////////// check 3x4 or 4x4 keypad ///////////////////////////
check_keypad_send_IR_code();
}
// 3x4 pad MTV super
// {'1', '2', '3'}, [MTS_HOME, MTS_up, MTS_INFO]
// {'4', '5', '6'}, [MTS_LEFT, MTS_OK, MTS_RIGHT]
// {'7', '8', '9'}, [goto_BBC, MTS_DOWN, MTS_RETURN]
// {'*', '0', '#'}, goto_NHK, goto_CANTONESE, goto_MAIYAR]
/////////////////////////////////////////////////////////////////
void check_keypad_send_IR_code()
{ char key = kpd.getKey();
if (key) // Check for a valid key.
{
switch (key)
{
case '1':
irCode = MTS_HOME; send_IR_code(irCode);
break;
case '2':
irCode = MTS_UP; send_IR_code( irCode);
break;
case '3':
irCode = MTS_INFO; send_IR_code(irCode);
break;
case '4':
irCode = MTS_LEFT; send_IR_code(irCode);
break;
case '5':
irCode = MTS_OK; send_IR_code(irCode);
break;
case '6':
irCode = MTS_RIGHT; send_IR_code(irCode);
break;
case '7':
goto_BBC();
break;
case '8':
irCode = MTS_DOWN; send_IR_code(irCode);
break;
case '9':
irCode = MTS_RETURN; send_IR_code(irCode);
break;
case '*':
goto_NHK();
break;
case '0':
goto_CANTONESE();
break;
case '#':
goto_MAIYAR();
break;
default:
Serial.println(key);
}
}
}
//////////////////////////////////////////////////
void goto_BBC()
{
irCode = MTS_HOME; send_IR_code( irCode);
delay(5000);
for (int i = 1 ; i <= 3; i++)
{ irCode = MTS_RIGHT; send_IR_code( irCode);
delay(1000);
}
////////////
for (int i = 1 ; i <= 11; i++)
{ irCode = MTS_DOWN; send_IR_code( irCode);
delay(1000);
}
irCode = MTS_OK; send_IR_code( irCode);
}
//////////////////////////////////////////////////
//////////////////////////////////////////////////
void goto_NHK()
{
irCode = MTS_HOME; send_IR_code( irCode);
delay(5000);
for (int i = 1 ; i <= 3; i++)
{ irCode = MTS_RIGHT; send_IR_code( irCode);
delay(1000);
}
////////////
for (int i = 1 ; i <= 9; i++)
{ irCode = MTS_DOWN; send_IR_code( irCode);
delay(1000);
}
irCode = MTS_OK; send_IR_code( irCode);
}
//////////////////////////////////////////////////
void goto_CANTONESE()
{
irCode = MTS_HOME; send_IR_code( irCode);
delay(5000);
for (int i = 1 ; i <= 1; i++)
{ irCode = MTS_RIGHT; send_IR_code( irCode);
delay(1000);
}
////////////
for (int i = 1 ; i <= 5; i++)
{ irCode = MTS_DOWN; send_IR_code( irCode);
delay(1000);
}
irCode = MTS_OK; send_IR_code( irCode);
}
/////////////////////////////////////////////////
void goto_MAIYAR()
{
irCode = MTS_HOME; send_IR_code( irCode);
delay(5000);
for (int i = 1 ; i <= 1; i++)
{ irCode = MTS_RIGHT; send_IR_code( irCode);
delay(1000);
}
////////////
for (int i = 1 ; i <= 6; i++)
{ irCode = MTS_DOWN; send_IR_code( irCode);
delay(1000);
}
irCode = MTS_OK; send_IR_code( irCode);
}
Stem2: Arduino experiments v0.d.1
58
Remote controller
IR receiver (pin11)
IR emitter(pin3)
Reason to make it: use any controller to control any devices.
50 Ohms
Out GND 5V
or
IR receiver module
KY-022
Out Vcc, GND

## Slide 59: Test2.11d rc_all1c2.ino 2020.07.16 Combined remote controller
/* rc_all1c2.ino 2020 July16 from: https://github.com/z3t0/Arduino-IRremote * IRremote: IRrecvDemo - demonstrates receiving IR codes with IRrecv
An IR detector/demodulator must be connected to the input RECV_PIN.
Version 0.1 July, 2009
Copyright 2009 Ken Shirriff
http://arcfn.com
*/
//////////////for keypad /////////////////////////////
//<script src="https://gist.github.com/francis2110/f04237b04c94218028e3.js"></script>
//https://gist.github.com/francis2110/f04237b04c94218028e3
//application for send infrared codes to LG tv with arduino
//irEmitterApp
#include <IRremote.h>
IRsend irsend;
static int cero = 0;
long unsigned int irCode;
int cmdReceived;
///////////////////////////////////////////////////////
// DEFINE table1 LGTV
#define LGTV_SOURCE 0x20DFD02F
#define LGTV_SUBTITLE 0x20DF9C63 //20DF9C63
#define LGTV_POWER 0x20DF10EF //on/off
#define LGTV_AV_TV 0x20DFF00F
#define LGTV_NICAM_I_II 0x20DF50AF
#define LGTV_SLEEP 0x20DF708F
#define LGTV_1 0x20DF8877
#define LGTV_2 0x20DF48B7
#define LGTV_3 0x20DFC837
#define LGTV_4 0x20DF28D7
#define LGTV_5 0x20DFA857
#define LGTV_6 0x20DF6897
#define LGTV_7 0x20DFE817
#define LGTV_8 0x20DF18E7
#define LGTV_9 0x20DF9867
#define LGTV_0 0x20DF08F7
#define LGTV_ARROW_UP 0x20DF02FD
#define LGTV_ARROW_DOWN 0x20DF827D
#define LGTV_ARROW_LEFT 0x20DFE01F
#define LGTV_ARROW_RIGHT 0x20DF609F
#define LGTV_OK 0x20DF22DD
#define LGTV_VOL_UP 0x20DF40BF
#define LGTV_VOL_DOWN 0x20DFC03F
#define LGTV_CHAN_UP 0x20DF00FF
#define LGTV_CHAN_DOWN 0x20DF807F
#define LGTV_RED 0x20DF4EB1
#define LGTV_GREEN 0x20DF8E71
#define LGTV_YELLOW 0x20DFC639
#define LGTV_BLUE 0x20DF8679
#define LGTV_REWIND 0x20DFF10E
#define LGTV_PLAY 0x20DF0DF2
#define LGTV_PAUSE 0x20DF5DA2
#define LGTV_FAST_FORWARD 0x20DF718E
#define LGTV_HOME 0x20DF3EC1
#define LGTV_NETFLIX 0x20DF6A95
#define LGTV_MENU 0x20DFC23D
#define LGTV_RETURN 0x20DF14EB
#define LGTV_TOOLS 0x20DFA25D
#define LGTV_EXIT 0x20DFDA25
#define LGTV_GUIDE 0x20DFD52A
#define LGTV_Q_VIEW 0x20DF55AA
///////////// for Black, 17-keys-keypad
//#define B17_01 0xFFA25D
///////////////////////////////////////////////////////
// DEFINE table2 : 17 keys black remote controls:
#define B17_01 0x00FFA25D
#define B17_02 0x00FF629D
#define B17_03 0x00FFE21D
#define B17_04 0x00FF22DD
#define B17_05 0x00FF02FD
#define B17_06 0x00FFC23D
#define B17_07 0x00FFE01F
#define B17_08 0x00FFA857
#define B17_09 0x00FF906F
#define B17_00 0x00FF9867
#define B17_STAR 0x00FF6897
#define B17_HASH 0x00FFB04F
#define B17_LEFT 0x00FF10EF
#define B17_RIGHT 0x00FF5AA5
#define B17_UP 0x00FF18E7
#define B17_DOWN 0x00FF4AB5
#define B17_OK 0x00FF38C7
///////////////////////////////////////////////////////
//My_TV_Super= MTS, NEC:
#define MTS_UP 0xFB0058A7
#define MTS_LEFT 0xFB00E21D
#define MTS_RIGHT 0xFB00E01F
#define MTS_DOWN 0xFB0012ED
#define MTS_OK 0xFB00609F
#define MTS_POWER 0xFB0038C7
#define MTS_MTS_VOD 0xFB0020DF
#define MTS_HOME 0xFB0050AF
#define MTS_RETURN 0xFB00926D
#define MTS_INFO 0xFB0018E7
#define MTS_RED 0xFB00807F //MTS_PLAY
#define MTS_GREEN 0xFB00FA05 //MTS_STOP
#define MTS_YELLOW 0xFB009867 //MTS_REW
#define MTS_BLUE 0xFB001AE5 //MTS_FFW
#define MTS_SILENT 0xFB003AC5
#define MTS_BACKSPACE 0xFB0008F7
#define MTS_KEY0 0xFB0030CF
#define MTS_KEY1 0xFB002AD5
#define MTS_KEY2 0xFB006897
#define MTS_KEY3 0xFB00A857
#define MTS_KEY4 0xFB000AF5
#define MTS_KEY5 0xFB0048B7
#define MTS_KEY6 0xFB008877
#define MTS_KEY7 0xFB0032CD
#define MTS_KEY8 0xFB00708F
#define MTS_KEY9 0xFB00B04F
#define SIGNAL_DELAY1 150 // at least 120
#define SIGNAL_DELAY2 0 // at least 0
#define REC_DELAY 10 // typical 250 , 10-100 is ok for slow key-press action
//////////////for keypad /////////////////////////////
#include <Keypad.h> //keypad by mark standley
const byte ROWS = 4; // 4 rows
const byte COLS = 4; // 4 columns
// Define the Keymap
char keys[ROWS][COLS] = {
{'0', '1', '2', '3'},
{'4', '5', '6', '7'},
{'8', '9', 'A', 'B'},
{'C', 'D', 'E', 'F'}
};
// Connect keypad ROW0, ROW1, ROW2 and ROW3 to these Arduino pins.
byte rowPins[ROWS] = { 5, 4, 10, 2 };
// Connect keypad COL0, COL1 and COL2 to these Arduino pins.
byte colPins[COLS] = { 6, 7, 8, 9};
// Create the Keypad
Keypad kpd = Keypad( makeKeymap(keys), rowPins, colPins, ROWS, COLS );
////////////////////////////////////////////////////////////////
// IR control rely, use 1 reciver to recive IR and send to another IR remote controller, 2020 April 23
//include <IRremote.h>
//IRsend irsend;
/////////////////////////////////////////////////
// by default IR transmitter pin is 3, you cannot change it, no need to declare here
int analog_switch_input_pin = A1;
//int RELAY_PIN = 4; //not used in this project
int RECV_PIN = 11;
#define ledpin 13
IRrecv irrecv(RECV_PIN);
//long unsigned int irCode;
decode_results results;
// Dumps out the decode_results structure.
// Call this after IRrecv::decode()
// void * to work around compiler issue
//void dump(void *v) {
// decode_results *results = (decode_results *)
////////////////////////
void send_IR_code(long unsigned int irCode_to_sent)
{
Serial.println(irCode_to_sent, HEX);
Serial.println("--------------");
// delay(SIGNAL_DELAY1);
irsend.sendNEC(irCode_to_sent, 32);
// delay(SIGNAL_DELAY2);
irrecv.enableIRIn(); //fix rec freeze after sent, see https://forum.arduino.cc/index.php?topic=192472.0
}
/////////////////////////////////////////////////////
void setup()
{ //pinMode(RELAY_PIN, OUTPUT);
pinMode(13, OUTPUT);
Serial.begin(9600);
irrecv.enableIRIn(); // Start the receiver
}
int on = 0;
unsigned long last = millis();
/////////////////////////////////////////////////////
void loop() {
////////////// check IR-code recived from IR-controller //////////
if (irrecv.decode(&results)) {
// If it's been at least 1/4 second since the last
// IR received, toggle the relay
if (millis() - last > REC_DELAY) {
on = !on;
// digitalWrite(RELAY_PIN, on ? HIGH : LOW);
digitalWrite(13, on ? HIGH : LOW);
dump(&results); // this is to received IR code recived and sedn to Seiral.println
}
last = millis();
irrecv.resume(); // Receive the next value
}
/////////// check 3x4 or 4x4 keypad ///////////////////////////
int analog_switch_input_val = analogRead( analog_switch_input_pin) ;
if ( analog_switch_input_val < 341) //low, divide 1024 into3 parts:1024/3=341, 341*2=682
{ //Serial.println("analog_switch_input_val LOW vvvv");
check_keypad_send_IR_code_LGTV();
}
if ( 341 < analog_switch_input_val && analog_switch_input_val < 682) //middle
{
check_keypad_send_IR_code_OTHERS();
}
if ( analog_switch_input_val > 682) //low
{ check_keypad_send_IR_code_MTV(); //my TV super
}
}
///////////// send recived IR code to Seiral.println//////
void dump(decode_results *results) {
int count = results->rawlen;
if (results->decode_type == UNKNOWN) {
Serial.println("Could not decode message");
}
else {
if (results->decode_type == NEC) {
Serial.print("Decoded NEC: ");
}
else if (results->decode_type == SONY) {
Serial.print("Decoded SONY: ");
}
else if (results->decode_type == RC5) {
Serial.print("Decoded RC5: ");
}
else if (results->decode_type == RC6) {
Serial.print("Decoded RC6: ");
}
Serial.print(results->value, HEX);
//send_code_to_TV(results->value); //not used here//////////
Serial.print(" (");
Serial.print(results->bits, DEC);
Serial.println(" bits)");
}
Serial.print("Raw (");
Serial.print(count, DEC);
Serial.print("): ");
for (int i = 0; i < count; i++) {
if ((i % 2) == 1) {
Serial.print(results->rawbuf[i]*USECPERTICK, DEC);
}
else {
Serial.print(-(int)results->rawbuf[i]*USECPERTICK, DEC);
}
Serial.print(" ");
}
Serial.println("");
}
/////////////////////////////////////////////////////////////////
void check_keypad_send_IR_code_LGTV()
{ char key = kpd.getKey();
if (key) // Check for a valid key.
{
switch (key)
{
case '0':
Serial.println("LGTV 0");
irCode = LGTV_POWER; send_IR_code( irCode);
break;
case '1':
Serial.println("LGTV 1");
irCode = LGTV_ARROW_UP; send_IR_code( irCode);
break;
case '2':
Serial.println("LGTV 2");
irCode = LGTV_SOURCE; send_IR_code( irCode);
break;
case '3':
Serial.println("LGTV 3");
irCode = LGTV_VOL_UP; send_IR_code( irCode);
break;
case '4':
Serial.println("LGTV 4");
irCode = LGTV_ARROW_LEFT; send_IR_code( irCode);
break;
case '5':
Serial.println("LGTV 5");
irCode = LGTV_OK; send_IR_code( irCode);
break;
case '6':
Serial.println("LGTV 6");
irCode = LGTV_ARROW_RIGHT; send_IR_code( irCode);
break;
case '7':
Serial.println("LGTV 7");
irCode = LGTV_VOL_DOWN; send_IR_code( irCode);
break;
case '8':
Serial.println("LGTV 8");
irCode = LGTV_HOME; send_IR_code( irCode);
break;
case '9':
Serial.println("LGTV 9");
irCode = LGTV_ARROW_DOWN; send_IR_code( irCode);
break;
case 'A':
Serial.println("LGTV A");
irCode = LGTV_RETURN; send_IR_code( irCode);
break;
case 'B':
Serial.println("LGTV B");
irCode = LGTV_CHAN_UP; send_IR_code( irCode);
break;
case 'C':
Serial.println("LGTV C");
irCode = LGTV_PLAY; send_IR_code( irCode);
break;
case 'D':
Serial.println("LGTV D");
irCode = LGTV_PAUSE; send_IR_code( irCode);
break;
case 'E':
Serial.println("LGTV E");
irCode = LGTV_EXIT; send_IR_code( irCode);
break;
case 'F':
Serial.println("LGTV F");
irCode = LGTV_CHAN_DOWN; send_IR_code( irCode);
break;
default:
Serial.println(key);
}
}
}
/*
char keys[ROWS][COLS] = {
{'0', '1', '2', '3'},
{'4', '5', '6', '7'},
{'8', '9', 'A', 'B'},
{'C', 'D', 'E', 'F'}
};
*/
/////////////////////////////////////////////////////////////////
void check_keypad_send_IR_code_MTV()
{ char key = kpd.getKey();
if (key) // Check for a valid key.
{
switch (key)
{
case '0':
Serial.println("MTV 0");
irCode = MTS_POWER; send_IR_code( irCode);
break;
case '1':
Serial.println("MTV 1");
irCode = MTS_UP; send_IR_code( irCode);
break;
case '2':
Serial.println("MTV 2");
goto_BBC();
break;
case '3':
Serial.println("MTV 3");
irCode = LGTV_VOL_UP; send_IR_code( irCode); //LGTV_VOL_UP
break;
case '4':
Serial.println("LGTV 4");
irCode = MTS_LEFT; send_IR_code(irCode);
break;
case '5':
Serial.println("LGTV 5");
irCode = MTS_OK; send_IR_code(irCode);
break;
case '6':
Serial.println("LGTV 6");
irCode = MTS_RIGHT; send_IR_code(irCode);
break;
case '7':
Serial.println("LGTV 7");
irCode = LGTV_VOL_DOWN; send_IR_code( irCode); //LGTV_VOL_DOWN
break;
case '8':
Serial.println("LGTV 8");
irCode = MTS_HOME; send_IR_code(irCode);
break;
case '9':
Serial.println("LGTV 9");
irCode = MTS_DOWN; send_IR_code(irCode);
break;
case 'A':
Serial.println("LGTV A");
irCode = MTS_RETURN; send_IR_code(irCode);
break;
case 'B':
Serial.println("LGTV B");
irCode = MTS_INFO; send_IR_code(irCode);
break;
case 'C':
Serial.println("LGTV C");
goto_CANTONESE();
break;
case 'D':
Serial.println("LGTV D");
goto_MAIYAR();
break;
case 'E':
Serial.println("LGTV E");
goto_NHK();
break;
case 'F':
Serial.println("LGTV F");
goto_FRANCE();
break;
default:
Serial.println(key);
}
}
}
////////////////////////////////////////////////////////////////
void check_keypad_send_IR_code_OTHERS()
{ char key = kpd.getKey();
if (key) // Check for a valid key.
{
switch (key)
{
case '0':
Serial.println("OTHERS 0");
irCode = B17_00; send_IR_code( irCode);
break;
case '1':
Serial.println("OTHERS 1");
irCode = B17_01; send_IR_code( irCode);
break;
case '2':
Serial.println("OTHERS 2");
irCode = B17_02; send_IR_code( irCode);
break;
case '3':
Serial.println("OTHERS 3");
irCode = B17_03; send_IR_code( irCode);
break;
case '4':
Serial.println("OTHERS 4");
goto_BBC();
break;
default:
Serial.println(key);
}
}
}
//**************************************************
////////////////////////////////////////////////////////
void goto_BBC()
{
irCode = MTS_HOME; send_IR_code( irCode);
delay(10000);
for (int i = 1 ; i <= 3; i++)
{ irCode = MTS_RIGHT; send_IR_code( irCode);
delay(500);
}
////////////
for (int i = 1 ; i <= 11; i++)
{ irCode = MTS_DOWN; send_IR_code( irCode);
delay(500);
}
irCode = MTS_OK; send_IR_code( irCode);
}
////////////////////////////////////////////////////////
void goto_CANTONESE()
{
irCode = MTS_HOME; send_IR_code( irCode);
delay(10000);
for (int i = 1 ; i <= 1; i++)
{ irCode = MTS_RIGHT; send_IR_code( irCode);
delay(500);
}
////////////
for (int i = 1 ; i <= 5; i++)
{ irCode = MTS_DOWN; send_IR_code( irCode);
delay(500);
}
irCode = MTS_OK; send_IR_code( irCode);
}
////////////////////////////////////////////////////////
void goto_MAIYAR()
{
irCode = MTS_HOME; send_IR_code( irCode);
delay(10000);
for (int i = 1 ; i <= 1; i++)
{ irCode = MTS_RIGHT; send_IR_code( irCode);
delay(500);
}
////////////
for (int i = 1 ; i <= 6; i++)
{ irCode = MTS_DOWN; send_IR_code( irCode);
delay(500);
}
irCode = MTS_OK; send_IR_code( irCode);
}
////////////////////////////////////////////////////////
void goto_NHK()
{
irCode = MTS_HOME; send_IR_code( irCode);
delay(10000);
for (int i = 1 ; i <= 3; i++)
{ irCode = MTS_RIGHT; send_IR_code( irCode);
delay(500);
}
////////////
for (int i = 1 ; i <= 9; i++)
{ irCode = MTS_DOWN; send_IR_code( irCode);
delay(500);
}
irCode = MTS_OK; send_IR_code( irCode);
}
////////////////////////////////////////////////////////
void goto_FRANCE()
{
irCode = MTS_HOME; send_IR_code( irCode);
delay(10000);
for (int i = 1 ; i <= 3; i++)
{ irCode = MTS_RIGHT; send_IR_code( irCode);
delay(500);
}
////////////
for (int i = 1 ; i <= 7; i++)
{ irCode = MTS_DOWN; send_IR_code( irCode);
delay(500);
}
irCode = MTS_OK; send_IR_code( irCode);
}

## Slide 60: Test2.12: L298 H-bridge drives 2 Direct Current D.C. motors
H-bridgeArduino
int ENA = 5;
int IN1 = 6;
int IN2 = 7;
int IN3 = 8;
int IN4 = 9;
int ENB = 10;
https://www.youtube.com/watch?v=9W5S5nqRegU
6V
battery
-
+
Keep the 5V jumper

## Slide 61: L298 D.C. (direct current) motor driver test12_L298Hbridge.ino
//modified
//from www.handsontec.com
//khwong
// Definitions Arduino pin
// connected to input H Bridge
int ENA = 5;
int IN1 = 6;
int IN2 = 7;
int IN3 = 8;
int IN4 = 9;
int ENB = 10;
void setup()
{
// Set the output pins
// 5 www.handsontec.com
pinMode(IN1, OUTPUT);
pinMode(IN2, OUTPUT);
pinMode(IN3, OUTPUT);
pinMode(IN4, OUTPUT);
}
void loop()
{
//Motor A moving
digitalWrite(ENA, HIGH);
digitalWrite(IN1, HIGH);
digitalWrite(IN2, LOW);
delay(2000);
digitalWrite(ENA, LOW);//stop motor
delay(2000);
//Motor A moving-reverse
digitalWrite(ENA, HIGH);
digitalWrite(IN1, LOW);
digitalWrite(IN2, HIGH);
delay(2000);
digitalWrite(ENA, LOW); //stop motor
delay(2000);
//---------------------------------
//Motor B moving
digitalWrite(ENB, HIGH);
digitalWrite(IN3, HIGH);
digitalWrite(IN4, LOW);
delay(2000);
digitalWrite(ENB, LOW);//stop motor
delay(2000);
//Motor B moving-reverse
digitalWrite(ENB, HIGH);
digitalWrite(IN3, LOW);
digitalWrite(IN4, HIGH);
delay(2000);
digitalWrite(ENB, LOW); //stop motor
delay(2000);
}

## Slide 62: Test2.13_2-axis Gyroscope test13_MPU6050_DMP6.ino
https://store.invensense.com/datasheets/invensense/MPU-6050_DataSheet_V3%204.pdf
Vcc
GND
A4
A5
Pin2
3 (X,Y,Z) rotational angles
Source code
https://github.com/ElectronicCats/mpu6050/tree/master/examples/MPU6050_DMP6
Video demo
https://www.youtube.com/watch?v=kyX9cRxJNdo
3D display is achieved by using
https://processing.org/

## Slide 63: How to use MPU6050_DMP6 (IMU) with processing GY80-master _tested_ok_200831.zip
How to run GY80-master _tested_ok_200831, 2020 Aug 31
Download GY80-master _tested_ok_200831 from
http://www.cse.cuhk.edu.hk/%7Ekhwong/www2/stem/GY80-master%20_tested_ok_200831.zip and unzip to a directory , say,
C:\Users\khwong\Documents\Arduino\GY80-master _tested_ok_200831, you have two major directories
directory 1: \ C:\Users\khwong\Documents\Arduino\GY80-master _tested_ok_200831\AHRS_9DOF_arduino\AHRS_9DOF
    It contains AHRS_9DOF.ino,
edit AHRS_9DOF.ino to check the correct Badu rate
      (line 51 #define OUTPUT_BAUD_RATE 57600 //115200)
    compile this .ino and upload to an Arduino–uno etc.
check which comm port you are using say “Com12”
You may open the Arduino/Tools/Serial_monito to see the data sending out from the Arduino, close the Com_window after the observation, otherwise processing cannot read this pot.
directory 2: C:\Users\khwong\Documents\Arduino\GY80-master _tested_ok_200831\AHRS_9DOF_processing\AHRS_9DOF_display
    That contains the “processing” code: AHRS_9DOF_display.pde
Install “processing”: Download processing (I tested the 32-bit version) from https://processing.org/download/
Save in somewhere: say c:\processing-3.5.4\
Go to the directory c:\processing-3.5.4\, double click “processing.exe” to start processing
In the processing window, open the *.pde (i.e. file AHRS_9DOF_display.pde) in directory 2(see above)
In AHRS_9DOF_display.pdeC , ceck if the correct prot is used, in
    line 24 of AHRS_9DOF_display, should conatin
      final static int SERIAL_PORT_BAUD_RATE = 57600; //115200; // choose the correct that matches the Arduino output baud rate, see above
Reference:
3D display is achieved by using
https://processing.org/

## Slide 64: SOUNDCIPHE with processing
2020.9.1 khw
Use of SOUNDCIPHER ( http://explodingart.com/soundcipher/download.html ) under processing. Assume you have installed processing (tested 32-bit) under C:\processing-3.5.4
Download http://explodingart.com/soundcipher/soundcipher.zip from http://explodingart.com/soundcipher/download.html
unzip \soundcipher and place the unzipped directory in
C:\processing-3.5.4\modes\java\libraries\soundcipher
also copy C:\processing-3.5.4\modes\java\libraries\soundcipher\examples
to C:\processing-3.5.4\ examples
run C:\processing-3.5.4\examples\Bing\Bing.pde to test if it is ok.

## Slide 65: Processing templates & 3D graphics
http://www.idea2ic.com/Processing_Template/ProcessingTemplate.html
https://forum.processing.org/two/discussion/23086/importing-3d-models-into-processing
https://forum.processing.org/two/discussion/24350/display-obj-file-in-3d
https://processing.org/reference/loadShape_.html
https://www.youtube.com/watch?v=6VSaneuiaWs (import .obj 3D into processing)
https://github.com/processing/processing/wiki/Advanced-OpenGL

## Slide 66: Test2.14a_self balance robot, test14_self_bal.ino Video demo: https://www.youtube.com/watch?v=9W5S5nqRegU
Use a 3-axis Gyroscope (MPU-6050 ) to sensor the orientation to balance the robot L298N dual H-bright http://www.handsontec.com/dataspecs/L298N%20Motor%20Driver.pdf
Reference Source Code: http://bit.ly/2RjHxOc
MPU-6050 3-axis Gyro with accelerometer: https://www.instructables.com/id/GY-521-MPU6050-3-Axis-Gyroscope-and-Accelerometer-/

## Slide 67: Test2.14b_self balance robot_code and circuit
Download Source Code: http://bit.ly/2RjHxOc
Arduino Compatible SCM & DIY Kits - https://goo.gl/yi21yB
Electronics Equipments & Tools - https://goo.gl/covX9J
Module Board For Arduino - https://goo.gl/81dafX
A4
A5
Pin2
Vcc
GND

## Slide 68: Test2.15_clap_sound_detection
Use the trimer and test15a_ky038_sound_cal.ino
to calibration the sensor by tuning the output to around 2.5V
https://www.hackster.io/iotboys/control-led-by-clap-using-arduino-and-sound-sensor-e31809
Video demo
https://www.youtube.com/watch?v=guZJT_h2gP0
test15b_ky038_sound_clap_detection.ino
A0, Gnd,5V,D0
A0 GND 5V Pin2 Pin4
Arduino UNO
LED
+
-
GND
Sound level LED
PowerLED

## Slide 69
//test15a_ky038_sound_cal.ino
//calibrtion code
int soundSensor=2; int LED=4;
int Analog_input_pin=A0;
boolean LEDStatus=false;
void setup() {
pinMode(soundSensor,INPUT);
pinMode(LED,OUTPUT);
pinMode (Analog_input_pin, INPUT);
Serial.begin (9600); // Serial output with 9600 bps
}
void loop() { float Analog;
// Current value will be read and converted to voltage
Analog = analogRead (Analog_input_pin) * (5.0 / 1023.0);
//for claibration of the sensor
Serial.print ("Analog voltage value:"); Serial.print (Analog, 4); Serial.print ("V, ");Serial.print ("Tune the sensor value around 2.5V \n");
}
//test15b_ky038_sound_clap_detection.ino
//https://www.hackster.io/iotboys/control-led-by-clap-using-arduino-and-sound-sensor-e31809. Calibration (IDE/Tools/Serial_monitor , tune the trimmer of the KY038 sound sensor to see display) and
//clap once led-on; clap another time led-off.
void loop() {
float Analog;
int SensorData=digitalRead(soundSensor);
if(SensorData==1){
if(LEDStatus==false){
LEDStatus=true;
digitalWrite(LED,HIGH);
}
else{
LEDStatus=false;
digitalWrite(LED,LOW); } } }

## Slide 70: Test2.16 Ultrasonic range sensor
Use the time of flight of sound to measure the range of an obstacle.
Use test16_usound.ino
And IDE/Tools/serial_monitor
For displaying the range:
distance to nearest object:13 cm
Video demo
https://www.youtube.com/watch?v=6F1B_N6LuKw
Vcc, Trig,Rx,Do,GND
5V 13 12 GND
Arduino UNO
https://create.arduino.cc/projecthub/Nicholas_N/distance-measurement-with-an-ultrasonic-sensor-hy-srf05-64554e
Or Y401
https://create.arduino.cc/projecthub/silicon-ripley-10/distance-measurement-using-ultrasonic-sensor-and-arduino-9bacd4?ref=similar&ref_id=47651&offset=0
obstacle
Y401, or
SRF05

## Slide 71: Test2.16_usound.ino
const unsigned int TRIG_PIN=13;
const unsigned int ECHO_PIN=12;
const unsigned int BAUD_RATE=9600;
void setup() {
pinMode(TRIG_PIN, OUTPUT);
pinMode(ECHO_PIN, INPUT);
Serial.begin(BAUD_RATE);
}
void loop() {
digitalWrite(TRIG_PIN, LOW);
delayMicroseconds(2);
digitalWrite(TRIG_PIN, HIGH);
delayMicroseconds(10);
digitalWrite(TRIG_PIN, LOW);
const unsigned long duration= pulseIn(ECHO_PIN, HIGH);
int distance= duration/29/2;
if(duration==0){
Serial.println("Warning: no pulse from sensor");
}
else{ Serial.print("distance to nearest object:");
Serial.println(distance);
Serial.println(" cm");
} delay(100);
}

## Slide 72: Test2.17a IMU GY-801 IMU BMP180 ADXL345 HMC5883L L3G4200D 9-Axis Module test17_gy80_IMU.ino
10-DOF Degree of Freedom , IMU (Inertial measurement unit) sensor
Nine-Axis Module (three-axis gyroscope + triaxial accelerometer + 3-axis magnetic field + pressure)
https://www.newegg.com/Product/Product.aspx?Item=2S7-00VK-00F30
Use AHRS_9DOF_display3_115200.pde to display 3D
Download testing code from
IMU_GY80_nano_ok2.zip
http://www.cse.cuhk.edu.hk/~khwong/www2/stem/IMU_GY80_nano_ok2.zip
SDA, SCL,GND, 3.3 VCC
4 5 GND Vcc
Arduino UNO
3D display on windows
Video demo
https://www.youtube.com/watch?v=XsF8foTqMaM

## Slide 73: Test2.17b Plotting Accelerometer reading of Y-axis
http://www.cse.cuhk.edu.hk/~khwong/www2/stem/AHRS_9DOF_test_ok1_accel_200824.zip
SDA, SCL,GND, 3.3 VCC
(N.C.)
4 5 GND Vcc
Arduino UNO
Y-axis

## Slide 74: Test2.18 OLED (SSD 1306, GME12864-13 model) display panel 0.96” 128x32 2-color
https://randomnerdtutorials.com/guide-for-oled-display-with-arduino/
Demo video https://www.youtube.com/watch?v=p5BoVGKdbW8
Update Arduino to 1.8.10 at least
In Arduino(IDE) Sketch/include libraries/manage libraries/”type “1306
Install Adafruit SSD 1306 by Adafruit version 2.1
In File/examples/Adafruit ssd1306/ssd1306_128x32 i2c.ino
SDAA4
SCL(SCK)A5
VCC—5V
GND0v
SCL(SCK)
SDA
GND
VCC
A4
A5

## Slide 75: Test2.19 Large LCD 12864 SPI (thru ST7920) size 73mm x 39mm //12864_spi_grahicstest_1a.ino https://github.com/olikraus/U8glib_Arduino //12864_spi_grahicstest_1a.ino
//12864_spi_grahicstest_1a.ino
/*https://github.com/olikraus/U8glib_Arduino
GraphicsTest.pde
>>> Before compiling: Please remove comment from the constructor of the
>>> connected graphics display (see below).
Universal 8bit Graphics Library, https://github.com/olikraus/u8glib/
Copyright (c) 2012, olikraus@gmail.com
All rights reserved.
Redistribution and use in source and binary forms, with or without modification,
are permitted provided that the following conditions are met:
* Redistributions of source code must retain the above copyright notice, this list
of conditions and the following disclaimer.
* Redistributions in binary form must reproduce the above copyright notice, this
list of conditions and the following disclaimer in the documentation and/or other
materials provided with the distribution.
THIS SOFTWARE IS PROVIDED BY THE COPYRIGHT HOLDERS AND
CONTRIBUTORS "AS IS" AND ANY EXPRESS OR IMPLIED WARRANTIES,
INCLUDING, BUT NOT LIMITED TO, THE IMPLIED WARRANTIES OF
MERCHANTABILITY AND FITNESS FOR A PARTICULAR PURPOSE ARE
DISCLAIMED. IN NO EVENT SHALL THE COPYRIGHT HOLDER OR
CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, INCIDENTAL,
SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES (INCLUDING, BUT
NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE GOODS OR SERVICES;
LOSS OF USE, DATA, OR PROFITS; OR BUSINESS INTERRUPTION) HOWEVER
CAUSED AND ON ANY THEORY OF LIABILITY, WHETHER IN CONTRACT,
STRICT LIABILITY, OR TORT (INCLUDING NEGLIGENCE OR OTHERWISE)
ARISING IN ANY WAY OUT OF THE USE OF THIS SOFTWARE, EVEN IF
ADVISED OF THE POSSIBILITY OF SUCH DAMAGE.
*/
#include "U8glib.h"
// setup u8g object, please remove comment from one of the following constructor calls
)_
U8GLIB_ST7920_128X64_4X u8g(13,11,10); // SPI Com: U8GLIB_ST7920_128X64_4X u8g(pin_E, pin_R/W, pin_/RS );//can chnage to another pin assignment scheme
//MODULE..........................Uang
//K (backlight cathode).........GND
//A (backlight anode)..........+5V
//PSD (SPI Mode).................GND or NC
//E (SCK)..........................D13
//R/W (MOSI)....................D11
//RS (CS)..........................D10*
//VDD.............................+5V
//VSS..............................GND
void u8g_prepare(void) {
u8g.setFont(u8g_font_6x10);
u8g.setFontRefHeightExtendedText();
u8g.setDefaultForegroundColor();
u8g.setFontPosTop();
}
void u8g_box_frame(uint8_t a) {
u8g.drawStr( 0, 0, "drawBox");
u8g.drawBox(5,10,20,10);
u8g.drawBox(10+a,15,30,7);
u8g.drawStr( 0, 30, "drawFrame");
u8g.drawFrame(5,10+30,20,10);
u8g.drawFrame(10+a,15+30,30,7);
}
void u8g_disc_circle(uint8_t a) {
u8g.drawStr( 0, 0, "drawDisc");
u8g.drawDisc(10,18,9);
u8g.drawDisc(24+a,16,7);
u8g.drawStr( 0, 30, "drawCircle");
u8g.drawCircle(10,18+30,9);
u8g.drawCircle(24+a,16+30,7);
}
void u8g_r_frame(uint8_t a) {
u8g.drawStr( 0, 0, "drawRFrame/Box");
u8g.drawRFrame(5, 10,40,30, a+1);
u8g.drawRBox(50, 10,25,40, a+1);
}
void u8g_string(uint8_t a) {
u8g.drawStr(30+a,31, " 0");
u8g.drawStr90(30,31+a, " 90");
u8g.drawStr180(30-a,31, " 180");
u8g.drawStr270(30,31-a, " 270");
}
void u8g_line(uint8_t a) {
u8g.drawStr( 0, 0, "drawLine");
u8g.drawLine(7+a, 10, 40, 55);
u8g.drawLine(7+a*2, 10, 60, 55);
u8g.drawLine(7+a*3, 10, 80, 55);
u8g.drawLine(7+a*4, 10, 100, 55);
}
void u8g_triangle(uint8_t a) {
uint16_t offset = a;
u8g.drawStr( 0, 0, "drawTriangle");
u8g.drawTriangle(14,7, 45,30, 10,40);
u8g.drawTriangle(14+offset,7-offset, 45+offset,30-offset, 57+offset,10-offset);
u8g.drawTriangle(57+offset*2,10, 45+offset*2,30, 86+offset*2,53);
u8g.drawTriangle(10+offset,40+offset, 45+offset,30+offset, 86+offset,53+offset);
}
void u8g_ascii_1() {
char s[2] = " ";
uint8_t x, y;
u8g.drawStr( 0, 0, "ASCII page 1");
for( y = 0; y < 6; y++ ) {
for( x = 0; x < 16; x++ ) {
s[0] = y*16 + x + 32;
u8g.drawStr(x*7, y*10+10, s);
}
}
}
void u8g_ascii_2() {
char s[2] = " ";
uint8_t x, y;
u8g.drawStr( 0, 0, "ASCII page 2");
for( y = 0; y < 6; y++ ) {
for( x = 0; x < 16; x++ ) {
s[0] = y*16 + x + 160;
u8g.drawStr(x*7, y*10+10, s);
}
}
}
void u8g_extra_page(uint8_t a)
{
if ( u8g.getMode() == U8G_MODE_HICOLOR || u8g.getMode() == U8G_MODE_R3G3B2) {
/* draw background (area is 128x128) */
u8g_uint_t r, g, b;
b = a << 5;
for( g = 0; g < 64; g++ )
{
for( r = 0; r < 64; r++ )
{
u8g.setRGB(r<<2, g<<2, b );
u8g.drawPixel(g, r);
}
}
u8g.setRGB(255,255,255);
u8g.drawStr( 66, 0, "Color Page");
}
else if ( u8g.getMode() == U8G_MODE_GRAY2BIT )
{
u8g.drawStr( 66, 0, "Gray Level");
u8g.setColorIndex(1);
u8g.drawBox(0, 4, 64, 32);
u8g.drawBox(70, 20, 4, 12);
u8g.setColorIndex(2);
u8g.drawBox(0+1*a, 4+1*a, 64-2*a, 32-2*a);
u8g.drawBox(74, 20, 4, 12);
u8g.setColorIndex(3);
u8g.drawBox(0+2*a, 4+2*a, 64-4*a, 32-4*a);
u8g.drawBox(78, 20, 4, 12);
}
else
{
u8g.drawStr( 0, 12, "setScale2x2");
u8g.setScale2x2();
u8g.drawStr( 0, 6+a, "setScale2x2");
u8g.undoScale();
}
}
uint8_t draw_state = 0;
void draw(void) {
u8g_prepare();
switch(draw_state >> 3) {
case 0: u8g_box_frame(draw_state&7); break;
case 1: u8g_disc_circle(draw_state&7); break;
case 2: u8g_r_frame(draw_state&7); break;
case 3: u8g_string(draw_state&7); break;
case 4: u8g_line(draw_state&7); break;
case 5: u8g_triangle(draw_state&7); break;
case 6: u8g_ascii_1(); break;
case 7: u8g_ascii_2(); break;
case 8: u8g_extra_page(draw_state&7); break;
}
}
void setup(void) {
// flip screen, if required
//u8g.setRot180();
#if defined(ARDUINO)
pinMode(13, OUTPUT);
digitalWrite(13, HIGH);
#endif
}
void loop(void) {
// picture loop
u8g.firstPage();
do {
draw();
} while( u8g.nextPage() );
// increase the state
draw_state++;
if ( draw_state >= 9*8 )
draw_state = 0;
// rebuild the picture after some delay
//delay(150);
}
U8GLIB_ST7920_128X64_4X u8g(13,11,10);
// SPI Com:
//U8GLIB_ST7920_128X64_4X u8g(E, R/W, /RS );
//can change to another pin assignment scheme
//MODULE..........................Uang
//K (backlight cathode).........GND
//A (backlight anode)..........+5V
//PSD (SPI Mode).................GND or NC
//E (SCK)..........................D13
//R/W (MOSI)....................D11
//RS (CS)..........................D10*
//VDD.............................+5V
//VSS..............................GND

## Slide 76: Test2.19a: keypad circuit 3x4 https://www.ardumotive.com/how-to-use-a-keypad-en.html

## Slide 77: Test2.19a: keypad code
//https://playground.arduino.cc/Main/KeypadTutorial/
#include <Keypad.h> //keypad by mark standley
const byte ROWS = 4; // Four rows
const byte COLS = 3; // Three columns
// Define the Keymap
char keys[ROWS][COLS] = {
{'1','2','3'},
{'4','5','6'},
{'7','8','9'},
{'#','0','*'}
};
// Connect keypad ROW0, ROW1, ROW2 and ROW3 to these Arduino pins.
//byte rowPins[ROWS] = { 9, 8, 7, 6 };
byte rowPins[ROWS] = { 5,4,3,2 };
// Connect keypad COL0, COL1 and COL2 to these Arduino pins.
//byte colPins[COLS] = { 12, 11, 10 };
byte colPins[COLS] = { 8,7,6};
// Create the Keypad
Keypad kpd = Keypad( makeKeymap(keys), rowPins, colPins, ROWS, COLS );
#define ledpin 13
void setup()
{ pinMode(ledpin,OUTPUT);
digitalWrite(ledpin, HIGH);
Serial.begin(9600);
}
void loop()
{ char key = kpd.getKey();
if(key) // Check for a valid key.
{
switch (key)
{
case '*':
digitalWrite(ledpin, LOW);
break;
case '#':
digitalWrite(ledpin, HIGH);
break;
default:
Serial.println(key);
}
}
}

## Slide 78: Test2.19.b keypad circuit 4x4
//ref: https://lastminuteengineers.com/arduino-keypad-tutorial/
#include <Keypad.h>
const byte ROWS = 4; //four rows
const byte COLS = 4; //four columns
char keys[ROWS][COLS] = {
{'1','2','3','A'},
{'4','5','6','B'},
{'7','8','9','C'},
{'*','0','#','D'}
};
/* 4x4 matrix keypad
{'s1','s2','s3','s4'},
{'s5','s6','s7','s8'},
{'s9','s10','s11','s12'},
{'s13','s14','s15','s16'}
*/
byte rowPins[ROWS] = {9, 8, 7, 6}; //connect to the row pinouts of the keypad
// arduino pin{9, 8, 7, 6}= {R1,R2,R3,R4} resp.
byte colPins[COLS] = {5, 4, 3, 2}; //connect to the column pinouts of the keypad
//arduino{5,4,3,2}={c1,c2,c3,c4} resp.
//Create an object of keypad
Keypad keypad = Keypad( makeKeymap(keys), rowPins, colPins, ROWS, COLS );
void setup(){
Serial.begin(9600);
}
void loop(){
char key = keypad.getKey();// Read the key
// Print if key pressed
if (key){
Serial.print("Key Pressed : ");
Serial.println(key);
}
}
Arduino-> keypad
p2->C4
P3->C3
P4->C2
P5->C1
P9->R1
P8->R2
P7->R3
P6->R4
// Arduino pin{9, 8, 7, 6}= {R1,R2,R3,R4} resp.
/ /Arduino pin{5, 4, 3, 2}= {c1,c2,c3,c4} resp.
4x4 key arrangement
{'s1','s2','s3','s4'},
{'s5','s6','s7','s8'},
{'s9','s10','s11','s12'},
{'s13','s14','s15','s16'}
Pin9—>pin2
0f Arduino
OR

## Slide 79: Test2.19c TV-box controller
//<script src="https://gist.github.com/francis2110/f04237b04c94218028e3.js"></script>
//https://gist.github.com/francis2110/f04237b04c94218028e3
//application for send infrared codes to LG tv with arduino
//irEmitterApp
#include <IRremote.h>
IRsend irsend;
//tv super box, NEC: FB0058A7 (32 bits)
#define UP 0xFB0058A7
#define LEFT 0xFB00E21D
#define RIGHT 0xFB00E01F
#define DOWN 0xFB0012ED
#define OK 0xFB00609F
#define POWER 0xFB0038C7
#define TV_VOD 0xFB0020DF
#define HOME 0xFB0050AF
#define RET 0xFB00926D
#define INFO_ 0xFB0018E7
#define PLAY 0xFB00807F
#define STOP 0xFB00FA05
#define REW 0xFB009867
#define FFW 0xFB001AE5
#define SILENT 0xFB003AC5
#define BACK_SPACE 0xFB0008F7
#define KEY0 0xFB0030CF
#define KEY1 0xFB002AD5
#define KEY2 0xFB006897
#define KEY3 0xFB00A857
#define KEY4 0xFB000AF5
#define KEY5 0xFB0048B7
#define KEY6 0xFB008877
#define KEY7 0xFB0032CD
#define KEY8 0xFB00708F
#define KEY9 0xFB00B04F
static int cero = 0;
long unsigned int irCode;
int cmdReceived;
//////////////for keypad /////////////////////////////
#include <Keypad.h> //keypad by mark standley
const byte ROWS = 4; // Four rows
const byte COLS = 3; // Three columns
// Define the Keymap
char keys[ROWS][COLS] = {
{'1', '2', '3'},
{'4', '5', '6'},
{'7', '8', '9'},
{'*', '0', '#'}
};
// Connect keypad ROW0, ROW1, ROW2 and ROW3 to these Arduino pins.
byte rowPins[ROWS] = { 9, 8, 7, 6 };
//byte rowPins[ROWS] = { 5, 4, 3, 2 };
// Connect keypad COL0, COL1 and COL2 to these Arduino pins.
byte colPins[COLS] = { 12, 11, 10 };
//byte colPins[COLS] = { 8, 7, 6};
// Create the Keypad
Keypad kpd = Keypad( makeKeymap(keys), rowPins, colPins, ROWS, COLS );
#define ledpin 13
void setup()
{ pinMode(ledpin, OUTPUT);
digitalWrite(ledpin, HIGH);
Serial.begin(9600);
}
/////////////////////////////////////////////
void send_IR_code(long unsigned int irCode_to_sent)
{
Serial.println(irCode_to_sent, HEX);
Serial.println("--------------");
delay(40);
irsend.sendNEC(irCode_to_sent, 32);
delay(40);
}
//
//void loop_IR_if_use_comm() {
// if (Serial.available() > 0 ) {
// cmdReceived = Serial.read();
// switch (cmdReceived ) {
// case 'a':
// irCode = UP;
// send_IR_code( irCode);
// break;
// case 'b':
// irCode = DOWN;
// send_IR_code( irCode);
// break;
// case 'o':
// irCode = OK;
// send_IR_code( irCode);
// break;
// }
// }
//}
void loop()
{ char key = kpd.getKey();
if (key) // Check for a valid key.
{
switch (key)
{
case '1':
irCode = LEFT; send_IR_code(irCode);
break;
case '2':
irCode = UP; send_IR_code( irCode);
break;
case '3':
irCode = RIGHT; send_IR_code(irCode);
break;
case '4':
irCode = HOME; send_IR_code(irCode);
break;
case '5':
irCode = DOWN; send_IR_code(irCode);
break;
case '6':
irCode = OK; send_IR_code(irCode);
break;
case '7':
irCode = PLAY; send_IR_code(irCode);
break;
case '8':
irCode = RET; send_IR_code(irCode);
break;
case '9':
irCode = INFO_; send_IR_code(irCode);
break;
case '*':
irCode = STOP; send_IR_code(irCode);
break;
case '0':
irCode = REW; send_IR_code(irCode);
break;
case '#':
irCode = FFW; send_IR_code(irCode);
break;
default:
Serial.println(key);
}
}
}
12,11,10,9,8,7,6
100
Ohms
GND
IR Emitter
R3,r2,R1,R0,C2,C1,C0
1=LEFT(<) | 2=UP (^) | 3=RIGHT(>)
4=HOME | 5=DOWN (V) | 6=OK
7=PLAY | 8=RET(return) | 9=INFO(rmation)
*=STROP | 0=REW(backward) | #>>FFW(forward)
Pin3
Arduino

## Slide 80: Test 19d: combine IR receiver, keypad for TV box control
/* from: https://github.com/z3t0/Arduino-IRremote * IRremote: IRrecvDemo - demonstrates receiving IR codes with IRrecv
An IR detector/demodulator must be connected to the input RECV_PIN.
Version 0.1 July, 2009
Copyright 2009 Ken Shirriff
http://arcfn.com
*/
//////////////for keypad /////////////////////////////
//<script src="https://gist.github.com/francis2110/f04237b04c94218028e3.js"></script>
//https://gist.github.com/francis2110/f04237b04c94218028e3
//application for send infrared codes to LG tv with arduino
//irEmitterApp
#include <IRremote.h>
IRsend irsend;
//tv super box, NEC: FB0058A7 (32 bits)
#define UP 0xFB0058A7
#define LEFT 0xFB00E21D
#define RIGHT 0xFB00E01F
#define DOWN 0xFB0012ED
#define OK 0xFB00609F
#define POWER 0xFB0038C7
#define TV_VOD 0xFB0020DF
#define HOME 0xFB0050AF
#define RET 0xFB00926D
#define INFO_ 0xFB0018E7
#define PLAY 0xFB00807F
#define STOP 0xFB00FA05
#define REW 0xFB009867
#define FFW 0xFB001AE5
#define SILENT 0xFB003AC5
#define BACK_SPACE 0xFB0008F7
#define KEY0 0xFB0030CF
#define KEY1 0xFB002AD5
#define KEY2 0xFB006897
#define KEY3 0xFB00A857
#define KEY4 0xFB000AF5
#define KEY5 0xFB0048B7
#define KEY6 0xFB008877
#define KEY7 0xFB0032CD
#define KEY8 0xFB00708F
#define KEY9 0xFB00B04F
static int cero = 0;
long unsigned int irCode;
int cmdReceived;
//////////////for keypad /////////////////////////////
#include <Keypad.h> //keypad by mark standley
const byte ROWS = 4; // Four rows
const byte COLS = 3; // Three columns
// Define the Keymap
char keys[ROWS][COLS] = {
{'1', '2', '3'},
{'4', '5', '6'},
{'7', '8', '9'},
{'*', '0', '#'}
};
// Connect keypad ROW0, ROW1, ROW2 and ROW3 to these Arduino pins.
byte rowPins[ROWS] = { 9, 8, 7, 6 };
//byte rowPins[ROWS] = { 5, 4, 3, 2 };
// Connect keypad COL0, COL1 and COL2 to these Arduino pins.
byte colPins[COLS] = { 12, 11, 10 };
//byte colPins[COLS] = { 8, 7, 6};
// Create the Keypad
Keypad kpd = Keypad( makeKeymap(keys), rowPins, colPins, ROWS, COLS );
#define ledpin 13
////////////////////////////////////////////////////////////////
// IR control rely, use 1 reciver to recive IR and send to another IR remote controller, 2020 April 23
//include <IRremote.h>
//IRsend irsend;
/// the black remote controls: 17 kets
#define B_01 0xFFA25D
#define B_02 0xFF629D
#define B_03 0xFFE21D
#define B_04 0xFF22DD
#define B_05 0xFF02FD
#define B_06 0xFFC23D
#define B_07 0xFFE01F
#define B_08 0xFFA857
#define B_09 0xFF906F
#define B_00 0xFF9867
#define B_STAR 0xFF6897
#define B_HASH 0xFFB04F
#define B_LEFT 0xFF10EF
#define B_RIGHT 0xFF5AA5
#define B_UP 0xFF18E7
#define B_DOWN 0xFF4AB5
#define B_OK 0xFF38C7
//My_TV_Super= MTS, NEC:
#define MTS_UP 0xFB0058A7
#define MTS_LEFT 0xFB00E21D
#define MTS_RIGHT 0xFB00E01F
#define MTS_DOWN 0xFB0012ED
#define MTS_OK 0xFB00609F
#define MTS_POWER 0xFB0038C7
#define MTS_MTS_VOD 0xFB0020DF
#define MTS_HOME 0xFB0050AF
#define MTS_RETURN 0xFB00926D
#define MTS_INFO 0xFB0018E7
#define MTS_PLAY 0xFB00807F
#define MTS_STOP 0xFB00FA05
#define MTS_REW 0xFB009867
#define MTS_FFW 0xFB001AE5
#define MTS_SILENT 0xFB003AC5
#define MTS_BACKSPACE 0xFB0008F7
#define MTS_KEY0 0xFB0030CF
#define MTS_KEY1 0xFB002AD5
#define MTS_KEY2 0xFB006897
#define MTS_KEY3 0xFB00A857
#define MTS_KEY4 0xFB000AF5
#define MTS_KEY5 0xFB0048B7
#define MTS_KEY6 0xFB008877
#define MTS_KEY7 0xFB0032CD
#define MTS_KEY8 0xFB00708F
#define MTS_KEY9 0xFB00B04F
#define SIGNAL_DELAY1 150 // at least 120
#define SIGNAL_DELAY2 0 // at least 0
#define REC_DELAY 10 // typical 250 , 10-100 is ok for slow key-press action
/////////////////////////////////////////////////
int RECV_PIN = 5 ; //11;
//int RELAY_PIN = 4;
IRrecv irrecv(RECV_PIN);
//long unsigned int irCode;
decode_results results;
// Dumps out the decode_results structure.
// Call this after IRrecv::decode()
// void * to work around compiler issue
//void dump(void *v) {
// decode_results *results = (decode_results *)
//////////////////////////////////////////////////////////////
void send_code_to_TV( long unsigned int irCode_recieved)
{
switch (irCode_recieved) {
case B_UP:
irCode = MTS_UP; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_DOWN:
irCode = MTS_DOWN; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_OK:
irCode = MTS_OK; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_LEFT:
irCode = MTS_LEFT; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_RIGHT:
irCode = MTS_RIGHT; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_STAR:
irCode = MTS_HOME; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_00:
irCode = MTS_RETURN; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_HASH:
irCode = MTS_INFO; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_01:
irCode = MTS_PLAY; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_02:
irCode = MTS_REW; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_03:
irCode = MTS_FFW; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_04:
irCode = MTS_STOP; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_07:
irCode = MTS_SILENT; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
case B_09:
irCode = MTS_BACKSPACE; Serial.println(irCode, HEX); send_IR_code( irCode);
break;
}
}
//////////////////////////////////////////////////
void dump(decode_results *results) {
int count = results->rawlen;
if (results->decode_type == UNKNOWN) {
Serial.println("Could not decode message");
}
else {
if (results->decode_type == NEC) {
Serial.print("Decoded NEC: ");
}
else if (results->decode_type == SONY) {
Serial.print("Decoded SONY: ");
}
else if (results->decode_type == RC5) {
Serial.print("Decoded RC5: ");
}
else if (results->decode_type == RC6) {
Serial.print("Decoded RC6: ");
}
Serial.print(results->value, HEX);
send_code_to_TV(results->value); /////////////////////////////////
Serial.print(" (");
Serial.print(results->bits, DEC);
Serial.println(" bits)");
}
Serial.print("Raw (");
Serial.print(count, DEC);
Serial.print("): ");
for (int i = 0; i < count; i++) {
if ((i % 2) == 1) {
Serial.print(results->rawbuf[i]*USECPERTICK, DEC);
}
else {
Serial.print(-(int)results->rawbuf[i]*USECPERTICK, DEC);
}
Serial.print(" ");
}
Serial.println("");
}
//////////////////////////////////////////////////////////////
void send_IR_code(long unsigned int irCode_to_sent)
{
Serial.println(irCode_to_sent, HEX);
Serial.println("--------------");
delay(SIGNAL_DELAY1);
irsend.sendNEC(irCode_to_sent, 32);
delay(SIGNAL_DELAY2);
irrecv.enableIRIn(); //fix rec freeze after sent, see https://forum.arduino.cc/index.php?topic=192472.0
}
/////////////////////////////////////////////////////
void setup()
{ //pinMode(RELAY_PIN, OUTPUT);
pinMode(13, OUTPUT);
Serial.begin(9600);
irrecv.enableIRIn(); // Start the receiver
}
int on = 0;
unsigned long last = millis();
/////////////////////////////////////////////////////
void loop() {
////////////// check IR-code recived from IR-controller //////////
if (irrecv.decode(&results)) {
// If it's been at least 1/4 second since the last
// IR received, toggle the relay
if (millis() - last > REC_DELAY) {
on = !on;
// digitalWrite(RELAY_PIN, on ? HIGH : LOW);
digitalWrite(13, on ? HIGH : LOW);
dump(&results); // this is to send the recived code to the TV
}
last = millis();
irrecv.resume(); // Receive the next value
}
/////////// check 3x4 or 4x4 keypad ///////////////////////////
check_keypad_send_IR_code();
}
/////////////////////////////////////////////////////////////////
void check_keypad_send_IR_code()
{ char key = kpd.getKey();
if (key) // Check for a valid key.
{
switch (key)
{
case '1':
irCode = LEFT; send_IR_code(irCode);
break;
case '2':
irCode = UP; send_IR_code( irCode);
break;
case '3':
irCode = RIGHT; send_IR_code(irCode);
break;
case '4':
irCode = HOME; send_IR_code(irCode);
break;
case '5':
irCode = DOWN; send_IR_code(irCode);
break;
case '6':
irCode = OK; send_IR_code(irCode);
break;
case '7':
irCode = PLAY; send_IR_code(irCode);
break;
case '8':
irCode = RET; send_IR_code(irCode);
break;
case '9':
irCode = INFO_; send_IR_code(irCode);
break;
case '*':
irCode = STOP; send_IR_code(irCode);
break;
case '0':
irCode = REW; send_IR_code(irCode);
break;
case '#':
irCode = FFW; send_IR_code(irCode);
break;
default:
Serial.println(key);
}
}
}
Stem2: Arduino experiments v0.d.1
80
Remote controller
IR receiver (pin11)
IR emitter(pin3)
Reason to make it: use any controller to control any devices.
50 Ohms
Out GND 5V
or
IR receiver module
KY-022
Out Vcc, GND

## Slide 81: MTV (My TV super) control rc_mtv1a.ino (2020.7.15 )
/* rc_mtv1a.ino 2020.7.15 from: https://github.com/z3t0/Arduino-IRremote * IRremote: IRrecvDemo - demonstrates receiving IR codes with IRrecv
An IR detector/demodulator must be connected to the input RECV_PIN.
Version 0.1 July, 2009
Copyright 2009 Ken Shirriff
http://arcfn.com
*/
//////////////for keypad /////////////////////////////
//<script src="https://gist.github.com/francis2110/f04237b04c94218028e3.js"></script>
//https://gist.github.com/francis2110/f04237b04c94218028e3
//application for send infrared codes to LG tv with arduino
//irEmitterApp
#include <IRremote.h>
IRsend irsend;
static int cero = 0;
long unsigned int irCode;
int cmdReceived;
///////////////////////////////////////////////////////
// DEFINE table1 LGTV
#define LGTV_SOURCE 0x20DFD02F
#define LGTV_SUBTITLE 0x20DF9C63 //20DF9C63
#define LGTV_POWER 0x20DF10EF //on/off
#define LGTV_AV_TV 0x20DFF00F
#define LGTV_NICAM_I_II 0x20DF50AF
#define LGTV_SLEEP 0x20DF708F
#define LGTV_1 0x20DF8877
#define LGTV_2 0x20DF48B7
#define LGTV_3 0x20DFC837
#define LGTV_4 0x20DF28D7
#define LGTV_5 0x20DFA857
#define LGTV_6 0x20DF6897
#define LGTV_7 0x20DFE817
#define LGTV_8 0x20DF18E7
#define LGTV_9 0x20DF9867
#define LGTV_0 0x20DF08F7
#define LGTV_ARROW_UP 0x20DF02FD
#define LGTV_ARROW_DOWN 0x20DF827D
#define LGTV_ARROW_LEFT 0x20DFE01F
#define LGTV_ARROW_RIGHT 0x20DF609F
#define LGTV_OK 0x20DF22DD
#define LGTV_VOL_UP 0x20DF40BF
#define LGTV_VOL_DOWN 0x20DFC03F
#define LGTV_CHAN_UP 0x20DF00FF
#define LGTV_CHAN_DOWN 0x20DF807F
#define LGTV_RED 0x20DF4EB1
#define LGTV_GREEN 0x20DF8E71
#define LGTV_YELLOW 0x20DFC639
#define LGTV_BLUE 0x20DF8679
#define LGTV_REWIND 0x20DFF10E
#define LGTV_PLAY 0x20DF0DF2
#define LGTV_PAUSE 0x20DF5DA2
#define LGTV_FAST_FORWARD 0x20DF718E
#define LGTV_HOME 0x20DF3EC1
#define LGTV_NETFLIX 0x20DF6A95
#define LGTV_MENU 0x20DFC23D
#define LGTV_RETURN 0x20DF14EB
#define LGTV_TOOLS 0x20DFA25D
#define LGTV_EXIT 0x20DFDA25
#define LGTV_GUIDE 0x20DFD52A
#define LGTV_Q_VIEW 0x20DF55AA
///////////// for Black, 17-keys-keypad
//#define B17_01 0xFFA25D
///////////////////////////////////////////////////////
// DEFINE table2 : 17 keys black remote controls:
#define B17_01 0xFFA25D
#define B17_02 0xFF629D
#define B17_03 0xFFE21D
#define B17_04 0xFF22DD
#define B17_05 0xFF02FD
#define B17_06 0xFFC23D
#define B17_07 0xFFE01F
#define B17_08 0xFFA857
#define B17_09 0xFF906F
#define B17_00 0xFF9867
#define B17_STAR 0xFF6897
#define B17_HASH 0xFFB04F
#define B17_LEFT 0xFF10EF
#define B17_RIGHT 0xFF5AA5
#define B17_UP 0xFF18E7
#define B17_DOWN 0xFF4AB5
#define B17_OK 0xFF38C7
///////////////////////////////////////////////////////
//My_TV_Super= MTS, NEC:
#define MTS_UP 0xFB0058A7
#define MTS_LEFT 0xFB00E21D
#define MTS_RIGHT 0xFB00E01F
#define MTS_DOWN 0xFB0012ED
#define MTS_OK 0xFB00609F
#define MTS_POWER 0xFB0038C7
#define MTS_MTS_VOD 0xFB0020DF
#define MTS_HOME 0xFB0050AF
#define MTS_RETURN 0xFB00926D
#define MTS_INFO 0xFB0018E7
#define MTS_RED 0xFB00807F //MTS_PLAY
#define MTS_GREEN 0xFB00FA05 //MTS_STOP
#define MTS_YELLOW 0xFB009867 //MTS_REW
#define MTS_BLUE 0xFB001AE5 //MTS_FFW
#define MTS_SILENT 0xFB003AC5
#define MTS_BACKSPACE 0xFB0008F7
#define MTS_KEY0 0xFB0030CF
#define MTS_KEY1 0xFB002AD5
#define MTS_KEY2 0xFB006897
#define MTS_KEY3 0xFB00A857
#define MTS_KEY4 0xFB000AF5
#define MTS_KEY5 0xFB0048B7
#define MTS_KEY6 0xFB008877
#define MTS_KEY7 0xFB0032CD
#define MTS_KEY8 0xFB00708F
#define MTS_KEY9 0xFB00B04F
#define SIGNAL_DELAY1 150 // at least 120
#define SIGNAL_DELAY2 0 // at least 0
#define REC_DELAY 10 // typical 250 , 10-100 is ok for slow key-press action
//////////////for keypad /////////////////////////////
#include <Keypad.h> //keypad by mark standley
const byte ROWS = 4; // 4 rows
const byte COLS = 4; // 4 columns
// Define the Keymap for keys_hard
char keys_hard[ROWS][COLS] = {
{'0', '1', '2', '3'},
{'4', '5', '6', '7'},
{'8', '9', 'A', 'B'},
{'C', 'D', 'E', 'F'}
};
// Define the Keymap for soft_keys
char keys[ROWS][COLS] = {
{'1', '2', '3', 'A'},
{'4', '5', '6', 'B'},
{'7', '8', '9', 'C'},
{'*', '0', '#', 'D'}
};
byte rowPins[ROWS] = {9, 8, 7, 6}; //connect to the row pinouts of the keypad
// arduino pin{9, 8, 7, 6}= {R1,R2,R3,R4} resp.
byte colPins[COLS] = {5, 4, 10, 2}; //connect to the column pinouts of the keypad
//arduino{5,4,3,2}={c1,c2,c3,c4} resp.
// Create the Keypad
Keypad kpd = Keypad( makeKeymap(keys), rowPins, colPins, ROWS, COLS );
////////////////////////////////////////////////////////////////
// IR control rely, use 1 reciver to recive IR and send to another IR remote controller, 2020 April 23
//include <IRremote.h>
//IRsend irsend;
/////////////////////////////////////////////////
// by default IR transmitter pin is 3, you cannot change it, no need to declare here
int analog_switch_input_pin = A1;
//int RELAY_PIN = 4; //not used in this project
int RECV_PIN = 11;
#define ledpin 13
IRrecv irrecv(RECV_PIN);
//long unsigned int irCode;
decode_results results;
// Dumps out the decode_results structure.
// Call this after IRrecv::decode()
// void * to work around compiler issue
//void dump(void *v) {
// decode_results *results = (decode_results *)
////////////////////////
void send_IR_code(long unsigned int irCode_to_sent)
{
Serial.println(irCode_to_sent, HEX);
Serial.println("--------------");
// delay(SIGNAL_DELAY1);
irsend.sendNEC(irCode_to_sent, 32);
// delay(SIGNAL_DELAY2);
irrecv.enableIRIn(); //fix rec freeze after sent, see https://forum.arduino.cc/index.php?topic=192472.0
}
/////////////////////////////////////////////////////
void setup()
{ //pinMode(RELAY_PIN, OUTPUT);
pinMode(13, OUTPUT);
Serial.begin(9600);
irrecv.enableIRIn(); // Start the receiver
}
int on = 0;
unsigned long last = millis();
/////////////////////////////////////////////////////
void loop() {
////////////// check IR-code recived from IR-controller //////////
if (irrecv.decode(&results)) {
// If it's been at least 1/4 second since the last
// IR received, toggle the relay
if (millis() - last > REC_DELAY) {
on = !on;
// digitalWrite(RELAY_PIN, on ? HIGH : LOW);
digitalWrite(13, on ? HIGH : LOW);
dump(&results); // this is to received IR code recived and sedn to Seiral.println
}
last = millis();
irrecv.resume(); // Receive the next value
}
check_keypad_send_IR_code_MTV();
}
///////////// send recived IR code to Seiral.println//////
void dump(decode_results *results) {
int count = results->rawlen;
if (results->decode_type == UNKNOWN) {
Serial.println("Could not decode message");
}
else {
if (results->decode_type == NEC) {
Serial.print("Decoded NEC: ");
}
else if (results->decode_type == SONY) {
Serial.print("Decoded SONY: ");
}
else if (results->decode_type == RC5) {
Serial.print("Decoded RC5: ");
}
else if (results->decode_type == RC6) {
Serial.print("Decoded RC6: ");
}
Serial.print(results->value, HEX);
//send_code_to_TV(results->value); //not used here//////////
Serial.print(" (");
Serial.print(results->bits, DEC);
Serial.println(" bits)");
}
Serial.print("Raw (");
Serial.print(count, DEC);
Serial.print("): ");
for (int i = 0; i < count; i++) {
if ((i % 2) == 1) {
Serial.print(results->rawbuf[i]*USECPERTICK, DEC);
}
else {
Serial.print(-(int)results->rawbuf[i]*USECPERTICK, DEC);
}
Serial.print(" ");
}
Serial.println("");
}
/////////////////////////////////////////////////////////////////
void check_keypad_send_IR_code_MTV()
{ char key = kpd.getKey();
if (key) // Check for a valid key.
{
switch (key)
{
case '1':
Serial.println("MTV 1");
irCode = MTS_POWER; send_IR_code( irCode);
break;
case '2':
Serial.println("MTV 2");
irCode = MTS_UP; send_IR_code( irCode);
break;
case '3':
Serial.println("MTV 3");
goto_BBC();
break;
case 'A':
Serial.println("LGTV A");
irCode = LGTV_VOL_UP; send_IR_code(irCode);
break;
case '4':
Serial.println("LGTV 4");
irCode = MTS_LEFT ; send_IR_code(irCode);
break;
case '5':
Serial.println("LGTV 5");
irCode = MTS_OK; send_IR_code(irCode);
break;
case '6':
Serial.println("LGTV 6");
irCode = MTS_RIGHT; send_IR_code(irCode);
break;
case 'B':
Serial.println("LGTV B");
irCode = LGTV_VOL_DOWN; send_IR_code(irCode);
break;
case '7':
Serial.println("LGTV 7");
irCode = MTS_HOME; send_IR_code( irCode);
break;
case '8':
Serial.println("LGTV 8");
irCode = MTS_DOWN; send_IR_code(irCode);
break;
case '9':
Serial.println("LGTV 9");
irCode = MTS_RETURN; send_IR_code(irCode);
break;
case 'C':
Serial.println("LGTV C");
irCode = MTS_INFO; send_IR_code(irCode);
break;
case '*':
Serial.println("LGTV *");
goto_CANTONESE();
break;
case '0':
Serial.println("MTV 0");
goto_MAIYAR();
break;
case '#':
Serial.println("LGTV #");
goto_NHK();
break;
case 'D':
Serial.println("LGTV D");
goto_FRANCE();
break;
default:
Serial.println(key);
}
}
}
//**************************************************
////////////////////////////////////////////////////////
void goto_BBC()
{
irCode = MTS_HOME; send_IR_code( irCode);
delay(5000);
for (int i = 1 ; i <= 3; i++)
{ irCode = MTS_RIGHT; send_IR_code( irCode);
delay(1000);
}
////////////
for (int i = 1 ; i <= 11; i++)
{ irCode = MTS_DOWN; send_IR_code( irCode);
delay(1000);
}
irCode = MTS_OK; send_IR_code( irCode);
}
////////////////////////////////////////////////////////
void goto_CANTONESE()
{
irCode = MTS_HOME; send_IR_code( irCode);
delay(5000);
for (int i = 1 ; i <= 1; i++)
{ irCode = MTS_RIGHT; send_IR_code( irCode);
delay(1000);
}
////////////
for (int i = 1 ; i <= 5; i++)
{ irCode = MTS_DOWN; send_IR_code( irCode);
delay(1000);
}
irCode = MTS_OK; send_IR_code( irCode);
}
////////////////////////////////////////////////////////
void goto_MAIYAR()
{
irCode = MTS_HOME; send_IR_code( irCode);
delay(5000);
for (int i = 1 ; i <= 1; i++)
{ irCode = MTS_RIGHT; send_IR_code( irCode);
delay(1000);
}
////////////
for (int i = 1 ; i <= 6; i++)
{ irCode = MTS_DOWN; send_IR_code( irCode);
delay(1000);
}
irCode = MTS_OK; send_IR_code( irCode);
}
////////////////////////////////////////////////////////
void goto_NHK()
{
irCode = MTS_HOME; send_IR_code( irCode);
delay(5000);
for (int i = 1 ; i <= 3; i++)
{ irCode = MTS_RIGHT; send_IR_code( irCode);
delay(1000);
}
////////////
for (int i = 1 ; i <= 9; i++)
{ irCode = MTS_DOWN; send_IR_code( irCode);
delay(1000);
}
irCode = MTS_OK; send_IR_code( irCode);
}
////////////////////////////////////////////////////////
void goto_FRANCE()
{
irCode = MTS_HOME; send_IR_code( irCode);
delay(5000);
for (int i = 1 ; i <= 3; i++)
{ irCode = MTS_RIGHT; send_IR_code( irCode);
delay(1000);
}
////////////
for (int i = 1 ; i <= 7; i++)
{ irCode = MTS_DOWN; send_IR_code( irCode);
delay(1000);
}
irCode = MTS_OK; send_IR_code( irCode);
}
P9,8,7,6,5,4,10,2
Pin3330ohms--->|--GND
IR emitter
1 (MTS_Home) | 2 (MTS_UP) | 3 (goto_BBC) | A (LGTV_VOL_UP)
4 (MTS_LEFT) | 5 (MTS_OK) | 6 (MTS_RIGHT) | B (LGTV_VOL_DOWN)
7(MTS_HOME) | 8(MTS_DOWN) | 9(MTS_RETURN) | C (MTS_INFO)
* (goto_CANTONESE) | 0 (goto_MAIYAR) | # (goto_NHK) | D (goto_FRANCE)

## Slide 82: Test 2.20: sliding camera (To be done)
https://www.youtube.com/watch?v=Yy15lyZ27XQ

## Slide 83: Test 2.21 blue tooth connection tutorial (HC-05 Bluetooth ) http://www.electronica60norte.com/mwfls/pdf/newBluetooth.pdf
It can be used
  Controlling the Arduino using a smartphone or PC https://www.electronicwings.com/arduino/hc-05-bluetooth-module-interfacing-with-arduino-uno
  communication between two separate Arduino Boards https://howtomechatronics.com/tutorials/arduino/how-to-configure-pair-two-hc-05-bluetooth-module-master-slave-commands/
https://howtomechatronics.com/tutorials/arduino/arduino-and-hc-05-bluetooth-module-tutorial/

## Slide 84: Test 2.22 gimbal self stablishing platform
Will follow this project
https://howtomechatronics.com/projects/diy-arduino-gimbal-self-stabilizing-platform/

## Slide 85: Test2.23a FM radio using chips
http://www.theorycircuit.com/arduino-rda5807m-fm-receiver/
https://os.mbed.com/users/edodm85/notebook/radio-fm-tea5767/
RDA5807 vs TEA5767
As rda5807 compared to the TEA5767, it boasts advantages on the following factors:
  RDA5807 requires lesser external components for usage
  Additional embedded audio power amplifier that’s loadable with 32 Ohm speakers
  Bonus features such as the bass boosting function

## Slide 86: Test 2.23b FM radio with rda5807
http://www.theorycircuit.com/arduino-rda5807m-fm-receiver/

## Slide 87: Test2.23cFM radio with tea5767
https://create.arduino.cc/projecthub/mircemk/diy-retro-look-fm-radio-with-tea5767-module-370b88

## Slide 88: Test 2.24 Metal detector
https://www.electroschematics.com/metal-detector/

## Slide 89: Test 2.25 Digital Storage Scope DSO
https://www.instructables.com/id/Make-Your-Own-OscilloscopeMini-DSO-With-STC-MCU-Ea/

## Slide 90: Test2.25:PAJ7620 9-gesture sensor https://www.innovatorsguru.com/paj7620u2-arduino-gesture-sensor/
/*https://github.com/Seeed-Studio/Gesture_PAJ7620
https://www.youtube.com/watch?v=k_nF05DVFP0
Copyright (c) 2015 seeed technology inc.
Website : www.seeed.cc
Author : Wuruibin
Modified Time: June 2015
Description: This demo can recognize 9 gestures and output the result, including move up, move down, move left, move right,
move forward, move backward, circle-clockwise, circle-counter clockwise, and wave.
The MIT License (MIT)
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY,
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
*/
#include <Wire.h>
#include "paj7620.h"
/*
Notice: When you want to recognize the Forward/Backward gestures, your gestures' reaction time must less than GES_ENTRY_TIME(0.8s).
You also can adjust the reaction time according to the actual circumstance.
*/
#define GES_REACTION_TIME 500 // You can adjust the reaction time according to the actual circumstance.
#define GES_ENTRY_TIME 800 // When you want to recognize the Forward/Backward gestures, your gestures' reaction time must less than GES_ENTRY_TIME(0.8s).
#define GES_QUIT_TIME 1000
void setup() {
uint8_t error = 0;
Serial.begin(9600);
Serial.println("\nPAJ7620U2 TEST DEMO: Recognize 9 gestures.");
error = paj7620Init(); // initialize Paj7620 registers
if (error) {
Serial.print("INIT ERROR,CODE:");
Serial.println(error);
} else {
Serial.println("INIT OK");
}
Serial.println("Please input your gestures:\n");
}
void loop() {
uint8_t data = 0, data1 = 0, error;
error = paj7620ReadReg(0x43, 1, &data); // Read Bank_0_Reg_0x43/0x44 for gesture result.
if (!error) {
switch (data) { // When different gestures be detected, the variable 'data' will be set to different values by paj7620ReadReg(0x43, 1, &data).
case GES_RIGHT_FLAG:
delay(GES_ENTRY_TIME);
paj7620ReadReg(0x43, 1, &data);
if (data == GES_FORWARD_FLAG) {
Serial.println("Forward");
delay(GES_QUIT_TIME);
} else if (data == GES_BACKWARD_FLAG) {
Serial.println("Backward");
delay(GES_QUIT_TIME);
} else {
Serial.println("Right");
}
break;
case GES_LEFT_FLAG:
delay(GES_ENTRY_TIME);
paj7620ReadReg(0x43, 1, &data);
if (data == GES_FORWARD_FLAG) {
Serial.println("Forward");
delay(GES_QUIT_TIME);
} else if (data == GES_BACKWARD_FLAG) {
Serial.println("Backward");
delay(GES_QUIT_TIME);
} else {
Serial.println("Left");
}
break;
case GES_UP_FLAG:
delay(GES_ENTRY_TIME);
paj7620ReadReg(0x43, 1, &data);
if (data == GES_FORWARD_FLAG) {
Serial.println("Forward");
delay(GES_QUIT_TIME);
} else if (data == GES_BACKWARD_FLAG) {
Serial.println("Backward");
delay(GES_QUIT_TIME);
} else {
Serial.println("Up");
}
break;
case GES_DOWN_FLAG:
delay(GES_ENTRY_TIME);
paj7620ReadReg(0x43, 1, &data);
if (data == GES_FORWARD_FLAG) {
Serial.println("Forward");
delay(GES_QUIT_TIME);
} else if (data == GES_BACKWARD_FLAG) {
Serial.println("Backward");
delay(GES_QUIT_TIME);
} else {
Serial.println("Down");
}
break;
case GES_FORWARD_FLAG:
Serial.println("Forward");
delay(GES_QUIT_TIME);
break;
case GES_BACKWARD_FLAG:
Serial.println("Backward");
delay(GES_QUIT_TIME);
break;
case GES_CLOCKWISE_FLAG:
Serial.println("Clockwise");
break;
case GES_COUNT_CLOCKWISE_FLAG:
Serial.println("anti-clockwise");
break;
default:
paj7620ReadReg(0x44, 1, &data1);
if (data1 == GES_WAVE_FLAG) {
Serial.println("wave");
}
break;
}
}
delay(100);
}
Demo:https://www.youtube.com/watch?v=k_nF05DVFP0

## Slide 91: Test 2.26: Apds-9960 gesture sensor- https://learn.sparkfun.com/tutorials/apds-9960-rgb-and-gesture-sensor-hookup-guide/all
/****************************************************************
GestureTest.ino
https://learn.sparkfun.com/tutorials/apds-9960-rgb-and-gesture-sensor-hookup-guide/all
APDS-9960 RGB and Gesture Sensor
Shawn Hymel @ SparkFun Electronics
May 30, 2014
https://github.com/sparkfun/APDS-9960_RGB_and_Gesture_Sensor
Tests the gesture sensing abilities of the APDS-9960. Configures
APDS-9960 over I2C and waits for gesture events. Calculates the
direction of the swipe (up, down, left, right) and displays it
on a serial console.
To perform a NEAR gesture, hold your hand
far above the sensor and move it close to the sensor (within 2
inches). Hold your hand there for at least 1 second and move it
away.
To perform a FAR gesture, hold your hand within 2 inches of the
sensor for at least 1 second and then move it above (out of
range) of the sensor.
Hardware Connections:
IMPORTANT: The APDS-9960 can only accept 3.3V!
Arduino Pin APDS-9960 Board Function
3.3V VCC Power
GND GND Ground
A4 SDA I2C Data
A5 SCL I2C Clock
2 INT Interrupt
Resources:
Include Wire.h and SparkFun_APDS-9960.h
Development environment specifics:
Written in Arduino 1.0.5
Tested with SparkFun Arduino Pro Mini 3.3V
This code is beerware; if you see me (or any other SparkFun
employee) at the local, and you've found our code helpful, please
buy us a round!
Distributed as-is; no warranty is given.
****************************************************************/
#include <Wire.h>
#include <SparkFun_APDS9960.h>
// Pins
#define APDS9960_INT 2 // Needs to be an interrupt pin
// Constants
// Global Variables
SparkFun_APDS9960 apds = SparkFun_APDS9960();
int isr_flag = 0;
void setup() {
// Set interrupt pin as input
pinMode(APDS9960_INT, INPUT);
// Initialize Serial port
Serial.begin(9600);
Serial.println();
Serial.println(F("--------------------------------"));
Serial.println(F("SparkFun APDS-9960 - GestureTest"));
Serial.println(F("--------------------------------"));
// Initialize interrupt service routine
attachInterrupt(0, interruptRoutine, FALLING);
// Initialize APDS-9960 (configure I2C and initial values)
if ( apds.init() ) {
Serial.println(F("APDS-9960 initialization complete"));
} else {
Serial.println(F("Something went wrong during APDS-9960 init!"));
}
// Start running the APDS-9960 gesture sensor engine
if ( apds.enableGestureSensor(true) ) {
Serial.println(F("Gesture sensor is now running"));
} else {
Serial.println(F("Something went wrong during gesture sensor init!"));
}
}
void loop() {
if( isr_flag == 1 ) {
detachInterrupt(0);
handleGesture();
isr_flag = 0;
attachInterrupt(0, interruptRoutine, FALLING);
}
}
void interruptRoutine() {
isr_flag = 1;
}
void handleGesture() {
if ( apds.isGestureAvailable() ) {
switch ( apds.readGesture() ) {
case DIR_UP:
Serial.println("UP");
break;
case DIR_DOWN:
Serial.println("DOWN");
break;
case DIR_LEFT:
Serial.println("LEFT");
break;
case DIR_RIGHT:
Serial.println("RIGHT");
break;
case DIR_NEAR:
Serial.println("NEAR");
break;
case DIR_FAR:
Serial.println("FAR");
break;
default:
Serial.println("NONE");
}
}
}
All tested are ok except gesture tests, may need another sensor

## Slide 92: Test2.27a: Joystick https://create.arduino.cc/projecthub/MisterBotBreak/how-to-use-a-joystick-with-serial-monitor-1f04f0
int VRx = A0;
int VRy = A1;
int SW = 2;
int xPosition = 0;
int yPosition = 0;
int SW_state = 0;
int mapX = 0;
int mapY = 0;
void setup() {
Serial.begin(9600);
pinMode(VRx, INPUT);
pinMode(VRy, INPUT);
pinMode(SW, INPUT_PULLUP);
}
void loop() {
xPosition = analogRead(VRx);
yPosition = analogRead(VRy);
SW_state = digitalRead(SW);
mapX = map(xPosition, 0, 1023, -512, 512);
mapY = map(yPosition, 0, 1023, -512, 512);
Serial.print("X: ");
Serial.print(mapX);
Serial.print(" | Y: ");
Serial.print(mapY);
Serial.print(" | Button: ");
Serial.println(SW_state);
delay(100);
}

## Slide 93: Test2.27b: using a joystick to control servo motors https://maker.pro/arduino/tutorial/how-to-control-servo-motors-with-an-arduino-and-joystick
#include <Servo.h>
Servo servo1;
Servo servo2;
int x_key = A1;
int y_key = A0;
int x_pos;
int y_pos;
int servo1_pin = 8;
int servo2_pin = 9;
int initial_position = 90;
int initial_position1 = 90;
void setup ( ) {
Serial.begin (9600) ;
servo1.attach (servo1_pin ) ;
servo2.attach (servo2_pin ) ;
servo1.write (initial_position);
servo2.write (initial_position1);
pinMode (x_key, INPUT) ;
pinMode (y_key, INPUT) ;
}
void loop ( ) {
x_pos = analogRead (x_key) ;
y_pos = analogRead (y_key) ;
if (x_pos < 300){
if (initial_position < 10) { } else{ initial_position = initial_position - 20; servo1.write ( initial_position ) ; delay (100) ; } } if (x_pos > 700){
if (initial_position > 180)
{
}
else{
initial_position = initial_position + 20;
servo1.write ( initial_position ) ;
delay (100) ;
}
}
if (y_pos < 300){
if (initial_position1 < 10) { } else{ initial_position1 = initial_position1 - 20; servo2.write ( initial_position1 ) ; delay (100) ; } } if (y_pos > 700){
if (initial_position1 > 180)
{
}
else{
initial_position1 = initial_position1 + 20;
servo2.write ( initial_position1 ) ;
delay (100) ;
}
}
}

## Slide 94: Test 2.27c1 : Add remote control to a manually switched fan using an IR controls servo (servo jitter problem solved)
/* from: https://github.com/z3t0/Arduino-IRremote * IRremote: IRrecvDemo - demonstrates receiving IR codes with IRrecv
An IR detector/demodulator must be connected to the input RECV_PIN.
Version 0.1 July, 2009
Copyright 2009 Ken Shirriff
http://arcfn.com
*/
//// IR control rely, use 1 reciver to recive IR and send to another IR remote controller, 2020 April 23
#include <Servo.h>
// Create a servo object
Servo Servo1;
//#include "ServoTimer2.h" //it is found that IR control also use timer 2, so don't use ServoTimer2 here
//// Create a servo object
//ServoTimer2 Servo1;
int servoPin = 9; // Declare the Servo pin
int RECV_PIN = 11;
int one_step_button = 5;
int RELAY_PIN = 4; //obselet not used
#include <IRremote.h>
IRsend irsend;
/// the black remote controls: 17 kets
#define LG_TV_RED 0x20DF4EB1 //(red)
#define LG_TV_GREEN 0x20DF8E71 //(green)
#define LG_TV_YELLOW 0x20DFC639 //(yellow)
#define LG_TV_BLUE 0x20DF8679 //(blue)
#define LG_TV_0 0x20DF08F7
#define LG_TV_1 0x20DF8877
#define LG_TV_2 0x20DF48B7
#define LG_TV_3 0x20DFC837
#define LG_TV_4 0x20DF28D7
#define LG_TV_5 0x20DFA857
#define LG_TV_6 0x20DF6897
#define LG_TV_7 0x20DFE817
#define LG_TV_8 0x20DF18E7
#define LG_TV_9 0x20DF9867
///////////// for Black, 17-keys-keypad
#define B17_01 0xFFA25D
#define B17_02 0xFF629D
#define B17_03 0xFFE21D
#define B17_04 0xFF22DD
#define B17_05 0xFF02FD
#define B17_06 0xFFC23D
#define B17_07 0xFFE01F
#define B17_08 0xFFA857
#define B17_09 0xFF906F
#define B17_00 0xFF9867
#define B17_STAR 0xFF6897
#define B17_HASH 0xFFB04F
#define B17_LEFT 0xFF10EF
#define B17_RIGHT 0xFF5AA5
#define B17_UP 0xFF18E7
#define B17_DOWN 0xFF4AB5
#define B17_OK 0xFF38C7
//My_TV_Super= MTS, NEC:
#define MTS_UP 0xFB0058A7
#define MTS_LEFT 0xFB00E21D
#define MTS_RIGHT 0xFB00E01F
#define MTS_DOWN 0xFB0012ED
#define MTS_OK 0xFB00609F
#define MTS_POWER 0xFB0038C7
#define MTS_MTS_VOD 0xFB0020DF
#define MTS_HOME 0xFB0050AF
#define MTS_RETURN 0xFB00926D
#define MTS_INFO 0xFB0018E7
#define MTS_PLAY 0xFB00807F
#define MTS_STOP 0xFB00FA05
#define MTS_REW 0xFB009867
#define MTS_FFW 0xFB001AE5
#define MTS_SILENT 0xFB003AC5
#define MTS_BACKSPACE 0xFB0008F7
#define MTS_KEY0 0xFB0030CF
#define MTS_KEY1 0xFB002AD5
#define MTS_KEY2 0xFB006897
#define MTS_KEY3 0xFB00A857
#define MTS_KEY4 0xFB000AF5
#define MTS_KEY5 0xFB0048B7
#define MTS_KEY6 0xFB008877
#define MTS_KEY7 0xFB0032CD
#define MTS_KEY8 0xFB00708F
#define MTS_KEY9 0xFB00B04F
#define SIGNAL_DELAY1 150 // at least 120
#define SIGNAL_DELAY2 0 // at least 0
#define REC_DELAY 10 // typical 250 , 10-100 is ok for slow key-press action
/////////////////////////////////////////////////
IRrecv irrecv(RECV_PIN);
long unsigned int irCode;
decode_results results;
// Dumps out the decode_results structure.
// Call this after IRrecv::decode()
// void * to work around compiler issue
//void dump(void *v) {
// decode_results *results = (decode_results *)
//////////////////////////////////////////////////////////////
void turn_servo_to_pull_fan_string( long unsigned int irCode_recieved)
{
switch (irCode_recieved) {
case LG_TV_RED :
turn_servo1();
break;
case LG_TV_GREEN : //servo turns 3 times
turn_servo1(); turn_servo1(); turn_servo1();
break;
case LG_TV_YELLOW ://servo turns 2 times
turn_servo1(); turn_servo1();
break;
case LG_TV_BLUE: //servo turn once
turn_servo1();
break;
/////////for Black, 17-keys-keypad
case B17_01 :
turn_servo1();
break;
case B17_02 ://servo turns 2 times
turn_servo1(); turn_servo1();
break;
case B17_03 : //servo turns 3 times
turn_servo1(); turn_servo1(); turn_servo1();
break;
///////////////////////////// for other applications
// case B_UP:
// irCode = MTS_UP; Serial.println(irCode, HEX); send_IR_code( irCode);
// break;
}
}
//////////////////////////////////////////////////
void dump(decode_results * results) {
int count = results->rawlen;
if (results->decode_type == UNKNOWN) {
Serial.println("Could not decode message");
}
else {
if (results->decode_type == NEC) {
Serial.print("Decoded NEC: ");
}
else if (results->decode_type == SONY) {
Serial.print("Decoded SONY: ");
}
else if (results->decode_type == RC5) {
Serial.print("Decoded RC5: ");
}
else if (results->decode_type == RC6) {
Serial.print("Decoded RC6: ");
}
Serial.print(results->value, HEX);
turn_servo_to_pull_fan_string(results->value);
Serial.print(" (");
Serial.print(results->bits, DEC);
Serial.println(" bits)");
}
Serial.print("Raw (");
Serial.print(count, DEC);
Serial.print("): ");
for (int i = 0; i < count; i++) {
if ((i % 2) == 1) {
Serial.print(results->rawbuf[i]*USECPERTICK, DEC);
}
else {
Serial.print(-(int)results->rawbuf[i]*USECPERTICK, DEC);
}
Serial.print(" ");
}
Serial.println("");
}
/////////////////////////////////////////////////////
void setup()
{ pinMode(RELAY_PIN, OUTPUT);
pinMode(13, OUTPUT);
Serial.begin(9600);
irrecv.enableIRIn(); // Start the receiver
//Servo1.attach(servoPin);
Servo1.detach(); //turn off first to avoid jitter due to the irrecv library
}
int on = 0;
unsigned long last = millis();
/////////////////////////////////////////////////////
void loop() {
if (irrecv.decode(&results)) {
// If it's been at least 1/4 second since the last
// IR received, toggle the relay
if (millis() - last > REC_DELAY)
{
on = !on;
//digitalWrite(RELAY_PIN, on ? HIGH : LOW);
//digitalWrite(13, on ? HIGH : LOW);
dump(&results); // this is to send the recived code to the TV
}
last = millis();
irrecv.resume(); // Receive the next value
}
if (digitalRead(one_step_button) == LOW)
{ turn_servo1();
}
}
void turn_servo1() {
int delay_step = 3;
Servo1.attach(servoPin); // turn on servo
for (int t = 0; t < 180; t++)
{
Servo1.write(t); delay(delay_step);
}
for (int t = 180 - 1; t > 0; t--)
{
Servo1.write(t); delay(delay_step);
}
Servo1.detach();// turn off servo
}
//alternative method , not used
void turn_servo2() {
int delay_step = 150;
Servo1.attach(servoPin); // turn on servo
Servo1.write(0);//------------
delay(delay_step);
Servo1.write(90);//------------
delay(delay_step);
Servo1.write(180);//------------
delay(delay_step);
Servo1.write(90);//------------
delay(delay_step);
Servo1.write(0);//------------
delay(delay_step);
Servo1.detach();// turn off servo
}
94
Arduino
Uno, or
Arduino-Nano
Processor:ATmega328
(choose old bootloader)
Infrared light
TV Remote Controller
Pin11
GND
Vcc (5V)
or
IR receiver module
KY-022
Out Vcc, GND
LG_RED_BUTTON
Pin9
Pin5
The servo motor pulls the string attached to the switch of the fan.

## Slide 95: Test 2.27c2 : Upgraded version of 2.27c1 fan control program (fan200708a.ino) updated added line tracker sensor KY-033, the system will automatic reset to 0, before execute a new command
//fan200708a.ino //fixed on_off_button bug
/* added 1) button 5, toggle fan (off or level2), ver6b, 2020Jun18 updated
* 2) added line tracker sensor KY-033, the system will atomatic reset to 0, before execute a new command
* This is to avoid manual chnage of the fan-level that confuse the control.
* It rest the fan to zero first before execute a comman
*/
/* from: https://github.com/z3t0/Arduino-IRremote * IRremote: IRrecvDemo - demonstrates receiving IR codes with IRrecv
An IR detector/demodulator must be connected to the input RECV_PIN.
Version 0.1 July, 2009
Copyright 2009 Ken Shirriff
http://arcfn.com
*/
int fan_counter;//global
int KY033_sensorPin = A0; // select the input pin
int KY033_sensorValue = 0; // variable to store the value coming from the sensorValue
//// IR control rely, use 1 reciver to recive IR and send to another IR remote controller, 2020 April 23
#include <Servo.h>
// Create a servo object
Servo Servo1;
//#include "ServoTimer2.h" //it is found that IR control also use timer 2, so don't use ServoTimer2 here
//// Create a servo object
//ServoTimer2 Servo1;
int servoPin = 9; // Declare the Servo pin
int led_default =13;
int RECV_PIN = 11;
int on_off_buton = 5;
int RELAY_PIN = 4; //obselet not used
#include <IRremote.h>
IRsend irsend;
/// the black remote controls: 17 kets
#define LG_TV_RED 0x20DF4EB1 //(red)
#define LG_TV_GREEN 0x20DF8E71 //(green)
#define LG_TV_YELLOW 0x20DFC639 //(yellow)
#define LG_TV_BLUE 0x20DF8679 //(blue)
#define LG_TV_0 0x20DF08F7
#define LG_TV_1 0x20DF8877
#define LG_TV_2 0x20DF48B7
#define LG_TV_3 0x20DFC837
#define LG_TV_4 0x20DF28D7
#define LG_TV_5 0x20DFA857
#define LG_TV_6 0x20DF6897
#define LG_TV_7 0x20DFE817
#define LG_TV_8 0x20DF18E7
#define LG_TV_9 0x20DF9867
///////////// for Black, 17-keys-keypad
#define B17_01 0x00FFA25D
#define B17_02 0x00FF629D
#define B17_03 0x00FFE21D
#define B17_04 0x00FF22DD
#define B17_05 0x00FF02FD
#define B17_06 0x00FFC23D
#define B17_08 0x00FFA857
#define B17_09 0x00FF906F
#define B17_00 0x00FF9867
#define B17_STAR 0x00FF6897
#define B17_HASH 0x00FFB04F
#define B17_LEFT 0x00FF10EF
#define B17_RIGHT 0x00FF5AA5
#define B17_UP 0x00FF18E7
#define B17_DOWN 0x00FF4AB5
#define B17_OK 0x00FF38C7
//My_TV_Super= MTS, NEC:
#define MTS_UP 0xFB
#define B17_07 0x00FFE01F0058A7
#define MTS_LEFT 0xFB00E21D
#define MTS_RIGHT 0xFB00E01F
#define MTS_DOWN 0xFB0012ED
#define MTS_OK 0xFB00609F
#define MTS_POWER 0xFB0038C7
#define MTS_MTS_VOD 0xFB0020DF
#define MTS_HOME 0xFB0050AF
#define MTS_RETURN 0xFB00926D
#define MTS_INFO 0xFB0018E7
#define MTS_PLAY 0xFB00807F
#define MTS_STOP 0xFB00FA05
#define MTS_REW 0xFB009867
#define MTS_FFW 0xFB001AE5
#define MTS_SILENT 0xFB003AC5
#define MTS_BACKSPACE 0xFB0008F7
#define MTS_KEY0 0xFB0030CF
#define MTS_KEY1 0xFB002AD5
#define MTS_KEY2 0xFB006897
#define MTS_KEY3 0xFB00A857
#define MTS_KEY4 0xFB000AF5
#define MTS_KEY5 0xFB0048B7
#define MTS_KEY6 0xFB008877
#define MTS_KEY7 0xFB0032CD
#define MTS_KEY8 0xFB00708F
#define MTS_KEY9 0xFB00B04F
#define SIGNAL_DELAY1 150 // at least 120
#define SIGNAL_DELAY2 0 // at least 0
#define REC_DELAY 10 // typical 250 , 10-100 is ok for slow key-press action
/////////////////////////////////////////////////
IRrecv irrecv(RECV_PIN);
long unsigned int irCode;
decode_results results;
// Dumps out the decode_results structure.
// Call this after IRrecv::decode()
// void * to work around compiler issue
//void dump(void *v) {
// decode_results *results = (decode_results *)
//////////////////////////////////////////////////////////////
void turn_servo_to_pull_fan_string( long unsigned int irCode_recieved)
{
switch (irCode_recieved) {
case LG_TV_RED : //fan level-1
turn_fan(1);
break;
case LG_TV_GREEN : //fan level-2
turn_fan(2);
break;
case LG_TV_YELLOW ://fan level-3
turn_fan(3);
break;
case LG_TV_BLUE: //fan level-0 , stops
turn_fan(0);
break;
/////***** for Black, 17-keys-keypad ****** /////
case B17_01 ://B17_01
turn_fan(1);
break;
case B17_02 :
turn_fan(2);
break;
case B17_03 :
turn_fan(3);
break;
case B17_04 :
turn_fan(0);
break;
///////////////////////////// for other applications
// case B_UP:
// irCode = MTS_UP; Serial.println(irCode, HEX); send_IR_code( irCode);
// break;
}
}
//////////////////////////////////////////////////
void dump(decode_results * results) {
int count = results->rawlen;
if (results->decode_type == UNKNOWN) {
Serial.println("Could not decode message");
}
else {
if (results->decode_type == NEC) {
Serial.print("Decoded NEC: ");
}
else if (results->decode_type == SONY) {
Serial.print("Decoded SONY: ");
}
else if (results->decode_type == RC5) {
Serial.print("Decoded RC5: ");
}
else if (results->decode_type == RC6) {
Serial.print("Decoded RC6: ");
}
Serial.print(results->value, HEX);
turn_servo_to_pull_fan_string(results->value);
Serial.print(" (");
Serial.print(results->bits, DEC);
Serial.println(" bits)");
}
Serial.print("Raw (");
Serial.print(count, DEC);
Serial.print("): ");
for (int i = 0; i < count; i++) {
if ((i % 2) == 1) {
Serial.print(results->rawbuf[i]*USECPERTICK, DEC);
}
else {
Serial.print(-(int)results->rawbuf[i]*USECPERTICK, DEC);
}
Serial.print(" ");
}
Serial.println("-----------");
Serial.println("============");
}
/////////////////////////////////////////////////////
void setup()
{
//pinMode(RELAY_PIN, OUTPUT); //not used in this program
pinMode(led_default, OUTPUT);
pinMode(5, INPUT);
pinMode(on_off_buton, INPUT);
Serial.begin(9600);
irrecv.enableIRIn(); // Start the receiver
//Servo1.attach(servoPin);
Servo1.detach(); //turn off first to avoid jitter due to the irrecv library
reset_to_fan_counter0();
}
int on = 0;
//bool on_off_tag = false; //init to be false, fan off
unsigned long last = millis();
/////////////////////////////////////////////////////
void loop() {
if (irrecv.decode(&results)) {
// If it's been at least 1/4 second since the last
// IR received, toggle the relay
if (millis() - last > REC_DELAY)
{
on = !on;
//digitalWrite(RELAY_PIN, on ? HIGH : LOW);
//digitalWrite(13, on ? HIGH : LOW);
dump(&results); // this is to send the recived code to the TV
}
last = millis();
irrecv.resume(); // Receive the next value
}
// if (digitalRead(on_off_buton) == LOW)
// { on_off_tag = !on_off_tag; //if on_off_tag==0 then off fan, otherwise turn_fan(2)
// if (on_off_tag != false) {
// turn_fan(2);
// delay(1000);
// }
// else
// { turn_fan(0);
// delay(1000);
// }
// }
//handle external on-off-key, if fan is already off, press on_off_buton will turn_fan(2)
//else turn off fan ( set turn_fan(0)
if (digitalRead(on_off_buton) == LOW)
{
if (fan_counter ==0) {
turn_fan(2);
delay(100); //for debounce
}
else
{ turn_fan(0);
delay(100);//for debounce
}
}
KY033_sensorValue = analogRead (KY033_sensorPin);
Serial.print("KY033_sensorValue .. = ");
Serial.println(KY033_sensorValue);
//delay(1000);
}
void turn_servo1() {
int delay_step = 3;
Servo1.attach(servoPin); // turn on servo
for (int t = 0; t < 180; t++)
{
Servo1.write(t); delay(delay_step);
}
for (int t = 180 - 1; t > 0; t--)
{
Servo1.write(t); delay(delay_step);
}
Servo1.detach();// turn off servo
}
//alternative method , not used
void turn_servo2() {
int delay_step = 150;
Servo1.attach(servoPin); // turn on servo
Servo1.write(0);//------------
delay(delay_step);
Servo1.write(90);//------------
delay(delay_step);
Servo1.write(180);//------------
delay(delay_step);
Servo1.write(90);//------------
delay(delay_step);
Servo1.write(0);//------------
delay(delay_step);
Servo1.detach();// turn off servo
}
void turn_servo1b(int count_servo_turn) {
// // if (count_servo_turn == 0) {};
if (count_servo_turn == 1) {
turn_servo1();
};
if (count_servo_turn == 2) {
turn_servo1();
turn_servo1();
};
if (count_servo_turn == 3) {
turn_servo1();
turn_servo1();
turn_servo1();
};
}
/////////////////////////////////////////////////////
void reset_to_fan_counter0()
{
for (int ct = 0; ct < 5 ; ct++)
{
KY033_sensorValue = analogRead (KY033_sensorPin);
// if ( KY033_sensorValue > 200) { //depends on sensor, this is for black >200
if ( KY033_sensorValue < 200) {//depends on sensor, this is for black <200
break;
};
turn_servo1b(1);
}
fan_counter = 0;
}
/////////////////////////////////////////////////////////
void turn_fan(int fan_level) {
reset_to_fan_counter0();
switch (fan_counter) {
case 0 : ////////////////////////////////
if (fan_level == 0) {
turn_servo1b(0);
fan_counter = 0;
}; // no change
if (fan_level == 1) {
turn_servo1b(1);
fan_counter = 1;;
};
if (fan_level == 2) {
turn_servo1b(2);
fan_counter = 2;
};
if (fan_level == 3) {
turn_servo1b(3);
fan_counter = 3;
};
break;
case 1 : ////////////////////////////////
if (fan_level == 0) {
turn_servo1b(3);
fan_counter = 0;
};
if (fan_level == 1) {
turn_servo1b(0);
fan_counter = 1;
};
if (fan_level == 2) {
turn_servo1b(1);
fan_counter = 2;
};
if (fan_level == 3) {
turn_servo1b(2);
fan_counter = 3;
};
break;
case 2 : ////////////////////////////////
if (fan_level == 0) {
turn_servo1b(2);
fan_counter = 0;
};
if (fan_level == 1) {
turn_servo1b(3);
fan_counter = 1;
};
if (fan_level == 2) {
turn_servo1b(0);
fan_counter = 2;
};
if (fan_level == 3) {
turn_servo1b(1);
fan_counter = 3;
};
break;
case 3 : ////////////////////////////////
if (fan_level == 0) {
turn_servo1b(1);
fan_counter = 0;
};
if (fan_level == 1) {
turn_servo1b(2);
fan_counter = 1;
};
if (fan_level == 2) {
turn_servo1b(3);
fan_counter = 2;
};
if (fan_level == 3) {
turn_servo1b(0);
fan_counter = 3;
};
break;
} Serial.println("fan control system .........");
Serial.print("fan_counter= ");
Serial.println(fan_counter);
Serial.print("fan_level= ");
Serial.println(fan_level);
Serial.println("fan control system //////////");
Serial.println("...................");
Serial.print("KY033_sensorValue = ");
Serial.println(KY033_sensorValue);
}

## Slide 96: Test 2.27c3 : IR controls 2 servos (amplifier volume control—not fully tested, may have bug) (servo jitter problem solved)
// 2022.1.22 IR control 2 servos. 2:24pm
/* from: https://github.com/z3t0/Arduino-IRremote * IRremote: IRrecvDemo - demonstrates receiving IR codes with IRrecv
An IR detector/demodulator must be connected to the input RECV_PIN.
Version 0.1 July, 2009
Copyright 2009 Ken Shirriff
http://arcfn.com
*/
//// IR control rely, use 1 reciver to recive IR and send to another IR remote controller, 2020 April 23
#include <Servo.h>
// Create a servo object
Servo servo_A, servo_B;
//#include "ServoTimer2.h" //it is found that IR control also use timer 2, so don't use ServoTimer2 here
//// Create a servo object
//ServoTimer2 servo_A;
int servoPin_A = 9; // Declare the Servo pin
int servoPin_B = 10; // Declare the Servo pin
int RECV_PIN = 11;
int one_step_button = 5;
int RELAY_PIN = 4; //obselet not used
int init_t = 90; // this is the initial position, may adjsut to the suitbale position rather than 90 (range 0 -180)
int current_t = init_t; // this is the initial position
int delay_step =10 ;//need this to giev enough delay for each truning step of servo
int servo_step=10;
int servo_t_max=180;
int servo_t_min=0;
#include <IRremote.h>
IRsend irsend;
/// the black remote controls: 17 kets
#define LG_TV_RED 0x20DF4EB1 //(red)
#define LG_TV_GREEN 0x20DF8E71 //(green)
#define LG_TV_YELLOW 0x20DFC639 //(yellow)
#define LG_TV_BLUE 0x20DF8679 //(blue)
#define LG_TV_0 0x20DF08F7
#define LG_TV_1 0x20DF8877
#define LG_TV_2 0x20DF48B7
#define LG_TV_3 0x20DFC837
#define LG_TV_4 0x20DF28D7
#define LG_TV_5 0x20DFA857
#define LG_TV_6 0x20DF6897
#define LG_TV_7 0x20DFE817
#define LG_TV_8 0x20DF18E7
#define LG_TV_9 0x20DF9867
///////////// for Black, 17-keys-keypad
#define B17_01 0xFFA25D
#define B17_02 0xFF629D
#define B17_03 0xFFE21D
#define B17_04 0xFF22DD
#define B17_05 0xFF02FD
#define B17_06 0xFFC23D
#define B17_07 0xFFE01F
#define B17_08 0xFFA857
#define B17_09 0xFF906F
#define B17_00 0xFF9867
#define B17_STAR 0xFF6897
#define B17_HASH 0xFFB04F
#define B17_LEFT 0xFF10EF
#define B17_RIGHT 0xFF5AA5
#define B17_UP 0xFF18E7
#define B17_DOWN 0xFF4AB5
#define B17_OK 0xFF38C7
//////////////
///////////////////////////////////////////////////////
//22.1.22 updated DEFINE table2 : white 21 keys remote controls:
#define W21_LEFT 0xFF10EF
#define W21_RIGHT 0xFF5AA5
#define W21_UP 0xFF18E7
#define W21_DOWN 0xFF4AB5
#define W21_OK 0xFF38C7
#define W21_CH_plus 0xFFA25D
#define W21_CH 0xFF629D
#define W21_CH_minus 0xFFE21D
#define W21_PREV 0xFF22DD
#define W21_NEXT 0xFF02FD
#define W21_PLAY 0xFFC23D
#define W21_VOL_plus 0xFFA857
#define W21_VOL_minus 0xFFE01F
#define W21_EQ 0xFF906F
#define W21_0 0xFF6897
#define W21_100_plus 0xFF9867
#define W21_200_puls 0xFFB04F
#define W21_1 0xFF30CF
#define W21_2 0xFF18E7
#define W21_3 0xFF7A85
#define W21_4 0xFF10EF
#define W21_5 0xFF38C7
#define W21_6 0xFF5AA5
#define W21_7 0xFF42BD
#define W21_8 0xFF4AB5
#define W21_9 0xFF52AD
//My_TV_Super= MTS, NEC:
#define MTS_UP 0xFB0058A7
#define MTS_LEFT 0xFB00E21D
#define MTS_RIGHT 0xFB00E01F
#define MTS_DOWN 0xFB0012ED
#define MTS_OK 0xFB00609F
#define MTS_POWER 0xFB0038C7
#define MTS_MTS_VOD 0xFB0020DF
#define MTS_HOME 0xFB0050AF
#define MTS_RETURN 0xFB00926D
#define MTS_INFO 0xFB0018E7
#define MTS_PLAY 0xFB00807F
#define MTS_STOP 0xFB00FA05
#define MTS_REW 0xFB009867
#define MTS_FFW 0xFB001AE5
#define MTS_SILENT 0xFB003AC5
#define MTS_BACKSPACE 0xFB0008F7
#define MTS_KEY0 0xFB0030CF
#define MTS_KEY1 0xFB002AD5
#define MTS_KEY2 0xFB006897
#define MTS_KEY3 0xFB00A857
#define MTS_KEY4 0xFB000AF5
#define MTS_KEY5 0xFB0048B7
#define MTS_KEY6 0xFB008877
#define MTS_KEY7 0xFB0032CD
#define MTS_KEY8 0xFB00708F
#define MTS_KEY9 0xFB00B04F
#define SIGNAL_DELAY1 150 // at least 120
#define SIGNAL_DELAY2 0 // at least 0
#define REC_DELAY 10 // typical 250 , 10-100 is ok for slow key-press action
/////////////////////////////////////////////////
IRrecv irrecv(RECV_PIN);
long unsigned int irCode;
decode_results results;
// Dumps out the decode_results structure.
// Call this after IRrecv::decode()
// void * to work around compiler issue
//void dump(void *v) {
// decode_results *results = (decode_results *)
//////////////////////////////////////////////////////////////
void turn_servo_when_code_recieved( long unsigned int irCode_recieved)
{
switch (irCode_recieved) {
case B17_LEFT :
turn_servo_A_vol_plus() ;
Serial.println("\n-- B17_RIGHT -- turn_servo_A_vol_plus()\n");
break;
case B17_RIGHT :
turn_servo_A_vol_minus() ;
Serial.println("\n-- B17_RIGHT -- turn_servo_A_vol_minus()\n");
break;
case B17_OK :
turn_servo_A_center(); //power button
Serial.println("\n-- B17_OK -- LG_TV_RED depressed\n");
break;
case B17_HASH :
turn_servo_B(); //power button
Serial.println("\n-- B17_HASH -- turn_servo_B()-- power button \n");
break;
//////////////////////////////////////////////////////////////////////
}
}
//////////////////////////////////////////////////
void dump(decode_results * results) {
int count = results->rawlen;
if (results->decode_type == UNKNOWN) {
Serial.println("Could not decode message");
}
else {
if (results->decode_type == NEC) {
Serial.print("Decoded NEC: ");
}
else if (results->decode_type == SONY) {
Serial.print("Decoded SONY: ");
}
else if (results->decode_type == RC5) {
Serial.print("Decoded RC5: ");
}
else if (results->decode_type == RC6) {
Serial.print("Decoded RC6: ");
}
Serial.print(results->value, HEX);
turn_servo_when_code_recieved(results->value);
Serial.print(" (");
Serial.print(results->bits, DEC);
Serial.println(" bits)");
}
Serial.print("Raw (");
Serial.print(count, DEC);
Serial.print("): ");
for (int i = 0; i < count; i++) {
if ((i % 2) == 1) {
Serial.print(results->rawbuf[i]*USECPERTICK, DEC);
}
else {
Serial.print(-(int)results->rawbuf[i]*USECPERTICK, DEC);
}
Serial.print(" ");
}
Serial.println("");
}
//////sssssssssssssssssssssssssssssssssssssssssssssssss
void setup()
{ pinMode(RELAY_PIN, OUTPUT);
pinMode(13, OUTPUT);
Serial.begin(9600);
irrecv.enableIRIn(); // Start the receiver
//servo_A.attach(servoPin_A);
servo_A.detach(); //turn off first to avoid jitter due to the irrecv library
turn_servo_A_init_pos();
}
int on = 0;
unsigned long last = millis();
///// LLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLL
void loop() {
if (irrecv.decode(&results)) {
// If it's been at least 1/4 second since the last
// IR received, toggle the relay
if (millis() - last > REC_DELAY)
{
on = !on;
//digitalWrite(RELAY_PIN, on ? HIGH : LOW);
//digitalWrite(13, on ? HIGH : LOW);
dump(&results); // this is to send the recived code to the TV
}
last = millis();
irrecv.resume(); // Receive the next value
}
// if (digitalRead(one_step_button) == LOW)
// { turn_servo_A();
// }
}
/// ++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
void turn_servo_A_vol_minus() {
int t;
servo_A.attach(servoPin_A); // turn on servo
for (t = current_t; t <current_t +servo_step; t++)//dir depend on var. resistor truning angle
{ if (t>servo_t_max )
{t =servo_t_max;}
servo_A.write(t); delay(delay_step);
}
current_t=t;
servo_A.detach();// turn off servo
}
///// ----------------------------------------------------------------
void turn_servo_A_vol_plus() {
int t;
servo_A.attach(servoPin_A); // turn on servo
for (t = current_t; t > current_t - servo_step; t--)//dir depend on var. resistor truning angle
{if (t<servo_t_min )
{t=servo_t_min;}
servo_A.write(t); delay(delay_step);
}
current_t=t;
servo_A.detach();// turn off servo
}
// IIIIIIIIIIIIIIIIIIIIIIIIIIIIIIIIIIIIIIIIIIIIIIIII
void turn_servo_A_init_pos() {
servo_A.attach(servoPin_A); // turn on servo
//int t=90;
// servo_A.write(t); delay(delay_step);
for (int t = 0; t < init_t; t++)
{
servo_A.write(t); delay(delay_step);
}
servo_A.detach();// turn off servo
}// cccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccccc
void turn_servo_A_center() {
servo_A.attach(servoPin_A); // turn on servo
if (current_t < init_t)
{
for (int t = current_t ; t < init_t; t++)
{
servo_A.write(t); delay(delay_step);
}
}
if (current_t > init_t)
{
for (int t = current_t ; t > init_t; t--)
{
servo_A.write(t); delay(delay_step);
}
}
servo_A.detach();// turn off servo
}
// PPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPPP
// for power button pressing
void turn_servo_B() {
servo_B.attach(servoPin_B); // turn on servo
for (int t = 0; t < servo_t_max; t++)
{
servo_B.write(t); delay(delay_step);
}
for (int t = 180 - 1; t >servo_t_min; t--)
{
servo_B.write(t); delay(delay_step);
}
servo_B.detach();// turn off servo
}
////alternative method , not used
//void turn_servo2() {
// int delay_step = 150;
// servo_A.attach(servoPin_A); // turn on servo
//
// servo_A.write(0);//------------
// delay(delay_step);
// servo_A.write(90);//------------
// delay(delay_step);
// servo_A.write(180);//------------
// delay(delay_step);
// servo_A.write(90);//------------
// delay(delay_step);
// servo_A.write(0);//------------
//
// delay(delay_step);
// servo_A.detach();// turn off servo
//}
//void turn_servo_A() {
//
// servo_A.attach(servoPin_A); // turn on servo
// for (int t = 0; t < 180; t++)
// {
// servo_A.write(t); delay(delay_step);
// }
// for (int t = 180 - 1; t > 0; t--)
// {
// servo_A.write(t); delay(delay_step);
// }
// servo_A.detach();// turn off servo
//}
96
Arduino
Uno, or
Arduino-Nano
Processor:ATmega328
(choose old bootloader)
Infrared light
Pin11
GND
Vcc (5V)
or
IR receiver module
KY-022
Out Vcc, GND
B17 remote controller
Arrow left = vol. minus
Arrow right = vol. plus
OK = vol. central
# Hash =power on/off
Servo_A
Pin9
Pin5
The servo motor pulls the string attached to the switch of the fan.
Servo_B
Pin10

## Slide 97: Test 2.27c4 : IR controls 1 servo (amplifier volume control) Working version
// 2022.2.11, ok control 1 servo vol control and 1 relay to control the power for ampfliers
/* from: https://github.com/z3t0/Arduino-IRremote * IRremote: IRrecvDemo - demonstrates receiving IR codes with IRrecv
An IR detector/demodulator must be connected to the input RECV_PIN.
Version 0.1 July, 2009
Copyright 2009 Ken Shirriff
http://arcfn.com
*/
//// IR control rely, use 1 reciver to recive IR and send to another IR remote controller, 2020 April 23
#include <Servo.h>
// Create a servo object
Servo servo1;
int servoPin1 = 9; // Declare the Servo pin
int RECV_PIN = 11;
int one_step_button = 5;
int RELAY_PIN = 4; //obselet not used
int init_t = 90; // this is the initial position, may adjsut to the suitbale position rather than 90 (range 0 -180)
int current_t = init_t; // this is the initial position
int delay_step = 10 ; //need this to giev enough delay for each truning step of servo
int servo_step = 10;
int servo_t_max = 180 - servo_step - 2;
int servo_t_min = servo_step + 2;
int servo_t_neutral = 90;
int power_on_off_tag;
#include <IRremote.h>
IRsend irsend;
/// the black remote controls: 17 kets
#define LG_TV_RED 0x20DF4EB1 //(red)
#define LG_TV_GREEN 0x20DF8E71 //(green)
#define LG_TV_YELLOW 0x20DFC639 //(yellow)
#define LG_TV_BLUE 0x20DF8679 //(blue)
#define LG_TV_0 0x20DF08F7
#define LG_TV_1 0x20DF8877
#define LG_TV_2 0x20DF48B7
#define LG_TV_3 0x20DFC837
#define LG_TV_4 0x20DF28D7
#define LG_TV_5 0x20DFA857
#define LG_TV_6 0x20DF6897
#define LG_TV_7 0x20DFE817
#define LG_TV_8 0x20DF18E7
#define LG_TV_9 0x20DF9867
///////////// for Black, 17-keys-keypad
#define B17_01 0xFFA25D
#define B17_02 0xFF629D
#define B17_03 0xFFE21D
#define B17_04 0xFF22DD
#define B17_05 0xFF02FD
#define B17_06 0xFFC23D
#define B17_07 0xFFE01F
#define B17_08 0xFFA857
#define B17_09 0xFF906F
#define B17_00 0xFF9867
#define B17_STAR 0xFF6897
#define B17_HASH 0xFFB04F
#define B17_LEFT 0xFF10EF
#define B17_RIGHT 0xFF5AA5
#define B17_UP 0xFF18E7
#define B17_DOWN 0xFF4AB5
#define B17_OK 0xFF38C7
//////////////
///////////////////////////////////////////////////////
//22.1.22 updated DEFINE table2 : white 21 keys remote controls:
#define W21_LEFT 0xFF10EF
#define W21_RIGHT 0xFF5AA5
#define W21_UP 0xFF18E7
#define W21_DOWN 0xFF4AB5
#define W21_OK 0xFF38C7
#define W21_CH_plus 0xFFA25D
#define W21_CH 0xFF629D
#define W21_CH_minus 0xFFE21D
#define W21_PREV 0xFF22DD
#define W21_NEXT 0xFF02FD
#define W21_PLAY 0xFFC23D
#define W21_VOL_plus 0xFFA857
#define W21_VOL_minus 0xFFE01F
#define W21_EQ 0xFF906F
#define W21_0 0xFF6897
#define W21_100_plus 0xFF9867
#define W21_200_puls 0xFFB04F
#define W21_1 0xFF30CF
#define W21_2 0xFF18E7
#define W21_3 0xFF7A85
#define W21_4 0xFF10EF
#define W21_5 0xFF38C7
#define W21_6 0xFF5AA5
#define W21_7 0xFF42BD
#define W21_8 0xFF4AB5
#define W21_9 0xFF52AD
//My_TV_Super= MTS, NEC:
#define MTS_UP 0xFB0058A7
#define MTS_LEFT 0xFB00E21D
#define MTS_RIGHT 0xFB00E01F
#define MTS_DOWN 0xFB0012ED
#define MTS_OK 0xFB00609F
#define MTS_POWER 0xFB0038C7
#define MTS_MTS_VOD 0xFB0020DF
#define MTS_HOME 0xFB0050AF
#define MTS_RETURN 0xFB00926D
#define MTS_INFO 0xFB0018E7
#define MTS_PLAY 0xFB00807F
#define MTS_STOP 0xFB00FA05
#define MTS_REW 0xFB009867
#define MTS_FFW 0xFB001AE5
#define MTS_SILENT 0xFB003AC5
#define MTS_BACKSPACE 0xFB0008F7
#define MTS_KEY0 0xFB0030CF
#define MTS_KEY1 0xFB002AD5
#define MTS_KEY2 0xFB006897
#define MTS_KEY3 0xFB00A857
#define MTS_KEY4 0xFB000AF5
#define MTS_KEY5 0xFB0048B7
#define MTS_KEY6 0xFB008877
#define MTS_KEY7 0xFB0032CD
#define MTS_KEY8 0xFB00708F
#define MTS_KEY9 0xFB00B04F
#define SIGNAL_DELAY1 150 // at least 120
#define SIGNAL_DELAY2 0 // at least 0
#define REC_DELAY 10 // typical 250 , 10-100 is ok for slow key-press action
/////////////////////////////////////////////////
IRrecv irrecv(RECV_PIN);
long unsigned int irCode;
decode_results results;
// Dumps out the decode_results structure.
// Call this after IRrecv::decode()
// void * to work around compiler issue
//void dump(void *v) {
// decode_results *results = (decode_results *)
//////////////////////////////////////////////////////////////
void turn_servo_when_code_recieved( long unsigned int irCode_recieved)
{
switch (irCode_recieved) {
case B17_RIGHT :
turn_servo1_vol_minus() ;
Serial.println("\n-- B17_RIGHT -- turn_servo_A_vol_minus()\n");
break;
case B17_LEFT :
turn_servo1_vol_plus() ;
Serial.println("\n-- B17_LEFTT -- turn_servo_A_vol_plus()\n");
break;
case B17_OK :
current_t=90;
servo1.write(current_t);
Serial.println("\n-- B17_OK -- turn to center, 90 degress\n");
break;
case B17_STAR :
//toggle power button
//turn on/off relay
power_on_off_tag = !power_on_off_tag;
digitalWrite(RELAY_PIN, power_on_off_tag);
Serial.println("\n-- B17_OK -- LG_TV_RED depressed\n");
break;
//////////////////////////////////////////////////////////////////////
}
}
//////////////////////////////////////////////////
void dump(decode_results * results) {
int count = results->rawlen;
if (results->decode_type == UNKNOWN) {
Serial.println("Could not decode message");
}
else {
if (results->decode_type == NEC) {
Serial.print("Decoded NEC: ");
}
else if (results->decode_type == SONY) {
Serial.print("Decoded SONY: ");
}
else if (results->decode_type == RC5) {
Serial.print("Decoded RC5: ");
}
else if (results->decode_type == RC6) {
Serial.print("Decoded RC6: ");
}
Serial.print(results->value, HEX);
turn_servo_when_code_recieved(results->value);
Serial.print(" (");
Serial.print(results->bits, DEC);
Serial.println(" bits)");
}
Serial.print("Raw (");
Serial.print(count, DEC);
Serial.print("): ");
for (int i = 0; i < count; i++) {
if ((i % 2) == 1) {
Serial.print(results->rawbuf[i]*USECPERTICK, DEC);
}
else {
Serial.print(-(int)results->rawbuf[i]*USECPERTICK, DEC);
}
Serial.print(" ");
}
Serial.println("");
}
//////sssssssssssssssssssssssssssssssssssssssssssssssss
void setup()
{ pinMode(RELAY_PIN, OUTPUT);
pinMode(13, OUTPUT);
Serial.begin(9600);
irrecv.enableIRIn(); // Start the receiver
servo1.attach(servoPin1);
// Make servo go to 0 degrees
servo1.write(servo_t_neutral); //%a neutal position for vol
power_on_off_tag = 1; //init value
}
int on = 0;
unsigned long last = millis();
///// LLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLLL
void loop() {
if (irrecv.decode(&results)) {
// If it's been at least 1/4 second since the last
// IR received, toggle the relay
if (millis() - last > REC_DELAY)
{
on = !on;
//digitalWrite(RELAY_PIN, on ? HIGH : LOW);
//digitalWrite(13, on ? HIGH : LOW);
dump(&results); // this is to send the recived code to the TV
}
last = millis();
irrecv.resume(); // Receive the next value
}
// if (digitalRead(one_step_button) == LOW)
// { turn_servo_A();
// }
}
/// ++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
void turn_servo1_vol_minus() {
int t;
for (t = current_t; t < current_t + 10; t++) //dir depend on var. resistor truning angle
{
if (t >= 180 )
{
t = 180;
break;
}
servo1.write(t);
delay(10);
Serial.print("\nt======================\n");
Serial.print(t);
Serial.print("\nt======================\n");
}
current_t = t;
}
///// ----------------------------------------------------------------
void turn_servo1_vol_plus() {
int t;
for (t = current_t; t > current_t - 10 ; t--) //dir depend on var. resistor truning angle
{
if (t < 1 )
{
t = 1;
break;
}
servo1.write(t);
delay(10);
Serial.print("\nt======================\n");
Serial.print(t);
Serial.print("\nt======================\n");
}
current_t = t;
}
Stem2: Arduino experiments v_2a.(220210a)
97
97
Arduino
Uno, or
Arduino-Nano
Processor:ATmega328
(choose old bootloader)
Infrared light
Pin11
GND
Vcc (5V)
or
IR receiver module
KY-022
Out Vcc, GND
B17 remote controller
Arrow left = vol. minus
Arrow right = vol. plus
OK = vol. central
# Hash =power on/off
Servo1
Pin9
Pin5
The servo motor pulls the string attached to the switch of the fan.
Relay (s)
pin4

## Slide 98: Tooth brush timer (230615)
Arduino A0 Obstcale senor
GPIO2 LED_A
GPIO3 LED_B
GPIO4 LED_C
GPIO5 LED_
When the tooth brush is there, the LED are off. When the tooth brush is away it starts to count.

## Slide 99: Tooth brush timer (230615)
// 2023.6.15 khw
// after switched, on when the toothbrush in cradle nothing happen
// when the tooth brush is removed, 4 LEDS are on, one will switch off for an interval of 30seconds
// until all are off, then all 4 will flash for 20 seconds.
//Whenever the brush is in the cradle, LEDs will flash for a while and then off.
// the setup function runs once when you press reset or power the board
int LED_A = 2;
int LED_B = 3;
int LED_C = 4;
int LED_D = 5;
int In1 = A0;
//analogRead(In1) > 128) // brush is away;analogRead(In1) < 128) // brush is in cradle
void setup() {
Serial.begin(115200); // open the serial port at 9600 bps:
// initialize digital pin LED_BUILTIN as an output.
pinMode(LED_A, OUTPUT);
pinMode(LED_B, OUTPUT);
pinMode(LED_C, OUTPUT);
pinMode(LED_D, OUTPUT);
pinMode(In1, INPUT);
}
void delay2(int time) { //one unit is 1/10 secs
int j;
for (j = 1; j < time; j++) {
delay(100); //100 is 1/10 second is ok
//analogRead(In1) > 128) // brush is away;analogRead(In1) < 128) // brush is in cradle
if (analogRead(In1) < 128) { //in cradle
Serial.print(j);
Serial.print('\n');
break;
}
}
}
// the loop function runs over and over again forever
int i = 1;
void loop() {
digitalWrite(LED_A, LOW); // turn the LED off by making the voltage LOW
digitalWrite(LED_B, LOW); // turn the LED off by making the voltage LOW
digitalWrite(LED_C, LOW); // turn the LED off by making the voltage LOW
digitalWrite(LED_D, LOW); // turn the LED off by making the voltage LOW
if (analogRead(In1) > 128) { //analogRead(In1) > 128) means brush is away
run_counting();
}
/*
digitalWrite(LED_A, LOW); // turn the LED off by making the voltage LOW
digitalWrite(LED_B, LOW); // turn the LED off by making the voltage LOW
digitalWrite(LED_C, LOW); // turn the LED off by making the voltage LOW
digitalWrite(LED_D, LOW); // turn the LED off by making the voltage LOW
for (;;); //%stop for ever
*/
}
void run_counting() {
for (i = 1; i <= 20; i++) {
if (i <= 4) {
if (i == 1) {
digitalWrite(LED_A, HIGH); // turn the LED on (HIGH is the voltage level)
digitalWrite(LED_B, HIGH); // turn the LED on (HIGH is the voltage level)
digitalWrite(LED_C, HIGH); // turn the LED on (HIGH is the voltage level)
digitalWrite(LED_D, HIGH); // turn the LED on (HIGH is the voltage level)
delay2(100); // wait for extra 10 seconds for the first session , fof adding tooth paste
}
if (i == 2) { //digitalWrite(LED_A, HIGH); // turn the LED on (HIGH is the voltage level)
digitalWrite(LED_B, HIGH); // turn the LED on (HIGH is the voltage level)
digitalWrite(LED_C, HIGH); // turn the LED on (HIGH is the voltage level)
digitalWrite(LED_D, HIGH); // turn the LED on (HIGH is the voltage level)
}
if (i == 3) { //digitalWrite(LED_A, HIGH); // turn the LED on (HIGH is the voltage level)
//digitalWrite(LED_B, HIGH); // turn the LED on (HIGH is the voltage level)
digitalWrite(LED_C, HIGH); // turn the LED on (HIGH is the voltage level)
digitalWrite(LED_D, HIGH); // turn the LED on (HIGH is the voltage level)
}
if (i == 4) { //digitalWrite(LED_A, HIGH); // turn the LED on (HIGH is the voltage level)
//digitalWrite(LED_B, HIGH); // turn the LED on (HIGH is the voltage level)
//digitalWrite(LED_C, HIGH); // turn the LED on (HIGH is the voltage level)
digitalWrite(LED_D, HIGH); // turn the LED on (HIGH is the voltage level)
}
delay2(300); // wait for 30 seconds for each one of the 4 sessions
//turn off all LEDs
digitalWrite(LED_A, LOW); // turn the LED off by making the voltage LOW
digitalWrite(LED_B, LOW); // turn the LED off by making the voltage LOW
digitalWrite(LED_C, LOW); // turn the LED off by making the voltage LOW
digitalWrite(LED_D, LOW); // turn the LED off by making the voltage LOW
}
// i more than 4, couting finishes
if (i > 4) // % all flashing
{
digitalWrite(LED_A, LOW); // turn the LED off by making the voltage LOW
digitalWrite(LED_B, LOW); // turn the LED off by making the voltage LOW
digitalWrite(LED_C, LOW); // turn the LED off by making the voltage LOW
digitalWrite(LED_D, LOW); // turn the LED off by making the voltage LOW
delay2(10);
digitalWrite(LED_A, HIGH); // turn the LED on (HIGH is the voltage level)
digitalWrite(LED_B, HIGH); // turn the LED on (HIGH is the voltage level)
digitalWrite(LED_C, HIGH); // turn the LED on (HIGH is the voltage level)
digitalWrite(LED_D, HIGH); // turn the LED on (HIGH is the voltage level)
delay2(10);
}
}
}

## Slide 100: Amplifier rc controller relay interface (Uno, don’t use nano, the servo draws large current , it ,may will damage the small nano)
// for RC -amp controller , relayt interface, this is to tune on the amplfier av716
//2022.2.10
#include <Servo.h>
int servoPin = 3; // Declare the Servo pin
int input_pin = 5; // from RC controller replay output, (ON+5V --> input_pint), GND--> arduino_uno_ground
// becareful: nano may not haev enough power for servo, it may dmage the nano if connected directly.
int delay_step = 10;
// Create a servo object
Servo Servo1;
void setup() {
pinMode(input_pin, INPUT);
Servo1.attach(servoPin);
// Make servo go to 0 degrees
Servo1.write(0);
delay(1000);
}
void rotate_servo()
{
// Make servo go to 180 degrees
// servo.write(t); delay(delay_step);
for (int t = 0; t < 180; t++)
{
Servo1.write(t); delay(delay_step);
}
//delay(1000);
for (int t = 180; t > 0; t--)
{
Servo1.write(t); delay(delay_step);
}
delay(1000);
}
void loop() {
//////////////////////////////////////////////////
if (digitalRead(input_pin) == HIGH)
{
//delay(10);
delay(delay_step);
if (digitalRead(input_pin) == LOW)
{ rotate_servo();
}
}
//////////////////////////////////////////////////
if (digitalRead(input_pin) == LOW)
{
// delay(10);
delay(delay_step);
if (digitalRead(input_pin) == HIGH)
{ rotate_servo();
}
}
}
https://item.taobao.com/item.htm?spm=a1z09.2.0.0.49bd2e8dl0GBJP&id=535402623392&_u=a2qidpvo6585

## Slide 101: Using Wifi based Arduino Uno d1 mini
Reference:
原廠技術文件說明 https://www.wemos.cc/product/d1.html
Arduino 安裝說明 https://www.wemos.cc/tutorial/get-started-arduino.html
NodeMCU 安裝說明 https://www.wemos.cc/tutorial/get-started-nodemcu.html
教學 http://www.instructables.com/id/Programming-the-WeMos-Using-Arduino-SoftwareIDE/
相關入門程式開發與說明 https://github.com/wemos
Installation:
  https://sites.google.com/site/wenyumaker/10-esp8266/02memos-d1?tmpl=%2Fsystem%2Fapp%2Ftemplates%2Fprint%2F&showPrintDialog=1
  https://arduino-esp8266.readthedocs.io/en/latest/esp8266wifi/readme.html
Example:
  https://makersportal.com/blog/2019/6/12/wemos-d1-mini-esp8266-arduino-wifi-board
For Arduino IDE2 , read the following doc to install drivers for the board
  https://randomnerdtutorials.com/installing-esp8266-nodemcu-arduino-ide-2-0/
  Installing ESP8266 NodeMCU Board in Arduino IDE 2.0 (Windows, Mac OS X, Linux) | Random Nerd Tutorials (install this before using Arduino D1 Wemos board)
  ULR: http://arduino.esp8266.com/stable/package_esp8266com_index.json, https://raw.githubusercontent.com/espressif/arduino-esp32/gh-pages/package_esp32_index.json
  Install esp8266 and NodeMCU Board, NodeMCU 1.0 (ESP-12E Module)

## Slide 102: Arduino_wifi_test1: Testing Arduino D1, Esp8266 board
Run the code in
https://www.instructables.com/Quick-Start-to-Nodemcu-ESP8266-on-Arduino-IDE/
Connect Pin13 of Arduino-esp8266-D1 board to an LED,
Use the serial monitor to find out the IP address of the server
Use a computer browser (http:// 192.168.xx.yy) to control the :LED
Arduino-D1 with
ESp8266
1K
GND
LED
Pin13

## Slide 103: Arduino_wifi_test1: D1 WeMos board wifi. Use web to control LED https://makersportal.com/blog/2019/6/12/wemos-d1-mini-esp8266-arduino-wifi-board
#include <ESP8266WiFi.h>
const char* ssid = "doublebass";
const char* password = "bbc201271";
int ledPin = 13; // GPIO13
WiFiServer server(80);
void setup() {
Serial.begin(115200);
delay(10);
pinMode(ledPin, OUTPUT);
digitalWrite(ledPin, LOW);
// Connect to WiFi network
Serial.println();
Serial.println();
Serial.print("Connecting to ");
Serial.println(ssid);
WiFi.begin(ssid, password);
while (WiFi.status() != WL_CONNECTED) {
delay(500);
Serial.print(".");
}
Serial.println("");
Serial.println("WiFi connected");
// Start the server
server.begin();
Serial.println("Server started");
// Print the IP address
Serial.print("Use this URL to connect: ");
Serial.print("http://");
Serial.print(WiFi.localIP());
Serial.println("/");
}
void loop() {
// Check if a client has connected
WiFiClient client = server.available();
if (!client) {
return;
}
// Wait until the client sends some data
Serial.println("new client");
while(!client.available()){
delay(1);
}
// Read the first line of the request
String request = client.readStringUntil('\r');
Serial.println(request);
client.flush();
// Match the request
int value = LOW;
if (request.indexOf("/LED=ON") != -1) {
digitalWrite(ledPin, HIGH);
value = HIGH;
}
if (request.indexOf("/LED=OFF") != -1) {
digitalWrite(ledPin, LOW);
value = LOW;
}
// Set ledPin according to the request
//digitalWrite(ledPin, value);
// Return the response
client.println("HTTP/1.1 200 OK");
client.println("Content-Type: text/html");
client.println(""); // do not forget this one
client.println("<!DOCTYPE HTML>");
client.println("<html>");
client.print("Led pin is now: ");
if(value == HIGH) {
client.print("On");
} else {
client.print("Off");
}
client.println("<br><br>");
client.println("<a href=\"/LED=ON\"\"><button>Turn On </button></a>");
client.println("<a href=\"/LED=OFF\"\"><button>Turn Off </button></a><br />");
client.println("</html>");
delay(1);
Serial.println("Client disonnected");
Serial.println("");
}

## Slide 104: Arduino_wifi_test2: Arduino D1 esp8266 Read DHT11 sensor, show on webpage (230615) Arduino D1 Pin D5-physical pin (Note: but in program set Pin 14) Because for Wemos D board pins are not mapped as usual
WeMos Arduino-D1 board pins are not mapped as usual
See the following mapping
LED_BUILTIN = blue LED 0 = D3 1 = TX 2 = blue LED 3 = RX 4 = D2 5 = D1 12 = D6 13 = D7 14 = D5 (This our selection for this demo) 15 = D8 16 = D0
https://forum.arduino.cc/t/pinout-of-a-wemos-d1-mini/490765/2
https://microdigisoft.com/dht11-web-server-with-wemos-d1-mini-using-arduino-ide/
Read time update of temperature and humidity
VCC
Ground
Data
Pull up resistor

## Slide 105: Arduino_wifi_test2: Arduino D1 esp8266 . Test of the esp8266 Board (Arduino D1 board) the code tested ok 230615: https://www.instructables.com/Quick-Start-to-Nodemcu-ESP8266-on-Arduino-IDE/
//https://microdigisoft.com/dht11-web-server-with-wemos-d1-mini-using-arduino-ide/
#include <ESP8266WiFi.h>
#include <ESP8266WebServer.h>
#include <DFRobot_DHT11.h>
DFRobot_DHT11 DHT;
#define DHT11_PIN 14
/*Put your SSID & Password*/
const char* ssid = “ddddddddd"; // Enter SSID here
const char* password = "bbbbbbbb"; //Enter Password here
ESP8266WebServer server(80);
int Temperature;
int Humidity;
void setup() {
Serial.begin(115200);
delay(100);
// pinMode(DHTPin, INPUT);
//dht.begin();
DHT.read(DHT11_PIN);
Serial.println("Connecting to ");
Serial.println(ssid);
//connect to your local wi-fi network
WiFi.begin(ssid, password);
//check wi-fi is connected to wi-fi network
while (WiFi.status() != WL_CONNECTED) {
delay(1000);
Serial.print(".");
}
Serial.println("");
Serial.println("WiFi connected..!");
Serial.print("Got IP: ");
Serial.println(WiFi.localIP());
server.on("/", handle_OnConnect);
server.onNotFound(handle_NotFound);
server.begin();
Serial.println("HTTP server started");
}
int i=1;
void loop() {
server.handleClient();
DHT.read(DHT11_PIN);
Serial.print("---- reading sensors now ----- current count = ");
Serial.print(i);
i=i+1;
Serial.print(" seconds");
Temperature = DHT.temperature;
Serial.print('\n');
Serial.print("Temperature = ");
Serial.print(Temperature);
Serial.print('\n');
Humidity = DHT.humidity;
Serial.print("Humidity = ");
Serial.print(Humidity);
Serial.print('\n');
delay(1000);
}
void handle_OnConnect() {
DHT.read(DHT11_PIN);
Temperature = DHT.temperature;
Humidity = DHT.humidity;
server.send(200, "text/html", SendHTML(Temperature, Humidity));
}
void handle_NotFound() {
server.send(404, "text/plain", "Not found");
}
String SendHTML(float Temperaturestat, float Humiditystat) {
String ptr = "<!DOCTYPE html> <html>\n";
ptr += "<head><meta name=\"viewport\" content=\"width=device-width, initial-scale=1.0, user-scalable=no\">\n";
ptr += "<title>ESP8266 with DHT11 Sensor</title>\n";
ptr += "<style>html { font-family: Helvetica; display: inline-block; margin: 0px auto; text-align: center;}\n";
ptr += "body{margin-top: 50px;} h1 {color: #444444;margin: 50px auto 30px;}\n";
ptr += "p {font-size: 24px;color: #444444;margin-bottom: 10px;}\n";
ptr += "</style>\n";
ptr += "</head>\n";
ptr += "<body>\n";
ptr += "<div id=\"webpage\">\n";
ptr += "<h1>Well-Come to MICRODIGISOFT</h1>\n";
ptr += "<h1>ESP8266 with DHT11 sensor </h1>\n";
ptr += "<p>Temperature: ";
ptr += (int)Temperaturestat;
ptr += "&degC</p>"; //ptr += "°C</p>";
ptr += "<p>Humidity: ";
ptr += (int)Humiditystat;
ptr += "%</p>";
ptr += "</div>\n";
ptr += "</body>\n";
ptr += "</html>\n";
return ptr;
}

## Slide 106: Arduino D1 esp8266, code https://microdigisoft.com/dht11-web-server-with-wemos-d1-mini-using-arduino-ide/
//https://microdigisoft.com/dht11-web-server-with-wemos-d1-mini-using-arduino-ide/
#include <ESP8266WiFi.h>
#include <ESP8266WebServer.h>
#include <DFRobot_DHT11.h>
DFRobot_DHT11 DHT;
#define DHT11_PIN 14
/*Put your SSID & Password*/
const char* ssid = “dddddddddddd"; // Enter SSID here
const char* password = “bbbbbbbbbbb”; //Enter Password here
ESP8266WebServer server(80);
float Temperature;
float Humidity;
void setup() {
Serial.begin(115200);
delay(100);
// pinMode(DHTPin, INPUT);
//dht.begin();
DHT.read(DHT11_PIN);
Serial.println("Connecting to ");
Serial.println(ssid);
//connect to your local wi-fi network
WiFi.begin(ssid, password);
//check wi-fi is connected to wi-fi network
while (WiFi.status() != WL_CONNECTED) {
delay(1000);
Serial.print(".");
}
Serial.println("");
Serial.println("WiFi connected..!");
Serial.print("Got IP: ");
Serial.println(WiFi.localIP());
server.on("/", handle_OnConnect);
server.onNotFound(handle_NotFound);
server.begin();
Serial.println("HTTP server started");
}
int i=1;
void loop() {
server.handleClient();
DHT.read(DHT11_PIN);
Serial.print("---- reading sensors now ----- current count = ");
Serial.print(i);
i=i+1;
Serial.print(" seconds");
Temperature = DHT.temperature;
Serial.print('\n');
Serial.print("Temperature ==");
Serial.print(Temperature);
Serial.print('\n');
Humidity = DHT.humidity;
Serial.print("Humidity ==");
Serial.print(Humidity);
Serial.print('\n');
delay(1000);
}
void handle_OnConnect() {
DHT.read(DHT11_PIN);
Temperature = DHT.temperature;
/*
Serial.print('\n');
Serial.print("Temperature : ");
Serial.print(Temperature);
Serial.print('\n');
*/
Humidity = DHT.humidity;
/*
Serial.print('\n');
Serial.print("Humidity : ");
Serial.print(Humidity);
Serial.print('\n');
*/
server.send(200, "text/html", SendHTML(Temperature, Humidity));
}
void handle_NotFound() {
server.send(404, "text/plain", "Not found");
}
String SendHTML(float Temperaturestat, float Humiditystat) {
String ptr = "<!DOCTYPE html> <html>\n";
ptr += "<head><meta name=\"viewport\" content=\"width=device-width, initial-scale=1.0, user-scalable=no\">\n";
ptr += "<title>ESP8266 with DHT11 Sensor</title>\n";
ptr += "<style>html { font-family: Helvetica; display: inline-block; margin: 0px auto; text-align: center;}\n";
ptr += "body{margin-top: 50px;} h1 {color: #444444;margin: 50px auto 30px;}\n";
ptr += "p {font-size: 24px;color: #444444;margin-bottom: 10px;}\n";
ptr += "</style>\n";
ptr += "</head>\n";
ptr += "<body>\n";
ptr += "<div id=\"webpage\">\n";
ptr += "<h1>Well-Come to MICRODIGISOFT</h1>\n";
ptr += "<h1>ESP8266 with DHT11 sensor </h1>\n";
ptr += "<p>Temperature: ";
ptr += (int)Temperaturestat;
ptr += "°C</p>";
ptr += "<p>Humidity: ";
ptr += (int)Humiditystat;
ptr += "%</p>";
ptr += "</div>\n";
ptr += "</body>\n";
ptr += "</html>\n";
return ptr;
}

## Slide 107: Dehumidifier control dehumid1d4.ino, (15 July 2020)
/* dehumid1d4.ino, khwong 2020 July 15, 10:16 servo+light sensor_RTC, 200322, DS3231+LCD+serail-port display
2020 jul 11, dehumidier project, RTC + Servo_light sensor
using DS3231 library, by Andrew Wickert, Eric Ayars, Jean-Claude Wippler version 1.02
installation: //Sketch/inlucde_library/manage librray/type DS3231,
Can try examples : Files/Exaples/DS3231/
Reference :DS3231_test.pde, Eric Ayars, 4/11, Test/demo of read routines for a DS3231 RTC.
Turn on the serial monitor after loading this to check if things are
working as they should.
*/
/*
DHT11--> pin 7 (UNO)
LCR --> pinA0 (UNO analog input)
Arduino Uno (UNO)pin3--> servo
LCD address:0x27 (SCL, SDA) shared bus
RTC DS3231 (SCL, SDA) shared bus
LED-indiciator-pin5---10K_Ohms-->|---GND
*/
//-----DHT11 ---------------------------------------------------------------
/// https://www.circuitbasics.com/how-to-set-up-the-dht11-humidity-sensor-on-an-arduino/
#include <dht.h> //temperature and humdity sensor DHT11 //////
dht DHT;
#define DHT11_PIN 7
#define LED_1 5
//----------------------- SERVO +light sensor LDR -----------------------------
#include <Servo.h>
int analogPin = A0; //for light sensor LDR
int LDR_val = 0;
int servoPin = 4; // Declare the Servo pin
// Create a servo object
Servo Servo1;
//------------------ LCD -----------------------------------------------
//#include <Wire.h>
#include <LiquidCrystal_I2C.h>
LiquidCrystal_I2C lcd(0x27, 16, 2);
// set the LCD address to 0x27 for a 16 chars and 2 line display
//LiquidCrystal_I2C lcd(0x3F,20,2); // set the LCD address to 0x27 for a 16 chars and 2 line display
//LiquidCrystal_I2C lcd(0x3F,16,2); // set the LCD address to 0x27 for a 16 chars and 2 line display
//---------- for RTC ds3231 -------------------------------------
#include <DS3231.h>
#include <Wire.h>
DS3231 Clock;
bool Century = false;
bool h12;
bool PM;
byte ADay, AHour, AMinute, ASecond, ABits;
bool ADy, A12h, Apm;
void setup_RTC_DS3231() {
// Start the I2C interface
Wire.begin();
// Start the serial interface
Serial.begin(9600);
// cooment the folllowing if the RTC chip DS3231 is already setup the correct time
// See http://misclab.umeoce.maine.edu/boss/Arduino/bensguides/DS3231_Arduino_Clock_Instructions.pdf
// Clock.setSecond(30);//Set the second
// Clock.setMinute(31);//Set the minute
// Clock.setHour(8); //Set the hour
// Clock.setDoW(1); //Set the day of the week
// Clock.setDate(13); //Set the date of the month
// Clock.setMonth(7); //Set the month of the year
// Clock.setYear(20); //Set the year (Last two digits of the year)
}
// Time table
int on_off_time[25]; // on off time, 1= on, 0=off, array assignment in setup() not here
void setup()
{
on_off_time[1] = 1; //assignment must bve iun setup not above setup
on_off_time[2] = 1;
on_off_time[3] = 1;
on_off_time[4] = 0;//0;
on_off_time[5] = 0;
on_off_time[6] = 1;
on_off_time[7] = 1;
on_off_time[8] = 1;//0;
on_off_time[9] = 0;
on_off_time[10] = 0;
on_off_time[11] = 1;
on_off_time[12] = 1;//0;
on_off_time[13] = 1;
on_off_time[14] = 0;
on_off_time[15] = 0;
on_off_time[16] = 1; //0;
on_off_time[17] = 1;
on_off_time[18] = 1;
on_off_time[19] = 1;
on_off_time[20] = 0; //0;
on_off_time[21] = 0;
on_off_time[22] = 1; //0;
on_off_time[23] = 1;
on_off_time[24] = 1;
pinMode(LED_1, OUTPUT);
Serial.begin(9600);
// init servo -------------------1---------------------
Servo1.attach(servoPin);
// initialize the lcd ---------2---------------------
lcd.init();
lcd.backlight();
lcd.setCursor(3, 0); //first row: line 0,cursor index 3. first postion is index 0
lcd.print("Hello, world!");
lcd.setCursor(2, 1); //second row : line 1, position index 2
lcd.print("from KH WONG");
delay(500);
lcd.clear ();
//setup RTC -------------------3---------------------
setup_RTC_DS3231();//////////////////
}
//**************************************************************
///////////overall loop /////////////////////////
void loop() {
LDR_val = analogRead(analogPin); // read the input pin
Serial.print("--1. light sensor LDR_val = ");
Serial.println(LDR_val);
Serial.println("");
if (LDR_val < 200)
digitalWrite(LED_1, HIGH);
else
digitalWrite(LED_1, LOW);
// delay(1000);
Serial.print("--2. Clock.getSecond = ");
Serial.println(Clock.getSecond(), DEC);
Serial.println("");
DHT_display_serial_LCD();
Serial.println("............................");
// delay(1000);;
RTC_loop_display();
//read hour to t // read every hour, do something when minute ==00
Serial.print("--4. Clock.getMinute() = ");
Serial.print(Clock.getMinute(), DEC);
Serial.println("");
//***********************************************************************************
// check every hour, if on_time_time ==1 and humidity > 60 //turn on/off dehimdidifier
if (Clock.getMinute() == 0 && Clock.getSecond() == 00 && on_off_time == 1 && DHT.temperature > 65 )
//if ( Clock.getSecond() <= 10 ) //turn on/off dehimdidifier //??????????
{ turn_on_dehumidifier();
delay (12000);// make sure 12 seconds have passed, becuase only turn on/off hourly
}
else
{ turn_off_dehumidifier();
delay (1200);// make sure 12 seconds have passed, becuase only turn on/off hourly
}
}
//========================================================================
void turn_on_dehumidifier()
{
if (LDR_val < 200 ) //check the LED, if LDR_val is lower than 200, it is on
{} // The dehumidifier is already on, so do thing
else // it is now on, so press once to tturn off the dehumidifier
{ Servo1.write(180);
delay(1000);
Servo1.write(0);
delay(1000);
Servo1.write(180);
delay(1000);
}
}
//========================================================================
void turn_off_dehumidifier()
{
if (LDR_val >= 200 ) //check the LED, if LDR_val is higher than 200, it is off
{} // The dehumidifier is already off, so do thing
else // it is now off, so press once to turn on the dehumidifier
{ Servo1.write(180);
delay(1000);
Servo1.write(0);
delay(1000);
Servo1.write(180);
delay(1000);
}
}
//////////////////////////////////////////////////////
void DHT_display_serial_LCD()
{
int chk = DHT.read11(DHT11_PIN);
/// serial display
Serial.print("--3a. Temperature = ");
Serial.println(DHT.temperature);
Serial.print("--3b. Humidity = ");
Serial.println(DHT.humidity);
// delay(1000);
//LCD display
lcd.setCursor(9, 1);
lcd.print("T");
lcd.setCursor(10, 1);
lcd.print(DHT.temperature);
//--------------------------------
lcd.setCursor(13, 1);
lcd.print("H");
lcd.setCursor(14, 1);
lcd.print(DHT.humidity);
}
void RTC_loop_display() {
// send what's going on to the serial monitor.
// Start with the year
int serial_display_tag = 1; ///1 for on, 0 for off
if (serial_display_tag == 1) Serial.print("2");
lcd.setCursor(0, 0); lcd.print("2");
if (Century) { // Won't need this for 89 years.
if (serial_display_tag == 1) Serial.print("1");
lcd.setCursor(1, 0); lcd.print("1");
} else {
if (serial_display_tag == 1) Serial.print("0");
lcd.setCursor(1, 0); lcd.print("0");
}
if (serial_display_tag == 1) Serial.print(Clock.getYear(), DEC);
lcd.print(Clock.getYear()); lcd.print(Clock.getYear());
if (serial_display_tag == 1) Serial.print(' ');
lcd.setCursor(4, 0); lcd.print("-");
// then the month
if (serial_display_tag == 1)Serial.print(Clock.getMonth(Century), DEC);
lcd.setCursor(5, 0);
switch (Clock.getMonth(Century)) {
case 1: lcd.print("Jan"); break;
case 2: lcd.print("Feb"); break;
case 3: lcd.print("Mar"); break;
case 4: lcd.print("Apr"); break;
case 5: lcd.print("May"); break;
case 6: lcd.print("Jun"); break;
case 7: lcd.print("Jul"); break;
case 8: lcd.print("Aug"); break;
case 9: lcd.print("Sept"); break;
case 10: lcd.print("Oct"); break;
case 11: lcd.print("Nov"); break;
case 12: lcd.print("Dec"); break;
default: lcd.print("???"); break;
}
if (serial_display_tag == 1) Serial.print(' ');
lcd.setCursor(8, 0); lcd.print("-");
// then the date
if (serial_display_tag == 1) Serial.print(Clock.getDate(), DEC);
lcd.setCursor(9, 0); lcd.print(Clock.getDate());
if (serial_display_tag == 1) Serial.print(' ');
lcd.setCursor(11, 0); lcd.print(",");
// and the day of the week
if (serial_display_tag == 1) Serial.print(Clock.getDoW(), DEC);
lcd.setCursor(12, 0);
switch (Clock.getDoW()) {
case 1: lcd.print("Mon"); break;
case 2: lcd.print("Tue"); break;
case 3: lcd.print("Wed"); break;
case 4: lcd.print("Thu"); break;
case 5: lcd.print("Fri"); break;
case 6: lcd.print("Sat"); break;
case 7: lcd.print("Sun"); break;
default: lcd.print("???"); break;
}
if (serial_display_tag == 1) Serial.print(' ');
// Finally the hour, minute, and second
if (serial_display_tag == 1) Serial.print(Clock.getHour(h12, PM), DEC);
lcd.setCursor(0, 1); lcd.print(Clock.getHour(h12, PM));
if (serial_display_tag == 1) Serial.print(' ');
lcd.setCursor(2, 1); lcd.print(":");
if (serial_display_tag == 1) Serial.print(Clock.getMinute(), DEC);
lcd.setCursor(3, 1); lcd.print(Clock.getMinute());
if (serial_display_tag == 1) Serial.print(' ');
lcd.setCursor(5, 1); lcd.print(":");
if (serial_display_tag == 1) Serial.print(Clock.getSecond(), DEC);
lcd.setCursor(6, 1); lcd.print(Clock.getSecond(), DEC);
// Add AM/PM indicator
if (h12) {
if (PM) {
if (serial_display_tag == 1) Serial.print(" PM ");
} else {
if (serial_display_tag == 1) Serial.print(" AM ");
}
} else {
if (serial_display_tag == 1) Serial.print(" 24h ");
}
// Display the temperature
if (serial_display_tag == 1) Serial.print("T=");
if (serial_display_tag == 1) Serial.print(Clock.getTemperature(), 2);
// Tell whether the time is (likely to be) LDR_valid
if (Clock.oscillatorCheck()) {
if (serial_display_tag == 1) Serial.print(" O+");
} else {
if (serial_display_tag == 1) Serial.print(" O-");
}
// Indicate whether an alarm went off
if (Clock.checkIfAlarm(1)) {
if (serial_display_tag == 1) Serial.print(" A1!");
}
if (Clock.checkIfAlarm(2)) {
if (serial_display_tag == 1) Serial.print(" A2!");
}
// New line on display
if (serial_display_tag == 1) Serial.print('\n');
// Display Alarm 1 information
if (serial_display_tag == 1) Serial.print("Alarm 1: ");
Clock.getA1Time(ADay, AHour, AMinute, ASecond, ABits, ADy, A12h, Apm);
if (serial_display_tag == 1) Serial.print(ADay, DEC);
if (ADy) {
if (serial_display_tag == 1) Serial.print(" DoW");
} else {
if (serial_display_tag == 1) Serial.print(" Date");
}
if (serial_display_tag == 1) Serial.print(' ');
if (serial_display_tag == 1) Serial.print(AHour, DEC);
if (serial_display_tag == 1) Serial.print(' ');
if (serial_display_tag == 1) Serial.print(AMinute, DEC);
if (serial_display_tag == 1) Serial.print(' ');
if (serial_display_tag == 1) Serial.print(ASecond, DEC);
if (serial_display_tag == 1) Serial.print(' ');
if (A12h) {
if (Apm) {
if (serial_display_tag == 1) Serial.print('pm ');
} else {
if (serial_display_tag == 1) Serial.print('am ');
}
}
if (Clock.checkAlarmEnabled(1)) {
if (serial_display_tag == 1) Serial.print("enabled");
}
if (serial_display_tag == 1) Serial.print('\n');
// Display Alarm 2 information
if (serial_display_tag == 1) Serial.print("Alarm 2: ");
Clock.getA2Time(ADay, AHour, AMinute, ABits, ADy, A12h, Apm);
if (serial_display_tag == 1) Serial.print(ADay, DEC);
if (ADy) {
if (serial_display_tag == 1) Serial.print(" DoW");
} else {
if (serial_display_tag == 1) Serial.print(" Date");
}
if (serial_display_tag == 1) Serial.print(' ');
if (serial_display_tag == 1) Serial.print(AHour, DEC);
if (serial_display_tag == 1) Serial.print(' ');
if (serial_display_tag == 1) Serial.print(AMinute, DEC);
if (serial_display_tag == 1) Serial.print(' ');
if (A12h) {
if (Apm) {
if (serial_display_tag == 1) Serial.print('pm');
} else {
if (serial_display_tag == 1) Serial.print('am');
}
}
if (Clock.checkAlarmEnabled(2)) {
if (serial_display_tag == 1) Serial.print("enabled");
}
// display alarm bits
if (serial_display_tag == 1) Serial.print('\nAlarm bits: ');
if (serial_display_tag == 1) Serial.print(ABits, BIN);
if (serial_display_tag == 1) Serial.print('\n');
if (serial_display_tag == 1) Serial.print('\n');
//delay(1000);
}

## Slide 108: Dehumidifier control with lcd2x16 (working simplified approach) // 2022.3.22b dehumid1d6.ino,
/* 2022.3.22b , dehumid1d6.ino, khwong 2020 July 15, 10:16 servo+light sensor_RTC, 200322, DS3231+LCD+serail-port display
2020 jul 11, dehumidier project, RTC + Servo_light sensor
using DS3231 library, by Andrew Wickert, Eric Ayars, Jean-Claude Wippler version 1.02
installation: //Sketch/inlucde_library/manage librray/type DS3231,
Can try examples : Files/Exaples/DS3231/
Reference :DS3231_test.pde, Eric Ayars, 4/11, Test/demo of read routines for a DS3231 RTC.
Turn on the serial monitor after loading this to check if things are
working as they should.
*/
/*
DHT11--> pin 7 (UNO)
LCR --> pinA0 (UNO analog input)
Arduino Uno (UNO)pin3--> servo
LCD address:0x27 (SCL, SDA) shared bus
RTC DS3231 (SCL, SDA) shared bus
LED-indiciator-pin5---10K_Ohms-->|---GND
*/
//-----DHT11 ---------------------------------------------------------------
/// https://www.circuitbasics.com/how-to-set-up-the-dht11-humidity-sensor-on-an-arduino/
#include <dht.h> //temperature and humdity sensor DHT11 //////
dht DHT;
#define DHT11_PIN 7
#define LED_1 5
//----------------------- SERVO +light sensor LDR -----------------------------
#include <Servo.h>
int analogPin = A0; //for light sensor LDR
int LDR_val = 0;
int servoPin = 4; // Declare the Servo pin
// Create a servo object
Servo Servo1;
//------------------ LCD -----------------------------------------------
//#include <Wire.h>
#include <LiquidCrystal_I2C.h>
LiquidCrystal_I2C lcd(0x27, 16, 2);
// set the LCD address to 0x27 for a 16 chars and 2 line display
//LiquidCrystal_I2C lcd(0x3F,20,2); // set the LCD address to 0x27 for a 16 chars and 2 line display
//LiquidCrystal_I2C lcd(0x3F,16,2); // set the LCD address to 0x27 for a 16 chars and 2 line display
//---------- for RTC ds3231 -------------------------------------
#include <DS3231.h>
#include <Wire.h>
DS3231 Clock;
bool Century = false;
bool h12;
bool PM;
byte ADay, AHour, AMinute, ASecond, ABits;
bool ADy, A12h, Apm;
void setup_RTC_DS3231() {
// Start the I2C interface
Wire.begin();
// Start the serial interface
Serial.begin(9600);
// comment the folllowing if the RTC chip DS3231 is already setup the correct time
// See http://misclab.umeoce.maine.edu/boss/Arduino/bensguides/DS3231_Arduino_Clock_Instructions.pdf
// Clock.setSecond(00);//Set the second
// Clock.setMinute(04);//Set the minute
// Clock.setHour(11); //Set the hour
// Clock.setDoW(7); //Set the day of the week
// Clock.setDate(20); //Set the date of the month
// Clock.setMonth(3); //Set the month of the year
// Clock.setYear(22); //Set the year (Last two digits of the year)
}
// Time table
//int on_off_time[25]; // on off time, 1= on, 0=off, array assignment in setup() not here
void setup()
{
pinMode(LED_1, OUTPUT);
Serial.begin(9600);
// init servo -------------------1---------------------
Servo1.attach(servoPin);
// initialize the lcd ---------2---------------------
lcd.init();
lcd.backlight();
lcd.setCursor(2, 0); //first row: line 0,cursor index 3. first postion is index 0
lcd.print("Ver. 22.3.22b");
lcd.setCursor(2, 1); //second row : line 1, position index 2
lcd.print("by: KH WONG");
delay(1000);
lcd.clear ();
pinMode(8, INPUT_PULLUP); //testing input , press once servo toggle
//setup RTC -------------------3---------------------
setup_RTC_DS3231();//////////////////
Servo1.write(180); // reset to off position, jus tomake sure
}
//**************************************************************
///////////overall loop /////////////////////////
//int hour_counter = 0;
int old_hour, hour;
void loop() {
LDR_val = analogRead(analogPin); // read the input pin
// Serial.print("--1. light sensor LDR_val = ");
// Serial.println(LDR_val);
// Serial.println("");
// if (LDR_val < 200)
// digitalWrite(LED_1, HIGH);
// else
// digitalWrite(LED_1, LOW);
// delay(1000);
DHT_display_serial_LCD();
//Serial.println("............................");
// delay(1000);;
RTC_loop_display();
hour = Clock.getHour(h12, PM); // current hour
Serial.print("\n"); Serial.print("oldhour=");
Serial.print(old_hour);
Serial.print("\n");
Serial.print("==========================================");
Serial.print("hour=");
Serial.print(hour);
Serial.print("\n");
Serial.print("\n");
Serial.print("\n");
////////////////////////////////////////////////////////////////////////////////////////
int switch_time[] = { 0, 4, 8, 12, 16, 20}; //this list starts from 1 not 0,the array elements are indexed from 0
if ((switch_time[0] <= hour && hour < switch_time[1]) ||
(switch_time[2] <= hour && hour < switch_time[3]) ||
(switch_time[4] <= hour && hour < switch_time[5]) )
{toggle_led_1();
//digitalWrite(LED_1, HIGH);//.turn on led if it is on time
}
else {
digitalWrite(LED_1, LOW);//.turn off led if it is off time
}
////////////////////////////////////////////////////////////////////////////////////////////////////////
if ((old_hour == 23 && hour == switch_time[0]) || //
(old_hour == switch_time[1] - 1 && hour == switch_time[1]) ||
(old_hour == switch_time[2] - 1 && hour == switch_time[2]) ||
(old_hour == switch_time[3] - 1 && hour == switch_time[3]) ||
(old_hour == switch_time[4] - 1 && hour == switch_time[4]) ||
(old_hour == switch_time[5] - 1 && hour == switch_time[5]) )
{
toggle_servo() ;
}
old_hour = hour;
///////////testing switch (yellow reset switch, pressed once to toggle servo///
if (digitalRead(8) == LOW) {//it is normally HIGH, when pressed it is LOW
toggle_servo() ;
Serial.print("digitalRead(8) == LOW \n ");
}
delay(100);
//toggle_led_1();
}
//////////////////////////////////////////////////////////////////
byte led_count;
void toggle_led_1()
{ led_count++;
if ((led_count %2)==1){
digitalWrite(LED_1, HIGH);//.turn on led if it is on time
}
else {
digitalWrite(LED_1,LOW);//.turn on led if it is on time
}
}
//========================================================================
void toggle_servo() // turn on/off dehumidifier
{
Servo1.write(180);
delay(1000);
Servo1.write(0);
delay(1000);
Servo1.write(180);
delay(1000);
}
//////////////////////////////////////////////////////
void DHT_display_serial_LCD()
{
int chk = DHT.read11(DHT11_PIN);
/// serial display
// Serial.print("--3a. Temperature = ");
// Serial.println(DHT.temperature);
// Serial.print("--3b. Humidity = ");
// Serial.println(DHT.humidity);
// // delay(1000);
//LCD display
lcd.setCursor(8, 1);
lcd.print(" ");
//lcd.setCursor(9, 1);
//lcd.print(DHT.temperature);
print_lcd2x16_2digits(9, 1, DHT.temperature);
lcd.setCursor(11, 1);
lcd.print("C");
//--------------------------------
lcd.setCursor(12, 1);
lcd.print(" ");
//lcd.setCursor(13, 1);
//lcd.print(DHT.humidity);
print_lcd2x16_2digits(13, 1, DHT.humidity);
lcd.setCursor(15, 1);
lcd.print("%");
}
void print_lcd2x16_2digits(int x, int y, int val) {
if (val <= 9) {
lcd.setCursor(x, y);
lcd.print("0");
lcd.setCursor(x + 1, y);
lcd.print(val);
}
else {
lcd.setCursor(x, y);
lcd.print(val);
}
}
void RTC_loop_display() {
// send what's going on to the serial monitor.
// Start with the year
int serial_display_tag = 1; ///1 for on, 0 for off
// if (serial_display_tag == 1)
// { Serial.print("2");
//
// if (Century) { // Won't need this for 89 years.
// if (serial_display_tag == 1) Serial.print("1");
// // lcd.setCursor(1, 0); lcd.print("1");
// } else {
// if (serial_display_tag == 1) Serial.print("0");
// //lcd.setCursor(1, 0); lcd.print("0");
// }
// Serial.print(Clock.getYear(), DEC);
// Serial.print(' ');
// Serial.print(Clock.getMonth(Century), DEC);
// }
lcd.setCursor(0, 0); lcd.print("2");
if (Century) { // Won't need this for 89 years.
// if (serial_display_tag == 1) Serial.print("1");
lcd.setCursor(1, 0); lcd.print("1");
} else {
//if (serial_display_tag == 1) Serial.print("0");
lcd.setCursor(1, 0); lcd.print("0");
}
print_lcd2x16_2digits(2, 0, Clock.getYear());
// Serial.print("=============\n\n");
// Serial.print(Clock.getYear());
// Serial.print("............\n\n");
// Serial.print("\n\n");
// delay(5000);
// lcd.print(Clock.getYear()); lcd.print(Clock.getYear());
lcd.setCursor(4, 0); lcd.print("-");
// then the month
lcd.setCursor(5, 0);
switch (Clock.getMonth(Century)) {
case 1: lcd.print("Jan"); break;
case 2: lcd.print("Feb"); break;
case 3: lcd.print("Mar"); break;
case 4: lcd.print("Apr"); break;
case 5: lcd.print("May"); break;
case 6: lcd.print("Jun"); break;
case 7: lcd.print("Jul"); break;
case 8: lcd.print("Aug"); break;
case 9: lcd.print("Sept"); break;
case 10: lcd.print("Oct"); break;
case 11: lcd.print("Nov"); break;
case 12: lcd.print("Dec"); break;
default: lcd.print("???"); break;
}
if (serial_display_tag == 1)
{ Serial.print(' ');
Serial.print(Clock.getDate(), DEC);
Serial.print(' ');
Serial.print(Clock.getDoW(), DEC);
}
lcd.setCursor(8, 0); lcd.print("-");
// then the date
//lcd.setCursor(9, 0); lcd.print(Clock.getDate());
print_lcd2x16_2digits(9, 0, Clock.getDate());
lcd.setCursor(11, 0); lcd.print(",");
// and the day of the week
lcd.setCursor(12, 0);
switch (Clock.getDoW()) {
case 1: lcd.print("Mon"); break;
case 2: lcd.print("Tue"); break;
case 3: lcd.print("Wed"); break;
case 4: lcd.print("Thu"); break;
case 5: lcd.print("Fri"); break;
case 6: lcd.print("Sat"); break;
case 7: lcd.print("Sun"); break;
default: lcd.print("???"); break;
}
if (serial_display_tag == 1)
{ Serial.print(' ');
Serial.print(Clock.getHour(h12, PM), DEC);
Serial.print(' ');
Serial.print(Clock.getMinute(), DEC);
Serial.print(' ');
Serial.print(Clock.getSecond(), DEC);
}
print_lcd2x16_2digits(0, 1, Clock.getHour(h12, PM));
lcd.setCursor(2, 1); lcd.print(":");
print_lcd2x16_2digits(3, 1, Clock.getMinute());
lcd.setCursor(5, 1); lcd.print(":");
print_lcd2x16_2digits(6, 1, Clock.getSecond());
// Add AM/PM indicator
if (h12) {
if (PM) {
if (serial_display_tag == 1) Serial.print(" PM ");
} else {
if (serial_display_tag == 1) Serial.print(" AM ");
}
} else {
if (serial_display_tag == 1) Serial.print(" 24h ");
}
// Display the temperature
if (serial_display_tag == 1) Serial.print("T=");
if (serial_display_tag == 1) Serial.print(Clock.getTemperature(), 2);
// Tell whether the time is (likely to be) LDR_valid
if (Clock.oscillatorCheck()) {
if (serial_display_tag == 1) Serial.print(" O+");
} else {
if (serial_display_tag == 1) Serial.print(" O-");
}
delay(100);
}

## Slide 109: Test2.28: touch sensor Adafruit MPR121. https://raw.githubusercontent.com/adafruit/Adafruit_MPR121/master/examples/MPR121test/MPR121test.ino
// https://raw.githubusercontent.com/adafruit/Adafruit_MPR121/master/examples/MPR121test/MPR121test.ino
/********************************************************* MPR121
This is a library for the MPR121 12-channel Capacitive touch sensor
Designed specifically to work with the MPR121 Breakout in the Adafruit shop
----> https://www.adafruit.com/products/
These sensors use I2C communicate, at least 2 pins are required
to interface
Adafruit invests time and resources providing this open source code,
please support Adafruit and open-source hardware by purchasing
products from Adafruit!
Written by Limor Fried/Ladyada for Adafruit Industries.
BSD license, all text above must be included in any redistribution
**********************************************************/
#include <Wire.h>
#include "Adafruit_MPR121.h"
#ifndef _BV
#define _BV(bit) (1 << (bit))
#endif
// You can have up to 4 on one i2c bus but one is enough for testing!
Adafruit_MPR121 cap = Adafruit_MPR121();
// Keeps track of the last pins touched
// so we know when buttons are 'released'
uint16_t lasttouched = 0;
uint16_t currtouched = 0;
void setup() {
Serial.begin(9600);
while (!Serial) { // needed to keep leonardo/micro from starting too fast!
delay(10);
}
Serial.println("Adafruit MPR121 Capacitive Touch sensor test");
// Default address is 0x5A, if tied to 3.3V its 0x5B
// If tied to SDA its 0x5C and if SCL then 0x5D
if (!cap.begin(0x5A)) {
Serial.println("MPR121 not found, check wiring?");
while (1);
}
Serial.println("MPR121 found!");
}
void loop() {
// Get the currently touched pads
currtouched = cap.touched();
for (uint8_t i=0; i<12; i++) {
// it if *is* touched and *wasnt* touched before, alert!
if ((currtouched & _BV(i)) && !(lasttouched & _BV(i)) ) {
Serial.print(i); Serial.println(" touched");
}
// if it *was* touched and now *isnt*, alert!
if (!(currtouched & _BV(i)) && (lasttouched & _BV(i)) ) {
Serial.print(i); Serial.println(" released");
}
}
// reset our state
lasttouched = currtouched;
// comment out this line for detailed data from the sensor!
return;
// debugging info, what
Serial.print("\t\t\t\t\t\t\t\t\t\t\t\t\t 0x"); Serial.println(cap.touched(), HEX);
Serial.print("Filt: ");
for (uint8_t i=0; i<12; i++) {
Serial.print(cap.filteredData(i)); Serial.print("\t");
}
Serial.println();
Serial.print("Base: ");
for (uint8_t i=0; i<12; i++) {
Serial.print(cap.baselineData(i)); Serial.print("\t");
}
Serial.println();
// put a delay so it isn't overwhelming
delay(100);
}
Arduino
MPR121
SCL
SDA
5V GND

## Slide 110: Test2.29 Pressure sensor MPS20N0040D
https://cdn.sparkfun.com/assets/home_page_posts/1/9/0/2/Pressure_Sensor.pdf
Pressure Sensor MPS20N0040D-S Introduction Pressure range :0-5 .8 psi (40kpa); Product Features: Solid, MEMS technology, high reliability
Vs
https://www.nxp.com/docs/en/data-sheet/MPX5010.pdf
Max 4-Kpa
https://cdn.sparkfun.com/assets/home_page_posts/1/9/0/2/Pressure_Sensor.pdf
Top-down-view

## Slide 111: Circuit for MPS20N0040D +opamp http://langster1980.blogspot.com/2014/11/how-to-use-pressure-sensor-with.html https://www.electroschematics.com/pressure-sensor-guide/
Use opamp-CA3410 (or uA741)
Output (1) connects to - In on the Opam
+ Input (2) connects to +5 Vdc
+ Output (3) connects to + In on the Opamp
Output (4) does not connect to anything!
- Input (5) connects to 0 Vdc
- Output (6) connects to - In on the Opamp
0Volt
5Volt
Pin
1
2
3
Pin
6
5
4
2
3
6
4
7

## Slide 112: https://www.faranux.com/product/mps20n0040d-d-sphygmomanometer-pressure-sensor-0-40kpa-dip-6-for-arduino/
LM358
Op-Amp
MPS20N0040D-D
8
1
10K
10K
47K
47K
out
or
7
6
4
2
3

## Slide 113: https://www.electroschematics.com/pressure-sensor-guide/

## Slide 114: https://forum.hobbycomponents.com/viewtopic.php?t=1524 HX711 MPS20N0040D
v
https://www.instructables.com/id/How-to-Interface-HX711-Balance-Module-With-Load-Ce/

## Slide 115: Computer controlled PLARAIL (by Tomy ) using Arduino-Uno Rail mechanical switch is controlled by a small servo motor. Car passing sensor used is the tracking sensor KY033
#include <Servo.h>
int servoPin = 3; // Declare the Servo pin
int Sensor = 10; // Declaration of the sensor input pin
int tag = 0;
// Create a servo object
Servo Servo1;
void setup() {
Serial.begin(9600); // Initialization serial output
Servo1.attach(servoPin);
pinMode (Sensor, INPUT) ; // Initialization sensor pin
}
void loop() {
bool val = digitalRead (Sensor) ; // The current signal of the sensor will be read
if (val == HIGH) // If a signal is detected the LED will light up.
{
Serial.println("yes------LineTracker is on the line");
// Make servo go to 0 degrees
//toggle rail selection
if (tag == 1)
{
Servo1.write(0);
tag = 0;
delay(100);
}
else {
Servo1.write(70);
tag = 1;
delay(100);
}
delay(5000); //for slower trains--c571
}
//delay(3000);
}
Tracking sensor:
https://sensorkit.en.joy-it.net/index.php?title=KY-033_Tracking_sensor_module
Video show, https://youtu.be/QrAWuykn1QA

## Slide 116: Appendix

## Slide 117: Test2.25) Micro-SD CARD write/read Library manager: SD build-IN by Arduino , SparkFun version v.1.2.3 using #include <SPI.h> and #include <SD.h>
https://create.arduino.cc/projecthub/electropeak/sd-card-module-with-arduino-how-to-read-write-data-37f390
GND
VCC
MISO
MOSI
SCK
CS
Micro-SD card reader

## Slide 118: Test program for test.2.25 micro-sdcard write/read Library manager: SD build-IN by Arduino , SparkFun version v.1.2.3 using #include <SPI.h> and #include <SD.h>
//micro-sdcard_write.ino
#include <SPI.h>
#include <SD.h>
File myFile;
void setup() {
// Open serial communications and wait for port to open:
Serial.begin(9600);
while (!Serial) {
; // wait for serial port to connect. Needed for native USB port only
}
Serial.print("Initializing SD card...");
if (!SD.begin(10)) {
Serial.println("initialization failed!");
while (1);
}
Serial.println("initialization done.");
// open the file. note that only one file can be open at a time,
// so you have to close this one before opening another.
myFile = SD.open("test.txt", FILE_WRITE);
// if the file opened okay, write to it:
if (myFile) {
Serial.print("Writing to test.txt...");
myFile.println("This is a test file :)");
myFile.println("testing 1, 2, 3.");
for (int i = 0; i < 30; i++) {
myFile.println(i);
}
// close the file:
myFile.close();
Serial.println("done.");
} else {
// if the file didn't open, print an error:
Serial.println("error opening test.txt");
}
}
void loop() {
// nothing happens after setup
}
// micro-sdcard_read.ino
#include <SPI.h>
#include <SD.h>
File myFile;
void setup() {
// Open serial communications and wait for port to open:
Serial.begin(9600);
while (!Serial) {
; // wait for serial port to connect. Needed for native USB port only
}
Serial.print("Initializing SD card...");
if (!SD.begin(10)) {
Serial.println("initialization failed!");
while (1);
}
Serial.println("initialization done.");
// open the file for reading:
myFile = SD.open("test.txt");
if (myFile) {
Serial.println("test.txt:");
// read from the file until there's nothing else in it:
while (myFile.available()) {
Serial.write(myFile.read());
}
// close the file:
myFile.close();
} else {
// if the file didn't open, print an error:
Serial.println("error opening test.txt");
}
}
void loop() {
// nothing happens after setup
}

## Slide 119: Other advanced topics
Digital electronics
Sensors
Self balancing robot, PID control
VR hand glove, use of Bluetooth
Projects: ultrasonic scanner
Gyroscope MEMS
Use motor to build a gyroscope for balancing robot
See the next slide for possible projects

## Slide 120: References
Top 10 Best Arduino Projects - Maker Tutor
https://www.youtube.com/watch?v=nfm3qQoZIuo
TOP 10 Arduino Projects Of All Time | 2018
https://www.youtube.com/watch?v=-p_8u_0GNZE
Inside an Autonomous Self Balancing Robot #1 (Tutorial)
https://www.youtube.com/watch?v=s5m-DTn8jyw
7 Pro Arduino Projects with DIY Instructions
https://www.youtube.com/watch?v=XxmD70Wvmdw

## Slide 121: Appendix RC_table.h
/////////////////////2020.7.26/////////////
// DEFINE table1 LGTV
#define LGTV_SOURCE 0x20DFD02F
#define LGTV_SUBTITLE 0x20DF9C63 //20DF9C63
#define LGTV_POWER 0x20DF10EF //on/off
#define LGTV_AV_TV 0x20DFF00F
#define LGTV_NICAM_I_II 0x20DF50AF
#define LGTV_SLEEP 0x20DF708F
#define LGTV_1 0x20DF8877
#define LGTV_2 0x20DF48B7
#define LGTV_3 0x20DFC837
#define LGTV_4 0x20DF28D7
#define LGTV_5 0x20DFA857
#define LGTV_6 0x20DF6897
#define LGTV_7 0x20DFE817
#define LGTV_8 0x20DF18E7
#define LGTV_9 0x20DF9867
#define LGTV_0 0x20DF08F7
#define LGTV_ARROW_UP 0x20DF02FD
#define LGTV_ARROW_DOWN 0x20DF827D
#define LGTV_ARROW_LEFT 0x20DFE01F
#define LGTV_ARROW_RIGHT 0x20DF609F
#define LGTV_OK 0x20DF22DD
#define LGTV_VOL_UP 0x20DF40BF
#define LGTV_VOL_DOWN 0x20DFC03F
#define LGTV_CHAN_UP 0x20DF00FF
#define LGTV_CHAN_DOWN 0x20DF807F
#define LGTV_RED 0x20DF4EB1
#define LGTV_GREEN 0x20DF8E71
#define LGTV_YELLOW 0x20DFC639
#define LGTV_BLUE 0x20DF8679
#define LGTV_REWIND 0x20DFF10E
#define LGTV_PLAY 0x20DF0DF2
#define LGTV_PAUSE 0x20DF5DA2
#define LGTV_FAST_FORWARD 0x20DF718E
#define LGTV_HOME 0x20DF3EC1
#define LGTV_NETFLIX 0x20DF6A95
#define LGTV_MENU 0x20DFC23D
#define LGTV_RETURN 0x20DF14EB
#define LGTV_TOOLS 0x20DFA25D
#define LGTV_EXIT 0x20DFDA25
#define LGTV_GUIDE 0x20DFD52A
#define LGTV_Q_VIEW 0x20DF55AA
///////////// for Black, 17-keys-keypad
//#define B17_01 0xFFA25D
///////////////////////////////////////////////////////
// DEFINE table2 : black 17 keys remote controls:
#define B17_01 0xFFA25D
#define B17_02 0xFF629D
#define B17_03 0xFFE21D
#define B17_04 0xFF22DD
#define B17_05 0xFF02FD
#define B17_06 0xFFC23D
#define B17_07 0xFFE01F
#define B17_08 0xFFA857
#define B17_09 0xFF906F
#define B17_00 0xFF9867
#define B17_STAR 0xFF6897
#define B17_HASH 0xFFB04F
///////////////////////////////////////////////////////
// DEFINE table2 : white 21 keys remote controls:
#define W21_LEFT 0xFF10EF
#define W21_RIGHT 0xFF5AA5
#define W21_UP 0xFF18E7
#define W21_DOWN 0xFF4AB5
#define W21_OK 0xFF38C7
#define W21_CH- 0xFFA25D
#define W21_CH 0xFF629D
#define W21_CH+ 0xFFE21D
#define W21_PREV 0xFF22DD
#define W21_NEXT 0xFF02FD
#define W21_PLAY 0xFFC23D
#define W21_VOL+ 0xFFE01F
#define W21_VOL- 0xFFA857
#define W21_EQ 0xFF906F
#define W21_0 0xFF6897
#define W21_100+ 0xFF9867
#define W21_200+ 0xFFB04F
#define W21_1 0xFF30CF
#define W21_2 0xFF18E7
#define W21_3 0xFF7A85
#define W21_4 0xFF10EF
#define W21_5 0xFF38C7
#define W21_6 0xFF5AA5
#define W21_7 0xFF42BD
#define W21_8 0xFF4AB5
#define W21_9 0xFF52AD
///////////////////////////////////////////////////////
//My_TV_Super= MTS, NEC:
#define MTS_UP 0xFB0058A7
#define MTS_LEFT 0xFB00E21D
#define MTS_RIGHT 0xFB00E01F
#define MTS_DOWN 0xFB0012ED
#define MTS_OK 0xFB00609F
#define MTS_POWER 0xFB0038C7
#define MTS_MTS_VOD 0xFB0020DF
#define MTS_HOME 0xFB0050AF
#define MTS_RETURN 0xFB00926D
#define MTS_INFO 0xFB0018E7
#define MTS_RED 0xFB00807F //MTS_PLAY
#define MTS_GREEN 0xFB00FA05 //MTS_STOP
#define MTS_YELLOW 0xFB009867 //MTS_REW
#define MTS_BLUE 0xFB001AE5 //MTS_FFW
#define MTS_SILENT 0xFB003AC5
#define MTS_BACKSPACE 0xFB0008F7
#define MTS_KEY0 0xFB0030CF
#define MTS_KEY1 0xFB002AD5
#define MTS_KEY2 0xFB006897
#define MTS_KEY3 0xFB00A857
#define MTS_KEY4 0xFB000AF5
#define MTS_KEY5 0xFB0048B7
#define MTS_KEY6 0xFB008877
#define MTS_KEY7 0xFB0032CD
#define MTS_KEY8 0xFB00708F
#define MTS_KEY9 0xFB00B04F

## Slide 122: Raw IR-LED control emitter
A project To control the NAD amplifier
Code: http://www.remotecentral.com/cgi-bin/codes/nad/450/
Connect pin 3(UNO) to an IR-LED through a 50_Ohm resistor.
Installation:
Donald the zip from https://github.com/cyborg5/IRLib2
Use IDE/sketch/include library/add zip library to include that .zip
Run IDE file/example/seed Arduino/send, you will see light from IR led (pin3 with 50_Ohm, long side of led is +ve)
Run example https://wiki.seeedstudio.com/Grove-Infrared_Emitter/
https://github.com/cyborg5/IRLib2/issues/33
https://forum.allaboutcircuits.com/threads/using-arduino-to-control-ir-remote-consumer-electronics.137555/
Can try the following code for sending raw code. May import code from Code: http://www.remotecentral.com/cgi-bin/codes/nad/450/ (codes are in decimal)
+ ve
(long leg)
Pin3(UNO)
http://blog.sparkfuneducation.com/what-is-an-led
50 Ohm
GND
IR emitter
/* rawSend.ino Example sketch for IRLib2
* Illustrates how to send a code Using raw timings which were captured
* from the "rawRecv.ino" sample sketch. Load that sketch and
* capture the values. They will print in the serial monitor. Then you
* cut and paste that output into the appropriate section below.
*/
#include <IRLibSendBase.h> //We need the base code
#include <IRLib_HashRaw.h> //Only use raw sender
IRsendRaw mySender;
void setup() {
Serial.begin(9600);
delay(2000); while (!Serial); //delay for Leonardo
Serial.println(F("Every time you press a key is a serial monitor we will send."));
}
/* Cut and paste the output from "rawRecv.ino" below here. It will
* consist of a #define RAW_DATA_LEN statement and an array definition
* beginning with "uint16_t rawData[RAW_DATA_LEN]= {…" and concludes
* with "…,1000};"
*/
#define RAW_DATA_LEN 68
uint16_t rawData[RAW_DATA_LEN]={
4530, 4514, 562, 1686, 562, 1682, 566, 1682,
562, 590, 534, 590, 534, 590, 534, 590,
534, 590, 534, 1686, 558, 1686, 562, 1686,
562, 590, 534, 590, 534, 590, 530, 594,
530, 594, 530, 590, 534, 1686, 562, 590,
534, 590, 534, 590, 534, 590, 534, 594,
526, 594, 530, 1686, 562, 590, 534, 1690,
558, 1682, 562, 1686, 562, 1686, 562, 1686,
562, 1682, 562, 1000};
/*
* Cut-and-paste into the area above.
*/
void loop() {
if (Serial.read() != -1) {
//send a code every time a character is received from the
// serial port. You could modify this sketch to send when you
// push a button connected to an digital input pin.
mySender.send(rawData,RAW_DATA_LEN,36);//Pass the buffer,length, optionally frequency
Serial.println(F("Sent signal."));
}
}

## Slide 123: Use of LCD12864
https://electropeak.com/learn/interfacing-128x64-graphical-lcd-display-with-arduino/

## Slide 124: LCD12864 demo code
/*
Modified on Dec 2, 2020
Modified by MehranMaleki from Arduino Examples
Home
*/
/*
GraphicsTest.pde
>>> Before compiling: Please remove comment from the constructor of the
>>> connected graphics display (see below).
Universal 8bit Graphics Library, https://github.com/olikraus/u8glib/
Copyright (c) 2012, olikraus@gmail.com
All rights reserved.
Redistribution and use in source and binary forms, with or without modification,
are permitted provided that the following conditions are met:
* Redistributions of source code must retain the above copyright notice, this list
of conditions and the following disclaimer.
* Redistributions in binary form must reproduce the above copyright notice, this
list of conditions and the following disclaimer in the documentation and/or other
materials provided with the distribution.
THIS SOFTWARE IS PROVIDED BY THE COPYRIGHT HOLDERS AND
CONTRIBUTORS "AS IS" AND ANY EXPRESS OR IMPLIED WARRANTIES,
INCLUDING, BUT NOT LIMITED TO, THE IMPLIED WARRANTIES OF
MERCHANTABILITY AND FITNESS FOR A PARTICULAR PURPOSE ARE
DISCLAIMED. IN NO EVENT SHALL THE COPYRIGHT HOLDER OR
CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, INCIDENTAL,
SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES (INCLUDING, BUT
NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE GOODS OR SERVICES;
LOSS OF USE, DATA, OR PROFITS; OR BUSINESS INTERRUPTION) HOWEVER
CAUSED AND ON ANY THEORY OF LIABILITY, WHETHER IN CONTRACT,
STRICT LIABILITY, OR TORT (INCLUDING NEGLIGENCE OR OTHERWISE)
ARISING IN ANY WAY OUT OF THE USE OF THIS SOFTWARE, EVEN IF
ADVISED OF THE POSSIBILITY OF SUCH DAMAGE.
*/
#include "U8glib.h"
// setup u8g object, please remove comment from one of the following constructor calls
// IMPORTANT NOTE: The following list is incomplete. The complete list of supported
// devices with all constructor calls is here: https://github.com/olikraus/u8glib/wiki/device
//U8GLIB_NHD27OLED_BW u8g(13, 11, 10, 9); // SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9
//U8GLIB_NHD27OLED_2X_BW u8g(13, 11, 10, 9); // SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9
//U8GLIB_NHD27OLED_GR u8g(13, 11, 10, 9); // SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9
//U8GLIB_NHD27OLED_2X_GR u8g(13, 11, 10, 9); // SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9
//U8GLIB_NHD31OLED_BW u8g(13, 11, 10, 9); // SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9
//U8GLIB_NHD31OLED_2X_BW u8g(13, 11, 10, 9); // SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9
//U8GLIB_NHD31OLED_GR u8g(13, 11, 10, 9); // SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9
//U8GLIB_NHD31OLED_2X_GR u8g(13, 11, 10, 9); // SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9
//U8GLIB_DOGS102 u8g(13, 11, 10, 9, 8); // SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9
//U8GLIB_DOGM132 u8g(13, 11, 10, 9); // SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9
//U8GLIB_DOGM128 u8g(13, 11, 10, 9); // SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9
//U8GLIB_DOGM128_2X u8g(13, 11, 10, 9); // SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9
U8GLIB_ST7920_128X64_4X u8g(10);
//U8GLIB_ST7920_128X64_1X u8g(8, 9, 10, 11, 4, 5, 6, 7, 18, 17, 16); // 8Bit Com: D0..D7: 8,9,10,11,4,5,6,7 en=18, di=17,rw=16
//U8GLIB_ST7920_128X64_4X u8g(8, 9, 10, 11, 4, 5, 6, 7, 18, 17, 16); // 8Bit Com: D0..D7: 8,9,10,11,4,5,6,7 en=18, di=17,rw=16
//U8GLIB_ST7920_128X64_1X u8g(18, 16, 17); // SPI Com: SCK = en = 18, MOSI = rw = 16, CS = di = 17
//U8GLIB_ST7920_128X64_4X u8g(18, 16, 17); // SPI Com: SCK = en = 18, MOSI = rw = 16, CS = di = 17
//U8GLIB_ST7920_192X32_1X u8g(8, 9, 10, 11, 4, 5, 6, 7, 18, 17, 16); // 8Bit Com: D0..D7: 8,9,10,11,4,5,6,7 en=18, di=17,rw=16
//U8GLIB_ST7920_192X32_4X u8g(8, 9, 10, 11, 4, 5, 6, 7, 18, 17, 16); // 8Bit Com: D0..D7: 8,9,10,11,4,5,6,7 en=18, di=17,rw=16
//U8GLIB_ST7920_192X32_1X u8g(18, 16, 17); // SPI Com: SCK = en = 18, MOSI = rw = 16, CS = di = 17
//U8GLIB_ST7920_192X32_4X u8g(18, 16, 17); // SPI Com: SCK = en = 18, MOSI = rw = 16, CS = di = 17
//U8GLIB_ST7920_192X32_1X u8g(13, 11, 10); // SPI Com: SCK = en = 13, MOSI = rw = 11, CS = di = 10
//U8GLIB_ST7920_192X32_4X u8g(10); // SPI Com: SCK = en = 13, MOSI = rw = 11, CS = di = 10, HW SPI
//U8GLIB_ST7920_202X32_1X u8g(8, 9, 10, 11, 4, 5, 6, 7, 18, 17, 16); // 8Bit Com: D0..D7: 8,9,10,11,4,5,6,7 en=18, di=17,rw=16
//U8GLIB_ST7920_202X32_4X u8g(8, 9, 10, 11, 4, 5, 6, 7, 18, 17, 16); // 8Bit Com: D0..D7: 8,9,10,11,4,5,6,7 en=18, di=17,rw=16
//U8GLIB_ST7920_202X32_1X u8g(18, 16, 17); // SPI Com: SCK = en = 18, MOSI = rw = 16, CS = di = 17
//U8GLIB_ST7920_202X32_4X u8g(18, 16, 17); // SPI Com: SCK = en = 18, MOSI = rw = 16, CS = di = 17
//U8GLIB_LM6059 u8g(13, 11, 10, 9); // SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9
//U8GLIB_LM6063 u8g(13, 11, 10, 9); // SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9
//U8GLIB_DOGXL160_BW u8g(10, 9); // SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9
//U8GLIB_DOGXL160_GR u8g(13, 11, 10, 9); // SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9
//U8GLIB_DOGXL160_2X_BW u8g(13, 11, 10, 9); // SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9
//U8GLIB_DOGXL160_2X_GR u8g(13, 11, 10, 9); // SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9
//U8GLIB_PCD8544 u8g(13, 11, 10, 9, 8); // SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9, Reset = 8
//U8GLIB_PCF8812 u8g(13, 11, 10, 9, 8); // SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9, Reset = 8
//U8GLIB_KS0108_128 u8g(8, 9, 10, 11, 4, 5, 6, 7, 18, 14, 15, 17, 16); // 8Bit Com: D0..D7: 8,9,10,11,4,5,6,7 en=18, cs1=14, cs2=15,di=17,rw=16
//U8GLIB_LC7981_160X80 u8g(8, 9, 10, 11, 4, 5, 6, 7, 18, 14, 15, 17, 16); // 8Bit Com: D0..D7: 8,9,10,11,4,5,6,7 en=18, cs=14 ,di=15,rw=17, reset = 16
//U8GLIB_LC7981_240X64 u8g(8, 9, 10, 11, 4, 5, 6, 7, 18, 14, 15, 17, 16); // 8Bit Com: D0..D7: 8,9,10,11,4,5,6,7 en=18, cs=14 ,di=15,rw=17, reset = 16
//U8GLIB_LC7981_240X128 u8g(8, 9, 10, 11, 4, 5, 6, 7, 18, 14, 15, 17, 16); // 8Bit Com: D0..D7: 8,9,10,11,4,5,6,7 en=18, cs=14 ,di=15,rw=17, reset = 16
//U8GLIB_ILI9325D_320x240 u8g(18,17,19,U8G_PIN_NONE,16 ); // 8Bit Com: D0..D7: 0,1,2,3,4,5,6,7 en=wr=18, cs=17, rs=19, rd=U8G_PIN_NONE, reset = 16
//U8GLIB_SBN1661_122X32 u8g(8,9,10,11,4,5,6,7,14,15, 17, U8G_PIN_NONE, 16); // 8Bit Com: D0..D7: 8,9,10,11,4,5,6,7 cs1=14, cs2=15,di=17,rw=16,reset = 16
//U8GLIB_SSD1306_128X64 u8g(13, 11, 10, 9, 8); // SW SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9
//U8GLIB_SSD1306_128X64 u8g(4, 5, 6, 7); // SW SPI Com: SCK = 4, MOSI = 5, CS = 6, A0 = 7 (new white HalTec OLED)
//U8GLIB_SSD1306_128X64 u8g(10, 9); // HW SPI Com: CS = 10, A0 = 9 (Hardware Pins are SCK = 13 and MOSI = 11)
//U8GLIB_SSD1306_128X64 u8g(U8G_I2C_OPT_NONE|U8G_I2C_OPT_DEV_0); // I2C / TWI
//U8GLIB_SSD1306_128X64 u8g(U8G_I2C_OPT_DEV_0|U8G_I2C_OPT_NO_ACK|U8G_I2C_OPT_FAST); // Fast I2C / TWI
//U8GLIB_SSD1306_128X64 u8g(U8G_I2C_OPT_NO_ACK); // Display which does not send AC
//U8GLIB_SSD1306_ADAFRUIT_128X64 u8g(13, 11, 10, 9); // SW SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9
//U8GLIB_SSD1306_ADAFRUIT_128X64 u8g(10, 9); // HW SPI Com: CS = 10, A0 = 9 (Hardware Pins are SCK = 13 and MOSI = 11)
//U8GLIB_SSD1306_128X32 u8g(13, 11, 10, 9); // SW SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9
//U8GLIB_SSD1306_128X32 u8g(10, 9); // HW SPI Com: CS = 10, A0 = 9 (Hardware Pins are SCK = 13 and MOSI = 11)
//U8GLIB_SSD1306_128X32 u8g(U8G_I2C_OPT_NONE); // I2C / TWI
//U8GLIB_SSD1306_64X48 u8g(13, 11, 10, 9); // SW SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9
//U8GLIB_SSD1306_64X48 u8g(10, 9); // HW SPI Com: CS = 10, A0 = 9 (Hardware Pins are SCK = 13 and MOSI = 11)
//U8GLIB_SSD1306_64X48 u8g(U8G_I2C_OPT_NONE); // I2C / TWI
//U8GLIB_SH1106_128X64 u8g(13, 11, 10, 9); // SW SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9
//U8GLIB_SH1106_128X64 u8g(4, 5, 6, 7); // SW SPI Com: SCK = 4, MOSI = 5, CS = 6, A0 = 7 (new blue HalTec OLED)
//U8GLIB_SH1106_128X64 u8g(U8G_I2C_OPT_NONE); // I2C / TWI
//U8GLIB_SH1106_128X64 u8g(U8G_I2C_OPT_DEV_0|U8G_I2C_OPT_FAST); // Dev 0, Fast I2C / TWI
//U8GLIB_SH1106_128X64 u8g(U8G_I2C_OPT_NO_ACK); // Display which does not send ACK
//U8GLIB_SSD1309_128X64 u8g(13, 11, 10, 9); // SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9
//U8GLIB_SSD1327_96X96_GR u8g(U8G_I2C_OPT_NONE); // I2C
//U8GLIB_SSD1327_96X96_2X_GR u8g(U8G_I2C_OPT_NONE); // I2C
//U8GLIB_UC1611_DOGM240 u8g(U8G_I2C_OPT_NONE); // I2C
//U8GLIB_UC1611_DOGM240 u8g(13, 11, 10, 9); // SW SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9
//U8GLIB_UC1611_DOGM240 u8g(10, 9); // HW SPI Com: CS = 10, A0 = 9 (Hardware Pins are SCK = 13 and MOSI = 11)
//U8GLIB_UC1611_DOGM240 u8g(10, 9); // HW SPI Com: CS = 10, A0 = 9 (Hardware Pins are SCK = 13 and MOSI = 11)
//U8GLIB_UC1611_DOGM240 u8g(8, 9, 10, 11, 4, 5, 6, 7, 18, 3, 17, 16); // 8Bit Com: D0..D7: 8,9,10,11,4,5,6,7 en=18, cs=3, di/a0=17,rw=16
//U8GLIB_UC1611_DOGXL240 u8g(U8G_I2C_OPT_NONE); // I2C
//U8GLIB_UC1611_DOGXL240 u8g(13, 11, 10, 9); // SW SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9
//U8GLIB_UC1611_DOGXL240 u8g(10, 9); // HW SPI Com: CS = 10, A0 = 9 (Hardware Pins are SCK = 13 and MOSI = 11)
//U8GLIB_UC1611_DOGXL240 u8g(8, 9, 10, 11, 4, 5, 6, 7, 18, 3, 17, 16); // 8Bit Com: D0..D7: 8,9,10,11,4,5,6,7 en=18, cs=3, di/a0=17,rw=16
//U8GLIB_NHD_C12864 u8g(13, 11, 10, 9, 8); // SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9, RST = 8
//U8GLIB_NHD_C12832 u8g(13, 11, 10, 9, 8); // SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9, RST = 8
//U8GLIB_LD7032_60x32 u8g(13, 11, 10, 9, 8); // SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9, RST = 8
//U8GLIB_LD7032_60x32 u8g(11, 12, 9, 10, 8); // SPI Com: SCK = 11, MOSI = 12, CS = 9, A0 = 10, RST = 8 (SW SPI Nano Board)
//U8GLIB_UC1608_240X64 u8g(13, 11, 10, 9, 8); // SW SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9, RST = 8
//U8GLIB_UC1608_240X64_2X u8g(13, 11, 10, 9, 8); // SW SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9, RST = 8
//U8GLIB_UC1608_240X64 u8g(10, 9, 8); // HW SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9, RST = 8
//U8GLIB_UC1608_240X64_2X u8g(10, 9, 8); // HW SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9, RST = 8
//U8GLIB_UC1608_240X u8g(13, 11, 10, 9, 8); // SW SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9, RST = 8
//U8GLIB_UC1608_240X64_2X u8g(13, 11, 10, 9, 8); // SW SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9, RST = 8
//U8GLIB_UC1608_240X64 u8g(10, 9, 8); // HW SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9, RST = 8
//U8GLIB_UC1608_240X64_2X u8g(10, 9, 8); // HW SPI Com: SCK = 13, MOSI = 11, CS = 10, A0 = 9, RST = 8
//U8GLIB_T6963_240X128 u8g(8, 9, 10, 11, 4, 5, 6, 7, 14, 15, 17, 18, 16); // 8Bit Com: D0..D7: 8,9,10,11,4,5,6,7, cs=14, a0=15, wr=17, rd=18, reset=16
//U8GLIB_T6963_128X128 u8g(8, 9, 10, 11, 4, 5, 6, 7, 14, 15, 17, 18, 16); // 8Bit Com: D0..D7: 8,9,10,11,4,5,6,7, cs=14, a0=15, wr=17, rd=18, reset=16
//U8GLIB_T6963_240X64 u8g(8, 9, 10, 11, 4, 5, 6, 7, 14, 15, 17, 18, 16); // 8Bit Com: D0..D7: 8,9,10,11,4,5,6,7, cs=14, a0=15, wr=17, rd=18, reset=16
//U8GLIB_T6963_128X64 u8g(8, 9, 10, 11, 4, 5, 6, 7, 14, 15, 17, 18, 16); // 8Bit Com: D0..D7: 8,9,10,11,4,5,6,7, cs=14, a0=15, wr=17, rd=18, reset=16
//U8GLIB_HT1632_24X16 u8g(3, 2, 4); // WR = 3, DATA = 2, CS = 4
//U8GLIB_SSD1351_128X128_332 u8g(13, 11, 8, 9, 7); // Arduino UNO: SW SPI Com: SCK = 13, MOSI = 11, CS = 8, A0 = 9, RESET = 7 (http://electronics.ilsoft.co.uk/ArduinoShield.aspx)
//U8GLIB_SSD1351_128X128_332 u8g(76, 75, 8, 9, 7); // Arduino DUE: SW SPI Com: SCK = 13, MOSI = 11, CS = 8, A0 = 9, RESET = 7 (http://electronics.ilsoft.co.uk/ArduinoShield.aspx)
//U8GLIB_SSD1351_128X128_332 u8g(8, 9, 7); // Arduino: HW SPI Com: SCK = 13, MOSI = 11, CS = 8, A0 = 9, RESET = 7 (http://electronics.ilsoft.co.uk/ArduinoShield.aspx)
//U8GLIB_SSD1351_128X128_HICOLOR u8g(76, 75, 8, 9, 7); // Arduino DUE, SW SPI Com: SCK = 76, MOSI = 75, CS = 8, A0 = 9, RESET = 7 (http://electronics.ilsoft.co.uk/ArduinoShield.aspx)
//U8GLIB_SSD1351_128X128_HICOLOR u8g(8, 9, 7); // Arduino, HW SPI Com: SCK = 76, MOSI = 75, CS = 8, A0 = 9, RESET = 7 (http://electronics.ilsoft.co.uk/ArduinoShield.aspx)
//U8GLIB_SSD1351_128X128GH_332 u8g(8, 9, 7); // Arduino, HW SPI Com: SCK = 76, MOSI = 75, CS = 8, A0 = 9, RESET = 7 (Freetronics OLED)
//U8GLIB_SSD1351_128X128GH_HICOLOR u8g(8, 9, 7); // Arduino, HW SPI Com: SCK = 76, MOSI = 75, CS = 8, A0 = 9, RESET = 7 (Freetronics OLED)
void u8g_prepare(void) {
u8g.setFont(u8g_font_6x10);
u8g.setFontRefHeightExtendedText();
u8g.setDefaultForegroundColor();
u8g.setFontPosTop();
}
void u8g_box_frame(uint8_t a) {
u8g.drawStr( 0, 0, "drawBox");
u8g.drawBox(5,10,20,10);
u8g.drawBox(10+a,15,30,7);
u8g.drawStr( 0, 30, "drawFrame");
u8g.drawFrame(5,10+30,20,10);
u8g.drawFrame(10+a,15+30,30,7);
}
void u8g_disc_circle(uint8_t a) {
u8g.drawStr( 0, 0, "drawDisc");
u8g.drawDisc(10,18,9);
u8g.drawDisc(24+a,16,7);
u8g.drawStr( 0, 30, "drawCircle");
u8g.drawCircle(10,18+30,9);
u8g.drawCircle(24+a,16+30,7);
}
void u8g_r_frame(uint8_t a) {
u8g.drawStr( 0, 0, "drawRFrame/Box");
u8g.drawRFrame(5, 10,40,30, a+1);
u8g.drawRBox(50, 10,25,40, a+1);
}
void u8g_string(uint8_t a) {
u8g.drawStr(30+a,31, " 0");
u8g.drawStr90(30,31+a, " 90");
u8g.drawStr180(30-a,31, " 180");
u8g.drawStr270(30,31-a, " 270");
}
void u8g_line(uint8_t a) {
u8g.drawStr( 0, 0, "drawLine");
u8g.drawLine(7+a, 10, 40, 55);
u8g.drawLine(7+a*2, 10, 60, 55);
u8g.drawLine(7+a*3, 10, 80, 55);
u8g.drawLine(7+a*4, 10, 100, 55);
}
void u8g_triangle(uint8_t a) {
uint16_t offset = a;
u8g.drawStr( 0, 0, "drawTriangle");
u8g.drawTriangle(14,7, 45,30, 10,40);
u8g.drawTriangle(14+offset,7-offset, 45+offset,30-offset, 57+offset,10-offset);
u8g.drawTriangle(57+offset*2,10, 45+offset*2,30, 86+offset*2,53);
u8g.drawTriangle(10+offset,40+offset, 45+offset,30+offset, 86+offset,53+offset);
}
void u8g_ascii_1() {
char s[2] = " ";
uint8_t x, y;
u8g.drawStr( 0, 0, "ASCII page 1");
for( y = 0; y < 6; y++ ) {
for( x = 0; x < 16; x++ ) {
s[0] = y*16 + x + 32;
u8g.drawStr(x*7, y*10+10, s);
}
}
}
void u8g_ascii_2() {
char s[2] = " ";
uint8_t x, y;
u8g.drawStr( 0, 0, "ASCII page 2");
for( y = 0; y < 6; y++ ) {
for( x = 0; x < 16; x++ ) {
s[0] = y*16 + x + 160;
u8g.drawStr(x*7, y*10+10, s);
}
}
}
void u8g_extra_page(uint8_t a)
{
if ( u8g.getMode() == U8G_MODE_HICOLOR || u8g.getMode() == U8G_MODE_R3G3B2) {
/* draw background (area is 128x128) */
u8g_uint_t r, g, b;
b = a << 5;
for( g = 0; g < 64; g++ )
{
for( r = 0; r < 64; r++ )
{
u8g.setRGB(r<<2, g<<2, b );
u8g.drawPixel(g, r);
}
}
u8g.setRGB(255,255,255);
u8g.drawStr( 66, 0, "Color Page");
}
else if ( u8g.getMode() == U8G_MODE_GRAY2BIT )
{
u8g.drawStr( 66, 0, "Gray Level");
u8g.setColorIndex(1);
u8g.drawBox(0, 4, 64, 32);
u8g.drawBox(70, 20, 4, 12);
u8g.setColorIndex(2);
u8g.drawBox(0+1*a, 4+1*a, 64-2*a, 32-2*a);
u8g.drawBox(74, 20, 4, 12);
u8g.setColorIndex(3);
u8g.drawBox(0+2*a, 4+2*a, 64-4*a, 32-4*a);
u8g.drawBox(78, 20, 4, 12);
}
else
{
u8g.drawStr( 0, 12, "setScale2x2");
u8g.setScale2x2();
u8g.drawStr( 0, 6+a, "setScale2x2");
u8g.undoScale();
}
}
uint8_t draw_state = 0;
void draw(void) {
u8g_prepare();
switch(draw_state >> 3) {
case 0: u8g_box_frame(draw_state&7); break;
case 1: u8g_disc_circle(draw_state&7); break;
case 2: u8g_r_frame(draw_state&7); break;
case 3: u8g_string(draw_state&7); break;
case 4: u8g_line(draw_state&7); break;
case 5: u8g_triangle(draw_state&7); break;
case 6: u8g_ascii_1(); break;
case 7: u8g_ascii_2(); break;
case 8: u8g_extra_page(draw_state&7); break;
}
}
void setup(void) {
// flip screen, if required
//u8g.setRot180();
#if defined(ARDUINO)
pinMode(13, OUTPUT);
digitalWrite(13, HIGH);
#endif
}
void loop(void) {
// picture loop
u8g.firstPage();
do {
draw();
} while( u8g.nextPage() );
// increase the state
draw_state++;
if ( draw_state >= 9*8 )
draw_state = 0;
// rebuild the picture after some delay
//delay(150);
}

## Slide 125: LCD12864
https://www.electronicshub.org/interfacing-128x64-graphical-lcd-with-arduino/
..consists of ST7920 Controller. It is manufactured by Sitronix and supports three types of bus interfaces i.e., 8-bit mode, 4-bit mode and Serial interface.
Hardware Connections
There are three different ways in which you can interface the Graphical LCD with Arduino. They are:
4-bit Parallel Mode
8-bit Parallel Mode
Serial Mode

## Slide 126: https://electropeak.com/learn/interfacing-128x64-graphical-lcd-display-with-arduino/ (graphic demo code)
// khwong 2022.2.25, 2020 July 11,See http://misclab.umeoce.maine.edu/boss/Arduino/bensguides/DS3231_Arduino_Clock_Instructions.pdf
/* khwong 2020 march 22, cimbining DS3231+LCD+serail-port display
using DS3231 library, by Andrew Wickert, Eric Ayars, Jean-Claude Wippler version 1.02
installation: //Sketch/inlucde_library/manage librray/type DS3231,
Can try examples : Files/Exaples/DS3231/
Reference :DS3231_test.pde
Eric Ayars
4/11
Test/demo of read routines for a DS3231 RTC.
Turn on the serial monitor after loading this to check if things are
working as they should.
*/
/*
DS3231_test.pde
Eric Ayars
4/11
Test/demo of read routines for a DS3231 RTC.
Turn on the serial monitor after loading this to check if things are
working as they should.
*/
//////////////////////// LCD //////////////////////
#include <Wire.h>
#include "DHT.h"
#define DHTPIN 7
#define DHTTYPE DHT11
DHT dht(DHTPIN, DHTTYPE);
#include <LiquidCrystal_I2C.h>
LiquidCrystal_I2C lcd(0x27, 16, 2);
// set the LCD address to 0x27 for a 16 chars and 2 line display
//LiquidCrystal_I2C lcd(0x3F,20,2); // set the LCD address to 0x27 for a 16 chars and 2 line display
//LiquidCrystal_I2C lcd(0x3F,16,2); // set the LCD address to 0x27 for a 16 chars and 2 line display
void setup()
{ Serial.begin(9600);
lcd.init(); // initialize the lcd
lcd.backlight();
lcd.setCursor(3, 0); //first row: line 0,cursor index 3. first postion is index 0
lcd.print("Hello, world!");
lcd.setCursor(2, 1); //second row : line 1, position index 2
lcd.print("from KH WONG");
delay(500);
lcd.clear ();
////////////////////////////////
setup_new_time_RTC_DS3231();// if you want to change the time////////////////
Serial.println("DHTxx test!");
dht.begin();
}
#include <DS3231.h>
#include <Wire.h>
DS3231 Clock;
bool Century = false;
bool h12;
bool PM;
byte ADay, AHour, AMinute, ASecond, ABits;
bool ADy, A12h, Apm;
void setup_new_time_RTC_DS3231() {
// Clock.setSecond(50);//Set the second
//Clock.setMinute(23);//Set the minute
//Clock.setHour(13); //Set the hour
// Clock.setDoW(2); //Set the day of the week
// Clock.setDate(22); //Set the date of the month
// Clock.setMonth(2); //Set the month of the year
// Clock.setYear(22); //Set the year (Last two digits of the year)
}
//For clock hour/min/sec display , LCD cursor position: col= 0 to 15, 2 row=0,1;
void LCD2x16_print_2digit(int col, int row, int val) {
if (val <= 9) //special treatment to add prefix 0
{ lcd.setCursor(col, row);
lcd.print("0");
lcd.setCursor(col + 1, row);
lcd.print(val);
}
else
{ lcd.setCursor(col, row);
lcd.print(val);
}
}
int count;
float dht11_temperature , dht11_humidity; // make global
//////////////////////////////////////////////////////////////
void loop() {
delay(1000); // run once in 1 sec , give enough time for reading DHT.read11
count++; //since the loop is executed once in 1 second, 1 sec delay loopo at
// int chk = DHT.read11(DHT11_PIN);
if (count >= 3) // read at a period
{
dht11_temperature = dht.readTemperature();
dht11_humidity = dht.readHumidity();
count = 0;
}
/// ====== start lcd2x16 printing=========================================
lcd.setCursor(9, 1);
lcd.print(dht11_temperature );
lcd.setCursor(11, 1);
lcd.print("C");
lcd.setCursor(12, 1);
lcd.print(" ");
lcd.setCursor(13, 1); //
lcd.print(dht11_humidity);
lcd.setCursor(15, 1); //
lcd.print("%");
Serial.print("\nxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx");
Serial.print("\nxxxx xxxxxxx");
Serial.print("\nxxxx by KH WONG xxxxxxx");
Serial.print("\nxxxx xxxxxxx");
Serial.print("\nxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx");
Serial.print("\n");
//Serial.print("\n== Display temperature humidity : serial com port printing ======\n");
Serial.print("Temperature = ");
Serial.print(dht11_temperature );
//see https://forum.arduino.cc/t/solved-how-to-print-the-degree-symbol-extended-ascii/438685/21
Serial.write(0xC2); //these two must come togther 0xC2,0xB0
Serial.write(0xB0);
Serial.print("C, ");
//Serial.print(char(176));
//Serial.print(" degrees Celsus, Humidity = ");
Serial.print(" Humidity = ");
Serial.print(dht11_humidity);
Serial.print("%\n");
//Serial.print("\n========== Display time : serial com port printing ===========\n");
Serial.print("Date: 20");
Serial.print(Clock.getYear());// 20 of 20xx year, col=0, row=0
Serial.print("-");
Serial.print(Clock.getMonth(Century));
Serial.print("-");
Serial.print(Clock.getDate(), DEC);
Serial.print(" (");
switch (Clock.getDoW()) {
case 1: Serial.print("Mon"); break;
case 2: Serial.print("Tue"); break;
case 3: Serial.print("Wed"); break;
case 4: Serial.print("Thu"); break;
case 5: Serial.print("Fri"); break;
case 6: Serial.print("Sat"); break;
case 7: Serial.print("Sun"); break;
default: Serial.print("???"); break;
}
Serial.print(")");
Serial.print(" ");
Serial.print(Clock.getHour(h12, PM));
Serial.print(":");
Serial.print(Clock.getMinute());
Serial.print(":");
Serial.print(Clock.getMinute());
// Tell whether the time is (likely to be) valid
if (Clock.oscillatorCheck()) {
//Serial.print(", O+ : Clock.oscillatorCheck() =true, time is correct \n");
Serial.print(", O+ , clock ok\n");
} else {
Serial.print(", !!! O-: Clock.oscillatorCheck() =false, time is incorrect \n");
}
Serial.print("\n\n");
//////////////// optional /////////////////////////////////////////////////
// if (h12) {
// if (PM) {
// Serial.print(" PM ");
// } else {
// Serial.print(" AM ");
// }
// } else {
// Serial.print(" 24h ");
// }
/////////////////////////////////////////////////////////////////////////////
//// ====== LCD 2x16 printing -------------------------
LCD2x16_print_2digit(0, 0, 20); // for 20 of 20xx
LCD2x16_print_2digit(2, 0, Clock.getYear());// col=2, row=0
lcd.setCursor(4, 0); lcd.print("-");
lcd.setCursor(5, 0); //for month
//Serial.print(Clock.getDate(), DEC); // print date
switch (Clock.getMonth(Century)) {
case 1: lcd.print("Jan"); break;
case 2: lcd.print("Feb"); break;
case 3: lcd.print("Mar"); break;
case 4: lcd.print("Apr"); break;
case 5: lcd.print("May"); break;
case 6: lcd.print("Jun"); break;
case 7: lcd.print("Jul"); break;
case 8: lcd.print("Aug"); break;
case 9: lcd.print("Sept"); break;
case 10: lcd.print("Oct"); break;
case 11: lcd.print("Nov"); break;
case 12: lcd.print("Dec"); break;
default: lcd.print("???"); break;
}
lcd.setCursor(8, 0); lcd.print("-");
// then the date
// Serial.print(Clock.getDate(), DEC); lcd.setCursor(9, 0); lcd.print(Clock.getDate());
LCD2x16_print_2digit(9, 0, Clock.getDate());
lcd.setCursor(11, 0); lcd.print(",");
// and the day of the week
lcd.setCursor(12, 0);
switch (Clock.getDoW()) {
case 1: lcd.print("Mon"); break;
case 2: lcd.print("Tue"); break;
case 3: lcd.print("Wed"); break;
case 4: lcd.print("Thu"); break;
case 5: lcd.print("Fri"); break;
case 6: lcd.print("Sat"); break;
case 7: lcd.print("Sun"); break;
default: lcd.print("???"); break;
}
LCD2x16_print_2digit(0, 1, Clock.getHour(h12, PM)); //LCD2x16_print_2digit(col,row,val)
lcd.setCursor(2, 1); lcd.print(":");
LCD2x16_print_2digit(3, 1, Clock.getMinute());
lcd.setCursor(5, 1); lcd.print(":");
LCD2x16_print_2digit(6, 1, Clock.getSecond());
}

## Slide 127: LCD12864 ,world time USA/UK/HK time temperature/humidity/RTC demo, day light fix RTC_world_time_230830.ino
// 2023.8.30 fix the bug of resetting the clock
// use setup_new_time_RTC_DS3231 for setting the clock
// //remember to comment all after time is set correctly. Otherewise when power off it will affect the current time.
// 2022.3.16 rtc3b5.ino See http://misclab.umeoce.maine.edu/boss/Arduino/bensguides/DS3231_Arduino_Clock_Instructions.pdf
/* khwong 2020 march 22, combining DS3231+LCD+serail-port display
using DS3231 library, by Andrew Wickert, Eric Ayars, Jean-Claude Wippler version 1.02
installation: //Sketch/inlucde_library/manage librray/type DS3231,
Can try examples : Files/Exaples/DS3231/
Reference :DS3231_test.pde
Eric Ayars
4/11
Test/demo of read routines for a DS3231 RTC.
Turn on the serial monitor after loading this to check if things are
working as they should.
*/
/*
DS3231_test.pde
Eric Ayars
4/11
Test/demo of read routines for a DS3231 RTC.
Turn on the serial monitor after loading this to check if things are
working as they should.
*/
//////////////////////// LCD //////////////////////
#include <Wire.h>
#include "DHT.h"
#define DHTPIN 7
#define DHTTYPE DHT11
int sval;
int command_tag1 = 0;
int old_sval = 1;
#include "U8glib.h" // for lcd 128x64 display
U8GLIB_ST7920_128X64_4X u8g(10);
DHT dht(DHTPIN, DHTTYPE);
#include <LiquidCrystal_I2C.h>
LiquidCrystal_I2C lcd(0x27, 16, 2);
// set the LCD address to 0x27 for a 16 chars and 2 line display
//LiquidCrystal_I2C lcd(0x3F,20,2); // set the LCD address to 0x27 for a 16 chars and 2 line display
//LiquidCrystal_I2C lcd(0x3F,16,2); // set the LCD address to 0x27 for a 16 chars and 2 line display
int count;
float dht11_temperature , dht11_humidity; // make global because many modules are using it
int minute_count = 0;
void setup()
{
// u8g.setRot90();// u8g.setRot180();
Serial.begin(9600);
lcd.init(); // initialize the lcd
lcd.backlight();
lcd.setCursor(3, 0); //first row: line 0,cursor index 3. first postion is index 0
lcd.print("By KH WONG");
lcd.setCursor(0, 1); //second row : line 1, position index 2
lcd.print("ver. 2023.08.30");
delay(3000);
lcd.clear ();
////////////////////////////////
setup_new_time_RTC_DS3231();// if you want to change the time////////////////
Serial.println("DHTxx test!");
dht.begin();
pinMode(2, INPUT_PULLUP); //google input pin (yellow reset button)
}
#include <DS3231.h>
#include <Wire.h>
DS3231 Clock;
bool Century = false;
bool h12;
bool PM;
byte ADay, AHour, AMinute, ASecond, ABits;
bool ADy, A12h, Apm;
//remember to comment all after time is set correctly. Otherewise when power off it will affect the current time.
void setup_new_time_RTC_DS3231() {
// edit the following for clock adjustment
// Clock.setSecond(00);//Set the second
// Clock.setMinute(16);//Set the minute
// Clock.setHour(21); //Set the hour
// Clock.setDoW(3); //Set the day of the week
// Clock.setDate(2); //Set the date of the month
// Clock.setMonth(3); //Set the month of the year
// Clock.setYear(22); //Set the year (Last two digits of the year)
}
void clear_screen_12864() {
uint8_t x, y;
u8g.setColorIndex(0);
for ( y = 0; y < 128; y++ ) {
for ( x = 0; x < 64; x++ ) {
u8g.drawPixel(x, y);
}
}
u8g.setColorIndex(1); //restore color to 1
}
void u8g_prepare(void) {
u8g.setFont(u8g_font_6x10);
u8g.setFontRefHeightExtendedText();
u8g.setDefaultForegroundColor();
u8g.setFontPosTop();
}
void u8g_drawStr_12864_2digits(int x, int y, int val) {
char buf[12];
if (val <= 9) {
u8g.drawStr(x, y, "0");
u8g.drawStr(x + 8, y, itoa(val, buf, 10));
}
else {
u8g.drawStr(x, y, itoa(val, buf, 10));
}
}
///////////////////////////////////////////////////////////////////////////
void draw_vert_hk_uk_usa_time_LCD12864(int month, int date, int dow, int hour, int minute, int second) {
// graphic commands to redraw the complete screen should be placed here
u8g.setRot270();
u8g.setFont(u8g_font_unifont);
u8g.setFontPosTop();
//////////// draw style 2 //////////////////
//-------------HK ----------------------------------------
u8g.setScale2x2(); // Scale up all draw procedures
char buf[12]; // "-2147483648\0"
u8g_drawStr_12864_2digits(0, 0, hour);
u8g_drawStr_12864_2digits(0 + 1, 0, hour);
u8g_drawStr_12864_2digits(16, 0, minute);
u8g_drawStr_12864_2digits(16 + 1, 0, minute);
//-------------UK ----------------------------------------
byte summer_uk ;
////////////////////////////////////////////////////////////////////
//UK 2022 27 March sunday begins, 30 October sunday ends, Last sunday of march/oct
if (3 < month || month > 10) {
summer_uk = 0;
}
if (month >= 3 && month <= 10) {
summer_uk = 1;
}
if (month == 3 && ((31 - date) - dow) >= 0) { // for march only ??????
summer_uk = 0;
}
if (month == 10 && ((30 - date) - dow) <= 0) { // for nov only ????
summer_uk = 1;
}
////////////////////////////////////////////////////////////////
if (summer_uk == 1) {
u8g_drawStr_12864_2digits(0, 11, (hour + 16 + 1) % 24);
u8g_drawStr_12864_2digits(0 + 1, 11, (hour + 16 + 1) % 24);
} else {
u8g_drawStr_12864_2digits(0, 11, (hour + 16) % 24);
u8g_drawStr_12864_2digits(0 + 1, 11, (hour + 16) % 24);
}
u8g_drawStr_12864_2digits(16, 11, minute);
u8g_drawStr_12864_2digits(16 + 1, 11, minute);
//-------------US ----------------------------------------
// handle day_light_saving_us //////////////////////////////////////
// https://stackoverflow.com/questions/5590429/calculating-daylight-saving-time-from-only-date
byte summer_us ;
////////////////////////////////////////////////////////////////////
//USA summer time: //begin march 13 sunday; //end Nov.6 sunday
//January, february, and december are out.
if (3 < month || month > 11) {
summer_us = 0;
}
if (month >= 3 && month <= 11) {
summer_us = 1;
}
if (month == 3 && (date - dow) < 0) { // for march only
summer_us = 0;
}
if (month == 11 && (date - dow) > 0) { // for nov only
summer_us = 0;
}
////////////////////////////////////////////////////////////////
if (summer_us == 1) {
u8g_drawStr_12864_2digits(0, 22, ((hour + 8 + 1) % 24) ); //summer ; day light saving :usa time
u8g_drawStr_12864_2digits(0 + 1, 22, ((hour + 8 + 1) % 24)); //summer; day light saving :write again to make font larger
}
else {
u8g_drawStr_12864_2digits(0, 22, ((hour + 8) % 24) ); //usa time
u8g_drawStr_12864_2digits(0 + 1, 22, ((hour + 8) % 24)); //write again to make font larger
}
u8g_drawStr_12864_2digits(16, 22, minute);
u8g_drawStr_12864_2digits(16 + 1, 22, minute);
//---- second
u8g.drawStr(0, 33, ":");
u8g.drawStr(0 + 1, 33, ":");
u8g_drawStr_12864_2digits(6, 33, second);
u8g_drawStr_12864_2digits(6 + 1, 33, second);
//////////////////////////////////////////////////////////////
u8g.undoScale(); // IMPORTANT: Switch back to normal mode
// u8g.drawStr(112, 10, "HK");
// u8g.drawStr(112 + 1, 10, "HK");
if (summer_uk == 1 ) {
int y_pos_s = 90; //display light saving logo
int x_pos_s = 55; //display light saving logo
u8g.drawStr(x_pos_s, y_pos_s, "*");//display light saving logo *
}
if (summer_us == 1 ) {
int y_pos_s = 90; //display light saving logo
int x_pos_s = 55; //display light saving logo
u8g.drawStr(x_pos_s, y_pos_s, "+");//display light saving logo +
}
}
//////////////////////////////////////////////////////////////////////////////
void draw_vert_year_date_temp_humidity_LCD12864() {
char buf[12]; // "-2147483648\0"
int y_pos = 90;
int x_pos = 0;
////u8g.drawStr(x_pos,y_pos,"20");
//u8g_drawStr_12864_2digits(0,y_pos,Clock.getYear());
int x_pos1 = 0;
switch (Clock.getMonth(Century)) {
case 1: u8g.drawStr(x_pos1, y_pos, "Jan"); u8g.drawStr(x_pos1 + 1, y_pos, "Jan"); break;
case 2: u8g.drawStr(x_pos1, y_pos, "Feb"); u8g.drawStr(x_pos1 + 1, y_pos, "Feb"); break;
case 3: u8g.drawStr(x_pos1, y_pos, "Mar"); u8g.drawStr(x_pos1 + 1, y_pos, "Mar"); break;
case 4: u8g.drawStr(x_pos1, y_pos, "Apr"); u8g.drawStr(x_pos1 + 1, y_pos, "Apr"); break;
case 5: u8g.drawStr(x_pos1, y_pos, "May"); u8g.drawStr(x_pos1 + 1, y_pos, "May"); break;
case 6: u8g.drawStr(x_pos1, y_pos, "Jun"); u8g.drawStr(x_pos1 + 1, y_pos, "Jun"); break;
case 7: u8g.drawStr(x_pos1, y_pos, "Jul"); u8g.drawStr(x_pos1 + 1, y_pos, "Jul"); break;
case 8: u8g.drawStr(x_pos1, y_pos, "Aug"); u8g.drawStr(x_pos1 + 1, y_pos, "Aug"); break;
case 9: u8g.drawStr(x_pos1, y_pos, "Sep"); u8g.drawStr(x_pos1 + 1, y_pos, "Sep"); break;
case 10: u8g.drawStr(x_pos1, y_pos, "Oct"); u8g.drawStr(x_pos1 + 1, y_pos, "Oct"); break;
case 11: u8g.drawStr(x_pos1, y_pos, "Nov"); u8g.drawStr(x_pos1 + 1, y_pos, "Nov"); break;
case 12: u8g.drawStr(x_pos1, y_pos, "Dec"); u8g.drawStr(x_pos1 + 1, y_pos, "Dec"); break;
default: lcd.print("???"); break;
}
// u8g.drawStr(22, 46, ".");
// u8g.drawStr(22 + 1, 46, ".");
u8g_drawStr_12864_2digits(x_pos + 28, y_pos, Clock.getDate());
u8g_drawStr_12864_2digits(x_pos + 28 + 1, y_pos, Clock.getDate());
//u8g.drawStr(40, y_pos, "(");
int x_pos2 = 0;
int y_pos2 = 101;
int x_pos3 = 0;
int y_pos3 = 113;
// u8g_drawStr_12864_2digits(90-38,46,Clock.getDoW());
switch (Clock.getDoW()) {
case 1: u8g.drawStr(x_pos2, y_pos2, "Mon"); u8g.drawStr(x_pos2 + 1, y_pos2, "Mon"); break;
case 2: u8g.drawStr(x_pos2, y_pos2, "Tue"); u8g.drawStr(x_pos2 + 1, y_pos2, "Tue"); break;
case 3: u8g.drawStr(x_pos2, y_pos2, "Wed"); u8g.drawStr(x_pos2 + 1, y_pos2, "Wed"); break;
case 4: u8g.drawStr(x_pos2, y_pos2, "Thu"); u8g.drawStr(x_pos2 + 1, y_pos2, "Thu"); break;
case 5: u8g.drawStr(x_pos2, y_pos2, "Fri"); u8g.drawStr(x_pos2 + 1, y_pos2, "Fri"); break;
case 6: u8g.drawStr(x_pos2, y_pos2, "Sat"); u8g.drawStr(x_pos2 + 1, y_pos2, "Sat"); break;
case 7: u8g.drawStr(x_pos2, y_pos2, "Sun"); u8g.drawStr(x_pos2 + 1, y_pos2, "Sun"); break;
default: u8g.drawStr(x_pos2, y_pos2, "???"); break;
}
u8g.drawStr(30, y_pos2, "20");
u8g_drawStr_12864_2digits(46, y_pos2, Clock.getYear());
//u8g.drawStr(68, y_pos, ")");
///////////////////////////////////////////////////////////////
//////// draw temperture/ humidity //////////////////////
u8g.drawStr(x_pos3, y_pos3, itoa( dht11_temperature, buf, 10));
u8g.drawStr(x_pos3 + 1, y_pos3, itoa( dht11_temperature, buf, 10));
u8g.drawStr( x_pos3 + 17, y_pos3, "C");
u8g.drawStr(x_pos3 + 30, y_pos3, itoa( dht11_humidity, buf, 10));
u8g.drawStr(x_pos3 + 30 + 1, y_pos3, itoa( dht11_humidity, buf, 10));
u8g.drawStr(x_pos3 + 47, y_pos3, "%");
switch (command_tag1) {
case 0: u8g.drawLine(0, 126, 60, 126); break;
case 1: u8g.drawLine(40, 126, 80, 126); break;
case 2: u8g.drawLine(80, 126, 120, 126); break;
}
}
void draw_vert_LCD12864() {
char buf[12]; // "-2147483648\0"
//int year = Clock.getYear();
int date = Clock.getDate();
int month = Clock.getMonth(Century);
int dow = Clock.getDoW();
int hour = Clock.getHour(h12, PM); // (Clock.getHour(h12, PM) + 16) % 24); //uk time
int minute = Clock.getMinute();
int second = Clock.getSecond();
draw_vert_hk_uk_usa_time_LCD12864(month, date, dow, hour, minute, second); // upper part
draw_vert_year_date_temp_humidity_LCD12864(); //lower part
int dual_time_tag = 2; // 0 HK time only; 1= hk and uk time; 2 hk, uk and usa time
//////////////////////////////////////////////////////////////
// if (dual_time_tag == 0)
if (command_tag1 == 2)
{ //u8g.setRot270();
char buf[12]; // "-2147483648\0"
}
}
//////////////////////////////////////////////////////////////
void loop() {
// sval = digitalRead(2); // not used yet, keep, may use later
// if ( old_sval == 1 && sval == 0) { //pressed once , falling edge
// command_tag1++;
//
// if (command_tag1 >= 3) { //set max command value
// command_tag1 = 0;
// }
// }
// old_sval = sval;
// Serial.print(command_tag1);
count++; //since the loop is executed once in 1 second, 1 sec delay loop at
if (count >= 3) // read temperature/ humdity at a period of 3 seconds
{
dht11_temperature = dht.readTemperature();
dht11_humidity = dht.readHumidity();
count = 0;
}
////-------------------------------------------------------------------
u8g.firstPage();
u8g_prepare();
clear_screen_12864();
draw_vert_LCD12864();
do {
draw_vert_LCD12864();
} while ( u8g.nextPage() );
minute_count++;
delay(100); // rebuild the picture after some delay
}

## Slide 128: Old_RTC, with button control, HK_UK_USA(day light saving) rtc3b5.lcd128x64 ok, 2022.3.22
// 2022.3.16 rtc3b5.ino See http://misclab.umeoce.maine.edu/boss/Arduino/bensguides/DS3231_Arduino_Clock_Instructions.pdf
/* khwong 2020 march 22, cimbining DS3231+LCD+serail-port display
using DS3231 library, by Andrew Wickert, Eric Ayars, Jean-Claude Wippler version 1.02
installation: //Sketch/inlucde_library/manage librray/type DS3231,
Can try examples : Files/Exaples/DS3231/
Reference :DS3231_test.pde
Eric Ayars
4/11
Test/demo of read routines for a DS3231 RTC.
Turn on the serial monitor after loading this to check if things are
working as they should.
*/
/*
DS3231_test.pde
Eric Ayars
4/11
Test/demo of read routines for a DS3231 RTC.
Turn on the serial monitor after loading this to check if things are
working as they should.
*/
//////////////////////// LCD //////////////////////
#include <Wire.h>
#include "DHT.h"
#define DHTPIN 7
#define DHTTYPE DHT11
int sval;
int command_tag1 = 0;
int old_sval = 1;
#include "U8glib.h" // for lcd 128x64 display
U8GLIB_ST7920_128X64_4X u8g(10);
DHT dht(DHTPIN, DHTTYPE);
#include <LiquidCrystal_I2C.h>
LiquidCrystal_I2C lcd(0x27, 16, 2);
// set the LCD address to 0x27 for a 16 chars and 2 line display
//LiquidCrystal_I2C lcd(0x3F,20,2); // set the LCD address to 0x27 for a 16 chars and 2 line display
//LiquidCrystal_I2C lcd(0x3F,16,2); // set the LCD address to 0x27 for a 16 chars and 2 line display
int count;
float dht11_temperature , dht11_humidity; // make global because many modules are using it
int minute_count = 0;
void setup()
{
// u8g.setRot90();// u8g.setRot180();
Serial.begin(9600);
lcd.init(); // initialize the lcd
lcd.backlight();
lcd.setCursor(3, 0); //first row: line 0,cursor index 3. first postion is index 0
lcd.print("By KH WONG");
lcd.setCursor(0, 1); //second row : line 1, position index 2
lcd.print("ver.1a 2022.2.26");
delay(3000);
lcd.clear ();
////////////////////////////////
setup_new_time_RTC_DS3231();// if you want to change the time////////////////
Serial.println("DHTxx test!");
dht.begin();
pinMode(2, INPUT_PULLUP); //google input pin (yellow reset button)
}
#include <DS3231.h>
#include <Wire.h>
DS3231 Clock;
bool Century = false;
bool h12;
bool PM;
byte ADay, AHour, AMinute, ASecond, ABits;
bool ADy, A12h, Apm;
void setup_new_time_RTC_DS3231() {// for setting up new time
// Clock.setSecond(00);//Set the second
// Clock.setMinute(01);//Set the minute
// Clock.setHour(13); //Set the hour
// Clock.setDoW(3); //Set the day of the week
// Clock.setDate(2); //Set the date of the month
// Clock.setMonth(3); //Set the month of the year
// Clock.setYear(22); //Set the year (Last two digits of the year)
}
void clear_screen_12864() {
uint8_t x, y;
u8g.setColorIndex(0);
for ( y = 0; y < 128; y++ ) {
for ( x = 0; x < 64; x++ ) {
u8g.drawPixel(x, y);
}
}
u8g.setColorIndex(1); //restore color to 1
}
void u8g_prepare(void) {
u8g.setFont(u8g_font_6x10);
u8g.setFontRefHeightExtendedText();
u8g.setDefaultForegroundColor();
u8g.setFontPosTop();
}
void u8g_drawStr_12864_2digits(int x, int y, int val) {
char buf[12];
if (val <= 9) {
u8g.drawStr(x, y, "0");
u8g.drawStr(x + 8, y, itoa(val, buf, 10));
}
else {
u8g.drawStr(x, y, itoa(val, buf, 10));
}
}
///////////////////////////////////////////////////////////////////////////
void draw_vert_hk_uk_usa_time_LCD12864(int month, int date, int dow, int hour, int minute, int second) {
// graphic commands to redraw the complete screen should be placed here
u8g.setRot270();
u8g.setFont(u8g_font_unifont);
u8g.setFontPosTop();
//////////// draw style 2 //////////////////
//-------------HK ----------------------------------------
u8g.setScale2x2(); // Scale up all draw procedures
char buf[12]; // "-2147483648\0"
u8g_drawStr_12864_2digits(0, 0, hour);
u8g_drawStr_12864_2digits(0 + 1, 0, hour);
u8g_drawStr_12864_2digits(16, 0, minute);
u8g_drawStr_12864_2digits(16 + 1, 0, minute);
//-------------UK ----------------------------------------
byte summer_uk ;
////////////////////////////////////////////////////////////////////
//UK 2022 27 March sunday begins, 30 October sunday ends, Last sunday of march/oct
if (3 < month || month > 10) {
summer_uk = 0;
}
if (month >= 3 && month <= 10) {
summer_uk = 1;
}
if (month == 3 && ((31 - date) - dow) >= 0) { // for march only ??????
summer_uk = 0;
}
if (month == 10 && ((30 - date) - dow) <= 0) { // for nov only ????
summer_uk = 1;
}
////////////////////////////////////////////////////////////////
if (summer_uk == 1) {
u8g_drawStr_12864_2digits(0, 11, (hour + 16 + 1) % 24);
u8g_drawStr_12864_2digits(0 + 1, 11, (hour + 16 + 1) % 24);
} else {
u8g_drawStr_12864_2digits(0, 11, (hour + 16) % 24);
u8g_drawStr_12864_2digits(0 + 1, 11, (hour + 16) % 24);
}
u8g_drawStr_12864_2digits(16, 11, minute);
u8g_drawStr_12864_2digits(16 + 1, 11, minute);
//-------------US ----------------------------------------
// handle day_light_saving_us //////////////////////////////////////
// https://stackoverflow.com/questions/5590429/calculating-daylight-saving-time-from-only-date
byte summer_us ;
////////////////////////////////////////////////////////////////////
//USA summer time: //begin march 13 sunday; //end Nov.6 sunday
//January, february, and december are out.
if (3 < month || month > 11) {
summer_us = 0;
}
if (month >= 3 && month <= 11) {
summer_us = 1;
}
if (month == 3 && (date - dow) < 0) { // for march only
summer_us = 0;
}
if (month == 11 && (date - dow) > 0) { // for nov only
summer_us = 0;
}
////////////////////////////////////////////////////////////////
if (summer_us == 1) {
u8g_drawStr_12864_2digits(0, 22, ((hour + 8 + 1) % 24) ); //summer ; day light saving :usa time
u8g_drawStr_12864_2digits(0 + 1, 22, ((hour + 8 + 1) % 24)); //summer; day light saving :write again to make font larger
}
else {
u8g_drawStr_12864_2digits(0, 22, ((hour + 8) % 24) ); //usa time
u8g_drawStr_12864_2digits(0 + 1, 22, ((hour + 8) % 24)); //write again to make font larger
}
u8g_drawStr_12864_2digits(16, 22, minute);
u8g_drawStr_12864_2digits(16 + 1, 22, minute);
//---- second
u8g.drawStr(0, 33, ":");
u8g.drawStr(0 + 1, 33, ":");
u8g_drawStr_12864_2digits(6, 33, second);
u8g_drawStr_12864_2digits(6 + 1, 33, second);
//////////////////////////////////////////////////////////////
u8g.undoScale(); // IMPORTANT: Switch back to normal mode
// u8g.drawStr(112, 10, "HK");
// u8g.drawStr(112 + 1, 10, "HK");
if (summer_uk == 1 ) {
int y_pos_s = 90; //display light saving logo
int x_pos_s = 55; //display light saving logo
u8g.drawStr(x_pos_s, y_pos_s, "*");//display light saving logo *
}
if (summer_us == 1 ) {
int y_pos_s = 90; //display light saving logo
int x_pos_s = 55; //display light saving logo
u8g.drawStr(x_pos_s, y_pos_s, "+");//display light saving logo +
}
}
//////////////////////////////////////////////////////////////////////////////
void draw_vert_year_date_temp_humidity_LCD12864() {
char buf[12]; // "-2147483648\0"
int y_pos = 90;
int x_pos = 0;
////u8g.drawStr(x_pos,y_pos,"20");
//u8g_drawStr_12864_2digits(0,y_pos,Clock.getYear());
int x_pos1 = 0;
switch (Clock.getMonth(Century)) {
case 1: u8g.drawStr(x_pos1, y_pos, "Jan"); u8g.drawStr(x_pos1 + 1, y_pos, "Jan"); break;
case 2: u8g.drawStr(x_pos1, y_pos, "Feb"); u8g.drawStr(x_pos1 + 1, y_pos, "Feb"); break;
case 3: u8g.drawStr(x_pos1, y_pos, "Mar"); u8g.drawStr(x_pos1 + 1, y_pos, "Mar"); break;
case 4: u8g.drawStr(x_pos1, y_pos, "Apr"); u8g.drawStr(x_pos1 + 1, y_pos, "Apr"); break;
case 5: u8g.drawStr(x_pos1, y_pos, "May"); u8g.drawStr(x_pos1 + 1, y_pos, "May"); break;
case 6: u8g.drawStr(x_pos1, y_pos, "Jun"); u8g.drawStr(x_pos1 + 1, y_pos, "Jun"); break;
case 7: u8g.drawStr(x_pos1, y_pos, "Jul"); u8g.drawStr(x_pos1 + 1, y_pos, "Jul"); break;
case 8: u8g.drawStr(x_pos1, y_pos, "Aug"); u8g.drawStr(x_pos1 + 1, y_pos, "Aug"); break;
case 9: u8g.drawStr(x_pos1, y_pos, "Sep"); u8g.drawStr(x_pos1 + 1, y_pos, "Sep"); break;
case 10: u8g.drawStr(x_pos1, y_pos, "Oct"); u8g.drawStr(x_pos1 + 1, y_pos, "Oct"); break;
case 11: u8g.drawStr(x_pos1, y_pos, "Nov"); u8g.drawStr(x_pos1 + 1, y_pos, "Nov"); break;
case 12: u8g.drawStr(x_pos1, y_pos, "Dec"); u8g.drawStr(x_pos1 + 1, y_pos, "Dec"); break;
default: lcd.print("???"); break;
}
// u8g.drawStr(22, 46, ".");
// u8g.drawStr(22 + 1, 46, ".");
u8g_drawStr_12864_2digits(x_pos + 28, y_pos, Clock.getDate());
u8g_drawStr_12864_2digits(x_pos + 28 + 1, y_pos, Clock.getDate());
//u8g.drawStr(40, y_pos, "(");
int x_pos2 = 0;
int y_pos2 = 101;
int x_pos3 = 0;
int y_pos3 = 113;
// u8g_drawStr_12864_2digits(90-38,46,Clock.getDoW());
switch (Clock.getDoW()) {
case 1: u8g.drawStr(x_pos2, y_pos2, "Mon"); u8g.drawStr(x_pos2 + 1, y_pos2, "Mon"); break;
case 2: u8g.drawStr(x_pos2, y_pos2, "Tue"); u8g.drawStr(x_pos2 + 1, y_pos2, "Tue"); break;
case 3: u8g.drawStr(x_pos2, y_pos2, "Wed"); u8g.drawStr(x_pos2 + 1, y_pos2, "Wed"); break;
case 4: u8g.drawStr(x_pos2, y_pos2, "Thu"); u8g.drawStr(x_pos2 + 1, y_pos2, "Thu"); break;
case 5: u8g.drawStr(x_pos2, y_pos2, "Fri"); u8g.drawStr(x_pos2 + 1, y_pos2, "Fri"); break;
case 6: u8g.drawStr(x_pos2, y_pos2, "Sat"); u8g.drawStr(x_pos2 + 1, y_pos2, "Sat"); break;
case 7: u8g.drawStr(x_pos2, y_pos2, "Sun"); u8g.drawStr(x_pos2 + 1, y_pos2, "Sun"); break;
default: u8g.drawStr(x_pos2, y_pos2, "???"); break;
}
u8g.drawStr(30, y_pos2, "20");
u8g_drawStr_12864_2digits(46, y_pos2, Clock.getYear());
//u8g.drawStr(68, y_pos, ")");
///////////////////////////////////////////////////////////////
//////// draw temperture/ humidity //////////////////////
u8g.drawStr(x_pos3, y_pos3, itoa( dht11_temperature, buf, 10));
u8g.drawStr(x_pos3 + 1, y_pos3, itoa( dht11_temperature, buf, 10));
u8g.drawStr( x_pos3 + 17, y_pos3, "C");
u8g.drawStr(x_pos3 + 30, y_pos3, itoa( dht11_humidity, buf, 10));
u8g.drawStr(x_pos3 + 30 + 1, y_pos3, itoa( dht11_humidity, buf, 10));
u8g.drawStr(x_pos3 + 47, y_pos3, "%");
switch (command_tag1) {
case 0: u8g.drawLine(0, 126, 60, 126); break;
case 1: u8g.drawLine(40, 126, 80, 126); break;
case 2: u8g.drawLine(80, 126, 120, 126); break;
}
}
void draw_vert_LCD12864() {
char buf[12]; // "-2147483648\0"
//int year = Clock.getYear();
int date = Clock.getDate();
int month = Clock.getMonth(Century);
int dow = Clock.getDoW();
int hour = Clock.getHour(h12, PM); // (Clock.getHour(h12, PM) + 16) % 24); //uk time
int minute = Clock.getMinute();
int second = Clock.getSecond();
draw_vert_hk_uk_usa_time_LCD12864(month, date, dow, hour, minute, second); // upper part
draw_vert_year_date_temp_humidity_LCD12864(); //lower part
int dual_time_tag = 2; // 0 HK time only; 1= hk and uk time; 2 hk, uk and usa time
//////////////////////////////////////////////////////////////
// if (dual_time_tag == 0)
if (command_tag1 == 2)
{ //u8g.setRot270();
char buf[12]; // "-2147483648\0"
}
}
//////////////////////////////////////////////////////////////
void loop() {
// sval = digitalRead(2); // not used yet, keep, may use later
// if ( old_sval == 1 && sval == 0) { //pressed once , falling edge
// command_tag1++;
//
// if (command_tag1 >= 3) { //set max command value
// command_tag1 = 0;
// }
// }
// old_sval = sval;
// Serial.print(command_tag1);
count++; //since the loop is executed once in 1 second, 1 sec delay loop at
if (count >= 3) // read temperature/ humdity at a period of 3 seconds
{
dht11_temperature = dht.readTemperature();
dht11_humidity = dht.readHumidity();
count = 0;
}
////-------------------------------------------------------------------
u8g.firstPage();
u8g_prepare();
clear_screen_12864();
draw_vert_LCD12864();
do {
draw_vert_LCD12864();
} while ( u8g.nextPage() );
minute_count++;
delay(100); // rebuild the picture after some delay
}

## Slide 129: Test1: GY521 (MPU6050) accelerometer-gyroscope https://create.arduino.cc/projecthub/Nicholas_N/how-to-use-the-accelerometer-gyroscope-gy-521-6dfc19
#include<Wire.h>
const int MPU=0x68;
int16_t AcX,AcY,AcZ,Tmp,GyX,GyY,GyZ;
void setup(){
Wire.begin();
Wire.beginTransmission(MPU);
Wire.write(0x6B);
Wire.write(0);
Wire.endTransmission(true);
Serial.begin(9600);
}
void loop(){
Wire.beginTransmission(MPU);
Wire.write(0x3B);
Wire.endTransmission(false);
Wire.requestFrom(MPU,12,true);
AcX=Wire.read()<<8|Wire.read();
AcY=Wire.read()<<8|Wire.read();
AcZ=Wire.read()<<8|Wire.read();
GyX=Wire.read()<<8|Wire.read();
GyY=Wire.read()<<8|Wire.read();
GyZ=Wire.read()<<8|Wire.read();
Serial.print("Accelerometer: ");
Serial.print("X = "); Serial.print(AcX);
Serial.print(" | Y = "); Serial.print(AcY);
Serial.print(" | Z = "); Serial.println(AcZ);
Serial.print("Gyroscope: ");
Serial.print("X = "); Serial.print(GyX);
Serial.print(" | Y = "); Serial.print(GyY);
Serial.print(" | Z = "); Serial.println(GyZ);
Serial.println(" ");
delay(333);
}

## Slide 130: Test2: GY521 (MPU6050) accelerometer-gyroscope https://mschoeffler.com/2017/10/05/tutorial-how-to-use-the-gy-521-module-mpu-6050-breakout-board-with-the-arduino-uno/
// (c) Michael Schoeffler 2017, http://www.mschoeffler.de
#include "Wire.h" // This library allows you to communicate with I2C devices.
const int MPU_ADDR = 0x68; // I2C address of the MPU-6050. If AD0 pin is set to HIGH, the I2C address will be 0x69.
int16_t accelerometer_x, accelerometer_y, accelerometer_z; // variables for accelerometer raw data
int16_t gyro_x, gyro_y, gyro_z; // variables for gyro raw data
int16_t temperature; // variables for temperature data
char tmp_str[7]; // temporary variable used in convert function
char* convert_int16_to_str(int16_t i) { // converts int16 to string. Moreover, resulting strings will have the same length in the debug monitor.
sprintf(tmp_str, "%6d", i);
return tmp_str;
}
void setup() {
Serial.begin(9600);
Wire.begin();
Wire.beginTransmission(MPU_ADDR); // Begins a transmission to the I2C slave (GY-521 board)
Wire.write(0x6B); // PWR_MGMT_1 register
Wire.write(0); // set to zero (wakes up the MPU-6050)
Wire.endTransmission(true);
}
void loop() {
Wire.beginTransmission(MPU_ADDR);
Wire.write(0x3B); // starting with register 0x3B (ACCEL_XOUT_H) [MPU-6000 and MPU-6050 Register Map and Descriptions Revision 4.2, p.40]
Wire.endTransmission(false); // the parameter indicates that the Arduino will send a restart. As a result, the connection is kept active.
Wire.requestFrom(MPU_ADDR, 7*2, true); // request a total of 7*2=14 registers
// "Wire.read()<<8 | Wire.read();" means two registers are read and stored in the same variable
accelerometer_x = Wire.read()<<8 | Wire.read(); // reading registers: 0x3B (ACCEL_XOUT_H) and 0x3C (ACCEL_XOUT_L)
accelerometer_y = Wire.read()<<8 | Wire.read(); // reading registers: 0x3D (ACCEL_YOUT_H) and 0x3E (ACCEL_YOUT_L)
accelerometer_z = Wire.read()<<8 | Wire.read(); // reading registers: 0x3F (ACCEL_ZOUT_H) and 0x40 (ACCEL_ZOUT_L)
temperature = Wire.read()<<8 | Wire.read(); // reading registers: 0x41 (TEMP_OUT_H) and 0x42 (TEMP_OUT_L)
gyro_x = Wire.read()<<8 | Wire.read(); // reading registers: 0x43 (GYRO_XOUT_H) and 0x44 (GYRO_XOUT_L)
gyro_y = Wire.read()<<8 | Wire.read(); // reading registers: 0x45 (GYRO_YOUT_H) and 0x46 (GYRO_YOUT_L)
gyro_z = Wire.read()<<8 | Wire.read(); // reading registers: 0x47 (GYRO_ZOUT_H) and 0x48 (GYRO_ZOUT_L)
// print out data
Serial.print("aX = "); Serial.print(convert_int16_to_str(accelerometer_x));
Serial.print(" | aY = "); Serial.print(convert_int16_to_str(accelerometer_y));
Serial.print(" | aZ = "); Serial.print(convert_int16_to_str(accelerometer_z));
// the following equation was taken from the documentation [MPU-6000/MPU-6050 Register Map and Description, p.30]
Serial.print(" | tmp = "); Serial.print(temperature/340.00+36.53);
Serial.print(" | gX = "); Serial.print(convert_int16_to_str(gyro_x));
Serial.print(" | gY = "); Serial.print(convert_int16_to_str(gyro_y));
Serial.print(" | gZ = "); Serial.print(convert_int16_to_str(gyro_z));
Serial.println();
// delay
delay(1000);
}
The GY-521 breakout has eight pins:
VCC (The breakout board has a voltage regulator. Therefore, you can connect the board to 3.3V and 5V sources.)
GND
SCL (Serial Clock Line of the I2C protocol.)
SDA (Serial Data Line of the I2C protocol.)
XDA (Auxiliary data => I2C master serial data for connecting the module to external sensors.)
XCL (Auxiliary clock => I2C master serial clock for connecting the module to external sensors.)
AD0 (If this pin is LOW, the I2C address of the board will be 0x68. Otherwise, if the pin is HIGH, the address will be 0x69.)
INT (Interrupt digital output)

## Slide 131: Auto watering system
https://forum.fritzing.org/t/h-bridge-with-l298n-motor-driver/7711/2 https://geekyengineers.com/smart-irrigation-system-2/
医疗器械二位二通 DC5V-6V 常闭型 双向 电磁阀 DIY 电动气阀
5-35V GND
Power input
7, 8
GPIO
8
7
GPIO

## Slide 132: Auto watering system (code)
// the setup function runs once when you press reset or power the board
void setup() {
Serial.begin(115200);
// initialize digital pin LED_BUILTIN as an output.
pinMode(LED_BUILTIN, OUTPUT);
}
// the loop function runs over and over again forever
void loop() {
// wait for a second
float humidity1 = analogRead(A0);
Serial.print("humidity = ");
Serial.println(humidity1);
// if dry (0 is very wet, 1024 is very dry), inject water. et threashold = 500
if (humidity1 > 500) {
digitalWrite(7, HIGH);
digitalWrite(8, LOW);
} else {
digitalWrite(7, LOW);
digitalWrite(8, LOW);
}
delay(300);
}