## Slide 1: Stem 5 Arduino timer interrupt and external interrupt
KH Wong

## Slide 2: Overview
What is interrupt.
How to use timer interrupt?
  Test5.1
How to use external interrupt?

## Slide 3: What is interrupt?
Main ()
{
:
Doing something
(e.g. browsing)
:
}
Phone rings activate interrupt
Timer interrupt: you may set up a timer to activate interrupt
External interrupt: you may use an external pin to activate interrupt when the external pin changes state.
_isr() //Interrupt service routine
{
some tasks (e.g. answer
telephone)
}//when finished,
//goes back to main
Can happen anytime
Depends on types of interrupts
Phone rings
Phone rings

## Slide 4: Application examples
Regularly reading a sensor, or blinking an LED. Since the timer frequency is fixed, it is more accurate than blinking an LED by a time delay method.
  Timer interrupt: Timer interrupts the CPU at a rate of 1KHz. At each interrupt an timer interrupt service routine (timer_isr) will run to change the state of an LED.
When your computer is running, a key press will trigger an interrupt to input a character to your system
  External interrupt: When a key is pressed (the key is attached to an external pin, so its state will change) an interrupt service routine (ext_isr) will be executed to read the keyboard.

## Slide 5: TEst5.1 Blink LEDs at different frequencies.
// https://www.instructables.com/id/Arduino-Timer-Interrupts/
//this enables all three Arduino timer interrupts.
//timer0 will interrupt at 2kHz, blinking an LED at pin8 at 1KHz
//timer1 will interrupt at 1Hz, blinking an LED at pin13 at 0.5Hz
//timer2 will interrupt at 8kHz, blinking an LED at pin9 at 4KHz

## Slide 6: Setup test5.1.ino
//https://www.instructables.com/id/Arduino-Timer-Interrupts/
//this code will enable all three arduino timer interrupts.
//timer0 will interrupt at 2kHz, blinking an LED at pin8 at 1KHz
//timer1 will interrupt at 1Hz, blinking an LED at pin13 at 0.5Hz
//timer2 will interrupt at 8kHz, blinking an LED at pin9 at 4KHz
//storage variables
boolean toggle0 = 0;boolean toggle1 = 0;boolean toggle2 = 0;
void setup(){
//set pins as outputs
pinMode(8, OUTPUT); pinMode(9, OUTPUT); pinMode(13, OUTPUT);
cli();//stop interrupts
//set timer0 interrupt at 2kHz
TCCR0A = 0;// set entire TCCR2A register to 0
TCCR0B = 0;// same for TCCR2B
TCNT0 = 0;//initialize counter value to 0
// set compare match register for 2khz increments
OCR0A = 124;// = (16*10^6) / (2000*64) - 1 (must be <256)
// turn on CTC mode
TCCR0A |= (1 << WGM01);
// Set CS01 and CS00 bits for 64 prescaler
TCCR0B |= (1 << CS01) | (1 << CS00);
// enable timer compare interrupt
TIMSK0 |= (1 << OCIE0A);
//set timer1 interrupt at 1Hz
TCCR1A = 0;// set entire TCCR1A register to 0
TCCR1B = 0;// same for TCCR1B
TCNT1 = 0;//initialize counter value to 0
// set compare match register for 1hz increments
OCR1A = 15624;// = (16*10^6) / (1*1024) - 1 (must be <65536)
// turn on CTC mode
TCCR1B |= (1 << WGM12);
// Set CS12 and CS10 bits for 1024 prescaler
TCCR1B |= (1 << CS12) | (1 << CS10);
// enable timer compare interrupt
TIMSK1 |= (1 << OCIE1A);
//set timer2 interrupt at 8kHz
TCCR2A = 0;// set entire TCCR2A register to 0
TCCR2B = 0;// same for TCCR2B
TCNT2 = 0;//initialize counter value to 0
// set compare match register for 8khz increments
OCR2A = 249;// = (16*10^6) / (8000*8) - 1 (must be <256)
// turn on CTC mode
TCCR2A |= (1 << WGM21);
// Set CS21 bit for 8 prescaler
TCCR2B |= (1 << CS21);
// enable timer compare interrupt
TIMSK2 |= (1 << OCIE2A);
sei();//allow interrupts
}//end setup

## Slide 7: ISR Interrupt service routines of test5.1.ino
ISR(TIMER0_COMPA_vect){//timer0 interrupt
//2kHz toggles pin8
//generates pulse wave of frequency 2kHz/2 = 1kHz
// (takes 2 cycles for full wave- toggle high then low)
if (toggle0){
digitalWrite(8,HIGH);
toggle0 = 0;
} else{
digitalWrite(8,LOW);
toggle0 = 1;
}
}
ISR(TIMER1_COMPA_vect){//timer1 inter.1Hz toggles p13
//generates pulse wave of frequency 1Hz/2 = 0.5kHz
// (takes 2 cycles for full wave- toggle high then low)
if (toggle1){
digitalWrite(13,HIGH);
toggle1 = 0;
} else{
digitalWrite(13,LOW);
toggle1 = 1;
}
}
ISR(TIMER2_COMPA_vect){
//timer1 interrupt 8kHz toggles p9
//generates pulse wave of
//frequency 8kHz/2 = 4kHz
// (takes two cycles for full
//wave-toggle high
//then toggle low)
if (toggle2){
digitalWrite(9,HIGH);
toggle2 = 0;
}
else{
digitalWrite(9,LOW);
toggle2 = 1;
}
}
void loop(){
//do other things here
}

## Slide 8: Test5.1 code (full code) https://www.instructables.com/id/Arduino-Timer-Interrupts/
Test 5.1: Timer interrupt
//timer interrupts
//by Amanda Ghassaei
//June 2012
//https://www.instructables.com/id/Arduino-Timer-Interrupts/
//
/*
* This program is free software; you can redistribute it and/or modify
* it under the terms of the GNU General Public License as published by
* the Free Software Foundation; either version 3 of the License, or
* (at your option) any later version.
*
*/
//timer setup for timer0, timer1, and timer2.
//For arduino uno or any board with ATMEL 328/168.. diecimila, duemilanove, lilypad, nano, mini...
//https://www.instructables.com/id/Arduino-Timer-Interrupts/
//this code will enable all three arduino timer interrupts.
//timer0 will interrupt at 2kHz, blinking an LED at pin8 at 1KHz
//timer1 will interrupt at 1Hz, blinking an LED at pin13 at 0.5Hz
//timer2 will interrupt at 8kHz, blinking an LED at pin9 at 4KHz
//storage variables
boolean toggle0 = 0;
boolean toggle1 = 0;
boolean toggle2 = 0;
void setup(){
//set pins as outputs
pinMode(8, OUTPUT);
pinMode(9, OUTPUT);
pinMode(13, OUTPUT);
cli();//stop interrupts
//set timer0 interrupt at 2kHz
TCCR0A = 0;// set entire TCCR2A register to 0
TCCR0B = 0;// same for TCCR2B
TCNT0 = 0;//initialize counter value to 0
// set compare match register for 2khz increments
OCR0A = 124;// = (16*10^6) / (2000*64) - 1 (must be <256)
// turn on CTC mode
TCCR0A |= (1 << WGM01);
// Set CS01 and CS00 bits for 64 prescaler
TCCR0B |= (1 << CS01) | (1 << CS00);
// enable timer compare interrupt
TIMSK0 |= (1 << OCIE0A);
//set timer1 interrupt at 1Hz
TCCR1A = 0;// set entire TCCR1A register to 0
TCCR1B = 0;// same for TCCR1B
TCNT1 = 0;//initialize counter value to 0
// set compare match register for 1hz increments
OCR1A = 15624;// = (16*10^6) / (1*1024) - 1 (must be <65536)
// turn on CTC mode
TCCR1B |= (1 << WGM12);
// Set CS12 and CS10 bits for 1024 prescaler
TCCR1B |= (1 << CS12) | (1 << CS10);
// enable timer compare interrupt
TIMSK1 |= (1 << OCIE1A);
//set timer2 interrupt at 8kHz
TCCR2A = 0;// set entire TCCR2A register to 0
TCCR2B = 0;// same for TCCR2B
TCNT2 = 0;//initialize counter value to 0
// set compare match register for 8khz increments
OCR2A = 249;// = (16*10^6) / (8000*8) - 1 (must be <256)
// turn on CTC mode
TCCR2A |= (1 << WGM21);
// Set CS21 bit for 8 prescaler
TCCR2B |= (1 << CS21);
// enable timer compare interrupt
TIMSK2 |= (1 << OCIE2A);
sei();//allow interrupts
}//end setup
ISR(TIMER0_COMPA_vect){//timer0 interrupt 2kHz toggles pin 8
//generates pulse wave of frequency 2kHz/2 = 1kHz (takes two cycles for full wave- toggle high then toggle low)
if (toggle0){
digitalWrite(8,HIGH);
toggle0 = 0;
}
else{
digitalWrite(8,LOW);
toggle0 = 1;
}
}
ISR(TIMER1_COMPA_vect){//timer1 interrupt 1Hz toggles pin 13 (LED)
//generates pulse wave of frequency 1Hz/2 = 0.5kHz (takes two cycles for full wave- toggle high then toggle low)
if (toggle1){
digitalWrite(13,HIGH);
toggle1 = 0;
}
else{
digitalWrite(13,LOW);
toggle1 = 1;
}
}
ISR(TIMER2_COMPA_vect){//timer1 interrupt 8kHz toggles pin 9
//generates pulse wave of frequency 8kHz/2 = 4kHz (takes two cycles for full wave- toggle high then toggle low)
if (toggle2){
digitalWrite(9,HIGH);
toggle2 = 0;
}
else{
digitalWrite(9,LOW);
toggle2 = 1;
}
}
void loop(){
//do other things here
}

## Slide 9: Test 5.2 External interrupt test
Interrupt arises whenever the normal flow of a program has to be halted temporarily to another routine.
  For example to serve an interrupt (IRQ) for a hardware key press input
  The LED will toggle (change state: from high to low, or low to high) when the push button is depressed once.
Arduino
Computer

## Slide 10: Test5.2 external interrupt code https://www.allaboutcircuits.com/technical-articles/using-interrupts-on-arduino/ The resistor (10K) and capacitor (10uF) attached to the push button are used to minimize the denounce problem
const int buttonPin = 2;
const int ledPin = 13;
int buttonState = 0;
void setup() {
Serial.begin(9600);
pinMode(ledPin, OUTPUT);
// init input pin:
pinMode(buttonPin, INPUT);
//interrupt ISR vector
attachInterrupt(0, pin_ISR, CHANGE);
}
void loop() {
// Nothing here!
while (1)
{
Serial.println(“Main loop1");
delay(1000);
Serial.println(“Main loop2");
delay(1000);
}
}
void pin_ISR() {
buttonState = !buttonState;
digitalWrite(ledPin, buttonState);
Serial.println("INTERRUPTED");
Serial.println(buttonState);
}
The 100 Ohm resistor is used to limit current flow

## Slide 11: Test 5.2 External interrupt Full code
// Pull up resistor
//pin2 ----------10k Ohm--->5V
// | |
// 10uF--- / on-off sw1
// --- |
// | |
// GND GND
//
//Pin 13 ---100 Ohm -->|--GND
// LED
//
// variables will change:
const int buttonPin = 2; // the number of the pushbutton pin
const int ledPin = 13; // the number of the LED pin
// variables will change:
//volatile int buttonState = 0; // variable for reading the pushbutton status
int buttonState = 0; // variable for reading the pushbutton status
void setup() {
Serial.begin(9600);
// initialize the LED pin as an output:
pinMode(ledPin, OUTPUT);
// initialize the pushbutton pin as an input:
pinMode(buttonPin, INPUT);
// Attach an interrupt to the ISR vector
attachInterrupt(0, pin_ISR, CHANGE);
}
void loop() {
// Nothing here!
while (1)
{
Serial.println("Normal Working 1");
delay(1000);
Serial.println("Normal Working 2");
delay(1000);
}
}
void pin_ISR() {
//buttonState = digitalRead(buttonPin);
buttonState = !buttonState;
digitalWrite(ledPin, buttonState);
Serial.println("INTERRUPT C A L L E D");
Serial.println(buttonState);
}